| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#42 |
| Source:* | Rong Long, CMCC,longrong@chinamobile.com Muralidhar Vakkalagadda, TCS, muralidhar.vakkalagadda@tcs.com Sridhar.C V，TCS,Sridhar.cv@tcs.com |
| Date:* | 2019-09-18 |
| Reason for Change/s:* | Adding a new Device model |
| CR against: Release* | Rel.4 |
| CR against: WI* | Active WI-0084 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V4.1.0 |
| Clauses * | clauses in 6.3.2 new clause 5.5.4.x |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces a new Device model

-----------------------Start of change 1-------------------------------------------

#### 5.5.4.x deviceWaterPurifier

A Water Purifier is an appliance to filter the impurity substance in water by different filter elements. This Water Purifier information model provides capabilities to control and monitor Water Purifier specific functions and resources.

Table 5.5.4.x-1: Modules of deviceWaterPurifier Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.1.12. |
| runState | runState | true | See clause 5.3.1.75. |
| timer | timer | true | See clause 5.3.1.90. |
| waterQualityMonitor | waterQualityMonitor | true | See clause 5.3.1.98 |
| filterInfo | filterInfo | true | See clause 5.3.1.35. |
| waterLevel | liquidRemaining | true | See clause 5.3.1.51 |
| waterFilter | waterFilterType | true | See clause 5.3.1.x |

-----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------6.3.2  Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| Device3DPrinter | dTDPr |
| deviceAirConditioner | deACr |
| deviceAirPurifier | deAPr |
| deviceAirQualityMonitor | dAQMr |
| deviceAudioReceiver | deARr |
| deviceBloodPressureMonitor | dBPMr |
| deviceCamera | devCa |
| deviceClothesDryer | deCDr |
| deviceClothesWasher | deCWr |
| deviceClothesWasherDryer | dCWDr |
| deviceCoffeeMachine | deCMe |
| deviceCookerHood | deCHd |
| deviceCooktop | devCp |
| deviceDehumidifier | devDr |
| deviceDishWasher | deDWr |
| deviceDoor | devD0 |
| deviceDoorLock | deDLk |
| deviceElectricVehicleCharger | dEVCr |
| deviceFan | devFn |
| deviceFoodProbe | deFPe |
| deviceFreezer | devFr |
| deviceGlucosemeter | devGr |
| deviceHeartRateMonitor | dHRMr |
| deviceHomeCCTV | dHCCT |
| deviceHumidifier | devHr |
| deviceKettle | devKe |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceMultiFunctionPrinter | dMFPr |
| deviceOutdoorLamp | deOLp |
| deviceOven | devOn |
| devicePrinter | devPr |
| devicePulseOximeter | dePOr |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceScanner | devSr |
| deviceSecurityPanel | deSPl |
| deviceSetTopBox | dSTBx |
| deviceSmartElectricMeter | dSEMr |
| deviceSmartPlug | deSPg |
| deviceSteamCloset | deSCt |
| deviceStorageBattery | deSBy |
| deviceSwitch | devSh |
| deviceTelevision | devTn |
| deviceThermometer | devTr |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| deviceWaterValve | deWVe |
| deviceWeightScaleAndBodyCompositionAnalyser | dWSAB |
| deviceWindowShade | deWSe |
| deviceWaterPurifier | deWPr |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.3.1.x	waterFilterType

This ModuleClass indicates the type of the water purifier.

Table 5.3.1.x.: DataPoints of waterFilterType ModuleClass

| Name | Type | R-W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| filterType | hd:enumWaterFilterType | R | false |  | The type of water purifier. list of Water Filter Type(see clause5.6.x). |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 5.6.x hd:enumWaterFilterType

Used for the “filterType” data point of the “waterFilterType” ModuleClass.

Table 5.6.x-1: Interpretation of hd:enumWaterFilterType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | RO | This value indicates the Revers Osmosis type water filter. |
| 2 | UV | This value indicates the Ultraviolet type water filter. |
| 3 | UF | This value indicates the UltraFiltration type water filter. |
| 4 | AC | This value indicates the Activate Carbon type water filter. |
| 5 | SF | This value indicates the Sediment type water filter. |

### -----------------------End of change 4---------------------------------------------