| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM 42 |
| Source:* | Andrew Min-gyu Han, Hansung University, andyhan@hansung.ac.kr Joong-kwon Lim,Hansung University, naulim@hansung.ac.kr |
| Date:* | 2019-09-23 |
| Reason for Change/s:* | Provides contents on External Organization Activity of 3GPP |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <WI-0092> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR0058 v0.0.1 |
| Clauses * | 2.2, 11.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This documents contains a summary of 3GPP activities for railway domain. It will be included in TR-0058 and provide brief information to railway vertical industry on 3GPP railway domain activities.

### -----------------------Start of change 1-------------------------------------------

# 11	External Organization Activities on Railway Domain

## 11.1	3GPP

### 11.1.1	Introduction

The railway industry is beginning to consider the next generation communication system, as known as “Future Railway Mobile Communication System”.  Korea railway industry is building its communication system with LTE technology and named “LTE-R”. UIC will start its first FRMCS trial implementations expected to start around 2020.

To support these moving, 3GPP have set numbers of Work Items support the railway vertical domain. 3GPP SA WG1 focuses requirements of railway domain and SA WG6 considers systematic issues such as system architecture and functionality of railway communication system.

### 11.1.2	Activities

In 3GPP, the following Work Items are approved to support railway domain.

For Release 17:

- FS_FRMCS3: Study on Future Railway Mobile Communication System Phase 3 (SA WG1)

- MONASTERYEND: Complete Gap Analysis for Railways Mobile Communication System  (SA WG1)

- eMONASTERY2 - Enhancements to Application Architecture for the Mobile Communication System for Railways Phase 2 (SA WG6)

For Release 18:

- FS_RAILSS: Study on supporting Railway Smart Station Service (SA WG1)

The relations between Work Items and Releases of 3GPP are depicted in Figure 11.1.2-1.

Figure 11.1.2-1. Relations between Railway Domain Work Items and Releases in 3GPP

The starting point of considering railway domain in 3GPP is TR22.889[i.x] technical report is consisted of various use cases, potential requirements and gap analysises between the requirements and existed 3GPP specification.

The use cases are categorized as follows:

- Basic functionalities

- Critical communication applications

- Performance communication applications

- Business communication applications

- Critical support applications

- Performance support applications

- Business support applications

- FRMCS System principles

TR22.889 will adapt 3GPP transport to provide communication to railway users. It eventually will resemble GSM-R and will additionally provide communication capabilities beyond what GSM-R has been able to. It will provide higher data rates, lower data latencies, multimedia communication, and improved communication reliability. FRMCS considers end-to-end use cases and also provides requirements that might or might not be in scope of 3GPP existing specifications. To facilitate smooth migration from legacy communication systems (e.g. GSM) to FRMCS, interworking requirements between legacy communication systems and FRMCS are provided.

Figure 11.1.2-2. High-level relation of FRMCS and legacy systems

In the persfact of IoT, the FS_RAILSS covers usecases on smart station services which are consisted of various sensors, actuators and components to implement IoT services for railway.

Mostly, 3GPP specifications which related to railway domain, focuses communication functions, but also handles basic considerations for IoT functions as well.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Clause -------------

## 2.2	Informative references

[i.x]	3GPP TR22.889 Technical Specification Group Services and System Aspects; Study on Future Railway Mobile Communication System; Stage 1

### -----------------------End of Changes to References  -------------

### -Start of changes to Definition of terms symbols and abbreviations-

# 3	Definition of terms, symbols and abbreviations  3.1	Terms

## 3.3	Abbreviations

3GPP	3rd Generation Partnership Project

FRMCS	Future Railway Mobile Communication System

MONASTERY	Mobile Communiation System for Railway

MCPTT	Mission Critical Service Push-to-Talk

MCX	Mission Critical Service Push-to-Talk/Video/Data

RAILSS	Railway Smart Station Service

### ---End of changes to Definition of terms, symbols and abbreviations---

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?