| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM 42 |
| Source:* | Andrew Min-gyu Han, Hansung University, andyhan@hansung.ac.kr Joong-kwon Lim,Hansung University, naulim@hansung.ac.kr |
| Date:* | 2019-09-23 |
| Reason for Change/s:* | Provides contents on External Organization Activity of TTA |
| CR against: Release* | Rel-4 |
| CR against: WI* | Active <WI-0092> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR0058 v0.0.1 |
| Clauses * | 2.2, 11.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This documents contains a summary of TTA activities for railway domain. It will be included in TR-0058 and provide brief information to railway vertical industry on TTA railway domain activities.

### -----------------------Start of change 1-------------------------------------------

# 11	External Organization Activities on Railway Domain

## 11.3	TTA

### 11.3.1	Introduction

Korea has launched LTE-based railway communication system as an infrastructure for railway services and expands the scope into IoT converged smart services such as railway smart station.

TTA is the standard development organization of Korea and is developing railway domain standards focuses on LTE-based communication. WG9051 (Railway Communication Work Group) under the PG905(ITS and vehicle ICT Project Group) of TTA leads the railway standardization.

TTA defines specifications on railway domain which are related to requirements on railway communication, railway operation and maintenance and railway smart services in specific area such as smart station.

### 11.3.2	Activities

TTA WG9051 has published following specifications:

- TTAR-06.0175 On-Board Unit of LTE based Railay Communication System

- TTAK.KO-06.0437 LTE based Railway Communication System Requirements (Conventional and High Speed Railway)

- TTAK.KO-06.0438 LTE based Railway Communication System Architecture (Conventional and High Speed Railway)

- TTAK.KO-06.0457 Specification of Interoperability Methods between LTE Based Railway Communication systems and existing communication systems(VHF, TRS-ASTRO/TETRA)

- TTAR-06.0205 Configuration of Base station for LTE-R system of railway communications (Technical Report)

In the TTAK.KO-06.438[i.x] describes a structure for FRMCS as Figure 11.3.2-1.

Figure 11.3.2-1. Structure FRMCS system of TTA

TTA has plan to consider on requirements of information model for railway IoT.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Clause -------------

## 2.2	Informative references

[i.x]	TTAK.KO-06.0438 LTE based Railway Communication System Architecture (Conventional and High Speed Railway)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definition of terms symbols and abbreviations-

# 3	Definition of terms, symbols and abbreviations  3.1	Terms

## 3.3	Abbreviations

FRMCS	Future Railway Mobile Communication System

GSM-R	Global System for Mobile communications for Railway

TRS	Terrestrial Radio communication System

UE	User Equipments

### ---End of changes to Definition of terms, symbols and abbreviations---

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?