| Input Contribution |
| --- |
| Meeting ID* | RDM#43 |
| Title:* | Smart Ontology Gap Analysis |
| Source:* | Sunil Kumar, KETI, sunil75umar@keti.re.kr SeungMyeong Jeong, KETI, sm.jeong@keti.re.kr InSong Lee, KETI, insong@keti.re.kr |
| Date:* | 2019-11-30 |
| Input related to* | TR-0061 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | Incorporate the contribution into the TR. |
| Template Version: November 2018 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution is containing Gap Analysis of existing ontology model in smart city domain.

Please find details below.

In R01:

- Updates references and abbbreviations.

In R02:

- Corrects misspellings.

- Corrects punctuations.

- Replaces the term “section” with “clause”.

- Updates the points in clause 6.2.2.

- Updates the structure of clauses in 6.3.

- Adds clause 6.3.4 and 6.4.4.

- Converges similar points into single generalized points, in the clause 6.3.1, 6.3.2, 6.3.3, 6.4.1, 6.4.2 and 6.4.3.

- Excludes examples, that will be added in next revision.

- Updates headings for clause 6.2, 6.3, 6.4 and 6.5.

- In R03:

- Corrects Clause Identifier for clause 6.4.3 and 6.4.4

- Removes incomplete sentence in clause 6.5.

----------------------- Start of new text 1 -----------------------

# 6	Gap Analysis of existing ontology models for smart city domain

This clause provides the detailed analysis of the limitations in existing ontologies for the smart city domain. The limitations are analysed using principles based on current best practices of ontology design.These principles involve the considerations for topology and structure, terminologies, granularity, logical criteria, etc. The issues highlighted in this study are mainly focused on the selected standard ontology models, considering only smart city domain. Regarding this analysis, scope limitations are identified and discussed to provide more reliable conclusions, considering a controlled environement,  as an ontology model always remains the subject to be updated based on the open-world assumption [i.1].

## 6.1	Data Consideration for Smart City

The main goal of Smart City Ontologies is to enable semantic annotation, interoperability and reusability, for the data generated and exchanged in the smart city information systems. In this regard, the semantic support does not only considers devices, but different others as well. Smart City incorporates different IoT service provisioning, covering multiple domains, such as air-quality, weather, parking, public transportation, electricity, etc. In order to confine the scope of analysis, following aspects have been considered for Smart City domain:

1)	Device Aspect

The deployment of IoT devices in Smart City environment emphasizes the need to consider the device aspects in Ontology design and development. In this case, SSN [i.2] and other such standards have been referred, which specifically focused on Knowledge model representing IoT as well as non-IoT device concepts, for example, Input, Output, State, Function, Command, Variable, etc. This information are essential for the interworking with IoT applications. Using this knowledge model, Devices such as, sensors, actuators or any other computation capable IoT device can be represented and the semantically annotated information such as Function and Variable can be reused among devices and systems.

2)	Service Aspect

Although oneM2M, SAREF and other IoT standards covers service aspects at architecture level including interfaces and APIs, there is still a need for the semantic representation of the information at higher level for the systems and platforms supporting such IoT network, especially in Smart City domain. For example, Weather and Air-Quality data acquisition through Weather station, Parking Service Provider’s Profile, Parking Congestion Estimation, etc. These information cannot be annotated using above defined concepts. To overcome this limitation, standards such as SAREF and SEAS provide extended knowledge representation for the Smart City domain.

3)	Non-IoT Data Aspects

The existing approaches focused on data acquisition and analysis, considering the IoT devices and other embedded systems. However, smart city covers much broader scope, which includes not only the IoT sensor data, but also requires concentration towards static, historical and other data aspects. These includes: statistical evaluations, profile information regarding person, organizations, places, events, contact information, pricing related data, census data, information regarding device and system models, their specifications, compatibility, etc. Hence the considered systems and environments should be able to support all this data representation schemes as well structuring them semantically, to support interoperability.

4)	Modularization

Modularization is the key feature that is considered amongst almost all the IoT standards. The main advantage is the optimization in terms of data management, scalability, load balancing, query time, etc. For the efficient ontology management from both design and implementation aspects, we have considered modularization of ontology based on Information domains. The knowledge model has been designed considering two different aspects of representation. One is the Smart City common ontology model, which is the representation of generalized concepts and relationships, and second are the extensions of this model which represents specific domain information such as smart parking ontology, weather ontologym, air-quality ontology, etc.

## 6.2	Ontology Design Evaluation Criteria

This clause describes the required criteria  for the principle of ontology design, based on which the existing ontology models have been studied. These requirements are derived based on the best practices of ontology design[i.1, i.3, i.4]. Furthermore, these requirements have been categorized into two types of criteria: general evaluation and evaluation for granularity.

### 6.2.1	      General evaluation criteria

General evaluation criteria involves principles, which are independent of application domains and must be validated in ontology design process.

- Completeness: This involves the essential requirement to provide sufficient conceptual representations that can cover the required domain. Although, this criteria will always be limited to existing reseach in the considered domain, it should be validated against existing knowledge repositories in each stage of ontology design process.

- Adaptability: The concepts of adaptability offers to achieve monotonic revision of ontology. In addition, it also supports to achieve the application goals of integration and scalability. In order to satisfy this criteria, the ontology should anticipate the considered tasks and should adhere to changes as well as extensions. The defined axioms should be stable enough to allow changes and addition of new ones.

- Clarity: This criteria incorporates different considerations in ontology design process. This involves clear and well defined concept classes and relationships representing the considered domain. Specifically, the definitions should be independent of subjectivity and context, should be documented and should be able to convey accurately, the meaning to its considered users.

- Conciseness: The ontology is considered concise if it does not include redundant and irrelevant axioms based on the considered domain. In addition, the relevant and essential axioms used for the concept representation, should be minimal.

### 6.2.2	      Granularity based Evaluation criteria

In addition to the general evaluation criteria defined above, some requirement of particularity must be ascertain for ontology design evaluation. These are specified as follows.

- Logical criteria: that the ontology model should satisfy the basic logical constraints that are consistency and satisfiability. An ontology is inconsistent if it’s axioms does not hold true in any possible world. However, a class may be consistent, but it will be unsatisfiable, if it is evaluated as an empty set in any model. In other words, if any instance is defined for that class, it will be evaluated as unsatisfiable.

- Structural criteria: This criteria validates the ontology structure as a topological arrangement of classes and relationships, evaluating the appropriate knowledge representation.

  - The ontology should contain a valid taxanomy. A taxanomy serves as the backbone of an ontology, where the concept classes form a hierarchy representing a directed acyclic graph with single root class. This hierarchy is developed using at least one of the two relations: Inheritance (is-a subsumption) and composition (part-of subsumption). Generally, the hierarchy follows a direction from generic to specific concepts in inheritance and from aggregated to segregated concepts.

  - The ontology relations should not demonstrate any ambiguity with respect to terminology and direction. In particular, the terminology should be able to distinguish between general and specific concept. In addition, the relationship terminology should also indicate the direction. For example; instead of “subSystem”, the relation should be termed as “subSystemOf”, because it indicates the direction from one class to another.

- The ontology concepts should not include multiple inheritance. In other words, the taxanomy should not involve any class with multiple parent classes. There are multiple factors considered in order to define this criteria. One is the computation performance, as the time and computation complexity will be reduced in inference as well as reasoning tasks by avoiding multiple inheritance. Second is the design maintenance and update, as the addition and removal of axioms will easier for the designer considering and ontology with single inheritance. Third factor is the consideration of integration and reuse. For example, complexity of ontology mapping, merging and alignment will reduce drastically using the ontology with single inheritance.

  - Unique Identification: Each concept and relation in an ontology should be uniquely identified. This is one basic criteria which is essential for the application program, where the processes such as searching and crawling techniques are dependent on the predefined identifiers. In addition, the ontology itself should be associated with unique identifiers, for each version of the defined ontology.

  - Role characteristics: The ontology should ascertain role characteristics such as disjointness, transitivity, functional and other such relations where necessary.

    - Disjointness is necessary in concepts where one instance can be represented by only one of two classes. For example: the instance “smart_phone” can only be defined under class “Device” and can never be defined in class “Human_User”. In this case, the property of disjointness should be defined between these two classes.

    - Transitive properties are used for defining sequence of relationship between one or more classes. For example, consider the owl:ObjectProperty “subZoneOf” defined as transitive, having both rdfs:domain and rdfs:range as “Zone” class. Then by defining the relationships “parking_spot subZoneOf parking_lot” and “parking_lot subZoneOf city_district”, the ontology user can infer the relation “parking_spot subZoneOf city_district”.

    - The functional property restricts the owl:ObjectProperty or owl:DatatypeProperty to have single unique relationship for any rdfs:domain associated with it. For example, each instance of class “Device” will have only one relationship “hasID” as owl:DatatypeProperty.

    - There are other role characteristics besides mentioned above, which ensures the completeness at granular level of an ontology. For further details, refer to [i.5].

  - Univocity: The terminologies used in an ontology should ascertain univocity. That is, the term used to defined the concepts should communicate one unique meaning. In particular, the terms which are homographs (which have same spelling but different meaning), must include the exact definition to avoid ambiguity. For example, the term “lead” can be interperated as “to guide” or as “the metal”. Therefore appropriate meaning is required for the interpretation. For the case of different terms with same meanings, synonyms should be defined in annotations for the proper usage and to avoid any ambiguities in updating the ontology in future.

  - Rigidity: The concept classes in an ontology should ascertain rigidity. For this criteria, the concept definitions must involve essential features without which its’ members can not exist. For example, an IoT device will have all its essential features such, being able to communication through Internet, can perform computation, etc. without which it can not be identified as an IoT device. In addition, it supports the property that a rigit class will always be a subclass of a rigid one. This property can be used to evaluate taxonomy appropriately.

  - Singular terminology: The ontology concepts should be defined using singular terminology. Mostly the taxanomy defined in an ontology consists of either inheritance (is-a hierarchy) or composition (part-of hierarchy) of concepts. In such case, the representations are best representated when the defined terms are singular. For example, the relation “parking_lot is_a Zones” clearly shows ambiguous representation.

  - Definitions for non-root terms: The ontology should include definitions for atleast all the non-root terms, where the definitions should involve the essential features and avoid circularity. The criteria for defining essential features has been discussed previously. A cicular definition will involve same term used in it’s representation. For example, consider the following definition: “The area which represents Zone.”. This will be a considered as a circular definition of class “Zone”, because it does not stipulate additional information to describe it’s nature or any of it’s essential features. One recommendation to avoid circularity is to include the terminology from the parent or super class, followed by specifying the essential distinguishing features which defines it’s existence. For example, the class “ParkingLot”, which is defined as “The Zone, where cars or other vehicles are left temporarily”, validates the above defined criteria.

The other aspects such as context, representation, modularization, reusability, realism, adherence to reality, etc. vary based on domain and ontology design approach, hence will be discussed according to the relevance. .

## 6.3	Gap analysis of SAREF ontologies

This clause provides the detailed analysis of the gaps highlighted in SAREF ontologies considering the smart city domain. Some concepts which are relevant in smart city domain, are not included as part of SAREF4City ontology, however, are defined in SAREF ontology. Therefore, those concept definitions have been considered for the evaluation. The discussion is organised into point-based highlighted gaps and categorized according to the general evaluation criteria defined in clause 6.2.1.

Editor’s note: Examples involved for the respective points will be added later in Annex. The points involving the examples, contain a text label: <Example Reference>

6.3.1	      Gap analysis based on completeness

- The class saref:Service is defined as “a representation of a function to a network that makes the function discoverable, registerable, remotely controllable by other devices in the network”. Here, the class covers only some part of computing aspect. There can be other services such as; the ones which are provided as a commodity. Also, in computing concept, there can be other services, which may not consider device aspects, for example, data management and analysis, data security, task monitoring and management, etc. Hence, the other aspects of services are not available, which may cover possible smart city concept representation.

6.3.2	      Gap analysis based on adaptability

- SAREF provides relations with external ontology concept representations, which promotes reusability of existing ontologies. However, it lack the structure supporting taxonomy as well as open-ended ontology design process. <Example Reference>

- The classes saref:FunctionRelated and saref:BuildingRelated though demonstrate a valid taxonomy, they may not be optimized in terms of usage and concept representations. For example, there will be many cases where a single device will be performing many functions, therefore it will be difficult to create concise assertions for them, using the current taxanomy.

- The axiom ‘saref:DoorSwitch subClassOf( saref:consists of someValuesFrom saref:Switch )’ may lead to inconsistent taxanomy or unsatifiable assertions due to the existence of axiom: ‘saref:DoorSwitch subClassOf saref:Switch’.

6.3.3	      Gap analysis based on clarity

- There are different concepts and relationships in SAREF ontologies, in which the terminologies used in their assertions, posses the nature of covering either wider or narrower scope, unlike their respective definitions. Therefore, the constraints applied for the usage of those assertions lack clarity, considering the terminology compared to their respective descriptions. In addition, these terminologies are preoccupied with existing scope limitations. This will increase the uncertainty as well as the complexity to search the assertions relevant to the required usage, as there will be multiple assertions defined in the future, having similar terminologies with different scope limitations. <Example Reference>

- The class saref:State is defined as, “The state in which a device can be found …”. First, this definition assert circularity. Secondly, this definition has limited scope as it is only focused on device aspect whereas other events can also have states to define their life cycle in the considered environment. For example, some process or system having state as running, paused, finished, queued, etc.

- The relation saref:isMeasuredIn highlights ambiguity as it includes saref:Commodity as its domain. However, entities such as service as a commodity can not be measured using saref:UnitOfMeasure class.

- The class saref:State should be defined as subClassOf saref:Property, as it should be considered as a property which deals with the state of any entity.

- In certain property definitions, some of the terminology used, highlights uncertainity in identifying their proper usage. <Example Reference>

### 6.3.4	      Gap analysis based on conciseness

- Based on the current versions of the considered ontology modules, there are no assertions that are evaluated as redundant or irrelevant based on the criteria defined in clause 6.2.1.

- 6.4	Gap analysis of SEAS ontologies

This clause provides the detailed analysis of the gaps highlighted in SEAS ontologies considering the smart city domain. The following discussion considered the selected SEAS ontology modules that are highly relevant for the smart city domain. This includes all the core SEAS ontology modules as well as some of the vertical domain ontologies. The discussion is organised into point-based highlighted gaps and catagorized in accordance with the general evaluation criteria defined in clause 6.2.1

### 6.4.1	      Gap analysis based on completeness

- In seas:CityOntology module, there are some missing concept representations identified, with repsect to completing the scope of domain. For example, idustrial area, public area, neighbourhood, etc. <Example Reference>

- In seas:BuildingOntology, there are certain definitions, such as, those of seas:BuildingSpatialStructure, seas:BuildingSpace and seas:Ceiling, which do not provide enough details through which its usage can be ascertained. <Example Reference>

- Regarding the aspect of completeness in seas:DeviceOntology ontology, there are certain concepts whose representation is not available. <Example Reference>

### 6.4.2	      Gap analysis based on adaptability

- seas:Property can some times also be declared as seas:FeatureOfInterest. This may create different limitations as well as complexities in terms of ontology extension. For example, if an entity requires representation using properties (i.e owl:ObjectProperty and owl:DataProperty) involving both seas:Property and  seas:FeatureOfInterest, then two entities has to be created. In addition, seperate propery has to be defined, which represents the relationship between those two entities. Another complexity can be witnessed in deciding that which class should be used for representation, due to their dual nature of representation. In the class description (defined as a rdfs:comment) of seas:Property, it is well explained that how a seas:Property can be utilized as a seas:FeatureOfInterest. However, the example used in the description leads to another enigma regarding property subsumption, which will be discussed later in this clause. Besides, external applications can not identify this usage using any ontology definition other than the rdfs:comment defined for seas:Property.  Hence an agent based application has to rely on Natural Language Processing in order to identify this comprehensive usage of seas:Property.

- seas:PercentageProperty that is subsumed by seas:Property, although is correctly defined based on univocity and rigidity, is too specific to representing the data aspect rather than representing the high level aspects of the properties. This may result in increased complexity in creating relationships between classes of domain seas:FeatureOfInterest, seas:Property and seas:Evaluation. Since it covers only the data aspect of represention, additional assertions will be needed to be defined and related to seas:PercentageProperty. <Example Reference>

- In the Zone ontology, the properties seas:absoluteHumidity, seas:populationFlow, seas:saturatedVapourPressure and seas:specificHumidity are defined as a sub-property of seas:hasProperty, in seas:FeatureOfInterestOntology module. The property seas:hasProperty has its domain and range defined as seas:FeatureOfInterest and seas:Property respectively. However, the above mentioned properties include both of their domains and ranges as sub-classes of seas:Property. This may result in ambiguity in defining assertions as all the individuals in the property assertion, involving the above mentioned properties, can not be related to each other using the property seas:hasProperty [i.6]. <Example Reference>

- Certain classes in the modules, seas:PlayerOntology, seas:CityOntology and seas:BuildingOntology, support multiple inheritance, which may cause a drawback for ontology extensions. These classes are seas:Player, seas:Bridge, seas:CarPark, seas:Stadium and class seas:Building.

### 6.4.3	      Gap analysis based on clarity

- Based on the definition, the property seas:value, defined in seas:EvaluationOntology, should be renamed as seas:constantValue, in order to avoid preoccupation of the terms.

- Certain properties in the Procedure Execution Ontology (pep:) module, have unspecified or restricted domains and ranges defined, in contrast of the terminologies used. These properties are pep:hasCommand, pep:hasInput, pep:hasOutput, pep:hasResult, pep:hasSimpleCommand, pep:hasSimpleResult, pep:implements, pep:made and pep:madeby. <Example Reference>

- Different SEAS ontologies have used the term “agent” and the class seas:Player in different assertions and descriptions. However there is a potential obscurity between these two terminologies and their usage in SEAS ontologies. The class seas:Player is defined as “One of the important people, companies etc involved in a particular industry, market, situation etc”. There are different SEAS ontology modules, such as seas:OfferingOntology, seas:FlexibilityOntology, seas:BuildingOntology, etc. where seas:Player has been used in object property assertions, while involving the term “agent” in their descriptions. Additionally, the term “agent” used in different places in SEAS, lack proper referencing, as it is important for the user application to identify the exact usage of the considered class. <Example Reference>

- The definition for seas:CivilEngineeringWork accentuates subjectivity as it states that it should not be classified under buildings. In this case, there are two situations to be considered. First, this concept implies its existence more towards higher level ontology than seas:BuildingOntology module. Although its existence in seas:BuildingOntology is valid based on logical constraints, users may not expect such class in this ontology. Secondly, alghough it has provided different examples that can be considered as seas:CivilEngineeringWork, based on the open-world assumption, there can be infinite many concepts that may be considered under its definition since the it uses negation for describing it’s essential feature.

- The definition class seas:Garage in seas:BuildingOntology, and the classes seas:Authority, seas:ElectricityMarket and seas:SmartChargingProvider, in seas:PlayerOntology module, accentuates circularity.

- In seas:BuildingOntology module, the classes seas:Laundry, seas:LowEnergyHouse, seas:PassiveHouse, seas:Room and seas:Sauna, involve certain terms in their definitions, which highlights ambiguity in identifying their scope and usage. <Example Reference>

- In the seas:ZoneOntology, the terminologies used to define the properties seas:absoluteHumidity, seas:area, seas:humidity, seas:population, seas:populationFlow, seas:saturatedVapourPressure, seas:specificHumidity and seas:volume do not specify direction from their respective domains to ranges, which is not in accordance with the best practices of ontology design.

- The seas:CityOntology module definition is stated as: “The SEAS City ontology contains subclasses of zones usefull to describe cities”. However, it does not include the details that which aspect of features can be involved, for example infrastructure, administration, etc. Since the city domain requires extensive conceptual representation, therefore it is important for the user to realize the aspects which the ontology covers.

### 6.4.4	      Gap analysis based on conciseness

- Based on the current versions of the considered ontology modules, there are no assertions that are evaluated as redundant or irrelevant based on the criteria defined in clause 6.2.1.

- 6.5	Gap analysis summary

SAREF and SEAS ontologies and their extensions are aimed at supporting smart systems for different domains. Both standardization work mainly focused on semantic interoperability and reusability as well as on providing common model of consensus. The positive aspect of considering these ontologies is their high relevance towards smart city domain. SAREF has contributed by the development of SAREF4City ontology, specialized for smart city domain and SEAS ontologies involve different modules such as seas:CityOntology, seas:BuildingOntology, seas:PlayerOntology, etc. that support representation of smart city ecosystems. In this regard, these ontologies have been analysed based on the evaluation criteria defined in clause 6.2. Table 6.5-1 provides the overview of the highlighted gaps, identified in the considered ontologies discussed in clause 6.3 and clause 6.4, based on the general evaluation criteria defined in clause 6.2.1.

Table 6.5-1. General Citera Evaluation for SAREF/SAREF4City and SEAS

|  | SAREF / SAREF4City | SEAS |
| --- | --- | --- |
| Completeness | Missing Concept Representations | Missing Concept Representations |
| Adaptability | Segregated taxonomy, inconsistency, unoptimized subsumption | Lack of univocity, unoptimized subsumption, improper domain/range definitions in the subsumption of object property, multiple inheritance. |
| Clarity | Terminology with limited scope, terminology with uncertain meaning and usage in ontology, circularity. | Terminology with contra unclear scope definitions, lack of univocity, circularity, uncertain concept definition and usage based on taxonomy, subjectivity |
| Conciseness | - | - |

Table 6.5-2 provides the overview of the highlighted gaps, identified in the considered ontologies discussed in clause 6.3 and clause 6.4, based on the granular level evaluation criteria defined in clause 6.2.2.

Table 6.5-2. Granularity based Criteria Evaluation for SAREF/SAREF4City and SEAS

|  | SAREF / SAREF4City | SEAS |
| --- | --- | --- |
| Logical Criteria | Axioms with potential unsatisfiable assertions | owl:objectProperties with potential unsatisfiable assertions |
| Structural Criteria | Segregated taxonomy, unclear class subsumption | Multiple inheritance, misleading class position in taxonomy with respect to its definition |
| Unique Identification | - | - |
| Role Characteristics | - | - |
| Univocity | Class definition with less optimized usage | Class definitions with similar scope and lack of uniquely identified features |
| Rigidity | - | Definitions with lack of essential features |
| Non-singular Terminology | - | - |
| Definitions for non-root terms | Circular definitions | Circular definitions |

----------------------- End of new text 1 -----------------------

----------------------- Start of new text 2 -----------------------

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

- [i.1]		R. Arp, B. Smith, A. D.Spear, “Building Ontologies with Basic Formal Ontology” (Book)

- [i.2]		W3C Recommendation 19 October 2017: " Semantic Sensor Network Ontology"

- [i.3]		P. Hitzler, M. Krtzsch, S. Rudolph, “Foundations of Semantic Web Technologies”. (Book)

- [i.4]		S. Staab, R. Studer, “Handbook on Ontologies” (Book)

- [i.5]		W3C Recommendation 10 February 2004: “OWL Web Ontology Language Reference”

- NOTE:	Available at https://www.w3.org/TR/owl-ref/

- [i.6]		C. Maria Keet, 8 October 2012, “Detecting and Revising Flaws in OWL Object Property”.

- NOTE: 	Available at https://link.springer.com/chapter/10.1007/978-3-642-33876-2_23

----------------------- End of new text 2 -----------------------

----------------------- Start of new text 3 -----------------------

Annex <A>:
Examples of highlighted gaps

Examples of highlighted gaps, for the considered ontologies (SAREF and SEAS ontologies), are as follows.

# A.1	Examples of highlighted gaps in SAREF ontologies

TBD.

# A.2	Examples of highlighted gaps in SEAS ontologies

TBD.

----------------------- End of new text 3 -----------------------

----------------------- Start of change 1 -----------------------

## 3.3	Abbreviations

Abbreviations should be ordered alphabetically.

Clause numbering depends on applicability.

For the purposes of the present document, the [following] abbreviations [given in ... and the following] apply:

SAREF	Smart Appliances REFerence ontology

SAREF4CITY	SAREF extension for the smart cities domain

SAREF4ENER	SAREF extension for energy domain

SAREF4ENVI	SAREF extension for the environment domain

SAREF4BLDG	SAREF extension for the building domain

SAREF4INMA	SAREF extension for the industry & manufacturing domain

SAREF4AGRI	SAREF extension for the smart agriculture and food chain domain

AIOTI	Alliance for Internet of Things Innovation

FOAF	Friend of A Friend ontology

CPSV	Core Public Service Vocabulary

STF	Specialist Task Forces

s4city	namespaece used in the SAREF4City ontology

SEAS	Smart Energy Aware systems

ITEA	Information Technology for European Advancement

SDK	Software Development Kit

IRI	International Resource Identifier

OWL	Web Ontology Language

saref				namespace used in the SAREF ontology
	s4city				namespace used in the SAREF4City ontology
	seas				namespace used in the SEAS ontology
	foaf				namespace used in the FOAF ontology
	pep				namespace used in Procedure Execution Ontology, a module of SEAS ontologies

----------------------- End of change 1 -----------------------