| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM #44 |
| Source:* | Cyrille Bareau, Orange, cyrille.bareau@orange.com Marianne Mohali, Orange, marianne.mohali@orange.com Przemyslaw Ratuszek, Orange, przemyslaw.ratuszek@orange.com Bob Flynn, Chordant, Bob.Flynn@chordant.io Andreas Kraft, Deutsche Telekom, Andreas.Kraft@t-systems.com |
| Date:* | 2020-02-20 |
| Reason for Change/s:* | See the introduction below |
| CR against: Release* | Release 4 |
| CR against: WI* | Active WI-0084 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 v. 4.3.0 |
| Clauses * | New clauses: 5.6.xa-f, 5.8, 6.3.4 Modified clauses: 5.7, 6.2.2, 6.2.4, 6.2.5, 6.3.2, 6.3.3, A.2, C.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

Introduction

The SDT-based Harmonized Information Model is used to model the functional behaviour of devices, but it does not allow operating them in other ways: control, supervision, configuration, life cycle, firmware/software management, etc. In other words, TS-0023 does not specify how to manage these devices, in the classical sense of Device Management: this must be done through the CSF designed in TS-0001 6.2.4, using resources such as <mgmtObj> and <mgmtCmd>.

We propose here a new approach that consists in transposing the Device Management functions into SDT modules. We present some new modules that are very close to <mgmtObj> resources. The idea is to give the users a simple, unified framework for handling both functional and management behaviours of devices.

This approach is agnostic of existing DM protocols. The IPE in charge of NoDN devices can rely on a DM technology if it deals with devices that have a specific DM stack (e.g. OMA DM / LwM2M, BBF TR-069 / USP…), or it can use a proprietary protocol, or it can use standardized IoT protocols (e.g. ZigBee, Z-Wave…), etc.

As Device Management is a transversal set of functions that may concern all devices, we do not explicitly add these new modules as possible children of all the devices that are specified in TS-0023, but we define a new, optional flexNodeLink attribute in SDT devices flexContainers that is a link relation that points to a [flexNode] <flexContainer> specialization (similar to the nodeLink relation pointing to the CSEBase <node> child). This flexNode contains these new DM modules as children.

The concepts introduced in this CR are represented in green in the figure below. The [flexNode] is a <flexContainer> specialization that is the parent of SDT ModuleClasses (<flexContainer> resources), specialized for Device Management purposes. This [flexNode] is the target of a flexNodeLink attribute in the SDT device model. Note that it is still possible to have a nodeLink from a SDT device to a <node> resource, for other usages than Device Management. In this case, the [flexNode] will point to the same <node>. Its parent is not precised here because it could be created under an <AE>, a <CSEBase> or a <flexContainer> depending on the use cases.

### **********************  Start of change 1   **********************

## 5.8 Device Management

### 5.8.1 Introduction

The modules that are specified in this section allow performing classical Device Management (DM) functions: rebooting a device, upgrading it, reading / setting its configuration, monitoring its logs, checking its memory or battery status, managing its firmware or its software modules, etc.

In the case of a NoDN, it is the IPE in charge of exposing the device to oneM2M that creates / implements these modules. It may rely on external Device Management techniques like e.g. LwM2M (from OMA) or USP (from BBF), or any other technique, proprietary or standardized, that allows performing at least some DM functions, for instance a reboot.

### 5.8.2 flexNode

This flexContainer specialization is the root for SDT-based Device Management modules.

It is targeted by the flexNodeLink attribute of <flexContainer> SDT devices (see in 6.2.2 the rules 1-6, 1-7 and 1-8).

Table 5.8.2-1: Modules of flexNode model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| dmAgent | dmAgent | 1 | See clause 5.8.3 |
| dmDeviceInfo | dmDeviceInfo | 0..1 | See clause 5.8.4 |
| dmDataModelIO | dmDataModelIO | 0..N | See clause 5.8.5 |
| dmFirmware | dmFirmware | 1..N | See clause 5.8.6. |
| dmSoftware | dmSoftware | 0..N | See clause 5.8.7 |
| dmEventLog | dmEventLog | 0..N | See clause 5.8.8 |
| battery | battery | 0..N | See clause 5.3.1.10 |

NOTE: The current list of modules for Device Management is not fixed and can evolve with new optional features.

Table 5.8.2-2: Resource Specific Attributes of [flexNode] resource

| Attributes of [flexNode] | Multiplicity | RW/ RO/ WO | Description | [flexNodeAnnc] attributes |
| --- | --- | --- | --- | --- |
| nodeLink | 0..1 | RW | The resource identifier of a <node> resource, if any, that stores the node specific information of the NoDN on which the interworked service represented by this [flexNode]> resource resides. |  |
| hostedAELinks | 0..1(L) | RO | This attribute allows to find the AEs that are represented by this [flexNode] resource, if any. The attribute shall contain a list of resource identifiers of <AE> resources representing the ADN-Aes that are represented by the current [flexNode] resource. | OA |
| hostedServiceLinks | 0..1(L) | RO | This attribute allows to find SDT device <flexContainer> resources that have been created to represent services hosted on a device (ADN or NoDN proxied by an IPE), the device being represented by this [flexNode] resource. If the device hosts a set of services represented by SDT device <flexContainer>s, then the attribute shall contain the list of resource identifiers of these <flexContainer> resources. | OA |

If the <flexContainer>(s) that are listed in the hostedServiceLinks attribute have a nodeLink attribute that points to a <node>, then :

-	if there are more than one such <flexContainer>, they shall all have the same nodeLink attribute value, and

-	this [flexNode] resource shall have a nodeLink attribute with the same value.

### 5.8.3 dmAgent

This ModuleClass is the entry point module of [flexNode]; it provides capabilities to control and monitor the Device Management of the device.

Table 5.8.3-1 Actions of dmAgent ModuleClass

| Return Type | Name | Arguments | Optional | Description |
| --- | --- | --- | --- | --- |
| none | reboot | rebootType: hd:enumRebootType | false | Execute a reboot or a factory reset |

The DataPoints of dmAgent Module Class are as follows:

- ‘state’ represents the state of the agent for DM purposes (ready, sleeping, etc.).

- some optional device properties which can be used for Device Management purpose. The dmAgent can be seen as a ‘dashboard’ that gathers common information such as battery level, memory or CPU usage…

Table 5.8.3-2 DataPoints of dmAgent ModuleClass

| Name | Type | R/W | Optional | Unit | Description |
| --- | --- | --- | --- | --- | --- |
| state | hd:enumDmAgentState | R | false |  | The current state of the agent (ready, error, etc.) |
| storageAvailable | xs:integer | R | true | KB | The size of available storage memory. |
| storageTotal | xs:integer | R | true | KB | The size of total storage memory. |
| ramAvailable | xs:integer | R | true | KB | The size of available RAM memory. |
| ramTotal | xs:integer | R | true | KB | Total size of the RAM memory. |
| powerStatus | hd:enumPowerState | R | true |  | The status of the electrical power. |
| cpuUsage | xs:integer | R | true | % | Current CPU usage in percent. |
| systemTime | m2m:timestamp | RW | true |  | Reference time for the device. |
| friendlyName | xs:string | RW | true |  | The device friendly name. |
| description | xs:string | RW | true |  | A human readable description of the device (e.g. Alice’s cell phone, kitchen’s fridge…) |

### 5.8.4 dmDeviceInfo

This ModuleClass is used to share static information regarding the device.

Table 5.8.4-1 DataPoints of dmDeviceInfo ModuleClass

| Name | Type | R/W | Optional | Unit | Description |
| --- | --- | --- | --- | --- | --- |
| serialNumber | xs:string | R | true |  | Unique device label assigned by the manufacturer. The value of the datapoint typically exposes the device’s serial number that is specific to a manufacturer. |
| manufacturer | xs:string | R | true |  | The name/identifier of the device manufacturer. |
| manufacturerDetailsLink | xs:string | RW | true |  | URL to manufacturer’s website. |
| manufacturingDate | m2m:timestamp | R | true |  | Manufacturing date of device. |
| model | xs:string | R | true |  | The name/identifier of the device model assigned by the manufacturer. |
| subModel | xs:string | R | true |  | Device sub-model name. |
| hwVersion | xs:string | R | true |  | The hardware version / revision of the device. |
| osVersion | xs:string | R | true |  | Version of the operating system (defined by manufacturer). |
| country | m2m:countryCode | R | true |  | Country code of the device. It could be manufacturing country, deployment country or procurement country. |
| supportURL | xs:anyURI | RW | true |  | URL that points to product support information of the device. |
| presentationURL | xs:anyURI | RW | true |  | To quote UpnP: “the control point can retrieve a page from this URL, load the page into a web browser, and depending on the capabilities of the page, allow a user to control the device and/or view device status. The degree to which each of these can be accomplished depends on the specific capabilities of the presentation page and device”. |

NOTE: although all datapoints are optional, depending on the underlying DM technology, some datapoints should be filled, for instance serialNumber, manufacturer and model when this information is available.

### 5.8.5 dmDataModelIO

This ModuleClass provides capabilities to handle the device’s Data Model for cases where the underlying Device Management technology supports APIs that are not directly reflected in the flexNode modules.

Table 5.8.5-1 Actions of dmDataModelIO ModuleClass

| Return Type | Name | Arguments | Optional | Description |
| --- | --- | --- | --- | --- |
| result: xs:string | readIO | address: xs:string | true | Read the current values of parameters. Argument: the list of the parameter names. Returns a JSON serialization of the parameters (see Rule 3-6 in clause 6.2.4). |
| Result: xs:string | writeIO | address: xs:string payload: xs:string | true | Update the current values of parameters. Arguments: ‘address’: the list of the parameter names, ‘payload’: the list of the parameter values. Returns the list of the modified parameter names. |

NOTE: the specified ‘result’ value in the Return Type column shall be mapped to a ‘result’ [customArrribute] of the <flexContainer> that maps the action (cf Rule 3-2 in clause 6.2.4).

Table 5.8.5-2 DataPoints of dmDataModelIO ModuleClass

| Name | Type | R/W | Optional | Unit | Description |
| --- | --- | --- | --- | --- | --- |
| dataModelType | hd:enumDataModelType | R | false |  | The type of the data model (OMA DM, OMA LwM2M, BBF TR-181, etc.). |

The readIO and writeIO actions are defined for handling parameters of the underlying Device Management protocol using the APIs defined by those technologies. The values used in the address argument are dependent on the value of the dataModelType data point of the dmAgent module.

Example of address values could be ‘Device.WiFi.SSID.1’ if dataModelType=6 (BBF TR-181 USP) or ‘/9/1/1’ if dataModelType=4 (OMA LwM2M).

These address and payload argument can contain several values separated by a comma ‘,’. The payload argument’s value types are the valid JSON primitive types (string, number, boolean, null).

Examples:

readIO(address=”Device.WiFi.SSID.SSID”)

- {“Device.WiFi.SSID.SSID”: “SSIDName”}

readIO(address=”/3/0/1,/3/0/2”)

- {“/3/0/1”:“MyCompany”,“/3/0/2”:“SN376575A86”}

writeIO(address=”Device.DeviceInfo.FriendlyName,Device.WiFi.SSID.SSID”,

payload=”my device,my ssid”}

- {“Device.DeviceInfo.FriendlyName,Device.WiFi.SSID.SSID”}

writeIO(address=”/3/0/15”, payload=”Europe/Paris”)

- {“/3/0/15”}

NOTE: some datapoints of the dmAgent and dmDeviceInfo moduleClasses correspond to fixed parameters in OMA & BBF data models. The corresponding concepts in OMA DM / LwM2M data models (resp. BBF TR-181) are specified in oneM2M TS-0005 (resp. TS-0006). For instance the datapoint memAvailable corresponds to ‘Device.DeviceInfo.MemoryStatus.Free’ in TR-181 (see TS-0006 clause 7.3) and to ‘/3/0/10’ in LwM2M (TS-0005 clause 6.3.4).

### 5.8.6 dmFirmware

This ModuleClass provides Device Management capabilities to control and monitor the firmware of a device.

The device can contain multiple components (a graphic card for instance) that can have individual firmwares, and they need to be managed separately. The [flexNode] allows one [dmFirmware] module per component plus one ‘major’ [dmFirmware] for the device itself.

Individual firmwares are managed using the [dmFirmware] actions presented in Table 5.8.6-1.

Table 5.8.6-1 Actions of dmFirmware ModuleClass

| Return Type | Name | Argument | Optional | Description |
| --- | --- | --- | --- | --- |
| result: xs:string | updateFirmware | url: xs:url version: xs:string | true | Downloads a new firmware to the device / sub-component. In case of devices that do support toggling between multiple preinstalled firmware versions it also starts the firmware flashing/installation process. The updateFirmware action as it results returns an AE/IPE message indicating if the action was successful or not. |
| result: xs:string | toggle | none | true | Toggles between the firmware versions installed on a device/sub-component. In case of devices that do not support such toggling, it triggers the firmware flashing/installation process. The toggle action as it results returns an AE/IPE message indicating if the action was successful or not. |

The abstraction model used for [dmFirmware] manages the firmware through two images: a primary firmware image and a secondary one. Despite the naming both images are equivalent and a secondary image can be actively used by a device just like the primary one.

Using an abstraction model based on two firmware images it is possible to effectively manage firmware on devices with different firmware capabilities. The state machine for firmware management using two images is shown in Figure 5.8.6-1 for devices that do support toggling between multiple preinstalled firmware versions and in Figure 5.8.6-2 for devices that can have only one firmware version installed.

Table 5.8.6-2 DataPoints of dmFirmware ModuleClass

| Name | Type | R/W | Optional | Unit | Description |
| --- | --- | --- | --- | --- | --- |
| multiFirmware | xs:boolean | R | false |  | Indicates if the device/sub-component supports toggling between multiple preinstalled firmware versions |
| primaryState | hd:enumFirmwareState | R | false |  | The current state of the primary firmware image (active, downloading, etc.) |
| primaryName | xs:string | R | false |  | The name of the primary firmware image. |
| primaryVersion | xs:string | R | false |  | The version of the primary firmware image. |
| primaryUrl | xs:url | R | true |  | The URL from which the primary firmware image was downloaded |
| secondaryState | hd:enumFirmwareState | R | true |  | The current state of the secondary firmware image (active, downloading, etc.). Mandatory when updateFirmware is available |
| secondaryName | xs:string | R | true |  | The name of the secondary firmware image. |
| secondaryVersion | xs:string | R | true |  | The version of the secondary firmware image. |
| secondaryUrl | xs:url | R | true |  | The URL from which the secondary firmware image was downloaded |
| component | xs:string | R | true |  | Allows to identify the sub-component that uses this firmware. This datapoint is mandatory if this is a sub-component firmware. |

NOTE: both primary and secondary firmware image related dataPoints are mandatory when updateFirmware is available, however depending on the device capabilities one of the two state machines – the one presented in Figure 5.8.6-1 or the one shown in Figure 5.8.6-2 should be used.

Figure 5.8.6-1: Lifecycle of a dmFirmware for devices that support toggling between preinstalled firmware images

For devices that support toggling between multiple preinstalled firmware images the following rules apply:

-	There is always one firmware image that is in “Active” state.

-	Toggling between firmware images is only possible if one image is in “Ready” state and the other image is in “Active” state.

-	updateFirmware action is always performed on the  image that  is in “Ready” or “Failure” state.

NOTE: it is the AE/IPE responsibility to provide the appropriate action result pointing if the action was triggered on the device or not (e.g. if the current firmware state did not allow it).

In case of a device that can have only one firmware version installed the additional firmware image is used differently. First of all it’s treated as a temporary storage for the updateFirmware action that triggers the download process. When the download process is finished the status of the firmware image is changed to ”Ready”. It’s important to note that in this case the installation/flashing process is started after the toggle action is issued, making it a “long toggle”. At the very same moment the toggle is issued, the previously active firmware image is moved to “Archival” state, making it a historical record that cannot be restored. The reason why it cannot be restored is trivial – it was just overwritten by the flashing process.

For devices that can have only one firmware version installed the following rules apply:

- There is always no more than one firmware image that is in “Active” or “Installing” state.

- Toggling between firmware images is only possible if one image is in “Ready” state and the other image is in “Active” state.

- The toggle action moves the image that was previously in “Active” state to the “Archival” state.

- The toggle action moves the image that was previously in “Ready” state to the “Installing” state.

- updateFirmware action is always performed on the  image that  is in “Archival” or “Failure” state.

- If one image is in “Archival” state and the other is in “Failure” state the updateFirmware action is always performed on the image that is in “Archival” state.

NOTE: it is the AE/IPE responsibility to provide the appropriate action result pointing if the action was triggered on the device or not (e.g. if the current firmware state did not allow it).

### 5.8.7 dmSoftware

This ModuleClass provides DM capabilities to control and monitor software modules of the device.

An instance of this module class represents a software module hosted by the device.

Editor’s Note: This clause is under construction and subject to significant changes.

### 5.8.8 dmEventLog

This ModuleClass provides DM capabilities to control and monitor event logs of the device.

Editor’s Note: This clause is under construction and subject to significant changes.

### ********************* End of Change 1 ******************************************

### ********************* Start of Change 2 ******************************************

### 5.6.xa hd:enumDataModelType

Used for the “dataModelType” DataPoint of the “dmAgent” ModuleClass.

Table 5.6.xa-1 Interpretation of hd:enumDataModelType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | unknown | To be used for a proprietary/unknown protocol |
| 2 | OMA DM 1.3 |  |
| 3 | OMA DM 2.0 |  |
| 4 | OMA LwM2M |  |
| 5 | BBF TR-181 CWMP | Version of TR-181 for TR-069 |
| 6 | BBF TR-181 USP | Version of TR-181 for USP |
| 7 | oneM2M | For native oneM2M devices |

### 5.6.xb hd:enumDmAgentState

Used for the “state” DataPoint of the “dmAgent” ModuleClass.

Table 5.6.xb-1 Interpretation of hd:enumDmAgentState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | ready | The device is ready for DM operations |
| 2 | error | The device is known to be in an error state |
| 3 | sleeping | The device is known to be in sleeping mode |
| 4 | unreachable | The device is not accessible |

### 5.6.xc hd:enumFirmwareState

Used for the “state” DataPoint of the “dmFirmware” ModuleClass.

Table 5.6.xc-1 Interpretation of hd:enumFirmwareState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Active | The firmware is currently active |
| 2 | Ready | The firmware is ready for installation/activation |
| 3 | Downloading | The firmware is being downloaded |
| 4 | Installing | The firmware in being installed |
| 5 | Failure | The firmware installation/download has failed |
| 6 | Archival | The firmware is an archival record that cannot be reactivated. |

### 5.6.xd hd:enumPowerState

Used for the “powerStatus” DataPoint of the “dmAgent” ModuleClass.

Table 5.6.xd-1 Interpretation of hd:enumPowerState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | NORMAL |  |
| 2 | CHARGING |  |
| 3 | CHARGING_COMPLETE |  |
| 4 | DEGRADED |  |
| 5 | LOW |  |
| 6 | CRITICAL |  |
| 7 | NOT_INSTALLED |  |

### 5.6.xe hd:enumRebootType

Used for the “rebootType” argument of the “reboot” action of the “dmAgent” ModuleClass.

Table 5.6.xe-1 Interpretation of hd:enumRebootType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | reboot |  |
| 2 | rebootWhenReady | Reboot needed when the device is available for it |
| 3 | factoryReset | “hard” reset |
| 4 | softReset |  |

### 5.6.xf hd:enumSoftwareState

Table 5.6.xf-1 Interpretation of hd:enumSoftwareState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | NotInstalled |  |
| 2 | Installing |  |
| 3 | Downloading |  |
| 4 | Verifying |  |
| 5 | Inactive |  |
| 6 | Activating |  |
| 7 | Active |  |
| 8 | Deactivating |  |
| 9 | Uninstalling |  |
| 10 | Failure |  |

### **********************  End of change 2   **********************

### **********************  Start of change 3   **********************

## 5.7 Universal and Common Properties for Device models

Universal and common properties are defined either as the specialized [objectAttibute]s of the [deviceInfo] resource in annex D.8 of TS-0001[3] when the Device model contains a nodeLink attribute that links to a <node> resource, or as specialized custom attributes of the [dmDeviceInfo] in clause 5.8.4 when the Device model contains a flexNodeLink attribute that links to a [flexNode] resource (See Rule 1-8 in clause 6.2.2). Some properties are mandatory for all device models and called "Universal Properties", since they are universally seen in typical device types and carry necessary information to identify each device instance. Others are optional for all device models and called "Common Properties", since they are commonly used in many device types but not always.

Universal and common properties are applicable to all device models. They are not repeated in the property table of each device model in clause Erreur ! Source du renvoi introuvable., where only device specific properties shall be specified.

NOTE:	The instantiated values of the universal properties might be empty in case of exceptional scenarios, e.g. interworking with non-oneM2M device models.

### **********************  End of change 3   **********************

### **********************  Start of change 4   **********************

### 6.2.2 Resource mapping for Device model

When the AE exposes a controlling interface for a home domain device which is specified as an information model in clause Erreur ! Source du renvoi introuvable., a specialization of the <flexContainer> resource shall be created as the mapping of the model following conversion rules:

Rule 1-1: Each Device model defined in clause Erreur ! Source du renvoi introuvable. shall be mapped to a specialization of <flexContainer>. The containerDefinition attribute shall be set according to Erreur ! Source du renvoi introuvable..

Rule 1-2: Each entry in the ‘Module’ table shall be mapped to a child resource(s) which is mapped as a specialised <flexContainer> following the rule in clause Erreur ! Source du renvoi introuvable..

Rule 1-3: The specialized <flexContainer> resource of the Device model may contain an optional attribute nodeLink (as defined in TS-0001[3] and in TS-0004[4]). The value of nodeLink shall be set to the resource identifier of a <node> resource described in Rule 1-5 below. See also Rule 1-8.

Rule 1-4: XSD file for each Device model shall be named according to Erreur ! Source du renvoi introuvable..

Rule 1-5:  If the nodeLink attribute is present, a <node> resource shall be created on the same hosting CSE as the <flexContainer> representing this Device model. The <node> resource contains all the management information as specialized <mgmtObj> resources (e.g. [firmware]) about the Device model instance for device management purposes.

Rule 1-6: The specialized <flexContainer> resource of the Device model may contain an optional [customAttribute] named flexNodeLink. The value of flexNodeLink shall be set to the resource identifier of a <flexContainer> resource described in Rule 1-7 below. See also Rule 1-8.

Rule 1-7: If the flexNodeLink [customAttribute] is present, a [flexNode] specialization of a <flexContainer> resource shall be created on the same hosting CSE as the <flexContainer> representing this Device model. This [flexNode] resource contains all the Device Management information as specialized <flexContainer> resources defined in 5.8 (e.g. [dmFirmware]) about the device model instance for Device Management purposes. Its containerDefinition shall be “org.onem2m.devicemanagement.flexNode”.

Rule 1.8: at least one of nodeLink (Rule 1-3) or flexNodeLink (Rule 1-6) shall be present. If both are present, the [flexNode] resource pointed to by the flexNodeLink custom attribute shall contain a nodeLink attribute with the same value as this device model’s nodeLink.

### **********************  End of change 4   **********************

### **********************  Start of change 5   **********************

### 6.2.4 Resource mapping for Action

Actions defined as part of  a Device model or a ModuleClass model shall be mapped to the specializations of a <flexContainer> resource. The following rules shall be applied:

Rule 3-1: The containerDefinition attribute shall be set according to Erreur ! Source du renvoi introuvable..

Rule 3-2: When the Action supports any 'Arguments' or 'Return Type', they are mapped to [customizedAttribute] with its variable names.

Rule 3-3: XSD file for each Action shall be named according to Erreur ! Source du renvoi introuvable..

Rule 3-4: When the Action does not support any ‘Argument' or ‘Return Type', the Action shall have a [customizedAttribute] named action. The Action shall be triggered by updating the action attribute with any value.

Rule 3-5: The resourceName attribute for each Action model that appears as a child of a Device or ModuleClass model shall be CREATED with the value set to “Action name”.

Rule 3-6: If an action returns a value that is of a complex data type, i.e. not one of the standard scalar types, then this value shall be encoded as a JSON structure and returned serialized in an xs:string.

### **********************  End of change 5   **********************

### **********************  Start of change 6   **********************

### 6.2.5 Resource mapping for Property

When the Device model (in clause Erreur ! Source du renvoi introuvable.) or the ModuleClass model (in clause Erreur ! Source du renvoi introuvable.) is mapped to the <flexContainer> resource, and if the device supports a Property, the following rules shall be applied:

Rule 4-1: Each entry of ‘Property’ table in ModuleClass model, shall be mapped to the [customAttribute] of <flexContainer> resource which is mapped from associated ModuleClass model, with its Property name with prefix ‘prop’.

Rule 4-2: Each ‘Property’ of a Device model is either mapped to a specialized [objectAttribute] of a [deviceInfo] <mgmtObj> resource following Rule 1-3, when the nodeLink attribute is present, or to a [customAttribute] of a [dmDeviceInfo] <flexContainer> resource following Rule 1-6 otherwise.

### **********************  End of change 6   **********************

### **********************  Start of change 7   **********************

### Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| Device3Dprinter | dTDPr |
| deviceAirConditioner | deACr |
| deviceAirPurifier | deAPr |
| deviceAirQualityMonitor | dAQMr |
| deviceAudioReceiver | deARr |
| deviceBloodPressureMonitor | dBPMr |
| deviceCamera | devCa |
| deviceClothesDryer | deCDr |
| deviceClothesWasher | deCWr |
| deviceClothesWasherDryer | dCWDr |
| deviceCoffeeMachine | deCMe |
| deviceCookerHood | deCHd |
| deviceCooktop | devCp |
| deviceDehumidifier | devDr |
| deviceDishWasher | deDWr |
| deviceDoor | devD0 |
| deviceDoorLock | deDLk |
| deviceElectricVehicleCharger | dEVCr |
| deviceFan | devFn |
| deviceFoodProbe | deFPe |
| deviceFreezer | devFr |
| deviceGlucosemeter | devGr |
| deviceHeartRateMonitor | dHRMr |
| deviceHomeCCTV | dHCCT |
| deviceHumidifier | devHr |
| deviceKettle | devKe |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceMultiFunctionPrinter | dMFPr |
| deviceOutdoorLamp | deOLp |
| deviceOven | devOn |
| devicePrinter | devPr |
| devicePulseOximeter | dePOr |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceScanner | devSr |
| deviceSecurityPanel | deSPl |
| deviceSetTopBox | dSTBx |
| deviceSmartElectricMeter | dSEMr |
| deviceSmartPlug | deSPg |
| deviceSteamCloset | deSCt |
| deviceStorageBattery | deSBy |
| deviceSwitch | devSh |
| deviceTelevision | devTn |
| deviceThermometer | devTr |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| deviceWaterValve | deWVe |
| deviceWeightScaleAndBodyCompositionAnalyser | dWSAB |
| deviceWindowShade | deWSe |
| deviceBottleWarmer | deBWr |
| deviceGarbageDisposal | deGDp |
| deviceWaterPurifier | deWPr |
| flexNode | fleNe |

In protocol bindings resource type names for module classes shall be translated into short names ofTable 6.3.2-2.

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| 3Dprinter | thDPr |
| acousticSensor | acoSr |
| airCleanOperationMode | aCOM0 |
| airConJobMode | aCJMe |
| airConOperationMode | aCOMe |
| airFlow | airFw |
| airPurifierJobMode | aPJMe |
| airPurifierOperationMode | aPOMe |
| airQualitySensor | aiQSr |
| alarmSpeaker | alaSr |
| audioVolume | audVe |
| autoDocumentFeeder | auDFr |
| battery | bat |
| binaryObject | binOt |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| bodyCompositionAnalyser | boCAr |
| boiler | boilr |
| boilingSwitch | boiSh |
| brewing | brewg |
| brewingSwitch | breSh |
| brightness | brigs |
| channel | chanl |
| clock | clock |
| clothesDryerJobMode | cDJMe |
| clothesDryerOperationMode | cDOMe |
| clothesWasherDryerJobMode | cWDJM |
| clothesWasherDryerOperationMode | cWDOM |
| clothesWasherJobMode | cWJMe |
| clothesWasherJobModeOption | cWJMO |
| clothesWasherOperationMode | cWOMe |
| colour | color |
| colourSaturation | colSn |
| controlPanelLock | coPLk |
| cookerHoodJobMode | cHJMe |
| credentials | creds |
| customTemperature | cusTe |
| dataGenerationTime | dgt |
| dehumidifierJobMode | deJMe |
| dehumidifierOperationMode | deOMe |
| dishWasherJobMode | dWJMe |
| dmAgent | dmAgt |
| dmDataModelIO | dDMIO |
| dmDeviceInfo | dmDIo |
| dmEventLog | dmELg |
| dmFirmware | dmFie |
| dmSoftware | dmSoe |
| doorLock | dooLk |
| doorlock | doork |
| doorStatus | dooSs |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| filterInfo | filIo |
| foaming | foamg |
| fridgeTemperature | friTe |
| frozenTemperature | froTe |
| geoLocation | geoLn |
| glucometer | glucr |
| grinder | grinr |
| heatingZone | heaZe |
| heatingZone0 | heaZ0 |
| heatingZone1 | heaZ1 |
| heatingZone2 | heaZ2 |
| heatingZone3 | heaZ3 |
| heatingZone4 | heaZ4 |
| heatingZone5 | heaZ5 |
| height | heigt |
| hotWaterSupply | hoWSy |
| impactSensor | impSr |
| keepWarm | keeWm |
| keypad | keypd |
| liquidLevel | liqLl |
| liquidRemaining | liqRg |
| lock | lock |
| mediaInput | medIt |
| mediaOutput | medOt |
| mediaSelect | medSt |
| milkFoaming | milFg |
| milkQuantity | milQy |
| milkStatus | milSs |
| motionSensor | motSr |
| numberValue | numVe |
| openLevel | opeLl |
| operationMode | opeMe |
| overcurrentSensor | oveSr |
| oximeter | oximr |
| ozoneMeter | ozoMr |
| phoneCall | phoCl |
| playerControl | plaCl |
| powerSave | powS0 |
| printerRunState | prRSe |
| printQueue | priQe |
| pulsemeter | pulsr |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| remoteControlEnable | reCEe |
| robotCleanerJobMode | rCJMe |
| robotCleanerOperationMode | rCOMe |
| runState | runSe |
| scannerRunState | scRSe |
| securityMode | secMe |
| sessionDescription | sesDn |
| signalStrength | sigSh |
| sleepTimer | sleTr |
| smokeSensor | smoSr |
| sphygmomanometer | sphyr |
| spinLevel | spiLl |
| steamClosetJobMode | sCJMe |
| steamClosetOperationMode | sCOMe |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| textMessage | texMe |
| timer | timer |
| turbo | turbo |
| uvSensor | uveSr |
| waterFilterInfo | waFIo |
| waterFlow | watFw |
| waterSensor | watSr |
| waterStatus | watSs |
| weight | weigt |

In protocol bindings resource type names for actions shall be translated into short names of Table 6.3.2-3.

Table 6.3.2-3: Specialization type short names (Actions)

| Resource Type Name | Short Name |
| --- | --- |
| activate | actie |
| activateClockTimer | acCTr |
| answer | answr |
| call | call |
| close | close |
| deactivate | deace |
| deactivateClockTimer | deCTr |
| decrementNumberValue | deNVe |
| downChannel | dowCl |
| downVolume | dowVe |
| hangup | hangp |
| incrementNumberValue | inNVe |
| install | instl |
| nextTrack | nexTk |
| open | open |
| previousTrack | preTk |
| reboot | rebot |
| readIO | reaIO |
| resetNumberValue | reNVe |
| resetTextMessage | reTMe |
| start3Dprint | staDt |
| stop3Dprint | stoDt |
| toggle | togge |
| uninstall | uninl |
| upChannel | uphCl |
| updateFirmware | updFe |
| upVolume | upoVe |
| writeIO | wriIO |

### Resource attributes for properties and data points

In protocol bindings resource attributes names for properties of module classes shall be translated into short names of Table 6.3.3-1.

Table 6.3.3-1: Resource attribute short names (ModuleClass properties)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| chargingCapacity | electricVehicleConnector | chaCy |
| dischargingCapacity | electricVehicleConnector | disCy |
| electricEnergy | battery | eleEy |
| material | battery | matel |
| voltage | battery | volte |

In protocol bindings resource attributes names for data points of module classes shall be translated into short names of Table 6.3.3-2.

Table 6.3.3-2: Resource attribute short names (ModuleClass data points)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| absoluteEnergyConsumption | energyConsumption | abECn |
| absoluteStartTime | timer | abSTe |
| absoluteStopTime | timer | abST0 |
| acousticStatus | acousticSensor | acoSs |
| adfStates | autoDocumentFeeder | adfSs |
| alarm | motionSensor, smokeSensor, temperatureAlarm, waterSensor | alarm |
| alarmStatus | alarmSpeaker | alaSs |
| altitude | geoLocation | altie |
| automode | airFlow | autoe |
| availableChannels | televisionChannel | avaCs |
| basalMetabolism | bodyCompositionAnalyser | basMm |
| bath | hotWaterSupply | bath |
| batteryThreshold | battery | batTd |
| blue | colour | blue |
| bmi | bodyCompositionAnalyser | bmi |
| bodyLength | bodyCompositionAnalyser | bodLh |
| bone | bioElectricalImpedanceAnalysis | bone |
| brightness | brightness | brigs |
| callerID | phoneCall | calID |
| callState | phoneCall | calSe |
| capacity | battery | capay |
| ch2o | airQualitySensor | ch2o |
| channelId | televisionChannel | chaId |
| channelName | televisionChannel | chaNe |
| charging | battery | charg |
| chargingCapacity | electricVehicleConnector | chaCy |
| co | airQualitySensor | co |
| co2 | airQualitySensor | co2 |
| coarseness | grinder | coars |
| code | faultDetection, filterInfo | code |
| coldWash | clothesWasherJobModeOption | colWh |
| colourSaturation | colourSaturation | colSn |
| component | dmFirmware | compt |
| concentration | glucometer | concn |
| contextCarbohydratesAmount | glucometer | coCAt |
| contextCarbohydratesSource | glucometer | coCSe |
| contextExercise | glucometer | conEe |
| contextHealth | glucometer | conHh |
| contextLocation | glucometer | conLn |
| contextMeal | glucometer | conMl |
| contextMedication | glucometer | conMn |
| contextTester | glucometer | conTr |
| country | dmDeviceInfo | couny |
| cpuUsage | dmAgent | cpuUe |
| cupsNumber | brewing | cupNr |
| current | energyConsumption | currt |
| currentAdfState | autoDocumentFeeder | cuASe |
| currentDate | clock | curDe |
| currentJobMode | airConJobMode, airPurifierJobMode, clothesDryerJobMode, clothesWasherDryerJobMode, clothesWasherJobMode, cookerHoodJobMode, dehumidifierJobMode, dishWasherJobMode, robotCleanerJobMode, steamClosetJobMode | cuJMe |
| currentJobModeName | airConJobMode, airPurifierJobMode, clothesDryerJobMode, clothesWasherDryerJobMode, clothesWasherJobMode, cookerHoodJobMode, dehumidifierJobMode, dishWasherJobMode, robotCleanerJobMode, steamClosetJobMode | cJMNe |
| currentJobState | runState | cuJSe |
| currentMachineState | runState | cuMSe |
| currentPlayerMode | playerControl | cuPMe |
| currentPlayerModeName | playerControl | cPMNe |
| currentSecurityMode | securityMode | cuSMe |
| currentTemperature | temperature | curT0 |
| currentTime | clock | curTe |
| currentTimeZone | clock | cuTZe |
| currentValue | smokeSensor | crv |
| data | dmEventLog | data |
| dataModelType | dmDataModelIO | daMTe |
| defaultValue | numberValue, textMessage | defVe |
| defrost | refrigeration | defrt |
| description | faultDetection, dmAgent | dc |
| desiredHumidity | relativeHumidity | desHy |
| detectedTime | overcurrentSensor, smokeSensor | detTe |
| diastolicPressure | sphygmomanometer | diaPe |
| discharging | battery | discg |
| dischargingCapacity | electricVehicleConnector | disCy |
| doorState | doorStatus | dooSe |
| duration | overcurrentSensor, recorder | dur |
| electricEnergy | battery | eleEy |
| enabled | dmEventLog | enabd |
| energy | pulsemeter | enery |
| estimatedTimeToEnd | timer | eTTEd |
| extraRinse | clothesWasherJobModeOption | extRe |
| fat | bioElectricalImpedanceAnalysis | fat |
| fatFreeMass | bodyCompositionAnalyser | faFMs |
| filterLifetime | filterInfo | filLe |
| foamingStrength | foaming | foaSh |
| frequency | energyConsumption | freqy |
| friendlyName | dmAgent | friNe |
| fwVersion | dmDeviceInfo | fweVn |
| generationSource | energyGeneration | genSe |
| grainsRemaining | grinder | graRg |
| green | colour | green |
| hash | binaryObject | hash |
| hba1c | glucometer | hba1c |
| heading | geoLocation | headg |
| headingAccuracy | geoLocation | heaAy |
| heatingLevel | heatingZone | heaLl |
| height | height | heigt |
| horizontalAccuracy | geoLocation | horAy |
| horizontalDirection | airFlow | horDn |
| hwVersion | dmDeviceInfo | hweVn |
| impactDirectionHorizontal | impactSensor | imDHl |
| impactDirectionVertical | impactSensor | imDVl |
| impactLevel | impactSensor | impLl |
| impactStatus | impactSensor | impSs |
| impedance | bodyCompositionAnalyser | impee |
| jobModes | airConJobMode, airPurifierJobMode, clothesWasherDryerJobMode, clothesWasherJobMode, cookerHoodJobMode, dehumidifierJobMode, dishWasherJobMode, robotCleanerJobMode steamClosetJobMode, | jobMs |
| jobStates | runState | jobSs |
| kcal | bioElectricalImpedanceAnalysis | kcal |
| keyNumber | keypad | keyNr |
| latitude | geoLocation | latie |
| level | battery | lvl |
| light | alarmSpeaker | light |
| liquidLevel | liquidLevel | liqLl |
| liquidRemaining | liquidRemaining | liqRg |
| lock | lock | lock |
| loginName | credentials | logNe |
| longitude | geoLocation | longe |
| loudness | acousticSensor | louds |
| lowBattery | battery | lowBy |
| lqi | signalStrength | lqi |
| machineStates | runState | macSs |
| manufacturer | dmDeviceInfo | manur |
| manufacturerDetailsLink | dmDeviceInfo | maDLk |
| manufacturingDate | dmDeviceInfo | manDe |
| material | battery | matel |
| maxHeatingLevel | heatingZone | maHLl |
| maxLength | textMessage | maxLh |
| maxLevel | openLevel | maxLl |
| maxSpeed | airFlow | maxSd |
| maxValue | audioVolume, numberValue, ozoneMeter, temperature | maxVe |
| meanPressure | sphygmomanometer | meaPe |
| measuringScope | energyConsumption | meaSe |
| mediaID | mediaSelect | medID |
| mediaName | mediaSelect | medNe |
| mediaType | mediaSelect | medTe |
| memorySize | 3Dprinter | memSe |
| messageEncoding | textMessage | mesEg |
| minLength | textMessage | minLh |
| minLevel | openLevel | minLl |
| minSpeed | airFlow | minSd |
| minValue | numberValue, temperature | minVe |
| modality | pulsemeter | moday |
| model | dmDeviceInfo | model |
| monitoringEnabled | airQualitySensor | monEd |
| multiFirmware | dmFirmware | mulFe |
| multiplyingFactors | energyConsumption, energyGeneration | mulFs |
| muscle | bioElectricalImpedanceAnalysis | musce |
| muscleMass | bodyCompositionAnalyser | musMs |
| muteEnabled | audioVolume | mutEd |
| name | dmSoftware | name |
| network | 3Dprinter | netwk |
| numberValue | numberValue | numVe |
| object | binaryObject | objet |
| objectType | binaryObject | objTe |
| openAlarm | doorStatus | opeAm |
| openDuration | doorStatus | opeDn |
| openLevel | openLevel | opeLl |
| osVersion | dmDeviceInfo | oseVn |
| overcurrentStatus | overcurrentSensor | oveSs |
| oxygenSaturation | oximeter | oxySn |
| ozoneStatus | ozoneMeter | ozoSs |
| ozoneValueMG | ozoneMeter | ozVMG |
| ozoneValuePPM | ozoneMeter | oVPPM |
| password | credentials | pwd |
| power | energyConsumption | power |
| powerGenerationData | energyGeneration | poGDa |
| powerSaveEnabled | powerSave | poSEd |
| powerState | binarySwitch | powSe |
| powerStatus | dmAgent | powSs |
| presentationURL | dmDeviceInfo | prURL |
| previousChannel | televisionChannel | preCl |
| preWash | clothesWasherJobModeOption | preWh |
| primaryName | dmFirmware | priNe |
| primaryState | dmFirmware | priSe |
| primaryUrl | dmFirmware | priUl |
| primaryVersion | dmFirmware | priVn |
| printingState | printQueue | priSe |
| printSizeX | 3Dprinter | priSX |
| printSizeY | 3Dprinter | priSY |
| printSizeZ | 3Dprinter | priSZ |
| printType | 3Dprinter | priTe |
| progressPercentage | runState | proPe |
| pulseRate | pulsemeter | pulRe |
| pushed | pushButton | pushd |
| ramAvailable | dmAgent | ramAe |
| ramTotal | dmAgent | ramTl |
| rapidCool | refrigeration | rapCl |
| rapidFreeze | refrigeration | rapFe |
| recipientID | phoneCall | recID |
| red | colour | red |
| referenceTimer | timer | refTr |
| relativeHumidity | relativeHumidity | relHy |
| remoteControlEnabled | remoteControlEnable | reCEd |
| resistance | bioElectricalImpedanceAnalysis | resie |
| roundingEnergyConsumption | energyConsumption | roECn |
| roundingEnergyGeneration | energyGeneration | roEGn |
| rr | pulsemeter | r0 |
| rssi | signalStrength | rssi |
| runningTime | timer | runTe |
| sdp | sessionDescription | sdp |
| secondaryName | dmFirmware | secNe |
| secondaryState | dmFirmware | secSe |
| secondaryUrl | dmFirmware | secUl |
| secondaryVersion | dmFirmware | secVn |
| securityModes | securityMode | secMs |
| sensitivity | motionSensor | sensy |
| sensorHumidity | airQualitySensor | senHy |
| sensorOdor | airQualitySensor | senOr |
| sensorPM1 | airQualitySensor | sePM1 |
| sensorPM10 | airQualitySensor | sePM0 |
| serialNumber | dmDeviceInfo | serNr |
| sensorPM2 | airQualitySensor | sePM2 |
| significantDigits | energyConsumption, energyGeneration | sigDs |
| silentTime | motionSensor | silTe |
| size | binaryObject | size |
| smokeThreshhold | smokeSensor | smoTd |
| softLeanMass | bodyCompositionAnalyser | soLMs |
| soilLevel | clothesWasherJobModeOption | soiLl |
| speed | airFlow | speed |
| speedFactor | playerControl | speFr |
| speedWash | clothesWasherJobModeOption | speWh |
| spinLevelStrength | spinLevel | spLSh |
| spinSpeed | clothesWasherJobModeOption | spiSd |
| startPause | operationMode | staPe |
| state | dmAgent, dmSoftware | state |
| status | boiler, dmEventLog, electricVehicleConnector, faultDetection, filterInf, mediaSelect | sus |
| steamTreat | clothesWasherJobModeOption | steTt |
| step | numberValue | step |
| stepValue | audioVolume, openLevel, temperature | steVe |
| storageAvailable | dmAgent | stoAe |
| storageTotal | dmAgent | stoTl |
| strength | brewing | streh |
| subModel | dmDeviceInfo | subMl |
| supportedHorizontalDirection | airFlow | suHDn |
| supportedMediaSources | mediaSelect | suMSs |
| supportedMessageValues | textMessage | suMVs |
| supportedPlayerModes | playerControl | suPMs |
| supportedVerticalDirection | airFlow | suVDn |
| supportURL | dmDeviceInfo | suURL |
| swVersion | dmDeviceInfo | sweVn |
| systemTime | dmAgent | sysTe |
| systolicPressure | sphygmomanometer | sysPe |
| targetAltitude | geoLocation | tarAe |
| targetDuration | timer | tarDn |
| targetLatitude | geoLocation | tarLe |
| targetLongitude | geoLocation | tarL0 |
| targetTemperature | temperature | tarTe |
| targetTimeToStart | timer | tTTSt |
| targetTimeToStop | timer | tTTSp |
| temperature | temperatureAlarm | tempe |
| temperatureThreshhold | temperatureAlarm | temTd |
| textMessage | textMessage | texMe |
| time | keepWarm | time |
| token | credentials | tk |
| tone | alarmSpeaker | tone |
| turboEnabled | turbo | turEd |
| type | dmEventLog | type |
| unit | temperature | unit |
| uri | printQueue | ur0 |
| url | sessionDescription, dmSoftware | ur1 |
| useGrinder | grinder | useGr |
| uvStatus | uvSensor | uvtSs |
| uvValue | uvSensor | uvaVe |
| version | dmSoftware | versn |
| verticalAccuracy | geoLocation | verAy |
| verticalDirection | airFlow | verDn |
| visceraFat | bioElectricalImpedanceAnalysis | visFt |
| voc | airQualitySensor | voc |
| voltage | battery | volte |
| voltage | energyConsumption | volte |
| volumePercentage | audioVolume | volPe |
| washTemp | clothesWasherJobModeOption | wasTp |
| water | bioElectricalImpedanceAnalysis | water |
| waterFlowStrength | waterFlow | waFSh |
| weight | weight | weigt |

### **********************  End of change 7   **********************

### **********************  Start of change 8   **********************

### Resource attributes for actions arguments and return values

In protocol bindings resource attributes names for arguments of actions shall be translated into short names of Table 6.3.4-1.

Table 6.3.4-1: Resource attribute short names (Action arguments)

| Argument Name | Occurs in | Short Name |
| --- | --- | --- |
| address | readIO, writeIO | addrs |
| payload | writeIO | payld |
| rebootType | reboot | rebTe |

In protocol bindings resource attributes names for returned values of actions shall be translated into short names of Table 6.3.4-2.

Table 6.3.4-2: Resource attribute short names (Action return values)

| Returned Value Name | Occurs in | Short Name |
| --- | --- | --- |
| result | readIO, writeIO | resut |

### **********************  End of change 8   **********************

### **********************  Start of change 9   **********************

## A.2	Example for Device model ‘deviceAirConditioner'

The present clause explains the creation process for the device typed 'deviceAirConditioner' (see clause 5.5.1.1 for device model definition of ‘deviceAirConditioner').

Using the definition, 'deviceAirConditioner' model is mapped to [deviceAirConditioner] resource which is a specialization of <flexContainer> resource (See Figure A.2-1).

Figure A.2-1: Structure of [deviceAirConditioner] resource

The AE creates the [deviceAirConditioner] specialization of <flexContainer> resource for the Device model [deviceAirConditioner] resource.

The [deviceAirConditioner] resource contains the child resource specified in Table A.2-2.

Table A.2-2: Child resources of [deviceAirConditioner] resource

| Child Resources of [deviceAirConditioner] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <flexContainer> as defined in the specialization [binarySwitch] | 0..1 | This resource is used to map 'binarySwith' ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [runState] | 0..1 | This resource is used to map 'runState' ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [airConJobMode] | 0..1 | This resource is used to map ‘airConJobMode’ ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [airConOperationMode] | 0..1 | This resource is used to map ‘airConOperationMode’ ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [airCleanOperationMode] | 0..1 | This resource is used to map ‘airCleanOperationMode’ ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [temperature] | 0..1 | This resource is used to map ‘temperature’ ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [timer] | 0..1 | This resource is used to map 'timer' ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [sleepTimer] | 0..1 | This resource is used to map 'sleepTimer' ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [turbo] | 0..1 | This resource is used to map 'turbo' ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [airFlow] | 0..1 | This resource is used to map 'airFlow' ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [powerSave] | 0..1 | This resource is used to map 'powerSave' ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [airQualitySensor] | 0..1 | This resource is used to map 'airQualitySensor' ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <flexContainer> as defined in the specialization [filterInfo] | 0..1 | This resource is used to map 'filterInfo' ModuleClass defined in clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <subscription> | 0..n | See clause 9.6.8 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |

Editor’s Note: Above table should be updated compliant to present structure of deviceAirConditioner.

The [deviceAirConditioner] resource contains the attributes specified in Table A.2-3.

Table A.2-3: Attributes of [deviceAirConditioner] resource

| Attributes of [deviceAirConditioner] | Multiplicity | RW/ RO/ WO | Description |  |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| resourceID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| resourceName | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| parentID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| expirationTime | 1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| creationTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| Labels | 0..1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |  |
| stateTag | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |  |
| creator | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |  |
| containerDefinition | 1 | WO | The value is "org.onem2m.home.device.airconditioner" |  |
| ontologyRef | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| contentSize | 1 | RO | See clause 9.6.35 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |  |
| nodeLink | 0..1 | RO | nodeLink attribute links to a <node> resource that is hosted on the same hosting CSE of the <flexContainer>. See clause 0 and 0 for more details. | At least one of these shall be present |
| flexNodeLink | 0..1 | RO | flexNodeLink attribute links to a [flexNode] specialization of a <flexContainer> resource that is hosted on the same hosting CSE of the <flexContainer>. See clauses 5.8, 6.2.2 and 6.2.5 for more details. |  |

## A.3	Example of ModuleClass 'binarySwitch'

The [binarySwitch] resource is used to share information regarding the modeled binary switch module as a ModuleClass. The [binarySwitch] resource is a specialization of the <flexContainer> resource.

Figure A.3-1: Structure of [binarySwitch] resource

The [binarySwitch] resource contains the child resource specified in Table A.3-2.

Table A.3-2: Child resources of [binarySwitch] resource

| Child Resources of [binarySwitch] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <flexContainer> as defined in the specialization [toggle] | 0..1 | This resource is used to map 'toggle' Action defined in Clause Erreur ! Source du renvoi introuvable.. |
| [variable] | <subscription> | 0..n | See clause 9.6.8 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |

The [binarySwitch] resource contains the attributes specified in Table A.3-3.

Table A.3-3: Attributes of [binarySwitch] resource

| Attributes of [binarySwitch] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| resourceID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| resourceName | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| parentID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| expirationTime | 1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| creationTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| labels | 0..1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| stateTag | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| creator | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| containerDefinition | 1 | WO | The value is "org.onem2m.home.moduleclass.binaryswitch" |
| ontologyRef | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| contentSize | 1 | RO | See clause 9.6.35 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |
| nodeLink | 0..1 | RW | Not applicable to a ModuleClass specialization. This attribute is not present in an instantiation of this resource. |
| flexNodeLink | 0..1 | RW | Not applicable to a ModuleClass specialization. This attribute is not present in an instantiation of this resource. |
| powerState | 1 | RW | See clause Erreur ! Source du renvoi introuvable. |

## A.4	 Example of Action 'toggle'

The [toggle] resource is used to share information regarding the modeled toggle as an Action. The [toggle] resource is a specialization of the <flexContainer> resource.

Figure A.4-1: Structure of [toggle] resource

The [toggle] resource contains the child resource specified in Table A.4-2.

Table A.4-2: Child resources of [toggle] resource

| Child Resources of [toggle] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |

The [toggle] resource contains the attributes specified in Table A.4-3.

Table A.4-3: Attributes of [toggle] resource

| Attributes of [toggle] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| resourceID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| resourceName | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| parentID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| expirationTime | 1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| creationTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| labels | 0..1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| stateTag | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| creator | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| containerDefinition | 1 | WO | The value is "org.onem2m.home.moduleclass.binaryswitch.toggle" |
| ontologyRef | 0..1 | RW | See clause 9.6.35 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.] |
| contentSize | 1 | RO | See clause 9.6.35 in oneM2M TS-0001 [Erreur ! Source du renvoi introuvable.]. |
| nodeLink | 0..1 | RW | Not applicable to an Action specialization. This attribute is not present in an instantiation of this resource. |
| flexNodeLink | 0..1 | RW | Not applicable to an Action specialization. This attribute is not present in an instantiation of this resource. |

### **********************  End of change 9  **********************

### **********************  Start of change 10   **********************

C.1 Introduction

Current SDT models are used only in form of <flexContainer>s, and how to design content attribute of <contentInstance> and <timeSeriesInstance> is left to developers. There is no rule for design of content attribute, it means interoperability of content attribute is low. Then SDT can become one of the rules for design of content attribute, and the low interoperability problem will be solved.

The present clause explains how to use SDT as one of the rules for design of content attribute.

There are several benefits of using SDT in content attribute.

First, the resource architecture can be more simple than the one using <flexContainer>s. When using <flexContainer>s, universal attributes are mapped either into attributes of [deviceInfo] under a <node> besides <flexContainer>s, or into custom attributes of [dmDeviceInfo] under a [flexNode] (See Rule 1-8 in clause 6.2.2). Moreover, Action Class and DataPoint Class are the same layer in SDT, but Action Class is mapped to <flexContainer> itself and DataPoint Class is mapped to attributes of <flexContainer> expressing Module class. On the other hand, Using SDT in content attribute means using only one <contentInstance> or <timeSeriesInstance> so the resource architecture is simple.

Relating this benefit, it becomes easy to understand where to write information.

Second, <contentInstance> and <timeSeriesInstance> becomes more interoperable. How to write SDT in content attribute is able to become one of designs of content attribute and the low interoperability of <contentInstance> and <timeSeriesInstance> will be solved.

Third, If useful libraries are prepared, content attribute is able to be expressed in XML/JSON/CBOR with small changes on program.

In addition, tools can generate validator of the data and converter among the supported formats

### **********************  End of change 10   **********************

# Text boxes

Figure: Relationship between SDT Device, node and flexNode

Ready

Installing

Downloading

Installing

Downloading

Ready

Active

PRIMARY

SECONDARY

TOGGLE

Active

Failure

Failure

Figure 1 Lifecycle of a dmFirmware for devices that can have only one firmware version installed.

Archival

Active

Downloading

Active

Downloading

Archival

Installing

PRIMARY

SECONDARY

TOGGLE

Installing

Ready

Ready

Failure

Failure