| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM# 44 |
| Source:* | Cyrille Bareau, Orange, cyrille.bareau@orange.com Marianne Mohali, Orange, marianne.mohali@orange.com Andreas Kraft, Deutsche Telekom, Andreas.Kraft@t-systems.com Andreas Neubacher, Deutsche Telekom, andreas.neubacher@magenta.at |
| Date:* | 2020-02-18 |
| Reason for Change/s:* | Better reflecting multiplicity in SubDevices’ and Devices’ tables |
| CR against: Release* | Release 4 |
| CR against: WI* | Active WI-0084-SDT based Information Model and Mapping for Vertical Industries MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023, V4.3.0 |
| Clauses * | 5.4, 5.5, 6.2.3, 6.2.7, 6.3.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | n/a |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR presents a proposal to change the tables in sections 5.4 and 5.5 of TS-0023. SDT 4.0 not only supports optional specifications of SubDevices and ModuleClasses, but will allow a more fine grain cardinality of those elements. This fact must be reflected in the tables of the aforementioned sections of TS-0023 as well.

Since the number of tables in these sections is very big, Changes 1 and 2 are presented here in detail as examples to show the general direction of the change.

Change 1 presents a change to the “deviceAirQualityMonitor” specialization, which includes four different ModuleClasses, of which one is mandatory (multiplicity 1) and three are optional (multiplicity 0..1).

Change 2 presents 3 changes where the new ‘list’ cardinality can be applied. The “deviceBloodPressureMonitor” specialization, which includes a SubDevice “subDeviceCuff”, of which the existence of one instance is mandatory, more are optional. This changes the structure of “deviceBloodPressureMonitor”. Until now the number of SubDevices was arbitrary set to six, incrementally numbered. With SDT 4.0 this would now be a list with multiplicity 1..N (ie. at least one SubDevice must be present). Similar change for deviceSmartPlug with 1..N SubDevices powerOutlet.

For the deviceCooktop, this is the number of Module Classes heatingZone that is modified, replacing 6 explicit module instances by a 1..N multiplicity.

It must be warned that these 3 proposed changes would break the compatibility with the previous versions.

The full editing of sections 5.4 and 5.5 is presented in Change 6 and 7.

In 6.2.3, rule 2-4 is completed with more detail on how the multiplicity should be applied to generate a new resourceName index.

In 6.2.7, a new rule 7-4 is added for specifying how the resourceName attribute of SubDevice flexContainers should be created.

In 6.3.2, the table for specialization types short names is updated with the new structure proposed in this CR.

*******  Start of change 1 (extract of change 7 for CR understanding)******

#### 5.5.1.2	deviceAirQualityMonitor

An air quality monitor is an environmental monitoring device used to monitor the air quality.

Table 5.5.1.2-1: Modules of deviceAirQualityMonitor Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| airQualitySensor | airQualitySensor | 1 | See clause 5.3.1.6. |
| battery | battery | 0..1 | See clause 5.3.1.10. |
| connectivity | connectivity | 0..1 | See clause 5.3.1.25. |
| periodicalReportConfig | periodicalReportConfig | 0..1 | See clause 5.3.1.63. |

### ********************* End of Change 1 ************************************

### *******  Start of change 2 (extract of change 7 for CR understanding)******

#### deviceSmartPlug

A smart plug is a device that can turn on and off a connected appliance.

Table 5.5.1.11-1: Modules of deviceSmartPlug model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12. |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| remoteControlEnable | remoteControlEnable | 0..1 | See clause 5.3.1.73. |

Table 5.5.1.11-2: Subdevice of deviceSmartPlug Device model

| Subdevice Instance Name | Subdevice Name | Multiplicity | Description |
| --- | --- | --- | --- |
| powerOutlet | subDevicePowerOutlet | 1..N | See clause 5.4.1.2. |

#### 5.5.3.1	deviceBloodPressureMonitor

A blood pressure monitor is a device that can be used to monitor the blood pressure and is composed of one or more cuffs and a main montor machine.

Table 5.5.3.1-1: Modules of deviceBloodPressureMonitor Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| battery | battery | 1 | See clause 5.3.1.10 |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12 |

Table 5.5.3.1-2: Subdevice of deviceBloodPressureMonitor Device model

| Subdevice Instance Name | Subdevice Name | Multiplicity | Description |
| --- | --- | --- | --- |
| cuff | subDeviceCuff | 1..N | See clause 5.4.1.1 |

#### deviceCooktop

A cooktop is a device that is a kitchen appliance designed for the purpose of cooking food.

Table 5.5.4.8-1: Modules of deviceCooktop model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| heatingZone | heatingZone | 1..N | See clause 5.3.1.44. |

### ********************* End of Change 2 ***********************************

**********************  Start of change 3   **********************

### 6.2.3	Resource mapping for ModuleClass

The ModuleClass models (in clause 5.3) shall be mapped to the specializations of a <flexContainer> resource. The following rules shall be applied:

When the Device model in clause 5.5 is mapped to the <flexContainer> resource, and if the device supports the functionality associated with a ModuleClass in the model, a <flexContainer> resource which is mapped from ModuleClass definitions shall be created as a child resource:

- Rule 2-1: The containerDefinition attribute shall be set according to 6.4.3.

- Rule 2-2: Each entry of 'Action', 'Property', and 'DataPoint' in ModuleClass definitions shall be mapped following the resource mapping rules described in clauses 6.2.4 - 6.2.7.

- Rule 2-3: XSD file for each ModuleClass shall be named according to 6.5.3.

- Rule 2-4: The resourceName attribute for each module class that appears as a child of a Device model shall be CREATED with the value set to “Module Instance Name”. If the module class is contained in a list (multiplicity 0..N or 1..N), its resourceName attribute shall be set to “Module Instance Name” appended with an underscore ‘_’ and an incrementing index so that it is unique in the parent’s children (e.g. “firmware_0”, “firmware_1”, etc.). The index shall not have leading 0’s.

- Rule 2-5: The specialized <flexContainer> resource of the Module model may contain an optional [customAttribute] named dataGenerationTime. The value of dataGenerationTime contains the time when the data was generated by the device. The data type of this custom attribute is m2m:timestamp.

********************* End of Change 3 ******************************************

**********************  Start of change 4   **********************

### 6.2.7	Resource mapping for SubDevice model

When the AE exposes a controling interface for a home domain sub-device which is specified as an information model in clause 5.4, a specialization of the <flexContainer> resource shall be created as the mapping of the model following conversion rules:

- When the SubDevice model in clause 5.4 is mapped to the <flexContainer> resource, and if the device supports the functionality associated with a SubDevice in the model, a <flexContainer> resource which is mapped from SubDevices definitions shall be created as a child resource.

- Rule 7-1: Follow rules 1-1, 1-2, and 1-3 of 6.2.2 "Resource mapping for Device model".

- Rule 7-2: The XSD file for each SubDevice model shall be named following naming convention:

'HD-<name of SubDevice model>-v<version of TS>.xsd'

For example, the XSD file for ‘subDeviceCuff is named as ‘HD-subDeviceCuff-v1_0_0.xsd'.

- Rule 7-3: void.

- Rule 7-4: The resourceName attribute for each SubDevice that appears as a child of a Device model shall be created with the value set to “SubDevice Instance Name”. If the SubDevice is contained in a list (multiplicity 0..N or 1..N), its resourceName attribute shall be set to “SubDevice Instance Name” appended with an underscore ‘_’ and an incrementing index so that it is unique in the parent’s children (e.g. “cuff_0”, “cuff_1”, etc.). The index shall not have leading 0’s.

********************* End of Change 4 ******************************************

**********************  Start of change 5   **********************

### 6.3.2	Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| Device3DPrinter | dTDPr |
| deviceAirConditioner | deACr |
| deviceAirPurifier | deAPr |
| deviceAirQualityMonitor | dAQMr |
| deviceAudioReceiver | deARr |
| deviceBloodPressureMonitor | dBPMr |
| deviceCamera | devCa |
| deviceClothesDryer | deCDr |
| deviceClothesWasher | deCWr |
| deviceClothesWasherDryer | dCWDr |
| deviceCoffeeMachine | deCMe |
| deviceCookerHood | deCHd |
| deviceCooktop | devCp |
| deviceDehumidifier | devDr |
| deviceDishWasher | deDWr |
| deviceDoor | devD0 |
| deviceDoorLock | deDLk |
| deviceElectricVehicleCharger | dEVCr |
| deviceFan | devFn |
| deviceFoodProbe | deFPe |
| deviceFreezer | devFr |
| deviceGlucosemeter | devGr |
| deviceHeartRateMonitor | dHRMr |
| deviceHomeCCTV | dHCCT |
| deviceHumidifier | devHr |
| deviceKettle | devKe |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceMultiFunctionPrinter | dMFPr |
| deviceOutdoorLamp | deOLp |
| deviceOven | devOn |
| devicePrinter | devPr |
| devicePulseOximeter | dePOr |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceScanner | devSr |
| deviceSecurityPanel | deSPl |
| deviceSetTopBox | dSTBx |
| deviceSmartElectricMeter | dSEMr |
| deviceSmartPlug | deSPg |
| deviceSteamCloset | deSCt |
| deviceStorageBattery | deSBy |
| deviceSwitch | devSh |
| deviceTelevision | devTn |
| deviceThermometer | devTr |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| deviceWaterValve | deWVe |
| deviceWeightScaleAndBodyCompositionAnalyser | dWSAB |
| deviceWindowShade | deWSe |
| deviceBottleWarmer | deBWr |
| deviceGarbageDisposal | deGDp |
| deviceWaterPurifier | deWPr |

In protocol bindings resource type names for SubDevice model shall be translated into short names of Table 6.3.2-2.

Table 6.3.2-2: Specialization type short names (SubDevice models)

| Resource Type Name | Short Name |
| --- | --- |
| cuff | cuff |
| powerOutlet | powOt |
| subDeviceCuff | suDCf |
| subDevicePowerOutlet | sDPOt |

NOTE: see section 6.2.7, rule 7-4

In protocol bindings resource type names for module classes shall be translated into short names of Table 6.3.2-3.

Table 6.3.2-3: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| 3DPrinter | thDPr |
| acousticSensor | acoSr |
| airCleanOperationMode | aCOM0 |
| airConJobMode | aCJMe |
| airConOperationMode | aCOMe |
| airFlow | airFw |
| airPurifierJobMode | aPJMe |
| airPurifierOperationMode | aPOMe |
| airQualitySensor | aiQSr |
| alarmSpeaker | alaSr |
| audioVolume | audVe |
| autoDocumentFeeder | auDFr |
| battery | bat |
| binaryObject | binOt |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| bodyCompositionAnalyser | boCAr |
| boiler | boilr |
| boilingSwitch | boiSh |
| brewing | brewg |
| brewingSwitch | breSh |
| brightness | brigs |
| channel | chanl |
| clock | clock |
| clothesDryerJobMode | cDJMe |
| clothesDryerOperationMode | cDOMe |
| clothesWasherDryerJobMode | cWDJM |
| clothesWasherDryerOperationMode | cWDOM |
| clothesWasherJobMode | cWJMe |
| clothesWasherJobModeOption | cWJMO |
| clothesWasherOperationMode | cWOMe |
| colour | color |
| colourSaturation | colSn |
| controlPanelLock | coPLk |
| cookerHoodJobMode | cHJMe |
| credentials | creds |
| customTemperature | cusTe |
| dataGenerationTime | dgt |
| dehumidifierJobMode | deJMe |
| dehumidifierOperationMode | deOMe |
| dishWasherJobMode | dWJMe |
| doorLock | dooLk |
| doorlock | doork |
| doorStatus | dooSs |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| filterInfo | filIo |
| foaming | foamg |
| fridgeTemperature | friTe |
| frozenTemperature | froTe |
| geoLocation | geoLn |
| glucometer | glucr |
| grinder | grinr |
| heatingZone | heaZe |
| height | heigt |
| hotWaterSupply | hoWSy |
| impactSensor | impSr |
| keepWarm | keeWm |
| keypad | keypd |
| liquidLevel | liqLl |
| liquidRemaining | liqRg |
| lock | lock |
| mediaInput | medIt |
| mediaOutput | medOt |
| mediaSelect | medSt |
| milkFoaming | milFg |
| milkQuantity | milQy |
| milkStatus | milSs |
| motionSensor | motSr |
| numberValue | numVe |
| openLevel | opeLl |
| operationMode | opeMe |
| overcurrentSensor | oveSr |
| oximeter | oximr |
| ozoneMeter | ozoMr |
| phoneCall | phoCl |
| playerControl | plaCl |
| powerSave | powS0 |
| printerRunState | prRSe |
| printQueue | priQe |
| pulsemeter | pulsr |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| remoteControlEnable | reCEe |
| robotCleanerJobMode | rCJMe |
| robotCleanerOperationMode | rCOMe |
| runState | runSe |
| scannerRunState | scRSe |
| securityMode | secMe |
| sessionDescription | sesDn |
| signalStrength | sigSh |
| sleepTimer | sleTr |
| smokeSensor | smoSr |
| sphygmomanometer | sphyr |
| spinLevel | spiLl |
| steamClosetJobMode | sCJMe |
| steamClosetOperationMode | sCOMe |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| textMessage | texMe |
| timer | timer |
| turbo | turbo |
| uvSensor | uveSr |
| waterFilterInfo | waFIo |
| waterFlow | watFw |
| waterSensor | watSr |
| waterStatus | watSs |
| weight | weigt |

### ********************* End of Change 5 ******************************************

**********************  Start of change 6   **********************

## SubDevice models

### Common Domain

#### subDeviceCuff

A cuff is a subDevice that expresses the attachment device for measuring blood pressure.

Table 5.4.1.1-1: Modules of subDeviceCuff model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12. |
| sphygmomanometer | sphygmomanometer | 1 | See clause 5.3.1.83. |
| pulsemeter | pulsemeter | 1 | See clause 5.3.1.68. |

#### subDevicePowerOutlet

A powerOutlet is a subDevice that specifies the attachment device for deviceSmartPlug.

Table 5.4.1.2-1: Modules of subDevicePowerOutlet model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12. |
| energyConsumption | energyConsumption | 0..1 | See clause 5.3.1.32. |
| overcurrentSensor | overcurrentSensor | 0..1 | See clause 5.3.1.58. |
| dimmingLevel | numberValue | 0..1 | See clause 5.3.1.55. This provides the capability to change the energy. |

### City Domain

### Health Domain

### Home Domain

### Industry Domain

### Vehicular Domain

********************* End of Change 6 *******************************

**********************  Start of change 7   *************************

## Device models

### Common Domain

#### device3DPrinter

A 3D printer is a smart home appliance to provide 3D printing capabilities.

Table 5.5.1.1-1: Modules of device3DPrinter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| 3Dprinter | 3Dprinter | 1 | See clause 5.3.1.1. |
| runState | runState | 1 | See clause 5.3.1.75. |
| temperature | temperature | 1 | See clause 5.3.1.87. This value of “currentTemperature” in this module instance represents the temperature of the nozzle. This value SHALL be a float number in a range from 0.0 to 1000.0. |
| printQueue | printQueue | 1 | See clause 5.3.1.67. |

#### deviceAirQualityMonitor

An air quality monitor is an environmental monitoring device used to monitor the air quality.

Table 5.5.1.2-1: Modules of deviceAirQualityMonitor Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| airQualitySensor | airQualitySensor | 1 | See clause 5.3.1.6. |
| battery | battery | 0..1 | See clause 5.3.1.10. |
| connectivity | connectivity | 0..1 | See clause 5.3.1.25. |
| periodicalReportConfig | periodicalReportConfig | 0..1 | See clause 5.3.1.63. |

#### deviceAudioReceiver

An audio receiver is a device that receives audio signals from a number of sources, processing them to drive speakers.

Table 5.5.1.3-1: Modules of deviceAudioReceiver model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| audioVolume | audioVolume | 1 | See clause 5.3.1.8. |
| mediaInput | mediaSelect | 0..1 | See clause 5.3.1.53. |
| mediaOutput | mediaSelect | 0..1 | See clause 5.3.1.53. |

#### deviceCamera

A camera is an optical instrument for recording or capturing images, which may be stored locally or transmitted to another locations.

Table 5.5.1.4-1: Modules of deviceCamera Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| sessionDescription | sessionDescription | 1 | See clause 5.3.1.77. |
| playerControl | playerControl | 0..1 | See clause 5.3.1.65. |
| motionSensor | motionSensor | 0..1 | See clause 5.3.1.54. |

#### deviceDoor

A door is a device that is used to open and close a door.

Table 5.5.1.5-1: Modules of deviceDoor model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| openLevel | openLevel | 0..1 | See clause 5.3.1.56. |
| doorlock | lock | 0..1 | See clause 5.3.1.52. |
| doorStatus | doorStatus | 0..1 | See clause 5.3.1.29. |

#### deviceDoorLock

A door lock is a device that can be used to lock, for example, a door.

Table 5.5.1.6-1: Modules of deviceDoorLock Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| doorLock | lock | 1 | See clause 5.3.1.52. |
| doorStatus | doorStatus | 0..1 | See clause 5.3.1.29. |
| battery | battery | 0..1 | See clause 5.3.1.10. |

#### deviceLight

A light is a device that is used to control the state of an illumination appliance.

Table 5.5.1.7-1: Modules of deviceLight Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| colour | colour | 0..1 | See clause 5.3.1.23. |
| colourSaturation | colourSaturation | 0..1 | See clause 5.3.1.24. |
| brightness | brightness | 0..1 | See clause 5.3.1.17. |

#### deviceMultiFunctionPrinter

A Multi Function Printer (MFP) is an office machine which incorporates the functionality of multiple devices in one, so as to have a smaller footprint in home or office. A typical MFP may act as a combination of printer, scanner and more. This MFP information model provides capabilities to control and monitor MFP specific functions and resources.

Table 5.5.1.8-1: Modules of deviceMultiFunctionPrinter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| printerRunState | runState | 1 | See clause 5.3.1.75. |
| scannerRunState | runState | 0..1 | See clause 5.3.1.75. |
| autoDocumentFeeder | autoDocumentFeeder | 0..1 | See clause 5.3.1.9. |
| printQueue | printQueue | 0..1 | See clause 5.3.1.67. |

#### devicePrinter

A printer is a device that is used to monitor or control the state of a printing appliance.

Table 5.5.1.9-1: Modules of devicePrinter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| printQueue | printQueue | 0..1 | See clause 5.3.1.67. |

#### deviceScanner

A scanner is a device that optically scans images, printed text, handwriting or an object, and converts it to a digital image.

Table 5.5.1.10-1: Modules of deviceScanner model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 1 | See clause 5.3.1.75. |
| autoDocumentFeeder | autoDocumentFeeder | 0..1 | See clause 5.3.1.9. |

#### deviceSmartPlug

A smart plug is a device that can turn on and off a connected appliance.

Table 5.5.1.11-1: Modules of deviceSmartPlug model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12. |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| remoteControlEnable | remoteControlEnable | 0..1 | See clause 5.3.1.73. |

Table 5.5.1.11-2: Subdevice of deviceSmartPlug Device model

| Subdevice Instance Name | Subdevice Name | Multiplicity | Description |
| --- | --- | --- | --- |
| powerOutlet | subDevicePowerOutlet | 1..N | See clause 5.4.1.2. |

#### deviceSwitch

A switch is a device that is used to control and monitor the state of power.

Table 5.5.1.12-1: Modules of deviceSwitch Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |

#### deviceThermometer

A thermometer is a device that can be used to check, for example, the body or other temperatures.

Table 5.5.1.13-1: Modules of deviceThermoMeter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| temperature | temperature | 1 | See clause 5.3.1.87. |
| battery | battery | 1 | See clause 5.3.1.10. |

#### deviceThermostat

A thermostat is used to control the ambient temperature of rooms within, for example, a house. This information model provides capabilities to interact with specific functions of thermostats.

Table 5.5.1.14-1: Modules of deviceThermostat Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| runState | runState | 0..1 | See clause 5.3.1.75. The possible values of the “supportedModes” datapoint for the thermostat device are included in clause 5.6.23. |
| timer | timer | 0..1 | See clause 5.3.1.90. |
| temperature | temperature | 1 | See clause 5.3.1.87. |

#### deviceWaterValve

A water valve is a device that is used to turn the water supply ON or OFF remotely.

Table 5.5.1.15-1: Modules of waterValve model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| openLevel | openLevel | 1 | See clause 5.3.1.56. |

### City Domain

#### deviceOutdoorLamp

An outdoor lamp is a smart home appliance to provide lights and information for outside of home with smart sensing capabilities such as ultraviolet sensing.

Table 5.5.2.1-1: Modules of deviceOutdoorLamp Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| brightness | brightness | 0..1 | See clause 5.3.1.17. |
| motionSensor | motionSensor | 0..1 | See clause 5.3.1.54. |
| airQualitySensor | airQualitySensor | 0..1 | See clause 5.3.1.6. |
| uvSensor | uvSensor | 0..1 | See clause 5.3.1.92. |
| timer | timer | 0..1 | See clause 5.3.1.90. The timer is used to set duration of giving lights from the moment of triggering by the “brightness” module or “motionSensor” module. |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |

#### deviceMagneticParkingMonitor

A parking detector is used to detect the state of the parking space. When the vehicle enters the parking space, the detector measure the change of the geomagnetic field strength, and report the state of the parking space to a server.

Table 5.5.2.2-1: Modules of deviceMagneticParkingMonitor Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| battery | battery | 0..1 | See clause 5.3.1.10. |
| connectivity | connectivity | 0..1 | See clause 5.3.1.25. |
| periodicalReportConfig | periodicalReportConfig | 0..1 | See clause 5.3.1.63. |
| ParkingStatus | ParkingStatus | 1 | See clause 5.3.1.62. |
| magneticSensorParameters | magneticSensorParameter | 1 | See clause 5.3.1.61. |

#### deviceSmartElectricMeter

A smart electric meter is a metering device that is used to measure consumption data for electrictricity.

Table 5.5.2.3-1: Modules of deviceSmartElectricMeter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| battery | battery | 0..1 | See clause 5.3.1.10. |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| clock | clock | 0..1 | See clause 5.3.1.18. |
| energyConsumption | energyConsumption | 1 | See clause 5.3.1.32. |
| energyGeneration | energyGeneration | 0..1 | See clause 5.3.1.33. |

#### deviceSmartGasMeter

A smart gas meter is a metering device that is used to measure consumption data for gas.

Table 5.5.2.4-1: Modules of deviceSmartGasMeter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| battery | battery | 0..1 | See clause 5.3.1.10. |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| connectivity | connectivity | 0..1 | See clause 5.3.1.25. |
| periodicalReportConfig | periodicalReportConfig | 0..1 | See clause 5.3.1.63. |
| gasMeterReportInfo | gasMeterReportInfo | 1 | See clause 5.3.1.40. |
| gasMeterControl | binarySwitch | 0..1 | See clause 5.3.1.12. |
| gasMeterAlarm | gasMeterAlarm | 0..1 | See clause 5.3.1.39. |

#### deviceSmartWaterMeter

A smart water meter is a metering device that is used to measure consumption data for water.

Table 5.5.2.5-1: Modules of deviceSmartWaterMeter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| battery | battery | 0..1 | See clause 5.3.1.10. |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| connectivity | connectivity | 0..1 | See clause 5.3.1.25. |
| periodicalReportConfig | periodicalReportConfig | 0..1 | See clause 5.3.1.63. |
| waterMeterSetting | waterMeterSetting | 0..1 | See clause 5.3.1.96. |
| waterMeterReportInfo | waterMeterReportInfo | 1 | See clause 5.3.1.95. |
| waterMeterControl | binarySwitch | 0..1 | See clause 5.3.1.12. |
| waterMeterAlarm | waterMeterAlarm | 0..1 | See clause 5.3.1.94. |

#### deviceStreetLightController

A street light controller is used to control the opening and closing of the street light.

Table 5.5.2.6-1: Modules of deviceStreetLightController Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| geoLocation | geoLocation | 0..1 | See clause 5.3.1.41. |
| connectivity | connectivity | 0..1 | See clause 5.3.1.25. |
| periodicalReportConfig | periodicalReportConfig | 0..1 | See clause 5.3.1.63. |
| slcReportInfo | slcReportInfo | 1 | See clause 5.3.1.81. |
| slcParameterSetting | slcParameterSetting | 1 | See clause 5.3.1.80. |
| slcAlarm | slcAlarm | 1 | See clause 5.3.1.79. |

#### deviceWaterQualityMonitor

An water quality monitor is an environmental monitoring device used to monitor water quality.

Table 5.5.2.7-1: Modules of deviceWaterQualityMonitor Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| battery | battery | 0..1 | See clause 5.3.1.10. |
| connectivity | connectivity | 0..1 | See clause 5.3.1.25. |
| periodicalReportConfig | periodicalReportConfig | 0..1 | See clause 5.3.1.63. |
| waterQualityMonitor | waterQualityMonitor | 1 | See clause 5.3.1.98. |

### Health Domain

#### deviceBloodPressureMonitor

A blood pressure monitor is a device that can be used to monitor the blood pressure and is composed of one or more cuffs and a main montor machine.

Table 5.5.3.1-1: Modules of deviceBloodPressureMonitor Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| battery | battery | 1 | See clause 5.3.1.10 |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12 |

Table 5.5.3.1-2: Subdevice of deviceBloodPressureMonitor Device model

| Subdevice Instance Name | Subdevice Name | Multiplicity | Description |
| --- | --- | --- | --- |
| cuff | subDeviceCuff | 1..N | See clause 5.4.1.1 |

#### deviceGlucosemeter

A glucometer is a device that can be used to monitor the blood glucose level.

Table 5.5.3.2-1: Modules of deviceGlucoseMeter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| glucometer | glucometer | 1 | See clause 5.3.1.42. |
| battery | battery | 1 | See clause 5.3.1.10. |

#### deviceHeartRateMonitor

A heart rate monitor is a device that can be used to monitor the heart rate.

Table 5.5.3.3-1: Modules of deviceHeartRateMonitor Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| pulsemeter | pulsemeter | 1 | See clause 5.3.1.68. |
| battery | battery | 1 | See clause 5.3.1.10. |

#### devicePulseOximeter

A pulseoximeter is a device that can be used to monitor the blood characteristics.

Table 5.5.3.4-1: Modules of devicePulseOxiMeter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| pulsemeter | pulsemeter | 0..1 | See clause 5.3.1.68. When the “oximeter” module doesn’t exist, then the “pulsemeter” module is mandatory. |
| oximeter | oximeter | 0..1 | See clause 5.3.1.59. When the “pulsemeter” module doesn’t exist, then the “oximeter” module is mandatory. |
| battery | battery | 1 | See clause 5.3.1.10. |

#### deviceWeightScaleAndBodyCompositionAnalyser

A weight scale and body composition analyser is a device that can be used to monitor the weight and body composition.

Table 5.5.3.5-1: Modules of deviceWeightScaleAndBodyCompositionAnalyser Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| weight | weight | 1 | See clause 5.3.1.99. |
| bodyCompositionAnalyser | bodyCompositionAnalyser | 1 | See clause 5.3.1.14. |
| bioElectricalImpedanceAnalysis | bioElectricalImpedanceAnalysis | 1 | See clause 5.3.1.13. |
| battery | battery | 1 | See clause 5.3.1.10. |

### Home Domain

#### deviceAirConditioner

An air conditioner is a home appliance used to alter the properties of air (primarily temperature and humidity) to more comfortable conditions. This air conditioner information model provides capabilities to control and monitor air conditioner specific functions and resources.

Table 5.5.4.1-1: Modules of deviceAirConditioner Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| airConJobMode | airConJobMode | 0..1 | See clause 5.3.1.1. |
| airConOperationMode | operationMode | 0..1 | See clause 5.3.1.57. This module instance is used to trigger an airCon operation that is pre-set in “airConJobMode”. If this data point is not present, then the air conditioner’s job mode can be triggered by setting the “airConJobMode”. |
| airCleanOperationMode | operationMode | 0..1 | See clause 5.3.1.57. This module instance is used to trigger airClean operation. |
| temperature | temperature | 0..1 | See clause 5.3.1.87. |
| timer | timer | 0..1 | See clause 5.3.1.90. |
| sleepTimer | timer | 0..1 | See clause 5.3.1.90. The sleep function, which is vendor-specific algorithm (for example increasing the remperature by one degree for every 30 minutes), is triggered instantly when “targetDuration” is set, and it indicates the time to the end of appliance operation. It is set at runtime by a user application. |
| turbo | turbo | 0..1 | See clause 5.3.1.91. |
| airFlow | airFlow | 0..1 | See clause 5.3.1.4. |
| powerSave | powerSave | 0..1 | See clause 5.3.1.66. |
| airQualitySensor | airQualitySensor | 0..1 | See clause 5.3.1.6. |
| filterInfo | filterInfo | 0..1 | See clause 5.3.1.35. |

#### deviceAirPurifier

An airPurifieris a home appliance is used to prevent dust and other particles from air by filtering, washing or electrostatic precipitation. This airPurifier information model provides capabilities to control and monitor airPurifier specific functions and resources.

Table 5.5.4.2-1: Modules of deviceAirPurifier Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| airPurifierJobMode | airPurifierJobMode | 0..1 | See clause 5.3.1.5. |
| airPurifierOperationMode | operationMode | 0..1 | See clause 5.3.1.57. This module instance is used to trigger the airPurifier operation. |
| timer | timer | 0..1 | See clause 5.3.1.90. |
| powerSave | powerSave | 0..1 | See clause 5.3.1.66. |
| airQualitySensor | airQualitySensor | 0..1 | See clause 5.3.1.6. |
| filterInfo | filterInfo | 0..1 | See clause 5.3.1.35. |

#### deviceClothesDryer

A clothes dryer is a home appliance for drying clothes. This clothesDryer information model provides capabilities to control and monitor clothes dryer specific functions and resources.

Table 5.5.4.3-1: Modules of deviceClothesDryer Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| clothesDryerJobMode | clothesDryerJobMode | 0..1 | See clause 5.3.1.19. |
| clothesDryerOperationMode | operationMode | 0..1 | See clause 5.3.1.57. This module instance is used to trigger the clothesDryer operation. |

#### deviceClothesWasher

A clothes washer is a home appliance that is used to wash laundry, such as clothing and sheets. This information model provides capabilities to interact with specific functions and resources of clothes washers.

Table 5.5.4.4-1: Modules of deviceClothesWasher Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| clothesWasherOperationMode | operationMode | 0..1 | See clause 5.3.1.57. |
| runState | runState | 1 | See clause 5.3.1.75. |
| clothesWasherJobMode | clothesWasherJobMode | 1 | See clause 5.3.1.20. |
| clothesWasherJobModeOption | clothesWasherJobModeOption | 0..1 | See clause 5.3.1.22. |
| remoteControlEnable | remoteControlEnable | 0..1 | See clause 5.3.1.73. |
| timer | timer | 0..1 | See clause 5.3.1.90. |

#### deviceClothesWasherDryer

A clothes washer dryer is a home appliance that is a combination of cloth washer and cloth dryer in a single cabinet. This information model provides capabilities to interact with specific functions and resources of clothes washers and dryers.

Table 5.5.4.5-1: Modules of deviceClothesWasherDryer Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| clothesWasherDryerOperationMode | operationMode | 0..1 | See clause 5.3.1.57. |
| runState | runState | 1 | See clause 5.3.1.75. |
| clothesWasherDryerJobMode | clothesWasherDryerJobMode | 1 | See clause 5.3.1.21. |
| clothesWasherJobModeOption | clothesWasherJobModeOption | 0..1 | See clause 5.3.1.22. |
| remoteControlEnable | remoteControlEnable | 0..1 | See clause 5.3.1.73. |
| timer | timer | 0..1 | See clause 5.3.1.90. |

#### deviceCoffeeMachine

A coffee machine is a device that is used to brew a coffee, may add foamed milk, and may include some variants, for example a grinder.

Table 5.5.4.6-1: Modules of deviceCoffeeMachine Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| clock | clock | 0..1 | See clause 5.3.1.18. |
| brewing | brewing | 1 | See clause 5.3.1.16. |
| waterStatus | liquidRemaining | 0..1 | See clause 5.3.1.51. |
| milkStatus | liquidRemaining | 0..1 | See clause 5.3.1.51. |
| grinder | grinder | 0..1 | See clause 5.3.1.43. |
| milkFoaming | foaming | 0..1 | See clause 5.3.1.36. |
| milkQuantity | liquidLevel | 0..1 | See clause 5.3.1.50. |
| brewingSwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| keepWarm | keepWarm | 0..1 | See clause 5.3.1.48. |

#### deviceCookerHood

A cooker hood is a device containing a mechanical fan that hangs above the stove or cooktop in the kitchen.

Table 5.5.4.7-1: Modules of deviceCookerHood model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| airFlow | airFlow | 0..1 | See clause 5.3.1.4. |
| cookerHoodJobMode | cookerHoodJobMode | 0..1 | See clause 5.3.1.26. |

#### deviceCooktop

A cooktop is a device that is a kitchen appliance designed for the purpose of cooking food.

Table 5.5.4.8-1: Modules of deviceCooktop model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| heatingZone | heatingZone | 1..N | See clause 5.3.1.44. |

#### deviceDehumidifier

A dehumidifier is a device that is used to monitor or control the state of a dehumidifying appliance.

Table 5.5.4.9-1: Modules of deviceDehumidifier Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| relativeHumidity | relativeHumidity | 0..1 | See clause 5.3.1.72. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| dehumidifierJobMode | dehumidifierJobMode | 0..1 | See clause 5.3.1.28. |
| dehumidifierOperationMode | operationMode | 0..1 | See clause 5.3.1.57. This module instance is used to trigger dehumidifier operation. |
| Timer | timer | 0..1 | See clause 5.3.1.90. |
| powerSave | powerSave | 0..1 | See clause 5.3.1.66. |

#### deviceDigitalGallery

A digital gallery is a device that is used to display picture, e.g., paintings from artists, photos from photographers or personals etc.

Table 5.5.4.10-1: Modules of deviceDigitalGallery Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| galleryMode | galleryMode | 1 | See clause 5.3.xx |
| pictureInput | mediaSelect | 1 | See clause 5.3.48 |
| powerSave | powerSave | 0..1 | See clause 5.3.58 |
| clock | clock | 0..1 | See clause 5.3.18 |

#### deviceDishWasher

A dish washer is a home appliance used to wash dishes. This information model provides capabilities to interact with specific functions and resources of a dish washer.

Table 5.5.4.11-1: Modules of deviceDishWasher Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| dishWasherJobMode | dishWasherJobMode | 0..1 | See clause 5.3.1.29. |

#### deviceFan

A fan is a device that is used to monitor or control the state of a fanning device.

Table 5.5.4.12-1: Modules of deviceFan model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |

#### deviceFoodProbe

A food probe is a device that is used to measure the internal temperature of food.

Table 5.5.4.13-1: Modules of deviceFoodProbe model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| temperature | temperature | 1 | See clause 5.3.1.87. |

#### deviceFreezer

A freezer is a large container like a fridge in which the temperature is kept below freezing point, so that food can be storeed inside of it for long periods. This freezer information model provides capabilities to monitor freezer specific functions and resources.

Table 5.5.4.14-1: Modules of deviceFreezer Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| temperature | temperature | 1 | See clause 5.3.1.87. |

#### deviceHomeCCTV

A home CCTV is a smart home appliance to provide monitoring capabilities when people stay way from their home or a room, or to monitor the environmental status of their home or room.

Table 5.5.4.15-1: Modules of deviceHomeCCTV Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| sessionDescription | sessionDescription | 1 | See clause 5.3.1.77. |
| playerControl | playerControl | 0..1 | See clause 5.3.1.65. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| motionSensor | motionSensor | 0..1 | See clause 5.3.1.54. |
| airQualitySensor | airQualitySensor | 0..1 | See clause 5.3.1.6. |
| ozoneMeter | ozoneMeter | 0..1 | See clause 5.3.1.60. |
| smokeSensor | smokeSensor | 0..1 | See clause 5.3.1.82. |
| acousticSensor | acousticSensor | 0..1 | See clause 5.3.1.1. |
| impactSensor | impactSensor | 0..1 | See clause 5.3.1.47. |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| alarmSpeaker | alarmSpeaker | 0..1 | See clause 5.3.1.7. |

#### deviceHumidifier

A humidifier is a device that is used to monitor or control the state of a humidifying appliance.

Table 5.5.4.16-1: Modules of Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |

#### deviceKettle

Kettle is a device used to boil water. It may set a desired temperature for water and may keep water warm for a desired time.

Table 5.5.4.17-1: Modules of deviceKettle Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| waterStatus | liquidRemaining | 0..1 | See clause 5.3.1.51. |
| boilingSwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| temperature | temperature | 0..1 | See clause 5.3.1.87. |
| keepWarm | keepWarm | 0..1 | See clause 5.3.1.48. |

#### deviceMicrogeneration

A microgeneration is a Home Energy Management System (HEMS) device that is used to generate energy. Examples of microgeneration devices are photovoltaics device or fuel cells.

Table 5.5.4.18-1: Modules of deviceMicrogeneration Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| energyGeneration | energyGeneration | 1 | See clause 5.3.1.33. |

#### deviceOven

An oven is a home appliance used to roast and heat food in a complete stove. This information model is applicable to different types of ovens: gas ovens, electrical ovens, steam ovens, microwave ovens, etc. This information model provides capabilities to interact with specific functions and resources of ovens.

Table 5.5.4.19-1: Modules of deviceOven Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. Depending on the manufacturer policies or regulations, the binary switch might only be used to turn the device off. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| timer | timer | 0..1 | See clause 5.3.1.90. |
| temperature | temperature | 1 | See clause 5.3.1.87. |

#### deviceRefrigerator

A refrigerator is a home appliance used to store food at temperatures which are a few degrees above the freezing point of water. This information model provides capabilities to interact with specific functions and resource of refrigerators.

Table 5.5.4.20-1: Modules of deviceRefrigerator Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12. |
| powerSave | powerSave | 0..1 | See clause 5.3.1.66. |
| doorStatus | doorStatus | 0..1 | See clause 5.3.1.29. |
| frozenTemperature | temperature | 0..1 | See clause 5.3.1.87. |
| fridgeTemperature | temperature | 1 | See clause 5.3.1.87. |
| customTemperature | temperature | 0..1 | See clause 5.3.1.87. This module can be configured to fridge temperature or frozen temperature based on its usage by manufacturer |
| refrigeration | refrigeration | 0..1 | See clause 5.3.1.71. |
| controlPanelLock | lock | 0..1 | See clause 5.3.1.52. |
| waterFilterInfo | filterInfo | 0..1 | See clause 5.3.1.35. |

#### deviceRiceCooker

An rice cooker is a home appliance used to cook and heat food. It may set a desired heating time for food and may keep food warm for a desired time.

Table 5.5.4.21-1: Modules of deviceRiceCooker Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. Depending on the manufacturer policies or regulations, the binary switch might only be used to turn the device off. |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| timer | timer | 0..1 | See clause 5.3.1.90. |
| keepWarm | keepWarm | 0..1 | See clause 5.3.1.48. |

#### deviceRobotCleaner

A robot cleaner is an autonomous robotic vacuum cleaner that has intelligent programming and a limited vacuum cleaning system. This robot cleaner information model provides capabilities to control and monitor robot cleaner specific functions and resources.

Table 5.5.4.22-1: Modules of deviceRobotCleaner Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| robotCleanerJobMode | robotCleanerJobMode | 1 | See clause 5.3.1.74. |
| robotCleanerOperationMode | operationMode | 0..1 | See clause 5.3.1.57. |
| battery | battery | 0..1 | See clause 5.3.1.10. |
| timer | timer | 0..1 | See clause 5.3.1.90. |

#### deviceSecurityPanel

A security pannel is a device that can change the security mode of, for example, an alarm system.

Table 5.5.4.23-1: Modules of deviceSecurityPanel model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| securityMode | securityMode | 1 | See clause 5.3.1.76. |

#### deviceSetTopBox

A set top box is a device that in general contains a TV tuner input and displays output to a TV.

Table 5.5.4.24-1: Modules of deviceSetTopBox model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| audioVolume | audioVolume | 0..1 | See clause 5.3.1.8. |
| Channel | televisionChannel | 0..1 | See clause 5.3.1.86. |
| mediaInput | mediaSelect | 0..1 | See clause 5.3.1.53. |
| mediaOutput | mediaSelect | 0..1 | See clause 5.3.1.53. |

#### deviceSteamCloset

A deviceSteamCloset is a home appliance that de-wrinkles, sanitizes and dries to clean fabrics similar to a dry cleaner. This information model provides capabilities to interact with specific functions and resources of the steam closet.

Table 5.5.4.25-1: Modules of deviceSteamCloset Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| steamClosetJobMode | steamClosetJobMode | 1 | See clause 5.3.1.85. |
| steamClosetOperationMode | operationMode | 0..1 | See clause 5.3.1.57. |

#### deviceStorageBattery

A storage battery is a Home Energy Management System HEMS device that is used to provide the home with electrical energy.

Table 5.5.4.26-1: Modules of deviceStorageBattery Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| binarySwitch | binarySwitch | 0..1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| battery | battery | 1 | See clause 5.3.1.10. |

#### deviceTelevision

A television (TV) is a home appliance used to show audio and visual content such as broadcasting programs and network streaming. This TV information model provides capabilities to control and monitor TV specific resources.

Table 5.5.4.27-1: Modules of deviceTelevision Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| audioVolume | audioVolume | 0..1 | See clause 5.3.1.8. |
| televisionChannel | televisionChannel | 0..1 | See clause 5.3.1.86. |
| playerControl | playerControl | 0..1 | See clause 5.3.1.65. |
| mediaInput | mediaSelect | 0..1 | See clause 5.3.1.53. |
| mediaOutput | mediaSelect | 0..1 | See clause 5.3.1.53. |

#### deviceWaterHeater

A water heater is a device that is used to provide hot water through home facilities.

Table 5.5.4.28-1: Modules of deviceWaterHeater Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| clock | clock | 0..1 | See clause 5.3.1.18. |
| boiler | boiler | 0..1 | See clause 5.3.1.15. |
| hotWaterSupply | hotWaterSupply | 0..1 | See clause 5.3.1.46. |

#### deviceWindowShade

The window shade is an appliance that provides the ability to cover windows. This device type includes but not limited to roller shades, drapes, and tilt-only blinds.

Table 5.5.4.29-1: Modules of deviceWindowShade Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| openLevel | openLevel | 1 | See clause 5.3.1.56. |
| battery | battery | 0..1 | See clause 5.3.1.10. |

### Industry Domain

### Vehicular Domain

#### deviceElectricVehicleCharger

An electric vehicle charger is a device that is used for charging or discharging electric vehicles.

Table 5.5.6.1-1: Modules of deviceElectricVehicleCharger Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | 1 | See clause 5.3.1.34. |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 1 | See clause 5.3.1.75. |
| battery | battery | 1 | See clause 5.3.1.10. |
| electricVehicleConnector | electricVehicleConnector | 1 | See clause 5.3.1.31. |

********************* End of Change 7 ******************************************

### ******************End of changes*********************