| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM 44 |
| Source:* | Andrew Min-gyu Han, Hansung University,andyhan@hansung.ac.kr Joong-kwon Lim, Hansung University, naulim@hansung.ac.kr Yeonsang Koo, LGU+, yskoo@lguplus.co.kr |
| Date:* | 2020-02-20 |
| Reason for Change/s:* | Add a card recharging machine as a device model of the Railway Domain |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <WI-0084> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V4.3.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR adds a recharging machine of passenger card as a device model of the Railway Domain.

The passenger card is a kind of payment method which is used to pay for public transportation services such as subway or metro.

The following image shows an example of the machine.

|  | The machine is consisted of following components: binarySwitch clock touchScreen keypad emergencyButton audioVolume prePaidCardReader billDepositModule billWithdrawalModule coinDepositModule cashDispensor cardScanner connectivity machineState lock |
| --- | --- |

### -----------------------Start of change 1-------------------------------------------

#### 5.5.8.x	deviceCardRechargingMachine

A card recharging machine is a device of the Railway Domain. The machine provides recharging service for pre-paid card for transportation. Railway users simply recharging their cards and use it as a payment method for transportation fare.

Table 5.5.8.x-1: Modules of deviceCardRecharingMachine Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.1.12. |
| clock | clock | false | See clause 5.3.1.18. |
| touchScreen | touchScreen | false | See clause 5.3.1.a. |
| keypad | keypad | true | See clause 5.3.1.49. |
| emergencyButton | pushButton | false | See clause 5.3.1.69. |
| audioVolume | audioVolume | true | See clause 5.3.1.8. |
| prePaidCardReader | prePaidCardReader | false | See clause 5.3.1.b. |
| billDeposit | billDeposit | false | See clause 5.3.1.c. |
| billWithdrawal | billWithdrawal | false | See clause 5.3.1.d. |
| coinDeposit | coinDeposit | false | See clause 5.3.1.e. |
| cashDispensor | cashDispenser | false | See clause 5.3.1.f. |
| cardScanner | cardScanner | true | See clause 5.3.1.g. |
| connectivity | connectivity | false | See clause 5.3.1.25. |
| machineState | runState | false | See clause 5.3.1.75. |
| lock | lock | false | See clause 5.3.1.52. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 5.3.1.a	touchScreen

This ModuleClass provides the capability to get selections of a user from the pre-defined menus on the screen as parts of a process of charging transportation payment card of the user.

Table 5.3.1.a-1: DataPoints of touchScreen ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| pushed | xs:boolean | R | false |  | This data point indicates the press of the button. (1..N) |
| positionX | xs:integer | R | false | pixel | This data point indicates the horizontal position of the touching. (1..N) |
| positionY | xs:integer | R | false | pixel | This data point indicates the vertical position of the touching. (1..N) |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 5.3.1.b	prePaidCardReader

The Pre-paid card reader ModuleClass provides functions to read NFC card and indicates its information..

Table 5.3.1.b-1: DataPoints of prePaidCardReader ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| readStatus | xs:boolean | R | false |  | This data point indicates the status of reading the pre-paid card. “True” means the reader reads the pre-paid card successfully. |
| cardInfo | xs:integer | R | false |  | The card information is consisted of numbers of integer values. (1..N) |
| balance | xs:float | RW | false |  | This data point indicates the balance of the pre-paid card. |
| currency | xs:string | R | true |  | The currency is depended on the country which the card is used. For example, the unit could be “Dollar” or “$” in US, “Euro” in EU and “Won” in Korea. |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

#### 5.3.1.c	billDeposit

This ModuleClass provides the capability to deposit bills, indicates the balance of the deposited bills and detects fake.

Table 5.3.1.c-1: DataPoints of billDeposit ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| depositStatus | xs:boolean | R | false |  | This data point indicates the deposit is made successfully or not. |
| balance | xs:float | R | false |  | This data point indicates the balance of the deposited bills. |
| count | xs:integer | R | false |  | The data point indicates the number of bills which are deposited. [1..N] |
| currency | xs:string | R | true |  | The currency is depended on the country which the deposited bills are used. For example, the currency could be “Dollar” in US, “Euro” in EU and “Won” in Korea. |
| fakeStatus | xs:boolean | R | false |  | This data point indicates that the deposited bills are fake notes. |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

#### 5.3.1.d	billWithdrawal

This ModuleClass provides the capability to withdraw bills which are deposited by the billDepositModule.

Table 5.3.1.d-1: DataPoints of billWithdrawal ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| withdrawalStatus | xs:boolean | R | false |  | This data point indicates the withdrawal is made successfully or not. |
| balance | xs:float | R | false |  | This data point indicates the balance of the withdrawn bills. |
| count | xs:integer | R | false |  | The data point indicates the number of bills which are withdrawn. [1..N] |

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6-------------------------------------------

#### 5.3.1.e	coinDeposit

This ModuleClass provides the capability to deposit coins, indicates the balance of the deposited coins and detects fake.

Table 5.3.1.e-1: DataPoints of coinDeposit ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| depositStatus | xs:boolean | R | false |  | This data point indicates the deposit is made successfully or not. |
| balance | xs:float | R | false |  | This data point indicates the balance of the deposited coins. |
| count | xs:integer | R | false |  | The data point indicates the number of coins which are deposited. |
| currency | xs:string | R | true |  | The currency is depended on the country that the deposited coins are used. For example, the unit could be “Dollar” in US, “Euro” in EU and “Won” in Korea. |
| fakeStatus | xs:boolean | R | false |  | This data point indicates that the deposited coins are fake. |

### -----------------------End of change 6---------------------------------------------

### -----------------------Start of change 7-------------------------------------------

#### 5.3.1.f	cashDispenser

This ModuleClass provides the capability to withdraw designated amount of cash or returns all the deposited bills and coins by the billDepositModule and coinDepositModule.

Table 5.3.1.f-1: DataPoints of cashDispenser ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| dispenseStatus | xs:boolean | R | false |  | This data point indicates the dispense is successful or not. |
| balance | xs:float | R | false |  | This data point indicates the balance of the dispensed bills and coins. |
| count | xs:integer | R | false |  | The data point indicates the number of bills and coins which are dispensed. |
| currency | xs:string | R | true |  | The currency is depended on the country that the dispensed bills and coins are used. For example, the unit could be “Dollar” in US, “Euro” in EU and “Won” in Korea. |

### -----------------------End of change 7---------------------------------------------

### -----------------------Start of change 8-------------------------------------------

#### 5.3.1.g	cardScanner

This ModuleClass provides the capability to scan an image of a card, gets the card information from the image and provides the information..

Table 5.3.1.g-1: DataPoints of cardScanner ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| scanStatus | xs:boolean | R | false |  | This data point indicates the scanning process is successful. |
| cardInfo | xs:integer | R | false |  | The card information is consisted of numbers of integer values. (1..N) |

### -----------------------End of change 8---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?