| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM 44 |
| Source:* | Andrew Min-gyu Han, Hansung University,andyhan@hansung.ac.kr Joong-kwon Lim,Hansung University, naulim@hansung.ac.kr Yeonsang Koo, LGU+, yskoo@lguplus.co.kr |
| Date:* | 2020-02-20 |
| Reason for Change/s:* | Add a smart gate machine as a device model of the Railway Domain |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <WI-0084> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V4.3.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR adds a smart gate of passenger card as a device model of the Railway Domain.

The gate is used in subway or metro.

The following image shows an example of the machine.

|  | The machine is consisted of following components: binarySwitch clock touchScreen emergencyButton audioVolume ticketReader crossingSensor connectivity gateState directionPannel crossingIndicator crossingBarrier |
| --- | --- |

### -----------------------Start of change 1-------------------------------------------

#### 5.5.8.x	deviceSmartGate

A smart gate is a device of the Railway Domain. The gate provides pasenger service for checking ticket and control the gate usage. A railway users simply use the gate with their passenger card which migh have NFC function.

Table 5.5.8.x-1: Modules of deviceSmartGate Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.1.12. |
| clock | clock | false | See clause 5.3.1.18. |
| touchScreen | touchScreen | true | See clause 5.3.1.a. |
| emergencyButton | pushButton | true | See clause 5.3.1.69. |
| audioVolume | audioVolume | true | See clause 5.3.1.8. |
| ticketReader | nfcReader | false | See clause 5.3.1.b. |
| crossingSensor | traceSensor | false | See clause 5.3.1.c. |
| connectivity | connectivity | false | See clause 5.3.1.25. |
| gateState | runState | false | See clause 5.3.1.75. |
| directionPannel | directionPannel | true | See clause 5.3.1.d. |
| crossingIndicator | statusLight | false | See clause 5.3.1.e |
| crossingBarrier | crossingBarrier | false | See clause 5.3.1.f. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 5.3.1.a	touchScreen

This ModuleClass provides the capability to get selections of a user from the pre-defined menus on the screen as parts of a process of charging transportation payment card of the user.

Table 5.3.1.a-1: DataPoints of touchScreen ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| pushed | xs:boolean | R | false |  | This data point indicates the press of the button. (1..N) |
| positionX | xs:integer | R | false | pixel | This data point indicates the horizontal position of the touching. (1..N) |
| positionY | xs:integer | R | false | pixel | This data point indicates the vertical position of the touching. (1..N) |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 5.3.1.b	nfcReader

This ModuleClass provides the capability to indicate the operation of a push button style switch. A typical application can be an SOS button.

Table 5.3.1.b-1: DataPoints of nfcReader ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| readStatus | xs:boolean | R | false |  | This data point indicates the status of reading the NFC card. “True” means the reader reads the NFC card successfully. |
| cardInfo | xs:integer | R | false |  | The card information is consisted of numbers of integer values. (1..N) |
| balance | xs:float | RW | false |  | This data point indicates the vertical position of the touching. (1..N) |
| currencyUnit | xs:string | R | true |  | The currency unit is depended on the country which the card is used. For example, the unit could be “Doller” or “$” in US, “Euro” in EU and “Won” in Korea. |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

#### 5.3.1.c	traceSensor

This ModuleClass provides the capabilities to indicate the direction (status of get-in and get out) of passeners who crossing the gate.

Table 5.3.1.c-1: DataPoints of motionSensor ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| sensitivity | xs:integer | RW | true |  | The level of the detection accuracy of the trace sensor. This data point can be used to control the number of the report. |
| direction | xs:integer | R | false |  | This data point is used to indicate the direction of a passenger who is get-in or get-out. |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

#### 5.3.1.d	directionPannel

This ModuleClass displays a signal (e.g. direction arrow) to indicate a gate is permitted to get-in or get-out.

Table 5.3.1.d-1: DataPoints of motionSensor ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| direction | xs:boolean | RW | false |  | The direction is true, the panel indocates get-in signal and vice versa. |
| operation | xs:boolean | RW | false |  | The operation is true, the panel turns on and displays signal and the other way around. |

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6-------------------------------------------

#### 5.3.1.e	statusLight

This ModuleClass is used to indicate a status with its colour and brightness.

Table 5.3.1.e-1: DataPoints of statusLight ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| red | xs:integer | RW | false |  | The value of the Red colour channel of RGB. The range is [0,255]. |
| green | xs:integer | RW | false |  | The value of the Green colour channel of RGB. The range is [0,255]. |
| blue | xs:integer | RW | false |  | The value of the Blue colour channel of RGB. The range is [0,255]. |
| colourSaturation | xs:integer | RW | true |  | The status of colour saturation level. “colourSaturation” has a range of [0,100]. A “colourSaturation” value of 0 means that a device displays or produces black and white images. A “colourSaturation” value of 50 means that a device displays or produces normal colour images. A “colourSaturation” value of 100 means that a device displays or produces very colourfull images. |
| brightness | xs:integer | RW | true |  | The status of brightness level. |

### -----------------------End of change 6---------------------------------------------

### -----------------------Start of change 7-------------------------------------------

#### 5.3.1.f	crossingBarrier

An active barrier is used to block a pedestrian or vehicle from a control point (e.g. entrance and gate).

Table 5.5.1.7-1: DataPoints of crossingBarrier ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| barrierDefault | xs:boolean | RW | false |  | The value of the barrier default is true, the default status of the barrier is closed and vice versa. |
| barrierStatus | xs:boolean | RW | false |  | The value of the barrier status is true, the barrier is closed and vice versa. |
| timer | xs:time | RW | true |  | It depends on the barrierDefault. If the barrierDefault is true and the barrier is closed with the timer duration and vice versa. |

### -----------------------End of change 8---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?