| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#45 |
| Source:* | Andreas Kraft, Deutsche Telekom, Andreas.Kraft@t-systems.com Andreas Neubacher, Deutsche Telekom, andreas.neubacher@magenta.at |
| Date:* | 2020-04-12 |
| Reason for Change/s:* | SDT 4.0 – Removing “optional” from ModuleClass |
| CR against: Release* | REL 4 |
| CR against: WI* | Active WI-0081 Smart Device Template 4.0 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | SDT UML diagram |
| Clauses * | Various SDT entities |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | n/a |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This CR presents changes of oneM2m’s Gitlab SDT repository (see https://git.onem2m.org/MAS/SDT) to reflect the transition towards version 4.0 of the Smart Device Template.

This CR proposes to remove the “optional” attribute from the ModuleClass definition. The new attributes “minOccurs” and “maxOccurs” were introduced in the contribution “RDM-2020-0001- SDT 4.0 – Proposed Multiplicity for ModuleClasses and SubDevices”. The allow to express the same (and even more fine grain) cardinality as just the “optional” attribute as the following mapping shows:

- optional = true → minOccurs = 0, maxOccurs = 1

- optional = false → minOccurs = 1, maxOccurs = 1

In fact, keeping the “optional” attribute may lead to confusing and wrong definitions, e.g. when both methods to define the cardinality are used at the same time:

- optional = false, minOccurs = 0, maxOccurs = 1 → ???

The images referenced in “docs/SDT_Components.md” etc are NOT updated according with the changes proposed in this CR. They need to be consolidated when all changes are integrated, but the change to f the UML diagram looks as follows:

See the new branch in gitlab:

https://git.onem2m.org/MAS/SDT/tree/RDM-2020-0025-SDT_4_0_-_Removing_optional_from_ModuleClass