| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#46-02 |
| Source:* | Xiaotao Li, CMCC, lixiaotao@chinamobile.com Yawen Niu, CMCC, niuyawen@chinamobile.com |
| Date:* | 2020-06-28 |
| Reason for Change/s:* | Adding the temperatureAlarm Module to the deviceThermometer Device model |
| CR against: Release* | Rel.4 |
| CR against: WI* | Active WI-0084 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V4.4.1 |
| Clauses * | clauses in 5.5.1.13 clauses in 5.3.1.88 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR modifies the ModuleClass temperatureAlarm and adds it to the Device model deviceThermometer.

(1) the ModuleClass temperatureAlarm is added to the Device model deviceThermometer ;

(2) two datapoint including alarm and  temperatureThreshhold  are removed from the ModuleClass temperatureAlarm; and 4 new datapoints including highTemperatureAlarm, highTemperatureAlarmThreshold, lowTemperatureAlarm and lowTemperatureAlarmThreshold are added to the ModuleClass temperatureAlarm;

A use case:

The alarm function has become increasingly important since the outbreak of  the 2019-nCoV. Medical workers can use a thermometer to dectect whether a person's body temperature is higher tha 37.3 degrees Celsius (C). If a person is in a high fever, the thermometer will give an alarm to tell the medical workers that the temperature of this person is abnormal.

### -----------------------Start of change 1-------------------------------------------

#### 5.5.1.13	deviceThermometer

A thermometer is a device that can be used to check, for example, the body or other temperatures.

Table 5.5.1.13-1: Modules of deviceThermoMeter Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| temperature | temperature | 1 | See clause 5.3.1.87. |
| battery | battery | 1 | See clause 5.3.1.10. |
| temperatureAlarm | temperatureAlarm | 0..1 | See clause 5.3.1.88 |

-----------------------End of change 1---------------------------------------------

#### -----------------------Start of change 2-------------------------------------------5.3.1.88	temperatureAlarm

This ModuleClass provides the capabilities to indicate the detection of abnormal temperatures and raises an alarm if the triggering criterion is met.

Table 5.3.1.88-1: DataPoints of temperatureAlarm ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| unit | hd:enumTemperatureUnit | RW | true | C or F or K | Default value is ‘C’ |
| temperature | xs:float | R | true | Defined in the datapoint ‘unit’ | To report the value of the temperature. |
| highTemperatureAlarm | xs:boolean | R | false |  | High temperature alarm |
| highTemperatureAlarmThreshold | xs:float | RW | true | Defined in the datapoint ‘unit’ | The threshold of maximum temperature alarm. |
| lowTemperatureAlarm | xs:boolean | R | false |  | Low temperature alarm |
| lowTemperatureAlarmThreshold | xs:float | RW | true | Defined in the datapoint ‘unit’ | The threshold of maximum temperature alarm. |

-----------------------End of change 2---------------------------------------------