| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#46-02 |
| Source:* | Rong Long, CMCC,longrong@chinamobile.com Xiaotao Li,CMCC,lixiaotao@chinamobile.com |
| Date:* | 2020-07-01 |
| Reason for Change/s:* | Adding timer to deviceLight device model |
| CR against: Release* | Rel.4 |
| CR against: WI* | Active WI-0084 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V4.4.1 |
| Clauses * | clause 5.5.1.7 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces  timer to device  deviceLight. The timer set at runtime by a user application to give light or alarm. For example, to pretect eyes, it closes the light to inform user that you should have a rest after reading for 1 hour when “targetDuration” sets to 1 hours.

-----------------------Start of change 1-------------------------------------------

#### 5.5.1.7 deviceLight

A light is a device that is used to control the state of an illumination appliance.

Table 5.5.1.7-1: Modules of deviceLight Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| colour | colour | 0..1 | See clause 5.3.1.23. |
| colourSaturation | colourSaturation | 0..1 | See clause 5.3.1.24. |
| brightness | brightness | 0..1 | See clause 5.3.1.17. |
| timer | timer | 0..1 | See clause 5.3.1.90. |

-----------------------End of change 1---------------------------------------------