| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM 46 |
| Source:* | Massimo Vanetti (SBS) Enrico Scarrone (TIM) |
| Date:* | 2020-07-20 |
| Reason for Change/s:* | Support od Smart Lifts information exchange over oneM2M system |
| CR against: Release* | Release 4 |
| CR against: WI* | Active WI-0098 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023-V4.1.0 “SDT based Information Model and Mapping for Vertical Industries” |
| Clauses * | New clause and clause 2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | No impact envisaged on other stage 2 and 3 TSes. |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR proposed the data model to be adopted in the Smart Lift IoT system was developed in collaboration with sector stakeholders such as EFESME[ (www.EFESME.org). and anticipated in ETSI  TR 103 546 SmartM2M; Requirements & Feasibility study for Smart Lifts in IoT.

### -----------------------Start of change 1-------------------------------------------

## 5.5.7 Smart Lifts Domain

## 5.5.7.1 Introduction

Clause 5.5.7 contais the data to be exchanged by  smart lift system across its components and with external components from other systems. It has been developed to support the lift industry with a standard capable to provide seamless interoperability among the different lift solution, to assure sector specific services (e.g. remote diagnostic and predictive maintenance), and to exchange informations with services and solutions belonging to other sectors (e.g. with services in the building, with access control and energy monitoring services,  with services for the citizens and for impaired people).

It has been developed with the consultation of smart lift stakeholders and their associations, it is based on the  study (ETSI TR 103 546 SmartM2M; Requirements & Feasibility study for Smart Lifts in IoT) [i.y].

## 5.5.7.2 Lift identification and istallation informations

| Information | Type | Meas. unit | Values | Notes |
| --- | --- | --- | --- | --- |
| liftUniversalIdentifier | Text | NA | Value (Max 128 characters) | Globally unique identifier for the lift. |
| typeOfUse | Enumerated | N/A | LIFT GOODS LIFT GOODS ONLY LIFT LIFT PLATFORM | Defined according the following: LIFT: EN81.20; GOODS LIFT: EN81.20; GOODS ONLY LIFT: EN81.30-EN81.31; LIFT PLATFORM: EN81.41-EN81.42. |
| liftType | Enumerated | N/A | ELECTRICAL ELECTRICAL MRL HYDRAULIC HYDRAULIC MRL | It provides an indication of the principle of functioning of the elevator. |
| liftManufacturer | Text | N/A | Value (max 64 characters) | Name of the company that manufactures the lift. |
| identificationCode | Text | N/A | Value (max 64 characters) | ID (locally unique) assigned to the lift according to local regulations. Usually also inscribed on a plate attached to the lift car. |
| CarStops | Integer | Pure Number | 0 .. 9999 | Number of car stops. |
| Doors | Integer | Pure Number | 0 .. 10 | Number of doors in the lift. |
| CarServices | Integer | Pure Number | 0 .. 9999 | Number of car services, taking care of the case where the car has multiple doors that can give independent access to different locations on a given floor. It is expected to be greater or equal to the number of Car Stops. |
| CarServicesDescription | array of carSservice | N/A | Variable length array (max 9999 elements) | It provides configuration of the lift at a given service (the corrispondant car stop and door opening configuration) |
| floorNames | Array of text | N/A | Array [0..Number of car stops] of text (length 5 characters | It provides the corrispondence between the car stop and the corrisponding floor name. the index indicates the car stop. |
| carLoad | Integer | Kg (SI) | 0..99999 | Limit load that can be safely carried by the car. This is a design parameter. |
| emergencyCallSupport | Boolean | N/A | TRUE/FALSE | TRUE if emergency call support is available on the lift. Typically mandatory in new lifts, but may be lacking in old installations. |
| geographicLocation | Geographic Coordinates | N/A | Value (defined according to ISO 6709 formats) | Geographic Location where the lift is installed. |
| geographicLocationValidator | Text | N/A | Value (max 64 characters) | Name of who has provided the validation of the correctness of Geographic Location. |
| mainPowerSupply | Text | Enumerated | 3-PHASE SINGLE-PHASE |  |
| ain PowerSupply Voltage | Integer | Volt | Value | 380v, 220v, 110v, etc. |
| valueOfStandardPowerSupply | Integer | Volt | Value | 12v, 24v, 48v, etc. |

DEFINITION OF CarService

|  | Elements | Type | Values | Notes |
| --- | --- | --- | --- | --- |
| CarService | stop | Integer | 0..carStop | It indicates a specific stop |
|  | doorStatus | Variable size array of Boolean | Array [0..10] of TRUE/FALSE | TRUE indicates that indicates that the corresponding port indicated by the array index is open at the given stop FALSE indicates that the port is closed. |

## 5.5.7.3	Administrative Information

| Information | Type | Meas. unit | Values | Notes |
| --- | --- | --- | --- | --- |
| liftManifacturing company | Organization Entity | N/A | max 264 characters | E.g. the local representative of the manifacturing company. |
| liftInstallerCompany | Organization Entity | N/A | max 264 characters | E.g. the representative of the installer company. |
| liftMaintenanceCompany | Organization Entity | N/A | max 264 characters | E.g. the representative of the maintenance company. |
| liftLegalOwner | Organization Entity | N/A | max 264 characters |  |
| buildingManager | Organization Entity | N/A | max 264 characters |  |
| liftAlarmMonitoringCentre | Organization Entity | N/A | max 264 characters | The monitoring center of the alarms: user alarms from cars and periodic checks of the bidirectional communication system. |
| inspectionAuthority | Organization Entity | N/A | max 264 characters | The Authority that is entitled to periodically inspect the lift installation and certify its suitability for the intended use. |

## 5.5.7.4	Configuration Information

BIDIRECTIONAL COMMUNICATION SYSTEM

| Information | Type | Meas. Unit | Values | Notes |
| --- | --- | --- | --- | --- |
| homeNetworkOperator | Digits | N/A | MCC-MNC as defined in ITU-T E.212 (5 Digits) | The allocation of MCC-MNC codes in the different nations and regions is officially traced by ITU-T that releases periodic updates. The ITU-T list may be not fully up to date. This information is not configurable, it depends from the Home operator active on the SIM/USIM . |
| supportedNetworkTechnology | Text | Enumerated | FIXED_LINE 2G 3G 4G 5G OTHER | 2G, 3G,4G, 5G, fixed, etc |
| liftTelephoneNumber | Telephone number | N/A | According to ITU-T E.164 (max 15 digits) |  |
| mainEmergencyNumber | Telephone number | N/A | According to ITU-T E.164 (Max 15 digits) |  |
| otherEmergencyNumbers | Array of Telephone numbers | N/A | Array [0..20] of Telephone numbers. The format of each number is according ITU-T E.164 (max 15 digits) |  |
| openDoorTime | Integer | Seconds | 1..100 |  |
| closeDoorTime | Integer | Seconds | 1..100 |  |
| travelTime | Integer | Seconds | 1..300 |  |

## 5.5.7.4	Description of commands

GENERAL COMMANDS

| LIFT COMMAND | Type | Meas. Unit | Values | Additional information |
| --- | --- | --- | --- | --- |
| sendCarToSpecificService | Integer | Pure number | -1.. n | 0..n to call the car to a specific service. The value is reset to -1 when the command has been executed. |
| outOfService | Text | Enumerated | OUT_OF_SERVICE NORMAL | OUT_OF_SERVICE to set the lift in Out of Service mode. NORMAL to switch to the normal operation state. The value is OUT_OF_SERVICES when the lift id in OUT_OF_SERVICE state, NORMAL elesewhere. |
| testEmergencyNumber | Text | Enumerated | START STOP NONE | START to test emergency number; STOP to interrupt the testing; NONE when test is not in exceution. |
| mainBoardReset | Text | Enumerated | START EXECUTION NONE | START to initiate the board reset; EXECUTION when the reset is in execution; NONE after the bootstrap. |
| testRide | Text | Enumerated | START STOP COMPLETED FAILED | START to begin the test ride; STOP to interrupt the testing; COMPLETED when test has been succesfully excuted; FAILED when the test execution failed. |
| realTimeMode | Text | Enumerated | START STOP ACTIVE | START to begin the real time mode. The is value is set to ACTIVE when the real time mode is active. STOP to stop the real time mode. The value remains to STOP when the rreal time mode is not active. |

COMMANDS THAT CAN BE ACTIVATED ONLY IN LOCAL MODE

| LIFT COMMAND | Type | Meas. unit | Values | Additional information |
| --- | --- | --- | --- | --- |
| activateInspectionMode | Text | Enumerated | START STOP ACTIVE | Inspection mode can be only activated locally. START to begin the Inspection mode. The value is set to ACTIVE when the Inspection mode is active. STOP to stop the inspectione mode. The value remains to STOP when the Inspection mode is not active. |

## 5.5.7.5	Fault Signals

| Signal | Type | Meas. Unit | Values | Notes |
| --- | --- | --- | --- | --- |
| faults | Array of Fault | N/A | Variable length array (max 9999 elements) | The index indicates the sequence of the faults from the last reset. |
| floodInTheWell | Boolean | N/A | TRUE/FALSE | TRUE if a flood has been detected (not present in EN627). |

DEFINITION OF FAULT

Fault is defined by the fault code and the time of recording of the fault on the recording machine in the lift.

|  | Elements | Type | Values | Notes |
| --- | --- | --- | --- | --- |
| Fault | faultCode | As defined in EN627 | As defined in EN627 | E.g. : “01xx” broken security chain. |
|  | timeUTC | UTC format as defined in ISO 8601 | UTC format as defined in ISO 8601 | Time of the recording machine in the lift. |

## 5.5.7.6	Bidirectional communication system alarms

| Alarm | Type | Meas. unit | Values | Additional information |
| --- | --- | --- | --- | --- |
| alarmInTheCar | Boolean | N/A | TRUE/FALSE | TRUE when the alarm in the car has been activated. Reset to FALSE when the alarm is suspended. |
| alarmVoiceCommunicationActivated | Boolean | N/A | TRUE/FALSE | TRUE when alarm voice communication has been activated. Reset to FALSE when the alarm is suspended. |
| alarmInTheWell | Boolean | N/A | TRUE/FALSE | TRUE when the alarm in the well has been activated Reset to FALSE when the alarm is suspended |
| alarmInTheRoof | Boolean | N/A | TRUE/FALSE | TRUE when the alarm in the roof has been activated. Reset to FALSE when the alarm is suspended. |
| alarmSuspended | Boolean | N/A | TRUE/FALSE | As indicated in EN 81.28. |

## 5.5.7.7	Monitoring signals

PSEUDO REAL TIME SIGNAL

| Signal | Type | Meas. Unit | Values | Additional information |
| --- | --- | --- | --- | --- |
| currentCarStop | integer | Pure Number | 0-9999 |  |
| currentCarService | integer | Pure Number | 0-9999 |  |
| movingUpwardDirection | Boolean | N/A | TRUE/FALSE | TRUE if the car is moving upward. |
| movingDownwardDirection | Boolean | N/A | TRUE/FALSE | TRUE if the car is moving downward. |
| carInUnlockingZone | Boolean | N/A | TRUE/FALSE | TRUE when the car position enables door opening. |
| testRideInExecution | Boolean | N/A | TRUE/FALSE | TRUE if the test ride is in execution. |
| carTemperature | Real | Celsius | (3 digit and two decimals) | Expected maximum error +- 1 degree Celsius. |
| engineRoomTemperature | Real | Celsius | (3 digit and two decimals) | Expected maximum error +- 1 degree Celsius. |
| shaftTemperature | Real | Celsius | (3 digit and two decimals) | Expected maximum error +- 1 degree Celsius, |
| doorStatus | Variable size array of Boolean | N/A | Array [0..10] of TRUE/FALSE | The Boolean at each position in the array is TRUE if the corresponding door is open. Doors are typically identified by a letter. Door status[1] corrisponds to door A, door status [2] corrisponds to door B, etc. |
| Overload | Boolean | N/A | TRUE/FALSE | TRUE ndicates a condition of overloading in the car. |

BIDIRECTIONAL COMMUNICATION SYSTEM

| Signal | Type | Meas. Unit | Values | Additional information |
| --- | --- | --- | --- | --- |
| timeOfLastPeriodicTest72hAttempt | timeUTC | N/A | UTC format as defined in ISO 8601 | Periodic test as for EN81.28. UTC is defined in ISO 8601. |
| timeOfConfirmationOfLastPeriodicTest72hAttempt | timeUTC | N/A | UTC format as defined in ISO 8601 | Periodic test as for EN81.28. UTC is defined in ISO 8601. |
| registeredNetworkOperator | Digits | N/A | MCC-MNC as defined in ITU-T E.212 (5 Digits) | The allocation of MCC-MNC codes in the different nations and regions is officially traced by ITU-T that releases periodic updates. |
| networkQualityRSSI | integer | dBm | 0..31, 99 | Received SIgnal Streght (via AT commands from the transmission module): 0: -113 dBm or lower quality; 1: -111dBm; 2 .. 30: -109dBm ..-53dBm; 31: -51 Dbm or greater; 99: Not Known or non detectable. |
| networkQualityBER | integer | N/A | 0..7, 99 | Channel Bit Error Rate (via AT commands from the module); 0..7 as for RXQUAL defined by 3GPP TS 45.008 (ETSI TS 45 008). |

POWER SUPPLY SIGNALS

| Signal | Type | Meas. Unit | Values | Additional information |
| --- | --- | --- | --- | --- |
| emergencyBatteryPower | Text | Enumerated | GOOD WARN CRITICAL INSUFFICIENT | GOOD:The battery power is in good operating conditions; WARN: the Battery is functionally in operating conditions but shows signs of reduced capability; CRITICAL: the battery still has the power to send the car to the closest floor in case in failure, but needs to be replaced; INSUFFICIENT: the battery does not have the power to send the car to the closest floor in case in failure; It must be urgently replaced. |
| standardPowerSupply | Boolean | N/A | TRUE/FALSE | TRUE indicates that the standard power supply is currently present. |
| alarmSOSSystemPower | Boolean | N/A | TRUE/FALSE | TRUE Indicates that the power supply of the SOS system is currently present. |
| alarmSOSBatteryPower | Text | Enumerated | GOOD WARN CRITICAL INSUFFICIENT | GOOD: the Battery is functionally in operating conditions; WARN: the Battery is functionally in operating conditions but shows signs of reduced capability; CRITICAL: the battery still has the power to sustain the alarm system active for at least one hour (as required by EN 81.28), but needs to be replaced; INSUFFICIENT: the battery does not has the power to sustain the alarm system active for at least one hour (as required by EN 81.28); It must be urgently replaced. |

SYSTEM STATUS SIGNAL

| Signal | Type | Meas. Unit | Values | Additional information |
| --- | --- | --- | --- | --- |
| outOfService | Boolean | N/A | TRUE/FALSE | TRUE whe the lift is in out of service state. |
| inspectionOperation | Boolean | N/A | TRUE/FALSE | TRUE whe the lift is subject to inspection operation by the maintenance technician. |
| fireOperation | Boolean | N/A | TRUE/FALSE | TRUE whe the lift is subject to fire operation as per EN81.73 (EN81.77 for anti-sismic lifts). |
| DetectedLoad | Boolean | N/A | TRUE/FALSE | TRUE when a load is sensed in the car. Typically when at least one person is in the car. |
| reservedService | Boolean | N/A | TRUE/FALSE | TRUE when the reserved operation is on run. Today it is typically related to the use of a key or a proximity badge to reach a specific floor(s) or service(es). Some examples of reserved operation are the access to a hotel guest to the room floor, of the housekeeper to a floor (or a service door) to acces a personrel-only area, the access of surgical room area in a hospital, etc. |

STATISTIC SIGNALS

| Signal | Type | Meas. Unit | Values | Additional information |
| --- | --- | --- | --- | --- |
| calls | Integer | Pure Number | Value | Total counter from the last reset. |
| upwardTravels | Integer | Pure Number | Value | Total counter from the last reset. |
| downwardTravels | Integer | Pure Number | Value | Total counter from the last reset. |
| totalFloorsCovered | Integer | Pure Number | Value | Total counter from the last reset. |
| numberOfResetSequences | Integer | Pure Number | Value | Total counter from the last reset. |
| totalReversalDirection | Integer | Pure Number | Value | Total counter from the last reset. |
| totalNumberOfOpeningOfDoor | Integer | Pure Number | Value | Total counter from the last reset. |
| callsPerService | Array of integers | Array of pure numbers | Array [1..Number of car services] of integers | Total counter from the last reset. The index is the corrisponding car service. |
| three-phasePowersonsumption | Integer | kWh | Value | Total counter from the last reset. |
| single-phasePowerConsumption | Integer | kWh | Value | For lifts with both three-phase and single-phase power it provides the power consumtion for the services in the lift (e.g. the car lights). For lifts with single-phase power if provides the total power consumtion of the lift. |
| servicesPowerConsumption | Integer | kWh | Value | In case of Single-phase power lifts, it provides te power consumption for the services in the lift (e.g. the car lights). |

### -----------------------End of change 1--------------------------------------------

### -----------------------Start of Changes to References Clause -------------

## 2.2	Informative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

…….

[i.y]    ETSI TR 103 546 SmartM2M; Requirements & Feasibility study for Smart Lifts in IoT.

…….

### ---End of changes to Definition of terms, symbols and abbreviations---