| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM 47 |
| Source:* | TaeHyun KIM, SyncTechno Inc., thyun.kim@synctechno.com |
| Date:* | 2020-10-13 |
| Reason for Change/s:* | See the introduction. |
| CR against: Release* | Release 4 |
| CR against: WI* | Active WI-0070 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0037-V-4.0.5 IoT Public Warning Service Enablement |
| Clauses * | Clause 1, 5, 6 and Annex A, B |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR provides necessary inputs and changes to complete the TS-0037. Change 1 describes the scope of the TS. The new clause 5 defines public warning service information model based on the SDT. This information model is going to be used for things to understand the warning information from authorities. In clause 6, the information model is mapped to each <flexContainer> resource specializations. Finally the annex provides informative guide for implementation and analysis on the CAP.

### -----------------------Start of change 1-------------------------------------------

# 1	Scope

The present document specifies the unified information model of the public warning service and defines the resource mapping rule for the information model of the public warning service over oneM2M system. The information model of the public warning service described in this document is applicable not only for an emergency alerting that authorities send the public but also for warnings that used to be distributed to IoT devices in commercial services.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# 5	Information Model of Public Warning Service

## 5.1	Background

### 5.1.1	Public Warning Service for Things

Public warning service enables authorities in charge of public safety to send an emergency alert to things in order to make things take a proper action to reduce unexpected damages from an emergency when receiving an emergency alert.

Public warning messages for things include information related to an emergency event such as:

- Geographic targeting area where an emergency event happens;

- Detailed information to provide how to take actions when receiving a public warning message with things

- Effective period for a valid public warning message;

- Relevant information that is useful for things to take best-effort options to reduce the risk or avoid the emergency.

### 5.1.2	Common Alerting Protocol (CAP)

The CAP is widely used to specify the information model applied for systems of authorities in charge of initiating a public warning message. Figure 5.1.2-1 shows the CAP document object model describing the structure of CAP message and Annex B describe the classification of CAP-based information that is interpretable by things in CAP 1.2 specification [4]. The CAP based information needs to be transformed into oneM2M based information in order to make things understand an emergency event notified from authorities and take a proper action.

boldface: mandatory italics: have default values asterisks (*): multiple instances are permitted.

Figure 5.1.2-1 CAP document object model. (source: ITU-T REC X.1303)

### 5.1.3	SDT based information model

The information model of public warning service is specified by SDT schema [i.4].

### 5.1.4	Possible architecture for oneM2M based public warning service

Figure 5.1.4-1 Possible architecture and SDT mapping

Figure 5.1.4-1 describes the example of the oneM2M based architecture for public warning service and how ASN(public warning center) and devices(ADN) are defined as SDT based information model.

The example of the oneM2M based architecture consists of following functional entities.

- Authority Warning System is the system used by authorities who issue an alert. The CAP based message initiated by Authority Warning System is transmitted to oneM2M SP Gateway but also other warning dissemination media via R1 interface. The interface between Authority Warning System and oneM2M SP Gateway is out of scope of oneM2M specifications.

- oneM2M SP(Service Provider) Gateway (ASN) enables oneM2M Service Provider to interwork with external systems. When the Authority Warning System as an external system issues CAP based information to be disseminated via R1 interface, the oneM2M SP Gateway forwards that CAP based information to the Public Warning Center.

- Public Warning Center (ASN) is to transform CAP based information received from oneM2M SP Gateway into oneM2M based information that is interpretable by things. In addition, Public Warning Center (ASN) identifies targeted things that need to receive the public warning message issued by Authority Warning System.

- OneM2M Devices (ADN, NoDN) take an action specified in normal mode before receiving a public warning message but change into an emergency mode as receiving a public warning message in order to take an emergency action.

## 5.2	Domain

The domain for pubic warning service is identified as org.onem2m.publicsafety.

## 5.3	ModuleClasses

### 5.3.1	disseminator

This ModuleClass provides the capability of creating oneM2M based information from CAP based information received from oneM2M SP Gateway (ASN) and of controlling the change of received public warning messages such as updating oneM2M based information and cancelling the dissemination of oneM2M based information.

Table 5.3.1-1: Actions of disseminator ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| Ack/Error | create | warningMessage | false | Create an oneM2M based information |
| Ack/Error | update | warningUpdateMessage | true | update previously requested warning |
| Ack/Error | cancel | warningIdentifier | true | cancel previously requested warning |

Table 5.3.1-2: DataPoints of disseeminator ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| identifier | xs:string | W | false |  | The identifier of the warning message that uniquely identifying this message. |
| sender | xs:string | W | false |  | The identifier of the originator of this alert message. |
| sent | xs:dateTime | W | false |  | The time and date of the origination of this alert message. |
| status | pws:enumAlertStatus | W | false |  | The code to represent the appropriate handling of the alert message receiver. The value of this DataPoint is specified the CAP 1.2 specification (see clause 5.5.1). |
| msgType | pws:enumAlertMsgType | W | false |  | The code to represent the nature of the alert message. . The value of this DataPoint is specified the CAP 1.2 specification (see clause 5.5.2). |
| references | list of xs:string | W | false |  | The list of identifiers for earlier message(s) referenced by this alert message. |
| urgency | pws:enumUrgency | W | false |  | The code representing the urgency of the subject event of the alert message (see clause 5.5.3). |
| severity | pws:enumSeverty | W | false |  | The code representing the severity of the subject event of the alert message (see clause 5.5.4). |
| certainty | pws:enumCertainty | W | false |  | The code representing the certainty of the subject event of the alert message (see clause 5.5.5). |
| eventCodes | list of key-value pair | W | false |  | The definitions of system-specific codes identifying the event type of the alert message. A code definition consists of valueName and value. Multiple eventCode can be presented in an <info> element. |
| effective | xs:dateTime | W | false |  | The effective time of the information of the alert message. |
| onset | xs:dateTime | W | false |  | The expected time of the beginning of the subject event of the alert message. |
| expires | xs:dateTime | W | false |  | The expiry time of the information of the alert message. |
| area | pws:TargetArea | W | false |  | The definition of all component parts of the area identifying an affected area. |
| repeatitionPeriod | xs:integer | R | false | seconds | This specifies the repetition period for the warning message. The value of this DataPoint indicates the period of time in seconds after which re-send of the warning message should be repeated. |
| repeatitionCount | xs:integer | R | false |  | This specifies the number of times the warning message is to be sent. |

### 5.3.2	emergencyHandler

This ModuleClass provides the capability of triggering things to change into an emergency mode and of enabling things to identify whether an event described in oneM2M based information that is received from Public Warning Center (ASN) is relevant to things. If any change happens in received warning messages such as updating oneM2M based information and cancelling the dissemination of oneM2M based information of previously received public warning messages, this ModuleClass updates oneM2M based information corresponding to those received public warning messages to control behaviour of things.

Table 5.3.2-1: Actions of emergencyHandler ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | trigger | warningMessage | false | trigger emergency mode to public warning supporting equipment(device). |
| none | update | warningMessage | true | update previously triggered warning information. |
| none | terminate | warningId | true | terminate emergency mode process of public warning supporting device and resume peace time process. |

Table 5.3.2-2: DataPoints of emergencyHandler ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| emergencyMode | xs:boolean | R | false |  | This specifies the emergency mode of target device. "True" means the device is working in emergency mode. "False" means the device is working in normal model |

### 5.3.3	settings

This ModuleClass provides the capability of selecting the option that allows things to decide to take action as receiving oneM2M based information of public warning messages.

Table 5.3.3-1: Actions of settings ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | optout | flag | false | set the opt-out state for the device. The flag argument specifies new opt-out state. True means that this device does not want to response when a warning has been triggered. |

Table 5.3.3-1: DataPoints of settings ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| optoutStatus | xs:boolean | R | false |  | This specifies the opt-out state for the device. The value of this DataPoint specifies opt-out state. True means that this device does not want to response when a warning has been triggered. |

## 5.4	Device models

### 5.4.1	devicePWSCenter

Table 5.4.1-1: Modules of devicePWSEquipment Device

| Type | Name | Description | Type | Mandatory/ Optional |
| --- | --- | --- | --- | --- |
| Module | disseeminator | See clause 5.3.1-1 | - | M |

### 5.4.2	devicePWSEquipment

Table 5.4.2-1: Modules of devicePWSEquipment Device

| Type | Name | Description | Type | Mandatory/ Optional |
| --- | --- | --- | --- | --- |
| Module | emergencyHandler | See clause 5.3.2-1 | - | M |
|  | settings | See clause 5.3.3-1 | - | M |

## 5.5	Enumeration type definitions

This clause defines the enumeration type of the domain for public warning service. The “pws” namespace qualifier is used to indicate the terms of the domain for public warning service.

### 5.5.1	pws:enumAlertStatus

The enumeration type, pws:enumAlertStatus, enables things to identify the alert status that describes whether a received public warning message as oneM2M based information is an actual alert issued by authorities or an alert for testing the public warning service over oneM2M system.

Table 5.5.1-1: Interpretation of pws:enumAlertStatus

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Actual | Actionable by all targeted recipients |
| 2 | Exercise | Actionable only by designated exercise participants |
| 3 | System | For messages that support alert network internal functions |
| 4 | Test | Technical testing only, all recipients disregard |
| 5 | Draft | A preliminary template or draft, not actionable in its current form |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

### 5.5.2	pws:enumAlertMsgType

The enumeration type, pws:enumAlertMsgType, describes the message type of oneM2M based information transformed from CAP based information isssued by authorities.

Table 5.5.2-1: Interpretation of pws:enumAlertMsgType

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Alert | Initial information requiring attention by targeted recipients |
| 2 | Update | Updates and supercedes the earlier message(s) |
| 3 | Cancel | Cancels the earlier message(s) |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

### 5.5.3	pws:enumUrgency

The enumeration type, pws:enumUrgency, describes the urgency of the event defined in oneM2M based information transformed from CAP based information issued by authorities.

Table 5.5.3-1: Interpretation of pws:enumUrgency

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Immediate | Responsive action should be taken immediately |
| 2 | Expected | Responsive action should be taken soon (within next hour) |
| 3 | Future | Responsive action should be taken in the near future |
| 4 | Past | Responsive action is no longer required |
| 5 | Unknown | Urgency not known |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

### 5.5.4	pws:enumSeverity

The enumeration type, pws:enumSeverity, describes the severity of the event defined in oneM2M based information transformed from CAP based information issued by authorities.

Table 5.5.4-1: Interpretation of pws:enumSeverity

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Extreme | Extraordinary threat to life or property |
| 2 | Severe | Significant threat to life or property |
| 3 | Moderate | Possible threat to life or property |
| 4 | Minor | Minimal to no known threat to life or property |
| 5 | Unknown | Severity unknown |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

### 5.5.5	pws:enumCertainty

The enumeration type, pws:enumCertainty, describes the certainty of the event defined in oneM2M based information transformed from CAP based information issued by authorities.

Table 5.5.5-1: Interpretation of pws:enumCertainty

| Value | Name | Interpretation |
| --- | --- | --- |
| 1 | Observed | Determined to have occurred or to be ongoing |
| 2 | Likely | Likely (p > ~50%) |
| 3 | Possible | Possible but not likely (p <= ~50%) |
| 4 | Unlikely | Not expected to occur (p ~ 0) |
| 5 | Unknown | Certainty unknown |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

# 6	Resource Mapping

## 6.1	Resource Mapping Rules

The resource mapping rule of the information model of public warning service is defined according to the clause 6.2 of TS-0023 [i.3].

## 6.2	Short names

### 6.2.1	Resource types

In protocol bindings, resource type names for device models shall be translated into short names of Table 6.2.1-1.

Table 6.2.1-1: Specialization type short names (Devices)

| Resource Type Name | Short Name |
| --- | --- |
| devicePWSCenter | dPWC |
| devicePWSEquipment | dPWE |

In protocol bindings, resource type names for module classes shall be translated into short names of Table 6.2.1-2.

Table 6.2.1-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| disseminator | pwDsmt |
| enrollment | pwEnrl |
| emergency | pwEmgc |
| settings | pwSt |

In protocol bindings, resource type names for actions shall be translated into short names of Table 6.2.1-3.

Table 6.2.1-3: Specialization type short names (Actions)

| Resource Type Name | Short Name |
| --- | --- |
| initiate | pwcInit |
| update | pwcUpd |
| cancel | pwcCnc |
| enroll | pwcClo |
| update | pwcUpdr |
| withdraw | pwcWid |
| trigger | pwdTrg |
| update | pwdUpd |
| terminate | pwdTmt |
| optout | pwdOto |

## 6.3	containerDefinition values

### 6.3.1	Introduction

Each specialization has a containerDefinition attribute which can be used as a unique identifier and contains the information of the resource. In this clause, the detailed values of containerDenifition attributes in every specialization for the public warning service information models are given.

### 6.3.2	Device models

The containerDefinition attribute of specialization for device models shall have the values that comply with the following rule.

- Rule: “org.onem2m.publicsafety.device.[device name]”

According to the rule above, the containerDefinition attributes of the specialization for device models are defined as follow.

Table 6.3.2-1: Definition of containerDefinition attribute for public warning service device models

| Name | containerDefinition | Description |
| --- | --- | --- |
| devicePWSCenter | org.onem2m.publicsafety.device.devicePWSCenter | See clause 5.4.1 |
| devicePWSEquipment | org.onem2m.publicsafety.device.devicePWSEquipment | See clause 5.4.2 |

### 6.3.3	ModuleClasses

The containerDefinition attribute of specialization for module classes shall have the values that comply with the following rule.

- Rule: “org.onem2m.publicsafety.moduleclass.[moduleclass name]”

According to the rule above, the containerDefinition attributes of the specialization for module classes are defined as follows.

Table 6.3.3-1: Definition of containerDefinition attribute for public warning service module classes

| Name | containerDefinition | Description |
| --- | --- | --- |
| disseeminator | org.onem2m.publicsafety.moduleclass.disseeminator | See clause 5.3.1 |
| emergencyHandler | org.onem2m.publicsafety.moduleclass.emergencyHandler | See clause 5.3.2 |
| settings | org.onem2m.publicsafety.moduleclass.settings | See clause 5.3.3 |

### 6.3.4	Action Models

The containerDefinition attribute of specialization for action models shall have the values

that comply with the following rule.

- Rule: “org.onem2m.home.moduleclass.[name of moduleClass that the action belongs to].[action name]”

According to the rule above, the containerDefinition attributes of the specialization for action models are defined as follows

Table 6.3.4-1: Definition of containerDefinition attribute for public warning service action models

| Module Classe | Action | containerDefinition | Description |
| --- | --- | --- | --- |
| disseeminator | initiate | org.onem2m.publicsafety.moduleclass.disseeminator.initiate | See clause 5.3.1 |
|  | update | org.onem2m.publicsafety.moduleclass.disseeminator.update |  |
|  | cancel | org.onem2m.publicsafety.moduleclass.disseeminator.cancel |  |
| emergencyHandler | trigger | org.onem2m.publicsafety.moduleclass.emergency.trigger | See clause 5.3.2 |
|  | update | org.onem2m.publicsafety.moduleclass.emergency.update |  |
|  | terminate | org.onem2m.publicsafety.moduleclass.emergency.terminate |  |
| settings | optout | org.onem2m.publicsafety.moduleclass.settings.optout | See clause 5.3.3 |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

Annex <A>(Informative): Warning dissemination using group resource

The oneM2M system supports hierarchical group resources by using sub-group features that are applicable to the dissemination function of a public warning message to multiple devices.

Figure A-1 depicts an example of a hierarchical group structure to disseminate a public warning message to some of targeted areas selectively.

Hierarchical group mechanism is applicable to any multi-level categorization (e.g. type of devices, type of emergency events and severity of warning etc.).

Figure A-1: Example of <group> resource structure for disseminate warning messages.

- (A-1) request to create a warning message instance to a target <group> resource (e.g. C-Town-Group) to disseminate warning for emergence event (Warning-A).

- (A-2) fan out the requested operation to all members of the group. A member can be a <flexContainer> specialization of [trigger] (See clause 5.3.2) or a sub-group

- (A-3) fan out the requested operation repeatedly if faned out target is a sub-group

- (A-2, A-3) eventually, All members including members in sub-group can receive the request to create warning message instance for emergency event A

- (B-1) request to create a warning message instance to a target <group> resource (e.g. C-Town-Group) to disseminate warning for emergence event (Warning-B).

- (B-2) fan out the requested operation to all members of the group. eventually, All member devices of the target <group> resource (e.g. C-Town-Group) receive the request to create warning message instance for emergency event B

Annex <B>(Informative): Machine interpretable information of CAP message

# B.1	Machine interpretable information of the CAP <alert> element

The <alert> element provides basic information for current public warning message that consists of its purpose, source and status, as well as a unique indentifier for the current warning message. Table B.1-1 shows the classification of attributes for CAP <alert> element that is interpretable by things

Table B.1-1 The classification of attributes for <alert> element.

| Name | Type | Description | Machine interpetability |
| --- | --- | --- | --- |
| identifier | xs:string | The identifier of the alert message, contains a number or string value that uniquely identifying this message. | Interpretable |
| sender | xs:string | The identifier of the originator of this alert message. This value must guaranteed by assigner to be unique globally. | Interpretable |
| sent | xs:dateTime | The time and date of the origination of this alert message. This value shall be represented in the DateTime format (e.g., "2002-05-24T16:49:00-07:00" for 24 May 2002 at 16:49 PDT) | Interpretable |
| status | xs:string | The code to represent the appropriate handling of the alert message receiver. The CAP 1.2 specification restricts code values as belows. “Actual” - Actionable by all targeted recipients “Exercise” - Actionable only by designated exercise participants; exercise identifier SHOULD appear in <note> “System” - For messages that support alert network internal functions “Test” - Technical testing only, all recipients disregard “Draft” – A preliminary template or draft, not actionable in its current form | Interpretable |
| msgType | xs:string | The code to represent the nature of the alert message. The CAP 1.2 specification restricts code values as belows. “Alert” - Initial information requiring attention by targeted recipients “Update” - Updates and supercedes the earlier message(s) identified in <references> “Cancel” - Cancels the earlier message(s) identified in <references> “Ack” - Acknowledges receipt and acceptance of the message(s) identified in <references> “Error” - Indicates rejection of the message(s) identified in <references>; explanation SHOULD appear in <note> | Interpretable |
| source | xs:string | Not standardised human readable text identifying an operator or a specific device as the source of the alert message. | Not interpretable |
| scope | xs:string | The code to represent the intending scope of distribution for this alert message. The CAP 1.2 specification restricts code values as belows. “Public” - For general dissemination to unrestricted audiences “Restricted” - For dissemination only to users with a known operational requirement (see <restriction>, below) “Private” - For dissemination only to specified addresses (see <addresses>, below) | Interpretable |
| restriction | xs:string | Not standardised human readable text to denote the rule for limiting distribution of the restricted alert message. This property appears when “scope” value is “Restricted”. | Not interpretable |
| addresses | xs:string (Separated by white space) | The list of address for a recipients of the alert message. Value of address can be an identifier or an address. This property is required when “scope” value is “Private” and optional when “scope” value is “Public” or “Restricted”. | If the value of an address is an identifier, this field would be Machine interpretable |
| code | xs:string | User-defined flag or special code used to handle specially. Multiple code can be presented for an alert message. The format and semantics of the code value are not defined in CAP 1.2 specification. | Interpretable |
| note | xs:string | Not standardised human readable text clarifying the purpose or significant of the the alert message when “status” value is “Exercise” and “msgType” value is “Error”. | Not interpretable |
| references | xs:string (Separated by white space) | The list of identifiers for earlier message(s) referenced by this alert message. | Interpretable |
| incidents | xs:string (Separated by white space) | The list of names which are referenced incident(s) of the alert message. | Not interpretable |
| info | xs:complexType(<info> element) | The container for all component parts of the info sub-element of the alert message. Multiple occurrences are permitted within a single <alert> element to support multiple language or sequence of alert information for an alert message. | n/a (This property is a sub-element described in Table B.2-1) |

# B.2	Machine interpretable information of the CAP <info> element

The <info> element provides both categorical and textual description of the subject emergency event. It may also provide instructions for appropriate response against the received warning message and extra details (e.g. hazard duration, tehnical parameters, contact information, links to additional media resource, etc.). Table B.2-1 shows the classification of attributes for CAP <info> element that is interpretable by things

Table B.2-1 The classification of attributes for <info> element.

| Name | Type | Description | Machine interpetability |
| --- | --- | --- | --- |
| language | xs:language | Contains a [RFC 3066] code value denoting the language of the info sub-element of the alert message. | Interpretable |
| category | xs:string | The code denoting the category of the alerting event of the alert message. The CAP 1.2 specification restricts code values as belows. Multiple caterory can be presented in an <info> element. “Geo” - Geophysical (inc. landslide) “Met” - Meteorological (inc. flood) “Safety” - General emergency and public safety “Security” - Law enforcement, military, homeland and local/private security “Rescue” - Rescue and recovery “Fire” - Fire suppression and rescue “Health” - Medical and public health “Env” - Pollution and other environmental “Transport” - Public and private transportation “Infra” - Utility, telecommunication, other non-transport infrastructure “CBRNE” – Chemical, Biological, Radiological, Nuclear or High-Yield Explosive threat or attack “Other” - Other events | Interpretable |
| event | xs:string | Not standardised human readable text describing the type of the subject event of the alert message | Not interpretable |
| responseType | xs:string | The code denoting the type of recommended response action for the target audience when the alert message received. The CAP 1.2 specification restricts code values as belows. Multiple responseType can be presented in an <info> element. “Shelter” – Take shelter in place or per <instruction> “Evacuate” – Relocate as instructed in the <instruction> “Prepare” – Make preparations per the <instruction> “Execute” – Execute a pre-planned activity identified in <instruction> “Avoid” – Avoid the subject event as per the <instruction> “Monitor” – Attend to information sources as described in <instruction> “Assess” – Evaluate the information in this message. (This value SHOULD NOT be used in public warning applications.) “AllClear” – The subject event no longer poses a threat or concern and any follow on action is described in <instruction> “None” – No action recommended | Interpretable |
| urgency | xs:string | The code representing the urgency of the subject event of the alert message. The CAP 1.2 specification restricts code values as belows. “Immediate” - Responsive action SHOULD be taken immediately “Expected” - Responsive action SHOULD be taken soon (within next hour) “Future” - Responsive action SHOULD be taken in the near future “Past” - Responsive action is no longer required “Unknown” - Urgency not known | Interpretable |
| severity | xs:string | The code representing the severity of the subject event of the alert message. The CAP 1.2 specification restricts code values as belows. “Extreme” - Extraordinary threat to life or property “Severe” - Significant threat to life or property “Moderate” - Possible threat to life or property “Minor” – Minimal to no known threat to life or property “Unknown” - Severity unknown | Interpretable |
| certainty | xs:string | The code representing the certainty of the subject event of the alert message. The CAP 1.2 specification restricts code values as belows. “Observed” – Determined to have occurred or to be ongoing “Likely” - Likely (p > ~50%) “Possible” - Possible but not likely (p <= ~50%) “Unlikely” - Not expected to occur (p ~ 0) “Unknown” - Certainty unknown | Interpretable |
| audience | xs:string | Not standardised human readable text describing the intended audience of the alert message | Not interpretable |
| eventCode | xs:complexType | The definitions of system-specific codes identifying the event type of the alert message. A code definition consists of valueName and value. Multiple eventCode can be presented in an <info> element. | Interpretable |
| effective | xs:dateTime | The effective time of the information of the alert message. This value shall be represented in the DateTime format (e.g., "2002-05-24T16:49:00-07:00" for 24 May 2002 at 16:49 PDT). If this value is not presented, effective time is assumed to be the same time as in “sent” | Interpretable |
| onset | xs:dateTime | The expected time of the beginning of the subject event of the alert message. This value shall be represented in the DateTime format (e.g., "2002-05-24T16:49:00-07:00" for 24 May 2002 at 16:49 PDT). | Interpretable |
| expires | xs:dateTime | The expiry time of the information of the alert message. This value shall be represented in the Date Time format (e.g., "2002-05-24T16:49:00-07:00" for 24 May 2002 at 16:49 PDT). If this value is not presented, recipient can set own expiration policy. | Interpretable |
| senderName | xs:string | Not standardised human readable name of the agency or authority issuing this alert message. | Not interpretable |
| headline | xs:string | Not standardised human readable short headline text of the alert message. 160 characters are recommended. | Not interpretable |
| description | xs:string | Not standardised human readable extended description of the hazard or event that occasioned this message. | Not interpretable |
| instruction | xs:string | Not standardised human readable instruction describing recommended action to targeted recipients. | Not interpretable |
| web | xs:anyURI | The hyperlink URI for an HTML page or text resource to provide additional information for the alert message | Interpretable |
| contact | xs:string | Not standardised human readable text describing the contact for follow-up and confirmation of the alert message. | Not interpretable |
| parameter | xs:complexType | The definitions of system-specific parameter associated with the alert message. A parameter definition consists of valueName and value. Multiple parameter can be presented in an <info> element. | Interpretable |
| resource | xs:complexType(<resource> element) | The definitions of all component parts of the resource referes to an additional file. This definition to be used to provide multimedia file to recipients. Multiple resource can be presented in an <info> element. | n/a (This property is a sub-element described in Table B.3-1) |
| area | xs:complexType(<area> element) | The definition of all component parts of the area identifying an affected area. A <info> element may contain one or multiple area definition to identify union of all the included area. | n/a (This property is a sub-element described in Table B.4-1) |

# B.3	Machine interpretable information of the CAP <resource> element

The <resource> element provides additional information about subject event in the form of a digital asset such as an image or audio resource link. Table B.3-1 shows the classification of attributes for CAP <resource> element that is interpretable by things

Table B.3-1 The classification of attributes for <resource> element.

| Name | Type | Description | Machine interpetability |
| --- | --- | --- | --- |
| resourceDesc | xs:string | Not standardised human readable description of the thpe and content of a referenced resource file (for example a map or photograph). | Not interpretable |
| mimeType | xs:string | The MIME type, as described in [RFC2046], identifier describing the referenced resource file. | Interpretable |
| size | xs:integer | The approximate size of the resource file in bytes indicating the size of the referenced resource file. | Interpretable |
| uri | xs:anyURI | The hyperlink URL that can be used to retrieve the resource over the Internet. | Interpretable |
| derefUri | xs:string | An alternative to the uri resource hyperlink giving the Base64 encoded content of the resource file. | Interpretable |
| digest | xs:string | The SHA-1 hash value of the resource file for validation. | Interpretable |

# B.4	Machine interpretable information of the CAP <area> element

The <area> element describes a geographic area that specifies the target area to which propagate for the related emergency event. Table B.4-1 shows the classification of attributes for CAP <area> element that is interpretable by things

Table B.4-1 The classification of attributes for <area> element.

| Name | Type | Description | Machine interpetability |
| --- | --- | --- | --- |
| areaDesc | xs:string | Not standardised human readable description of the affected area of the alert message. | Not interpretable |
| polygon | xs:string | The space-separated list of coordinate pair defnes the polygon that identify the affected area of the alert message. Each coordinate value contains geolocation position value as specified in [WGS84] standard. Multiple polygon in an <area> element is used to identify union of all polygons. | Interpretable |
| circle | xs:string | The space-separated list of coordinates for a center position and a radius that identify the affected area of the alert message. The first two [WGS84] geolocation position value represents the center position of the circle, and last value represents the radius delineating in kilometres. Multiple circle in an <area> element is used to identify union of all polygons. | Interpretable |
| geocode | xs:complexType | The geographic code identifying the affected area of the alert message. A geocode consists of valueName and value. Multiple geocode can be presented in an <area> element. | Interpretable |
| altitude | xs:decimal | The specific or minimum altitude in feet above mean sea level of the affected area of the alert message. | Interpretable |
| ceiling | xs:decimal | The maximum altitude in feet above mean sea level of the affected area of the alert message. | Interpretable |

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?