| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM 47 |
| Source:* | Shane HE, Nokia, shane.he@nokia.com |
| Date:* | 2020-10-22 |
| Reason for Change/s:* | Adding a new use case for railway domain safety |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <WI-0092> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0058 V0.7.0 |
| Clauses * | 6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR is provided to add a new use case for TR-0058 to address the concern of railway domain safety.

### -----------------------Start of change 1-------------------------------------------

## 6.5	Railway crossing safety service

### 6.1.1	Description

In urban areas, pedestrians need to cross railways according to the traffic lights and/or crossing gates which are usually controlled according the train schedule. In some situation, unauthorized entry during the train passing through, which is difficult to be quickly detected by radar systems, may cause critical accidents. Video-based analytics can offer real-time monitoring functionality and performance to improve the safety of railway systems.

### 6.1.2	Source

RDM-2020-0082 Railway usecase

### 6.1.3	Actors

Railway Worker: A user to maintain the railway service. In this case can be s train driver.

CCTV: video cameras installed in the train station and cross joint for safety reason.

Edge Nodes: gateways or nodes which can apply real-time analytics functions and communicate with Cloud Nodes.

Cloud Nodes: Cloud Servers which can provide remote computation capabilities for analytics

Railway Operation System: M2M applications to manage railway operation.

### 6.1.4	Pre-conditions

Edge Nodes and Clouds Nodes are able to provide video-based analytics with pre-installed software.

The operation schedule is pre-defined in Railway Operation System.

### 6.1.5	Triggers

CCTVs detect abnormal image, and Edge Nodes identify the abnormal case via image analysing.

### Normal Flow

CCTVs detect abnormal image, and Edge Nodes identify the abnormal case via image analysing and the pre-defined operation schedule, as well as other information from such as sensors, radar systems.

Edge Nodes send analytics result to the Cloud Node. The Cloud Node identifies if it is critical satefy case based on further analytics functions.

The Cloud Node sends report to the Railway Operation System, and the Railway Operation System sends back the alerts.

The Cloud Node sends alerts to the Railway Worker who is in the operation schedule and authorized to manage this situation. The Railway Worker reports the result to Railway Operation System after the actions.

The Railway Operation System applys further operation, e.g. report to related stations and informative systems.

### 6.1.7	Alternative Flow

None

### 6.1.8	Post-conditions

None

### 6.1.9	High Level Illustration

Figure 6.1.9-1 : High Level Illustration - Accessing devices based on time schedule

### 6.1.10	Potential requirements

The oneM2M System shall support handover on specific services between Edge/Fog Nodes and Cloud Nodes.

The oneM2M System shall be able to dynamically obtain, process and preserve metadata.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?