| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM 48 |
| Source:* | Andrew Min-gyu Han, Hansung University,andyhan@hansung.ac.kr Seung-wook Lee, ETRI, tajinet@etri.re.kr |
| Date:* | 2020-12-08 |
| Reason for Change/s:* | Add a 3D scanner device in Common Domain |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <WI-0084> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V4.5.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR adds a 3D scanner device in the common domain

### -----------------------Start of change 1-------------------------------------------

#### 5.5.1.x	device3Dscanner

A 3D scanner is a device to scan 3D objects such as a statue of a character.

Table 5.5.1.x-1: Modules of device3Dscanner device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| clock | clock | 0..1 | See clause 5.3.1.18. |
| 3DScanState | runState | 1 | See clause 5.3.1.75. |
| 3DScanner | 3DScanner | 1 | See clause 5.3.1.y. |
| connectivity | connectivity | 1 | See clause 5.3.1.25. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 5.3.1.y	3DScanner

This ModuleClass provides the capability to get selections of a user from the pre-defined menus on the screen as parts of a process of charging transportation payment card of the user.

Table 5.3.1.y-1: DataPoints of 3DScanner ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| 3DScannerType | hd:enum3DScannerType | R | false |  | This data point indicates type of the 3D scanner |
| 3DScanResolution | xs:integer | R | false | dpi | This data point indicates the scanning resolution. |
| maxSizeX | xs:float | R | true | cm | This data point indicates the maximum horizontal size of the scanning. |
| maxSizeY | xs:float | R | true | cm | This data point indicates the maximum vertical size of the scanning. |
| maxSizeZ | xs:float | R | true | cm | This data point indicates the maximum depth of the scanning. |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 5.6.z	hd:enum3DScannerType

Used for the “3DScannerType” DataPoint of the “3DScanner” ModuleClass.

Table 5.6.z-1 Interpretation of hd:enum3DScannerType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | TOF | Use “Time Of Flight” method to scan 3D object. The technology calculates time gap between shooting and return of the reflected laser light. |
| 2 | Phase Shift | The technology uses “Phase shift waveform analysis”. It analysises the distance gap between two reflected laser beam phase which are shot from the scanner. |
| 3 | Waveform | The technology uses “Triangulation method”. Based on the triangulation method, it uses pointbeam or TOF method. |
| 4 | MPT | The technology uses “Miniaturized Projection Technique” to scan. It projects specific pattern of White light, indicates the size and depth by analysis of the reflected pattern on the object. |
| 5 | ETC | The other technology is used to scan an object. |

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?