| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#52 |
| Source:* | SeungMyeong JEONG, KETI, sm.jeong@keti.re.kr Il-Yeup Ahn, KETI, iyahn@keti.re.kr NakMyung Sungm, KETI, nmsung@keti.re.kr Chungjae Choe, KETI, cjchoe1@keti.re.kr |
| Date:* | 2021-11-12 |
| Reason for Change/s:* | To define water domain sensor data models |
| CR against: Release* | 5 |
| CR against: WI* | Active: WI-0075 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | n/a |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes to have a new domain as “Water Domain” with a couple of module classes. Having a separate Water Domain for further development would require relocation of several water domain related modules classess in the common domain at the moment (e.g. waterQualityMonitor).

It would be really preferrable to have domain experts in this work (e.g. K-Water in South Korea).

This contribution tries to open up the water domain model consolidation and several common Action features for other domains as well.

This would not be the final version but from the PoC adopted the draft models like:

### ********** Start of change 1 **********

### Water Domain

#### 5.5.9.1 deviceWaterQualityMeasurementInstrument

An water quality mesaurement instrument is an measurement device that reads different water quality properties and receive remote controls.

Table 5.5.9.1-1: Modules of deviceWaterQualityMeasurementInstrument Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| wtqltGnrlMesureSetup | waterQualityMeasuringSetup | 1 | See clause 5.3.9.xx |
| wtqltGnrlMesureEvent | waterQualityMeasuringEvent | 1 | See clause 5.3.9.xx |
| wtqltGnrlMesureItem | waterQualityGeneralMeasurementItem | 0..1 | See clause 5.3.9.xx |
| wtqltIonMesureIem | waterQualityIonMeasurementItem | 0..1 | See clause 5.3.9.xx |
| wtqltMtlMesureItem | waterQualityMetalMeasurementItem | 0..1 | See clause 5.3.9.xx |
| wtqltOrgMttrMesureItem | waterQualityOrganicMatterMeasurementItem | 0..1 | See clause 5.3.9.xx |
| wtqltVtlOrgCompMesureItem | waterQualityVolatileOrganicCompoundsMeasurementItem | 0..1 | See clause 5.3.9.xx |
| wtqltMcrbMesureItem | waterQualityMicrobeMeasurementItem | 0..1 | See clause 5.3.9.xx |
| wtqltRunState | runState | 0..1 | See clause 5.3.9.xx |

### ********** End of change 1 **********

### ********** Start of change 2 **********

### Water Domain

#### waterQualityMeasurementSetup Module

A balise is an electronic beacon or transponder placed between the rails of a railway as part of an automatic train protection (ATP) system.

The Balise Transmission Module(BTM) ModuleClasses provides capabilities to indicate and to get balise information.

Table 5.3.9.1-1: Actions of waterQualityMeasurementSetup ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | AlarmSwitch | none | true | Toggles alarmActivity Data Point. |
| none | MsrinsreprtSwitch | none | true | Toggles reportActivity Data Point. |

Table 5.3.9.1-2: DataPoints of waterQualityMeasurementSetup ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| maxValidNtu | xs:float | R | false | mg/L | Set the maximum measured value of the turbidity sensor set by the manufacturer. |
| minValidNtu | xs:float | R | false | mg/L | Set the minimum measured value of the turbidity sensor set by the manufacturer. |
| reportIntervl | xs:integer | RW | false | second | Change the measurement interval of turbidity value. |
| alarmActivity | xs:boolean | R | fase | - | Toggle to turn on and off user alarm when the sensor measurement is invalid per min and max setting by maxValidNtu and minValidNtu |
| reportActivity | xs:boolean | R | fase | - | Toggle to turn on and off whether sensor sends the measurement data. |

### ********** End of change 2 **********

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?