| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#55 |
| Source:* | Xiaotao Li, CMCC, lixiaotao@chinamobile.com Shujuan You, CMCC, youshujuan@ chinamobile.com Yawen Niu, CMCC, niuyawen@chinamobile.com |
| Date:* | 2022-07-02 |
| Reason for Change/s:* | Adding the remoteControlEnable Module to the deviceRobotCleaner Device model |
| CR against: Release* | Rel.5 |
| CR against: WI* | Active WI-0084 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V5.1.0 |
| Clauses * | clause in 5.5.4.22 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR adds a remoteControlEnable module to the deviceRobotCleaner model.

Users generally expect the robot cleaner to clean automatically when no people is around, so that they can have a clean environment when they come home from work or go out.  Hence the remote control is important for the robot cleaner.

Remotely control the robot cleaner with a mobile phone

### -----------------------Start of change 1------------------------------------------

### 5.5.4.22 deviceRobotCleaner

A robot cleaner is an autonomous robotic vacuum cleaner that has intelligent programming and a limited vacuum cleaning system. This robot cleaner information model provides capabilities to control and monitor robot cleaner specific functions and resources.

Table 5.5.4.22-1: Modules of deviceRobotCleaner Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| robotCleanerJobMode | robotCleanerJobMode | 1 | See clause 5.3.1.74. |
| robotCleanerOperationMode | operationMode | 0..1 | See clause 5.3.1.57. |
| battery | battery | 0..1 | See clause 5.3.1.10. |
| timer | timer | 0..1 | See clause 5.3.1.90. |
| remoteControlEnable | remoteControlEnable | 0..1 | See clause 5.3.1.73. |

-----------------------End of change 1---------------------------------------------