| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#55 |
| Source:* | Xiaotao Li, CMCC, lixiaotao@chinamobile.com Shujuan You, CMCC, youshujuan@ chinamobile.com Yawen Niu, CMCC, niuyawen@chinamobile.com |
| Date:* | 2022-07-02 |
| Reason for Change/s:* | Adding a new Device model deviceJuicer to TS-0023 |
| CR against: Release* | Rel.5 |
| CR against: WI* | Active WI-0084 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V5.1.0 |
| Clauses * | new clause 5.3.1.118 new clause 5.5.4.33 clause in 6.3.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

# oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR adds a new Device model deviceJuicer and adds a new ModuleClass blender.

- A new Device model deviceJuicer is added, including binarySwitch,  faultDetection, runState, blender, timer five Module Class.

- A new ModuleClass blender is added, including useBlender and spinSpeed two datapoints.

# A use case:

Juicer is a machine that can quickly press fruits and vegetables into juice. It is a very important equipment in people's life. Juicer may set a desired stir time for juice and  can choose the right spin speed of blender according to the hardness of the object (such as fruits and vegetables)  which you want to stir. And, the blender is an important module in the juicer. The stir speed and time of blender determines the effect of the juice.

### -----------------------Start of change 1-------------------------------------------

#### 5.3.1.118 blender

This ModuleClass is for controlling a blender, for example in a juicer.

Table 5.3.1.118-1: DataPoints of blender ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| useBlender | xs:boolean | RW | false |  | The current status of the blender enablement. "True" indicates enabled, and "False" indicates disabled. |
| spinSpeed | hd:enumSpinLevelStrength | RW | true |  | Choose the right spin speed according to the hardness of the object (eg.fruits and vegetables) |

-----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 5.5.4.33 deviceJuicer

Juicer is a machine that can quickly press fruits and vegetables into juice. It may set a desired stir time for juice and  can choose the right spin speed of blender according to the hardness of the object (such as fruits and vegetables)  which you want to stir.

Table 5.5.4.33-1: Modules of deviceJuicer Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. Depending on the manufacturer policies or regulations, the binary switch might only be used to turn the device off. |
| faultDetection | faultDetection | 0..1 | See clause 5.3.1.34. |
| runState | runState | 0..1 | See clause 5.3.1.75. |
| blender | blender | 0..1 | See clause 5.3.1.118. |
| timer | timer | 0..1 | See clause 5.3.1.90. |

-----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| Device3DPrinter | dTDPr |
| deviceAirConditioner | deACr |
| deviceAirPurifier | deAPr |
| deviceAirQualityMonitor | dAQMr |
| deviceAudioReceiver | deARr |
| deviceBloodPressureMonitor | dBPMr |
| deviceCamera | devCa |
| deviceClothesDryer | deCDr |
| deviceClothesWasher | deCWr |
| deviceClothesWasherDryer | dCWDr |
| deviceCoffeeMachine | deCMe |
| deviceCookerHood | deCHd |
| deviceCooktop | devCp |
| deviceDehumidifier | devDr |
| deviceDishWasher | deDWr |
| deviceDoor | devD0 |
| deviceDoorLock | deDLk |
| deviceElectricVehicleCharger | dEVCr |
| deviceFan | devFn |
| deviceFoodProbe | deFPe |
| deviceFreezer | devFr |
| deviceGlucosemeter | devGr |
| deviceHeartRateMonitor | dHRMr |
| deviceHomeCCTV | dHCCT |
| deviceHumidifier | devHr |
| deviceKettle | devKe |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceMultiFunctionPrinter | dMFPr |
| deviceOutdoorLamp | deOLp |
| deviceOven | devOn |
| devicePrinter | devPr |
| devicePulseOximeter | dePOr |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceScanner | devSr |
| deviceSecurityPanel | deSPl |
| deviceSetTopBox | dSTBx |
| deviceSmartElectricMeter | dSEMr |
| deviceSmartPlug | deSPg |
| deviceSteamCloset | deSCt |
| deviceStorageBattery | deSBy |
| deviceSwitch | devSh |
| deviceTelevision | devTn |
| deviceThermometer | devTr |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| deviceWaterValve | deWVe |
| deviceWeightScaleAndBodyCompositionAnalyser | dWSAB |
| deviceWindowShade | deWSe |
| deviceBottleWarmer | deBWr |
| deviceGarbageDisposal | deGDp |
| deviceWaterPurifier | deWPr |
| flexNode | fleNe |
| deviceJuicer | deJr |

-----------------------End of change 3---------------------------------------------