| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#55 |
| Source:* | Xiaotao Li, CMCC, lixiaotao@chinamobile.com Shujuan You, CMCC, youshujuan@chinamobile.com Yawen Niu, CMCC, niuyawen@chinamobile.com |
| Date:* | 2022-07-02 |
| Reason for Change/s:* | Adding a new Device model deviceShoesWasher to TS-0023 |
| CR against: Release* | Rel.5 |
| CR against: WI* | Active WI-0084 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V5.1.0 |
| Clauses * | new clauses 5.3.1.119, new clauses 5.5.4.34, new clause 5.6.54, clause in 6.3.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

# oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR adds a new device model deviceShoesWasher, adds a new module shoesWasherJobMode and adds a interpretation of hd:enumShoesWasherJobMode.

- A new Device model deviceShoesWasher is added, including binarySwitch,  runState, ShoesWasherJobMode, timer four Module Classes.

- A new module shoesWasherJobMode is added, including currentJobMode,  currentJobModeName, jobModes three datapoints.

- The  interpretation of hd:enumShoesWasherJobMode is added, including Normal wash, Intensive wash, Quick wash, Maintenance wash, Anti-bacterial wash five parts.

A use case:

With the continuous improvement of people's living standard, the consumption concept of the user tilts toward comfortable model and enjoy model gradually. New household appliances, such as shoes washing machines, can greatly reduce the burden of housework. So it is favored by people, especially the young.

-----------------------Start of change 1-------------------------------------------

#### 5.5.4.34 deviceShoesWasher

A shoes washer is a home appliance used to wash shoes. This information model provides capabilities to interact with specific functions and resources of a shoes washer.

Table 5.5.4.34-1: Modules of deviceShoesWasher Device model

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | 1 | See clause 5.3.1.12. |
| runState | runState | 1 | See clause 5.3.1.75. |
| ShoesWasherJobMode | ShoesWasherJobMode | 1 | See clause5.3.1.119. |
| timer | timer | 0..1 | See clause 5.3.1.90. |

-----------------------End of change 1---------------------------------------------

-----------------------Start of change 2-------------------------------------------

#### 5.3.1.119 shoesWasherJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of a shoesWasher.

Table 5.3.1.119-1: DataPoints: DataPoints of shoesWasherJobMode ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd: enumShoesWasherJobMode | RW | false |  | The currently active job mode. (see clause5.6.54) |
| currentJobModeName | xs:string | R | true |  | The name of the current job mode as a string. This can be used when the currentJobMode is vendor-specific. |
| jobModes | list of hd: enumShoesWasherJobMode | R | false |  | List of possible job states the device supports (see clause5.6.54) |

-----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.6.54 hd:enumShoesWasherJobMode

Used for the “currentJobMode” and “jobModes” DataPoints of the “shoedWasherJobMode” ModuleClass.

Table 5.6.54-1: Interpretation of hd:enumShoesWasherJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Normal wash |  |
| 2 | Intensive wash |  |
| 3 | Quick wash |  |
| 4 | Maintenance wash |  |
| 5 | Anti-bacterial wash |  |
| NOTE: See clause 5.3.1.119 "shoesWasherJobMode". Negative values are reserved for vendor specific modes. |

### --------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| Device3DPrinter | dTDPr |
| deviceAirConditioner | deACr |
| deviceAirPurifier | deAPr |
| deviceAirQualityMonitor | dAQMr |
| deviceAudioReceiver | deARr |
| deviceBloodPressureMonitor | dBPMr |
| deviceCamera | devCa |
| deviceClothesDryer | deCDr |
| deviceClothesWasher | deCWr |
| deviceClothesWasherDryer | dCWDr |
| deviceCoffeeMachine | deCMe |
| deviceCookerHood | deCHd |
| deviceCooktop | devCp |
| deviceDehumidifier | devDr |
| deviceDishWasher | deDWr |
| deviceDoor | devD0 |
| deviceDoorLock | deDLk |
| deviceElectricVehicleCharger | dEVCr |
| deviceFan | devFn |
| deviceFoodProbe | deFPe |
| deviceFreezer | devFr |
| deviceGlucosemeter | devGr |
| deviceHeartRateMonitor | dHRMr |
| deviceHomeCCTV | dHCCT |
| deviceHumidifier | devHr |
| deviceKettle | devKe |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceMultiFunctionPrinter | dMFPr |
| deviceOutdoorLamp | deOLp |
| deviceOven | devOn |
| devicePrinter | devPr |
| devicePulseOximeter | dePOr |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceScanner | devSr |
| deviceSecurityPanel | deSPl |
| deviceSetTopBox | dSTBx |
| deviceSmartElectricMeter | dSEMr |
| deviceSmartPlug | deSPg |
| deviceSteamCloset | deSCt |
| deviceStorageBattery | deSBy |
| deviceSwitch | devSh |
| deviceTelevision | devTn |
| deviceThermometer | devTr |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| deviceWaterValve | deWVe |
| deviceWeightScaleAndBodyCompositionAnalyser | dWSAB |
| deviceWindowShade | deWSe |
| deviceBottleWarmer | deBWr |
| deviceGarbageDisposal | deGDp |
| deviceWaterPurifier | deWPr |
| flexNode | fleNe |
| deviceShoesWasher | deSWr |

-----------------------End of change 4---------------------------------------------