| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#56 |
| Source:* | TaeHyun Kim, SyncTechno Inc., thyun@synctechno.com Sherzod Elamanov, SyncTechno Inc., elamanov@synctechno.com |
| Date:* | 2022-09-26 |
| Reason for Change/s:* | Add SDT definitions for Public Safety Domain |
| CR against: Release* | Release 5 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 v5.2.0 |
| Clauses * | 5.3.10, 5.5.10, 5.6.54, 5.6.55, 5.6.56, 5.6.57, 5.6.58 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Move SDT definitions of Public Safety Domain from TS-0037 as agreed in RDM#55

### -----------------------Start of change 1-------------------------------------------

### Public Safety Domain

#### Disseminator

This ModuleClass provides the capability of creating oneM2M based information from CAP based information received from oneM2M SP Gateway (ASN) and of controlling the change of received public warning messages such as updating oneM2M based information and canceling the dissemination of oneM2M based information.

Table 5.3.10.1-1: Actions of disseminator ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| result: xs:string | cancel | warningIdentifier: xs:string | true | cancel previously requested warning |

Table 5.3.10.1-2: DataPoints of disseminator ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| identifier | xs:string | RW | false |  | The identifier of the warning message that uniquely identifying this message. |
| sender | xs:string | RW | false |  | The identifier of the originator of this alert message. |
| sent | xs:dateTime | RW | false |  | The time and date of the origination of this alert message. |
| status | hd:enumAlertStatus | RW | false |  | The code to represent the appropriate handling of the alert message receiver. The value of this DataPoint is specified the CAP 1.2 specification [21] (see clause 5.5.2). |
| msgType | hd:enumAlertMsgType | RW | false |  | The code to represent the nature of the alert message. The value of this DataPoint is specified the CAP 1.2 specification [21] (see clause 5.5.3). |
| references | list of xs:string | RW | true |  | The list of identifiers for earlier message(s) referenced by this alert message. |
| urgency | hd:enumUrgency | RW | false |  | The code representing the urgency of the subject event of the alert message (see clause 5.5.4). |
| severity | hd:enumSeverty | RW | false |  | The code representing the severity of the subject event of the alert message (see clause 5.5.5). |
| certainty | hd:enumCertainty | RW | false |  | The code representing the certainty of the subject event of the alert message (see clause 5.5.6). |
| eventCodes | list of xs:string | RW | false |  | The definitions of system-specific codes identifying the event type of the alert message. A code definition consists of valueName and value pair separated by colon. |
| effective | xs:dateTime | RW | true |  | The effective time of the information of the alert message. |
| onset | xs:dateTime | RW | true |  | The expected time of the beginning of the subject event of the alert message. |
| expires | xs:dateTime | RW | true |  | The expiry time of the information of the alert message. |
| areaLatitude | xs:float | RW | true | degrees | The latitude of the affected area location. |
| areaLongitude | xs:float | RW | true | degrees | The longitude of the affected area location. |
| areaRadius | xs:float | RW | true | meters | The radius of the affected area location. |
| repetitionPeriod | xs:integer | RW | false | seconds | This specifies the repetition period for the warning message. The value of this DataPoint indicates the period of time in seconds after which re-send of the warning message should be repeated. |
| repetitionCount | xs:integer | RW | false |  | This specifies the number of times the warning message is to be sent. |

#### emergencyHandler

This ModuleClass provides the capability of triggering things to change into an emergency mode and of enabling things to identify whether an event described in oneM2M based information that is received from Public Warning Center (MN) is relevant to things. If any change happens in received warning messages such as updating oneM2M based information and cancelling the dissemination of oneM2M based information of previously received public warning messages, this ModuleClass updates oneM2M based information corresponding to those received public warning messages to control behaviour of things.

Table 5.3.10.2-1: DataPoints of emergencyHandler ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| emergencyMode | xs:boolean | RW | false |  | This specifies the emergency mode of target device. "True" means the device is working in emergency mode. "False" means the device is working in normal model |
| identifier | xs:string | RW | false |  | The identifier of the warning message that uniquely identifying this message. |
| sender | xs:string | RW | false |  | The identifier of the originator of this alert message. |
| sent | xs:dateTime | RW | false |  | The time and date of the origination of this alert message. |
| status | hd:enumAlertStatus | RW | false |  | The code to represent the appropriate handling of the alert message receiver. The value of this DataPoint is specified the CAP 1.2 specification [21] (see clause 5.5.2). |
| msgType | hd:enumAlertMsgType | RW | false |  | The code to represent the nature of the alert message. The value of this DataPoint is specified the CAP 1.2 specification [21] (see clause 5.5.3). |
| references | list of xs:string | RW | false |  | The list of identifiers for earlier message(s) referenced by this alert message. |
| urgency | hd:enumUrgency | RW | false |  | The code representing the urgency of the subject event of the alert message (see clause 5.5.4). |
| severity | hd:enumSeverty | RW | false |  | The code representing the severity of the subject event of the alert message (see clause 5.5.5). |
| certainty | hd:enumCertainty | RW | false |  | The code representing the certainty of the subject event of the alert message (see clause 5.5.6). |
| eventCodes | list of xs:string | RW | false |  | The definitions of system-specific codes identifying the event type of the alert message. A code definition consists of valueName and value pair separated by colon. |
| effective | xs:dateTime | RW | true |  | The effective time of the information of the alert message. |
| onset | xs:dateTime | RW | true |  | The expected time of the beginning of the subject event of the alert message. |
| expires | xs:dateTime | RW | true |  | The expiry time of the information of the alert message. |
| areaLatitude | xs:float | RW | true | deg | The latitude of the affected area location. |
| areaLongitude | xs:float | RW | true | deg | The longitude of the affected area location. |
| areaRadius | xs:float | RW | true | m | The radius of the affected area location. |

#### settings

This ModuleClass provides the capability of selecting the option that allows things to decide to take action as receiving oneM2M based information of public warning messages.

Table 5.3.10.3-1: DataPoints of settings ModuleClass

| Name | Type | R/W | Optional | Unit | Documentation |
| --- | --- | --- | --- | --- | --- |
| optoutStatus | xs:boolean | RW | false |  | This specifies the opt-out state for the device. The value of this DataPoint specifies opt-out state. True means that this device does not want to response when a warning has been triggered. |
| NOTE: Opt-out is refer to 3GPP TS 22.268 [i.11] Public Warning System (PWS) requirements specification. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.5.10 Public Safety Domain

#### 5.5.10.1	devicePWSCenter

Table 5.5.10.1-1: Modules of devicePWSEquipment Device

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| disseminator | disseminator | 1 | See clause 5.3.1 |

#### 5.5.10.2	devicePWSEquipment

Table 5.5.10.2-1: Modules of devicePWSEquipment Device

| Module Instance Name | Module Class Name | Multiplicity | Description |
| --- | --- | --- | --- |
| emergencyHandler | emergencyHandler | 1 | See clause 5.3.2 |
| settings | settings | 1 | See clause 5.3.3 |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.6.54	hd:enumAlertStatus

The enumeration type, hd:enumAlertStatus, enables things to identify the alert status that describes whether a received public warning message as oneM2M based information is an actual alert issued by authorities or an alert for testing the public warning service over oneM2M system.

Table 5.5.54-1: Interpretation of hd:enumAlertStatus

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Actual | Actionable by all targeted recipients |
| 2 | Exercise | Actionable only by designated exercise participants |
| 3 | System | For messages that support alert network internal functions |
| 4 | Test | Technical testing only, all recipients disregard |
| 5 | Draft | A preliminary template or draft, not actionable in its current form |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification [21]. |

### 5.6.55	hd:enumAlertMsgType

The enumeration type, hd:enumAlertMsgType, describes the message type of oneM2M based information transformed from CAP based information issued by authorities.

Table 5.6.55-1: Interpretation of hd:enumAlertMsgType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Alert | Initial information requiring attention by targeted recipients |
| 2 | Update | Updates and supersedes the earlier message(s) |
| 3 | Cancel | Cancels the earlier message(s) |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification [21]. |

### 5.6.56	hd:enumUrgency

The enumeration type, hd:enumUrgency, describes the urgency of the event defined in oneM2M based information transformed from CAP based information issued by authorities.

Table 5.6.56-1: Interpretation of hd:enumUrgency

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Immediate | Responsive action should be taken immediately |
| 2 | Expected | Responsive action should be taken soon (within next hour) |
| 3 | Future | Responsive action should be taken in the near future |
| 4 | Past | Responsive action is no longer required |
| 5 | Unknown | Urgency not known |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification [21]. |

### 5.6.57	hd:enumSeverity

The enumeration type, hd:enumSeverity, describes the severity of the event defined in oneM2M based information transformed from CAP based information issued by authorities.

Table 5.6.57-1: Interpretation of hd:enumSeverity

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Extreme | Extraordinary threat to life or property |
| 2 | Severe | Significant threat to life or property |
| 3 | Moderate | Possible threat to life or property |
| 4 | Minor | Minimal to no known threat to life or property |
| 5 | Unknown | Severity unknown |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification [21]. |

### 5.6.58	hd:enumCertainty

The enumeration type, hd:enumCertainty, describes the certainty of the event defined in oneM2M based information transformed from CAP based information issued by authorities.

Table 5.6.58-1: Interpretation of hd:enumCertainty

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Observed | Determined to have occurred or to be ongoing |
| 2 | Likely | Likely (p > ~50 %) |
| 3 | Possible | Possible but not likely (p ≤ ~50 %) |
| 4 | Unlikely | Not expected to occur (p ~ 0) |
| 5 | Unknown | Certainty unknown |
| NOTE: Listed names for this enumeration are specified on the CAP 1.2 specification [21]. |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of Changes to References Clause -------------

## Normative references

The following referenced documents are necessary, partially or totally, for the application of the present document. Their use in the context of this TS is specified by the normative statements that are referring back to this clause

[1]	oneM2M Smart Device Template.

NOTE:	Available at https://git.onem2m.org/MAS/SDT

[2]	Java coding rule.

[3]	oneM2M TS-0001: "Functional Architecture".

[4]	oneM2M TS-0004: “Service Layer Core Protocol Specification”

[5]	oneM2M TS-0005: ”Management Enablement (OMA)”.

[6]	ISO:80000-1: Quantities and units

NOTE:	Available at http://www.oracle.com/technetwork/java/codeconventions-135099.html.

[7]	Open Mobile AllianceTM: “OMA-ER-Device_WebAPIs-V1_0-20160419-C”.

NOTE:	Available at  http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-ERELD-DWAPI_V1_0-20160419-C.pdf

[8]	Open Mobile AllianceTM: “OMA-TS-Blood_Pressure_Monitor_APIs-V1_0-20160419-C”.

NOTE:	Available at  http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Blood_Pressure_Monitor_APIs-V1_0-20160419-C.pdf

[9]	Open Mobile AllianceTM: “OMA-TS-Glucometer_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Glucometer_APIs-V1_0-20160419-C.pdf

[10]	Open Mobile AllianceTM: “OMA-TS-Heart_Rate_Monitor_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Heart_Rate_Monitor_APIs-V1_0-20160419-C.pdf

[11]	Open Mobile AllianceTM: “OMA-TS-Pulse_Oximeter_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Pulse_Oximeter_APIs-V1_0-20160419-C.pdf

[12]	Open Mobile AllianceTM: “OMA-TS-Thermometer_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Thermometer_APIs-V1_0-20160419-C.pdf

[13]	Open Mobile AllianceTM: “OMA-TS-Weight_Scale_Body_Composition_Analyzer_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Weight_Scale_Body_Composition_Analyzer_APIs-V1_0-20160419-C.pdf

[14]	W3C Recommendation: “XML Schema Part 2: Datatypes”, 02 May 2001.

NOTE:	Available at http://www.w3.org/XML/Schema/.

[15]	NIST standard FIPS PUB 180-2

[16]	IETF RFC 4566: "SDP: Session Description Protocol".

[17]	IANA Time Zone Database

NOTE:	Available at https://www.iana.org/time-zones

[18]	Void

[19]	Open Mobile AllianceTM: “OMA-ER-GotAPI-V1_1-20151215-C”.

[20]	NIST SP 330:2019: “Special Publication 330 - The International System of Units (SI) 2019 Edition“

NOTE:	Available at https://www.nist.gov/pml/special-publication-330

[21]	Recommendation ITU-T X.1303 bis: "Common alerting protocol (CAP 1.2)".

NOTE:	Available at https://www.itu.int/rec/T-REC-X.1303bis-201403-I.

## Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules.

NOTE:	Available at http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf.

[i.2]	oneM2M TR-0017: "Home Domain Abstract Information Model".

[i.3]	oneM2M TS-0001: "Functional Architecture".

[i.4]	IEEE 802.15.4: "IEEE Standard for Local and metropolitan area networks--Part 15.4: Low-Rate Wireless Personal Area Networks (LR-WPANs)".

[i.5]	oneM2M TS-0012: "Base Ontology".

[i.6]	https://en.wikipedia.org/wiki/Multiple_inheritance

[i.7]	https://www.me.go.kr/home/web/index.do?menuId=10272&condition.code1=007

[i.8]	OCF DEVICE SPECIFICATION V1.3.0

NOTE:	Available at https://openconnectivity.org/specs/OCF_Device_Specification_v1.3.0.pdf

[i.9]	Ju-Hun Park, Hui Sik Kim, Sang-A Hong, Sun Young Jang, “A Study on the Definition of Terms for Domestic Train Control System”, Korean Society for Railway,  2015, http://railway.or.kr/Papers_Conference/201502/pdf/KSR2015A114.pdf

[i.10]	CTCS-3级列控系统总体技术方案 (Overall technology plan Train Control System), 中国铁道出版社(Chinese Railway Press), 2008, ISBN: 9787113091590

[i.11]	3GPP TS 22.268: "Public Warning System (PWS) requirements (Release 16)".

### -----------------------End of Changes to References  -------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?