| CHANGE REQUEST |
| --- |
| Meeting ID:* | RDM#58 |
| Source:* | JaeSeung Song, Sejong University, jssong@sejong.ac.kr |
| Date:* | 2023-02-18 |
| Reason for Change/s:* | Add new requirements for support AI/ML feature to oneM2M |
| CR against: Release* | Release 5 |
| CR against: WI* | Active: WI-0105 (System enhancements to support AI capabilities) MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0001 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution propses to add new requirements to TS-0002 v5.1.2 to enable AI/ML features to oneM2M as Release 5.

Especially, this contribution proposes to add requirements for AI/ML data augmentation based on the use case in TR-0068 AI/ML enablement. (Please refer Section 7.2 Use case #1 – Data Augmentation for Autonomous Driving)

The following are exerpt from Section 7.2 to explain the concept of data augmentation.

Applying data augmentation techniques to collected datasets require high computing power and large data storage. The autonomous driving application typically does not have such resources. IoT platforms serve the autonomous driving application can provide a common function for data augmentation. The application can offload their data augmentation tasks (e.g., applying image processing and storing large datasets) to IoT platforms. As many IoT services using AI/ML techniques require data augmentation function, the introduction of data augmentation function to IoT platforms benefits many intelligent IoT services.

Several reasons of data augmentation interest in autonomous driving are

- Limited size available dataset, e.g., road images, various objects

- The use of data augmentations helped to improve the results

- Sharing data is not easy due to data privacy regulations

### -------------------------------Start of change 1-----------------------------------

## 6.1	Overall System Requirements

Table 1: Overall System Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| OSR-00x | The oneM2M System shall be able to handle data augmentation requests for AI/ML purposes. | Rel-5 |
| OSR-00y | The oneM2M System shall be able to generate augmented data resources from a given source data and data augmentation technique. | Rel-5 |
| OSR-00z | The oneM2M System shall be able to manage data for AI/ML purposes such as model training and augmentation of training dataset. | Rel-5 |

### -------------------------------End of change 1-----------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?