| Input Contribution |
| --- |
| Meeting ID* | SDS#39 |
| Title:* | TR-0052 solution for tightly coupled Edge/Fog Computing with 3GPP T8 API |
| Source: * | Kenichi Yamamoto, KDDI, kc-yamamoto@kddi.com |
| Date: * | 2019-02-14 |
| Input related to* | WI-0080 Edge and Fog Computing TR-0052 V 0.5.0 |
| Intended purpose of document: * | Decision Discussion Information Other <specify> |
| Impacted another TS/TR(s) |  |
| Decision requested or recommendation: * | Agree for inclusion in TR-0052 |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution addresses Solution Y for the Key Issue X on Edge/Fog Computing with Underlying Network information in TR-0052.

### ---------------------- Start of change 1-------------------------------------------

# Proposed Solutions

Editor’s Note: The section provides solutions to the Key Issues identified for employing Edge and Fog technologies in oneM2M.

## Solution Y: Tightly coupled Edge/Fog Computing with 3GPP T8 API

Editor’s Note: Each Solution section references one or more Key Issues that it addresses and provides a brief solution description.

### Solution Applicability

Editor’s Note: The Solution Applicability states which Key Issues are addressed by the solution.

This solution addresses Key Issue X.

### Solution Description

Editor’s Note: This section provides a concise description of the solution which provides enough detail for further stage 2 development.

### Introduction

This solution addresses Edge/Fog computing with 3GPP T8 API. The purpose of this solution is to provide a means for an oneM2M Fog Node to inform the 3GPP Underlying Network of parameters that can be used for optimizing the data traffic over the Underlying Network for a set of Field Domain Nodes hosted on UEs. Unlike the solution X: Loosely coupled Edge/Fog Computing with 3GPP T8 API, Fog Node can communicate with 3GPP SCEF directly and retrieve T8 API information without an IN-CSE. As a result, oneM2M System can avoid the need for an IN-CSE to process data for the Field Domain Nodes and the IN-CSE can be freed from the burden for processing of 3GPP T8 API information. Figure 9.2.2.1-1 illustrates the high-level illustration for tightly coupled Edge/Fog Computing with 3GPP T8 API. The Fog Node retrieves the underlining network information in a particular area from a SCEF directly and adjusts data processing/transfer for the Field Domain Nodes.

Figure 9.2.2.1-1: High-level illustration - Tightly coupled Edge/Fog Computing with 3GPP T8 API

### Solution procedures

The clause introduces procedures for tightly coupled Edge/Fog computing with following 3GPP T8 API.

Editor’s Note: The procedures for Monitoring Event API (Number of UEs in an area) are currently FFS in WI-0058 3GPP interworking.

- Network Status Reports API

- Monitoring Event API (Monitoring Type: Number of UEs in an Area)

### Procedures for Network Status Reports and Monitoring Event API (Monitoring Type: Number of UEs in an Area)

Figure 9.2.2.2.1-1 shows the solution procedures for tightly coupled Edge/Fog computing with Network Status Reports API and Monitoring Event API (Number of UEs in an area). We propose a new resource <nwMonitoringReq> described in clause 9.2.2.3 for retrieving Underlying Network information with a MN-AE/CSE (Fog Node). The Edge/Fog Computing related procedures are Step 1, Step 3 and Step 4 in the figure.

Figure 9.2.2.2.2-1: Procedures for tightly coupled Edge/Fog computing with Network Status Reports and Monitoring Event (Number of UEs in an area)

The following steps are related to the Fog Node (MN-CSE, MN-AE):

Pre-conditions:

There is a relationship in place between the Service Provider and MNO allowing the MN-AE (Fog Node) to request 3GPP T8 API information from the 3GPP Underlying Network. The method for establishing this relationship is outside the scope of the present document.

The MN-CSE (Fog Node) is configured with system defaults for the following. The method for configuring these system defaults is outside the scope of the present document.

•	The specified actions to take based on the severity of each congestion level.

•	The network congestion levels to receive reports

•	The severity of each specified congestion level

•	The specified actions to generate the network congestion levels based on the number of UEs in an area.

Step 1: The MN-AE (Fog Node) sends a request for CREATE <nwMonitoringReq>

The MN-AE (Fog Node, Originator) sends a request to the MN-CSE (Fog Node, Hosting CSE) by creating a <nwMonitoringReq> resource. The <nwMonitoringReq> resource includes following attributes as described in clause 9.2.2.3.

- nwEnable will be set to type of network monitoring request (e.g. congestion status in an area and/or the number of devices in an area.)

- geographicalArea will be set to the geographic area where the Fog Node wants to retrieve an Underling Network information.

- congestionStatus will be set to one of following values:

  - The list of congestion level(s) with exact value and specify what congestion threshold(s) the Fog Node wants to receive a report for. Whenever the congestion in the geographical area goes above or below an indicated threshold, a report will be sent.  The threshold(s) that are indicated by the Fog Node are determined based on local Fog Node policies.  The definition of these policies is outside the scope of the present document.

  - The list of enumerated types with values HIGH, MEDIUM and LOW that specify the type of congestion status the Fog Node would like to receive a report for. The threshold type(s) that are indicated by the Fog Node are determined based on local Fog Node policies.  The definition of these policies is outside the scope of the present document.

Step 2a: Procedures for Network Status Reports

When the MN-CSE (Fog Node) receives the request from the MN-AE (Fog Node) to create the <nwMonitoringReq> resource, MN-CSE (Fog Node) checks if the request is valid. If the nwEnable attribute of the <nwMonitoringReq> resource is set to “enable congestion status in an area” or “enable both number of devices and congestion status in an area”, the MN-CSE (Fog Node) maps the attributes of the <nwMonitoringReq> resource to the following attributes of Network Status Reports API as described in clause 7.8 of TS-0026 [i.34].

- The MN-CSE (Fog Node) sets the fixed parameters with the corresponding attributes of the API (e.g. URI, monitorExpireTime, supportedFeatures).

- geographicalArea of the <nwMonitoringReq> resource will be set to locationArea.

- If congestionStatus indicates an abstracted value for congestion status (e.g. HIGH, MEDIUM or LOW), thresholdTypes will be set to the abstracted value of the congestionStatus. If congestionStatus indicates an exact value for congestion status (e.g. between 0 and 31), thresholdValues will be set to the exact value of the congestionStatus.

Then the MN-CSE (Fog Node) communicates with SCEF by using the procedures for Network Status Reports API described clause 7.8 of TS-0026 [i.34].

Step 2b: Procedures for Monitoring Event (Number of UEs in an area)

Editor’s Note: The procedures for Monitoring Event API (Number of UEs in an area) are currently FFS in WI-0058 3GPP interworking.

When the MN-CSE (Fog Node) receives the request from the MN-AE (Fog Node) to create the <nwMonitoringReq> resource, the MN-CSE (Fog Node) checks if the request is valid. If the nwEnable attribute of the <nwMonitoringReq> resource is set to “enable number of devices in an area” or “enable both number of devices and congestion status in an area”, the IN-CSE maps the attributes of the <nwMonitoringReq> resource to the following attributes of Monitoring Event API (Number of UEs in an area) as specified in 3GPP TS 29.122 [i.32].

- The MN-CSE (Fog Node) sets the fixed parameters with the corresponding attributes of the API (e.g. URI, supportedFeatures).

- geographicalArea of the <nwMonitoringReq> resource will be set to locationArea.

Step 3: The MN-CSE (Fog Node) sends a response for CREATE <nwMonitoringReq>

After completion of Step 2a or 2b, the MN-CSE (Fog Node) will map the response of 3GPP T8 API to the attributes of the <nwMonitoringReq> resource and send it to the MN-AE (Fog Node) as a <nwMonitoringReq> CREATE Response which includes following parameters as described in clause 9.2.2.3.

- If the response indicates nsiValue or nsiType, the MN-CSE (Fog Node) updates the congestionStatus attribute of <nwMonitoringReq> resource.

- If the response indicates ueCount, the MN-CSE (Fog Node) updates the numberOfDevices attribute of <nwMonitoringReq> resource.

See clause 8.3 of TS-0026 [i.34] for a list of possible error scenarios and error handling options for the MN-CSE (Fog Node).

Step 4: The Fog Node adjusts data processing/transfer for Field Domain Nodes (ASN/MN/ADN)

The Fog Node (the MN-AE, MN-CSE) may use the information provided in step 3 in order to adjusts data processing/transfer for Field Domain Nodes (ASN/MN/ADN).

### Impacted Resources

To implement this solution, a new resource <nwMonitoringReq> is proposed to retrieve Underlying Network information. The resource is described in Solution X: Loosely coupled Edge/Fog Computing with 3GPP T8 API.

### -----------------------End of Change 1 ---------------------------------------------