| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 39.6 |
| Source:* | Yuan Tao, CNIC, taoyuan@cnic.cn; Catalina Mladin, Convida, Mladin.Catalina@convidawireless.com; |
| Date:* | 2019-04-11 |
| Reason for Change/s:* | Provide the potential solution for interworking with OID resolution system via IPE. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active (WI-0069) MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0044 Version 0.5.0 |
| Clauses * | 8.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution intends to add the potential solution that interworking with OID resolution system via IPE.

R01: Add a normative reference, and do some editorial changes.

## ----------------------- Start of change 1 -----------------------

## 8.2.x Discovery based on interworking with OID resolution system via IPE

This clause provides details for implementing interworking with an OID resolution system via an IPE.

Figure 8.2.x-1: Discovery based on interworking with OID resolution system via IPE

Step 1: An Originator (e.g. an AE) sends a request to the CSE to discover information related to a tangible identifier. The parameters in the request are set as follows:

Operation: Retrieve

To: <CSEBase> or <physicalObject> by pre-provisioning

Filter Criteria: set the attribute (e.g. “tangibleID = /2/27”) and filterUsage to‘IPEOnDemandDiscovery’, and other necessary conditions

Editor’s Note: The request must also include the parameters security flag and ORS service type (see [8] for detailed specification). It is FFS how the request support these two parameters.

Step 2a: If there are no matched results found, the CSE checks if the IPE supports the OID resolution system. The type of tangible identifier may be identified by the heterogeneous identification recognition functionality of the CSE from the tangibleID or may be provided in the request of AE.

Editor’s Note: It is FFS how the CSE heterogeneous identification function discovers if the IPE supports a specific identification system (e.g. ORS).

Step 2b: If the type of tangible identifier is OID and a corresponding identification resolution IPE for OID resolution system is found, the CSE sends Notify request to the IPE. The Notify request contains the ID of the originator and the filterCriteria parameters, including the tangibleID condition.

Step 3a: The IPE consists of a ORS Client which has specific functions to convert the tangible identifier, process the results returned from DNS and standardized interface and protocol to communicate with DNS. When IPE receives the request from CSE, the client is responsible to encapsulate a new request message. Firstly, the ORS client converts the OID into an FQDN, and then encapsulates the FQDN, security flag (the value of security flag is copied from the request in Step 1) into the request.

NOTE: Converting an OID to an FQDN includes reversing of the order, puting dots (".") instead of "/", preceding the service identifier "ors-dummy.", and appending the DNS root of OID resolution system “oid-res.org”. For example, the canonical form of an OID “/2/27” can be converted to “ors-dummy.27.2.oid-res.org.”. A general OID “/joint-isoitu-t/tag-based” can be converted to “ors-dummy.tag-based.joint-iso-itu-t.oid-res.org.”. See [8] for detailed specification.

Step 3b: The ORS Client sends the request to the DNS.

Step 4a: The DNS responses either zero or more NAPTR resource records, or an error. The contents of a NAPTR resource record are as follows:

a) The order field shall be “0”;

b) The preference field shall be a non-negative integer;

c) The flags field shall be set to “u”;

d) The service field shall be set to “ORS+xxxx”, where “xxxx” is an ORS service type is defined in Table 8.2.x-2;

e) The regular expression field shall be the string “!^.*$!information!”, where “information” is specified according to the corresponding ORS service type .

An example of a NAPTR resource record for tag-based multimedia information: ors-dummy.27.2.oid-res.org. IN NAPTR 0 100 "u" "ORS+TINF" "!^.*$!27.2.anydomain.com!"

Step 4b: The ORS client processes the DNS results. If a DNS RCODE (described in Table 8.2.x-1) which is non-zero is returned, it indicates an error. If an RCODE of zero is returned, then ORS client will perform the following steps:

- Select the NAPTR resource records with flag field value "u".

- If there are any results from 1), select only NAPTR resource records with service field value "ORS+xxxx", where xxxx is the ORS service type, and the value is requested by originator AE in Step 1.

- If there are any results from 2), for all NAPTR resource records, extract the substring between the "!^.*$!" and the "!" in the regular expression (the information part of the NAPTR resource record), and the preference field value (non-negative integer).

The results also are decided by the value of security flag. The IPE creates physical entity resource(s) based on the processed results. How the IPE maps the results to the physical entity resource depends on the specific implementation of the used system. For example, a system may assign OID to oneM2M physicalObject resources. The corresponding IPE will create a local physicalObject resource with the exact representation of results. In another implementation, the results may be mapped to a single attribute of the corresponding physicalObject resource.

Step 4b: The IPE sends the Notify response to the CSE including the list of created physicalObject resource(s) with an RCODE of zero, or an error will be returned to the CSE with the RCODE value.

Step 5: CSE responds with the query results to the Originator AE.

# Table 8.2.x-1: DNS code values

| RCODE value | Interpretation by the application |
| --- | --- |
| 0 | OK |
| 1 | ORS system failure |
| 2 | DNS system failure |
| 3 | No such domain name |
| 4 | Retrieval of NAPTR resource records not supported for this domain name |
| 5 | Security policy restriction |
| 6 upwards | No interpretation available |

# Table 8.2.x-2: ORS Service Type

| Name of ORS service | Service type value | Description |
| --- | --- | --- |
| OID canonicalization | COID | Retrieval of OID canonicalization |
| Child Information | CINF | Retrieval of information for a child OID |
| Registration information | RINF | Retrieval of OID registration information |
| Module information | MINF | Retrieval of OID module information |
| Tag-based multimedia access | TINF | Reserved for use in the ID resolution protocol |
| Cybersecurity information | CYBEX | Reserved for use in discovery mechanisms in the exchange of cybersecurity information |

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

# 2	References

The following text block applies.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]		oneM2M TS-0001: "Functional Architecture".

[2]		oneM2M TS-0011: "Common Terminology".

[3]		GS1 Object Name Service (ONS) V.2.0.1. 2013.

[4]		GS1 EPC Tag Data Standard 1.6.2011.

[5]		IETF RFC 3650 Handle System Overview

[6]		IETF RFC 3651 Handle System Namespace and Service Definition.

[7]		ISO/IEC 9834-1 Information technology – Open Systems Interconnection – Procedures for the operation of OSI Registration Authorities: General procedures and top arcs of the International Object Identifier tree.

[8]   ITU-T X.672 Information technology – Open Systems Interconnection – Object identifier resolution system

## ----------------------- End of change 2 -----------------------