## Slide 1: Operations on a dynamic set of resources How to optimize workflow? ARC-2018-0348-discovery-based_operations_Usecase
Group Name: SDS
Source: mailto: Leila Le Brun (Orange), Cyrille Bareau (Orange), Sébastien Bolle (Orange)
Meeting Date: 2019-xx-xx
Agenda Item: TS-0001 and TS-0004 related

## Slide 2: Use cases & issue Use Case 1: Update a dynamic set of resources
Use-case 1: perform the same request on a dynamic set of resources (e.g. perform an UPDATE request to set the color GREEN to the lights that are RED)
Current workflow in 4 steps:
Perform a discovery request in order to find out Colour module FlexContainers matching conditions.
Based on the discovery result, create a new, temporary group.
Execute an UPDATE request on all members of the group through group’s fanOutPoint
Execute a DELETE request on the temporary group
Issue : performance issue (time and bandwidth)

## Slide 3: Focus on existing behavior
Current Use Case 1 workflow to update a dynamic set of resources requires
Performance issue
4 steps

## Slide 4: Use cases & issue Use Case 2: Delete a dynamic set of resources
Use-case 2: delete a dynamic set of resources (based on filtering conditions)
Current workflow in 4 steps:
Perform a discovery request in order to find out resources that match conditions.
Based on the discovery result, create a new group.
Execute a DELETE request on all members of the group through group’s fanOutPoint
Execute a DELETE request on the group
Issue : performance issue (time and bandwidth)

## Slide 5: Possible solution Discovery-based Operation
Introduce Discovery-Based Requests
Discovery-based Request is a single request to be executed on a set of resources
The set of resources identified by a filter criteria
The set of resources is not a permanent group
A single request instead of 4

## Slide 6: Discovery-based Operation Use Case 1: Update a dynamic set of resources
    The all in one request proposal

## Slide 7: Discovery-based Operation Use Case 2: Delete a dynamic set of resources
    The all in one request proposal