## Slide 1: Potential Solutions for Optimizing oneM2M Messages – TR-0053
JaeSeung Song
Convida Wireless, Hyundai Motors, KETI
May 9, 2019
SDS-2019-0228-TR-0053-Potential_Solutions_for_Optimizing_oneM2M_Messages

## Slide 2: TR-0053 Background: Issues with oneM2M Messages
6.1.2 – Limitations of oneM2M Messages
  If a oneM2M request (or response) message contains too many request (or response) parameters, it cannot be sent in one layer-2 frame, which causes high message overhead and increases message transmission latency.
  If a oneM2M request (or response) message is contained in multiple layer-2 frames, the loss of one layer-2 frame will results in the failure of oneM2M message delivery.
  Even if a oneM2M request (or response) message can be completely contained in one layer-2 frame, the large size of the oneM2M message increases the message loss probability over the wireless channel.
  Parameters contained in multiple consecutive oneM2M request (or response) messages could be the same and redundant, which increases message overhead unnecessarily.
  The resource representation in the “Content” parameter may contain some extra attributes which are not expected or required by the requestor.
  The resource representation in the “Content” parameter from multiple consecutive oneM2M request (or response) messages may contain the same or redundant attributes, which causes extra message overhead unnecessarily.
  The oneM2M service layer does not currently support any compression mechanisms and is unable to leverage existing header compression protocols (e.g. IETF RFC 3095 for robust header compression) which have been designed for network layer, transport layer, and application protocol layer.. None of these are directly applicable to the oneM2M service layer.
  If an oneM2M application wants to deliver the same oneM2M message repeatedly to oneM2M devices, it has to send multiple repeated oneM2M messages to the oneM2M service layer, which causes high message overhead and increases message transmission latency. This also increases the complexity of oneM2M Application logic.
Figure 6.1.2-1: Smart Metering Use Case based on Cellular IoT

## Slide 3: TR-0053 Background: Potential Requirements for oneM2M Messages
6.1.3 – Potential Requirements
  The oneM2M System shall support suitable request/response message interaction between a service layer and a constrained IoT device with low latency.
  The oneM2M System shall support suitable request/response message interaction between a service layer and a constrained IoT device with low communication overhead.
  The oneM2M System shall support suitable approaches for constrained IoT device to minimize request message size.
  The oneM2M System shall support suitable approaches for constrained IoT device to minimize response message size.
  The oneM2M System shall support suitable approaches for constrained IoT device to remove unrequired or redundant attributes from the resource representation as contained in the “Content” parameter.
  The oneM2M System shall support suitable approaches for sending repetitive messages based on some specified conditions (e.g. schedule) to minimize message exchange overhead between oneM2M applications and the oneM2M System.

## Slide 4: Solutions: Two-Level Optimizations
Level-1: to minimize the number of messages being exchanged between two oneM2M entities
  Solution-1: Message Delivery Repetition
Level-2: to minimize the message size by removing unnecessary request/response parameters and attributes in a resource representation
  Solution-2: Primitive Profile (or Message Template)
Note: Both optimizations are complementary to each other and they do not have any overlapping.

## Slide 5: Solution-1: Message Delivery Repetition
Possible solution:
  In Section 8.1.2 Request, various parameters are defined for oneM2M Request message over the Mca and Mcc reference points.
  A new optional parameter called “message repetition” can be introduced as as follows:
Message repetition:
  Definition: optional message repetition delivery identifier: Indicates the message needs to be delivered at a given number of times repeatedly within a specified time duration.
  Example usage of message repetition: Originator wants to send an UPDATE request message that configures the value of a specific resource to ‘0’ for 5 times within 60 seconds. As a service application using this value interprets the value ‘0’ as a warning message for high temperature, a corresponding message, e.g., “CAUTION: THE TEMPERATURE IS HIGH”, can be delivered several times to receiver(s).
  Once a request message with the message repetition parameter is received, the Receiver (i.e., CSE) can either:
    Replicate the message for the given number of times and place them in the <schedule> resource with the evenly distributed over the given time window
    Place the message to the target resource with proper configuration such as allowing multiple notifications via additional attribute to the <subscription> resource
4 times:60seconds
T0
T1
T2
T3
T4
<Schedule>
Receiver
Originator
Service Layer
Request message
Message repetition= 4:60seconds
Replicate
message

## Slide 6: Solution-2: Primitive Profile
Primitive Profile-based Solution: to solve the issues as demonstrated on the right figure (i.e., to reduce the size of request/response messages especially when retrieving a resource) with the following capabilities.
  A new resource type <primitiveProfile> is introduced. <primitiveProfile> resources are created and stored at CSEs.
  Each <primitiveProfile> can specify the required (or removed) attributes of a resource and/or parameters in a message when it is retrieved. As such, unnecessary parameters and/or attributes will not be included in a retrieval request and response and the size of the messages is reduced.
  Each <primitiveProfile> can be applied to different AEs, CSEs, resources, operations, and/or a combination of them.
  When a Hosting CSE receives a request message, it will first identify an applicable <primitiveProfile> and use what’s described in the <primitiveProfile> to process the request message and generate an appropriate response message. The objective is to reduce the size of request and response messages.
    Alternatively, the originator/requestor could explicitly indicate one more <primitiveProfile>s in the request message. Then, the Hosting CSE simply leverages these <primitiveProfile>s to process the request message.

## Slide 7: Comparison
Solutions | Can Do | Can Not Do
Message Delivery Repetition (SDS-2019-0194) | Feature-1: Remove repeated oneM2M messages | Feature-2
Primitive Profile (or Message Template) (SDS-2019-0214) | Feature-2: Reduce the number of request or response parameters and/or attributes of a resource in an oneM2M message | Feature-1
Details on each solution are provided in separate contributions. |  | 
Note: One of primary objectives for TR-0053 is to collect and analyze all potential and feasible solutions for optimizing oneM2M messages for constrained devices and constrained networks

## Slide 8: Comments?