| Input Contribution |
| --- |
| Meeting ID* | SDS#41 |
| Title:* | TR-0052 solution for tightly coupled Edge/Fog Computing with 3GPP T8 API #2 |
| Source:* | Kenichi Yamamoto, KDDI, kc-yamamoto@kddi.com |
| Date:* | 2019-06-28 |
| Input related to* | WI-0080 Edge and Fog Computing TR-0052 V 0.7.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | N/A |
| Decision requested or recommendation:* | Agree for inclusion in TR-0052 |
| Template Version: November 2018 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution addresses a solution for the Key Issue 3 on Edge/Fog Computing with Underlying Network information in TR-0052.

### -----------------------Start of change 1-------------------------------------------

## Solution Y: Tightly coupled Edge/Fog Computing with 3GPP T8 API #2

### Solution Applicability

This solution addresses Key Issue 3.

### Solution Description

### Introduction

This solution addresses Edge/Fog computing in a deployment where the T8 interface is exposed to MN-CSE(SCS), therefore there is a “tight coupling” between the Edge/Fog node and the Underlying Network. The Solution E introduces the procedures of tightly coupled Edge/Fog computing with Network Status Reports API and Monitoring Event API (Monitoring Type: Number of UEs in an Area). We propose to apply this concept for other T8 APIs. Table 9.7.2.1-1 shows the summary of the tightly coupled Edge/Fog computing with T8 APIs. Note that the table does not contains 3GPP connectivity establishment, which is addressed in Solution X: 3GPP connectivity establishment with Edge/Fog Computing.

Table 9.7.2.1-1: Summary of tightly coupled Edge/Fog computing with T8 APIs

| TS-0026 [i.34] | Interworking with MN-CSE (SCS) |
| --- | --- |
| Clause | APIs | Clause | Applicability | Remarks |
| 7.1 | Cellular IoT non-IP data delivery(NIDD) | 9.7.2.2.1 | T.B.D | How to use the concept of tight coupling Edge/Fog computing for the API is FFS. |
| 7.4.1 | UE Reachability monitoring of Monitoring events | 9.7.2.2.2 | ✓ |  |
| 7.4.2 | UE Availability after DDN Failure of Monitoring events | 9.7.2.2.3 | ✓ |  |
| 7.4.3 | UE Communication Failure of Monitoring events | 9.7.2.2.4 | ✓ |  |
| 7.4.4 | UE Loss of Connectivity of Monitoring events | 9.7.2.2.5 | ✓ |  |
| 7.4.5 | Roaming Status of Monitoring events | 9.7.2.2.6 | ✓ |  |
| 7.4.6 | Detecting Change of IMSI-IMEI(SV) Association of Monitoring events | 9.7.2.2.7 | ✓ |  |
| 7.4.7 | Location Reporting of Monitoring events | 9.7.2.2.8 | ✓ |  |
| 7.4.8 | Number of UEs in an Area of Monitoring events | 9.7.2.2.9 | ✓ | The procedure is described in Solution E with <nwMonitoringReq> resource. |
| 7.5 | 3GPP Based Device triggering | 9.7.2.2.10 | ✓ | The descriptions of triggerReferenceNumber for <remoteCSE> and <AE>, and the description of the triggerReference for <triggerRequest> need to be modified to support MN-CSE (SCS). |
| 7.6 | Configuration of Traffic Patterns | 9.7.2.2.11 | ✓ |  |
| 7.7 | Group message delivery using MBMS | 9.7.2.2.12 | T.B.D | No MBMS use case with Edge/Fog Computing is described in current oneM2M TR. Further consideration for this solution may be needed. |
| 7.8 | Informing about Potential Network Issues | 9.7.2.2.13 | ✓ | The procedure is described in Solution E with <nwMonitoringReq> resource. |
| 7.10 | Background Data Transfer | 9.7.2.2.14 | ✓ | The description of transferSelectionGuidance for <backgroundDataTransfer> resource needs to be modified to support MN-CSE (SCS). |
| 7.11 | Network Parameter Configuration | 9.7.2.2.15 | ✓ |  |

### Solution procedures

The clause introduces procedures for each SCEF APIs described in TS-0026 [i.34] for tightly coupled Edge/Fog computing.

### Cellular IoT non-IP data delivery(NIDD)

T.B.D.

NOTE: How to use the concept of tight coupling Edge/Fog computing for the API is FFS.

### UE Reachability monitoring of Monitoring events

The procedure with IN-CSE is depicted in clause 7.4.1 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS).

### UE Availability after DDN Failure of Monitoring events

The procedure with IN-CSE is depicted in clause 7.4.2 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS).

### UE Communication Failure of Monitoring events

The procedure with IN-CSE is depicted in clause 7.4.3 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS).

### UE Loss of Connectivity of Monitoring events

The procedure with IN-CSE is depicted in clause 7.4.4 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS).

### Roaming Status of Monitoring events

The procedure is depicted in clause 7.4.5 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS).

### Detecting Change of IMSI-IMEI(SV) Association of Monitoring events

The procedure with IN-CSE is depicted in clause 7.4.6 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS).

### Location Reporting of Monitoring events

The procedure with IN-CSE is depicted in clause 7.4.7 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS).

### Number of UEs in an Area of Monitoring events

The procedure is depicted in Solution E with <nwMonitoringReq> resource.

### 3GPP Based Device triggering

The procedure with IN-CSE is depicted in clause 7.5 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS). All the steps not detailed below are executed as specified in TS-0026 [i.34].

For pre-conditions of the Device Triggering Recall/Replace Procedure, the IN-CSE has already sent a device trigger request to the Underlying 3GPP Network. The IN-CSE has stored the previous device trigger information, e.g. trigger reference number, etc.

For Device Trigger Recall/Replace request, MN-CSE (SCS) issues the device trigger Recall/Replace request to the Underlying Network. In addition to same parameters in the original device trigger request, the following additional parameters for device trigger recall/replace include:

The old trigger reference number was assigned to the previously submitted trigger message that the MN-CSE (SCS) wants to recall/replace.

For trigger replace request, the new trigger reference number which is assigned by the MN-CSE (SCS) to the newly submitted trigger message.

For Device Trigger Recall/Replace response, if the MN-CSE (SCS) receives a success response, the MN-CSE (SCS) updates the device trigger information as following:

For device trigger replace success response, the MN-CSE (SCS) will store the new trigger reference number replace the old trigger reference number.

For device trigger recall success response, the MN-CSE (SCS) will clear the old trigger reference number.

### Configuration of Traffic Patterns

The procedure with IN-CSE is depicted in clause 7.6 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS).

### Group message delivery using MBMS

T.B.D.

NOTE: No MBMS use case with Edge/Fog Computing is described in current oneM2M TR. Further consideration for this solution may be needed.

### Informing about Potential Network Issues

The procedure is depicted in Solution E with <nwMonitoringReq> resource.

### Background Data Transfer

The procedure with IN-CSE is depicted in clause 7.10 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS). All the steps not detailed below are executed as specified in TS-0026 [i.34].

For Policy Request and Selection, if more than one transfer policy was received from the underlying network, the MN-CSE (SCS) uses the transferSelectionGuidance of <backgroundDataTransfer> resource and its own selection policies to select one of them. If transferSelectionGuidance is not provided, then the MN-CSE (SCS) uses internal policies to select a policy.

### Network Parameter Configuration

The procedure with IN-CSE is depicted in clause 7.12 of TS-0026 [i.34]. In this solution, the MN-CSE is operated as SCS and the procedure related the IN-CSE is replaced by the MN-CSE (SCS).

### Impacted Resources

### Introduction

To implement this solution, the following attributes are proposed:

- The descriptions of the triggerReferenceNumber for <remoteCSE> and <AE> resources are updated to support MN-CSE (SCS).

- The descriptions of the triggerReference for <triggerRequest> resource is updated to support MN-CSE (SCS).

- The descriptions of the transferSelectionGuidance for <backgroundDataTransfer> resource is updated to support MN-CSE (SCS).

### Modified <remoteCSE> resource

The description of the triggerReferenceNumber is updated to support MN-CSE as shown in the table below.

Table 9.7.2.3.2-1: Modified attribute of <remoteCSE> resource

| Attributes of <remoteCSE> | Multiplicity | RW/ RO/ WO | Description | <remoteCSEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| triggerReferenceNumber | 0..1 | RW | This is to identify device trigger procedure request. This attribute is used only for device trigger and assigned by the IN-CSE or MN-CSE. | NA |

### Modified <AE> resource

The description of the triggerReferenceNumber is updated to support MN-CSE as shown in the table below.

Table 9.7.2.3.3-1: Modified attribute of <AE> resource

| Attributes of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| triggerReferenceNumber | 0..1 | RW | This is to identify device trigger procedure request. This attribute is used only for device trigger and assigned by the IN-CSE or MN-CSE. | NA |

### Modified <triggerRequest> resource

The descriptions of the triggerReference is updated to support MN-CSE as shown in the table below.

Table 9.7.2.3.4-1: Attributes of <triggerRequest> resource

| Attributes of <triggerRequest> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| triggerReference | 0..1 | RO | This attribute is a reference number which is allocated by the IN-CSE or MN-CSE of a transaction and is used in all subsequent messages related to that transaction to support device triggering. |

### Modified <backgroundDataTransfer> resource

The description of the transferSelectionGuidance is updated to support MN-CSE as shown in the table below.

Table 9.7.2.3.5-1: Attributes of <backgroundDataTransfer> resource

| Attributes of < backgroundDataTransfer > | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| transferSelectionGuidance | 0..1(L) | WO | List that includes guidance to IN-CSE or MN-CSE in selecting from multiple transfer policies provided by underlying network. Possible values include:” lowest cost”, “highest throughput given maximum cost of X”, etc. If not included, the IN-CSE or MN-CSE may independently choose from among multiple transfer policies. |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?