| CHANGE REQUEST |
| --- |
| Meeting ID:* | ARC 41 |
| Source:* | Shu Wang, CNIC, wangshu@cnic.cn; |
| Date:* | 2019-07-08 |
| Reason for Change/s:* | Add a new attribute supportedIDType in <AE> to represent the specific identification resolution systems that the IPE supports. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active (WI-0069) MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0044 Version 0.5.0 |
| Clauses * | 8.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

In the process of discovery based on interworking with the external resolution system via an IPE, the CSE needs to checks if the IPE supports the corresponding resolution system for requested type of tangibleID. The solution on how the CSE discovers if the IPE supports a specific identification system (e.g. ORS, Handle) is needed to be provided.

This contribution intends to add a new attribute supportedIDType in <AE> to represent the specific identification resolution systems that the IPE supports.

## ----------------------- Start of change 1 -----------------------

8.2.x Attribute supportedIDType of <AE>

In the Table 9.6.5-2 of TS 0001, a new attribute supportedIDType of <AE> is proposed, and it is specified as follow.

Table 8.2.x: Attribute supportedIDType of <AE> resource

| Attributes of <AE> | Multiplicity | RW/ RO/ WO | Description | <AEAnnc> Attributes |
| --- | --- | --- | --- | --- |
| supportedIDType | 0..1 (L) | RW | This attribute represents the specific identification resolution systems that IPE supports to interwork with. It can be a list of identifier types, and the identifer type is expressed in string： handle system; ors; ucodeRP; ons. | OA |

## ----------------------- End of change 1 -----------------------