| Input Contribution |
| --- |
| Meeting ID* | SDS#41 |
| Title:* | TR-0052 solution for Tightly coupled Edge/Fog Computing with 3GPP T8 API #3(Originator: IN-AE) |
| Source:* | Kenichi Yamamoto, KDDI, kc-yamamoto@kddi.com |
| Date:* | 2019-06-28 |
| Input related to* | WI-0080 Edge and Fog Computing TR-0052 V 0.7.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | N/A |
| Decision requested or recommendation:* | Agree for inclusion in TR-0052 |
| Template Version: November 2018 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution addresses a solution for the Key Issue 3 on Edge/Fog Computing with Underlying Network information in TR-0052.

### -----------------------Start of change 1-------------------------------------------

## Solution Z: Tightly coupled Edge/Fog Computing with 3GPP T8 API #3 (Originator: IN-AE)

### Solution Applicability

This solution addresses Key Issue 3.

### Solution Description

### Introduction

This solution addresses Edge/Fog computing in a deployment where the T8 interface is exposed to the Edge/Fog node, therefore there is a “tight coupling” between the Edge/Fog node and the Underlying Network.

Unlike soltion E, an IN-AE works as an Originator and requests the creation of a <nwMonitoringReq> resource at the IN-CSE. In this deployment scenarios, the IN-AE can manage multiple MN-CSEs (Fog Nodes) and coordinate network congestions of its service area. Regarding communication with a SCEF and Field Domain Nodes hosted on UEs, oneM2M MN-CSEs play a major role instead of the IN-CSE. As a result, oneM2M System can avoid the need for the IN-CSE to process data for the Field Domain Nodes and the IN-CSE can be freed from the burden for processing of 3GPP T8 API information.

Figure 9.8.2.1-1 illustrates the high-level illustration for tightly coupled Edge/Fog Computing with 3GPP T8 API (Originator: IN-AE). The Fog Node retrieves underlining network information in a particular area from a SCEF directly based on IN-AE monitoring request and adjusts data processing/transfer for the Field Domain Nodes.

Figure 9.8.2.1-1: High-level illustration - Tightly coupled Edge/Fog Computing with 3GPP T8 API  (Originator: IN-AE)

### Solution procedures

The clause introduces procedures for using network status procedures for tightly coupled Edge/Fog computing with following 3GPP T8 API, i.e. the T8 interface is available to the MN-CSE.

Network Status Reports API

Monitoring Event API (Monitoring Type: Number of UEs in an Area)

### Procedures for Network Status Reports and Monitoring Event API (Number of UEs in an Area) (Originator: IN-AE)

Figure 9.8.2.2.1-1 shows the solution procedures for tightly coupled Edge/Fog computing with Network Status Reports API and Monitoring Event API (Number of UEs in an area). We propose a new resource <nwMonitoringReq> described in clause 9.4.2.3 for retrieving Underlying Network information with a MN-CSE (Fog Node). The procedure leverages existing solutions such as Solution D: Loosely coupled Edge/Fog Computing with 3GPP T8 API and Solution E: Tightly coupled Edge/Fog Computing with 3GPP T8 API.

Figure 9.8.2.2.1-1: Procedures for tightly coupled Edge/Fog computing with Network Status Reports and Monitoring Event (Number of UEs in an area) (Originator: IN-AE)

Pre-conditions:

There is a relationship in place between the Service Provider and MNO allowing the IN-AE to request 3GPP T8 API information from the 3GPP Underlying Network. The method for establishing this relationship is outside the scope of the present document.

If the deployment uses External Group Identifier (externalGroupId) as described in 3GPP TS29.122 [i.32], when ASN/MN-CSEs or ADN-AEs register with the MN-CSE (Fog Node), then they use externalGroupId information to configure the externalGroupID of the corresponding <remoteCSE> or <AE> resources (see clause 6.3 of TS-0026 [i.34] when externalGroupID is configured).

The MN-CSE (Fog Node) is configured with system defaults as described in Pre-conditions of clause 9.5.2.2.1.

The IN-AE has the coverage area information of each MN-CSE (Fog Node) in order to send a request to the MN-CSE (Fog Node) for retrieving Underlying Network information in a particular geographic area.

The method for configuring these system defaults is outside the scope of the present document.

Step 1: CREATE <nwMonitoringReq> Request & Response, Subscription creation

An Originator (IN-AE) requests the creation of a <nwMonitoringReq> resource at the IN-CSE and, if the operation is successful, receives a response message. The IN-CSE announces the resource to the MN-CSE (Fog Node) and the Originator subsequently subscribes to updates of the <nwMonitoringReqAnnc> resource.

Step 2: UPDATE enable network monitoring

In order to initiate a monitoring request, the Originator (IN-AE) sends a request to update the monitorEnable attribute of the <nwMonitoringReq> resource, which is also updated in the announced resource. The resource includes the attributes as described in step 1 of clause 9.5.2.2.1.

Step 3a: Procedures for Network Status Reports

See step 3a of clause 9.5.2.2.1.

Step 3b: Procedures for Monitoring Event (Number of UEs in an area)

See step 3b of clause 9.5.2.2.1.

Step 4: Notification of <nwMonitoringReq>

After completion of step 3a or 3b, the MN-CSE (Fog Node) will map the response of 3GPP T8 API to the attributes of the <nwMonitoringReq> resource as described in step 4 of clause 9.5.2.2.1. The update <nwMonitoringReqAnnc> resource generates a corresponding notification response to the originator.

See clause 8.3 of TS-0026 [i.34] for a list of possible error scenarios and error handling options for the MN-CSE (Fog Node).

Step 5: The IN-AE adjusts data processing/transfer for Field Domain Nodes (ASN/MN/ADN)

The Originator (IN-AE) may use the information provided in step 4 in order to adjusts data processing/transfer for Field Domain Nodes (ASN/MN/ADN).

### Impacted Resources

To implement this solution, a new resource <nwMonitoringReq> is proposed to retrieve Underlying Network information. The resource is described in Solution D: Loosely coupled Edge/Fog Computing with 3GPP T8 API.

### -----------------------End of Change 1 ---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?