## Slide 1: oneM2M – Modbus Interworking
Group Name: SDS #41
Source: JaeSeung Song (KETI), JongGwan An(KETI), Hyeonseo Son (KETI), Sherzod (KETI)
Meeting Date: 2019-07-09
SDS-2019-0367

## Slide 2: Outline
Scope
Modbus & oneM2M characteristics
  Topology & simplified examples
  How IPE works
oneM2M-Modbus Interworking overview
  Examples Scenario
  Interworking functions and procedures
  Flow for example scenario
Vision of Interworking

## Slide 3: Scope
CoAP
HTTP
Custom IoT Application
Interworking
Enhancements for oneM2M system support interworking with Modbus device, such as supporting Master-slaver communication method
Modbus data model is mapped to oneM2M resources
Instantiating Modbus data model by usage of oneM2M base ontology
Interworking procedure by operating oneM2M resource and reusing Gerneric Interworking

## Slide 4: Modbus Topology
Modbus-M
M
M: Modbus Master (Client), Only one in a network, Readable, Writable
S: Modbus Slave (Server), Passively respond to master request
Modbus-S
S
Modbus-S
S
Modbus-S
S
RS-485 Bus (RTU)
Modbus-S
S
< Industrial Communication Protocol >

## Slide 5: Modbus Example
Modbus-M
M
Modbus-S
S
Modbus-S
S
Modbus-S
S
RS-485 Bus (RTU)
Modbus-S
S
UPDATE
Unlock
Update Lock Status to “Open”

## Slide 6: oneM2M Topology
Application Service Node
Application Dedicated Node
Application Dedicated Node
Application Dedicated Node
Middle Node
Middle Node
Middle Node
Infrastructure Node
AE
AE
AE
AE
AE
CSE
CSE
CSE
AE
CSE
AE
AE
CSE
CSE
AE: Application Entity
CSE: Common Services Entity

## Slide 7: oneM2M Example
Application Dedicated Node
Application Dedicated Node
Application Dedicated Node
Middle Node
Middle Node
Middle Node
Infrastructure Node
AE
AE
AE
AE
AE
CSE
CSE
CSE
AE
CSE
AE
AE
CSE
CSE
Door Lock
Actuator
Sensors
Keypad
UPDATE
NOTIFY
Unlock
Update Lock Status to “Open”

## Slide 8: How IPE works
Resources in CSE are fully abstracted from underlying technology e.g. Modbus
TS-0023 was used as a reference to build resource tree from SDT objects
To convert oneM2M resources to Modbus objects IPE stores mapping tables for Devices and Data Points of Modules
Data points are mapped according to their data type and read&write properties to 4 Modbus object types
Primary tables | Object type | Type of access | Comments
Discretes Input | Single bit | Read-Only | This type of data can be provided by an I/O system, e.g. read the status of switch
Coils | Single bit | Read-Write | This type of data can be alterable by an application program, e.g. switch on a transducer
Input Registers | 16-bit word | Read-Only | This type of data can be provided by an I/O system, e.g. read temperature on a sensor
Holding Registers | 16-bit word | Read-Write | This type of data can be alterable by an application, e.g. set value to a controller.
oneM2M data type | Mapping to data type in OMA DWAPI | Description
xs:integer | int, number, string | Data type for 32-bit signed integer. For indicating 3D printerState, the integer value should be interpreted into string by referring the tables in clause 7.2.2.1.
xs:string | string, array | Data type for text. The length limitation should be considered for the mapping.
xs:float | float | Data type for a single precision 32-bit floating point type as defined in XML Schema 1.0 [13] as the float primitive type.
xs:boolean | boolean | Data type for Boolean.
< Modbus >
< oneM2M >

## Slide 9: Smart Device Template (SDT)
The Smart Device Template (SDT) is a template which is used to model the capabilities, actions and events of connected devices.
SDT can be applied to build oneM2M resource tree structure for connected devices
SDT has one-to-one mapping between its data points and Modbus Objects types

## Slide 10: Mapping between SDT Data points types and Modbus object types
oneM2M Data type | Readable | Writable
xs:Boolean (1 byte) | True | True
xs:Boolean (1 byte) | True | False
xs:integer (4 bytes) | True | True
xs:integer (4 bytes) | True | False
xs:float (4 bytes) | True | True
xs:float (4 bytes) | True | False
xs:double (8 bytes) | True | True
xs:double (8 bytes) | True | False
xs:string | True | True
xs:string | True | False
Mapping
Modbus object type | Number of required registers
Coil (Single bit), Read-Write | 1 (8bit)
Discrete Input (Single bit), Read-Only | 1 (8bit)
Holding Register (16-bit word), Read-Write | 2 (32bit)
Input Register (16-bit word), Read-Only | 2 (32bit)
Holding Register (16-bit word), Read-Write | 2 (32bit)
Input Register (16-bit word), Read-Only | 2 (32bit)
Holding Register (16-bit word), Read-Write | 4 (64bit)
Input Register (16-bit word), Read-Only | 4 (64bit)
Holding Register (16-bit word), Read-Write | varying
Input Register (16-bit word), Read-Only | varying
Notes: 데이터 크기 표현

## Slide 11: Use case for Modbus IPE
IN
AE
CSE
Modbus
Master
IPE
Mca
Smart Solar Power Management system
ADN
AE
A use case where a group of solar panels working over Modbus are remotely managed by client application will be described.
The use case configuration has two solar panels working on Modbus protocol which are connected to a local Modbus gateway (IPE) with an embedded application to communicate with oneM2M cloud server.
Modbus RTU
Device Solar Panel A
Device Solar Panel B

## Slide 12: Smart Device Template (SDT) Devices
IPE_AE
[deviceSolarPanelA]
[deviceSolarPanelB]
<subscriptions>
0..1
0..n
0..1
SDT “Module Class”
<flexContainer>
SDT “Device”
<flexContainer>
one M2M SDT Device name | Modbus Slave ID
deviceSolarPanelA | 01
deviceSolarPanelB | 02
Lookup table for device mapping to Modbus Slave ID
[mod_battery]
[mod_energyConsumption]
[mod_energyGen]
[mod_binarySwitch]

## Slide 13: Smart Data Template (SDT) Modules
< TS-0023 defined models for Home appliances information model & mapping >
address
functionCode
slaveID
numberRegisters
address
functionCode
slaveID
numberRegisters
address
functionCode
slaveID
numberRegisters

## Slide 14: Lookup table for “Battery Module” mapping to Modbus Object types
Battery Resource name | Type | Readable | Writable
level | xs:integer | true | false
capacity | xs:integer | true | false
charging | xs:boolean | true | false
discharging | xs:boolean | true | false
lowBattery | xs:boolean | true | false
batteryThreshold | xs:integer | true | true
electricEnergy | xs:integer | true | false
voltage | xs:integer | true | false
material | xs:string | true | false
Modbus object type | Number of required registers | Address
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0001-0x0002
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0003-0x0004
Coil (Single bit), Read-Write | 1 (8 bit) | 0x0001
Coil (Single bit), Read-Write | 1 (8 bit) | 0x0002
Coil (Single bit) , Read-Write | 1 (8 bit) | 0x0003
Holding Register (16-bit word), Read-Write | 2 (32bit) | 0x0001-0x0002
Input Register (16-bit word) , Read-Only | 2 (32bit) | 0x0005-0x0006
Input Register (16-bit word) , Read-Only | 2 (32bit) | 0x0007-0x0008
Input Register (16-bit word) , Read-Only | 8 (128bit) | 0x0009-0x0018
Mapping

## Slide 15: Lookup table for “energyConsumption Module” mapping to Modbus Object types
energyConsumption Resource name | Type | Readable | Writable
power | xs:float | true | false
absoluteEnergy Consumption | xs:float | true | false
roundingEnergy Consumption | xs: integer | true | false
significantDigits | xs:integer | true | false
multiplyingFactors | xs:float | true | false
voltage | xs:float | true | false
current | xs:float | true | false
frequency | xs:float | true | false
measuringScope | xs:string | true | true
Modbus object type | Number of required registers | Address
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0019-0x001A
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x001B-0x001C
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x001D-0x001E
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x001F-0x0020
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0021-0x0022
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0023-0x0024
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0025-0x0026
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0027-0x0028
Holding Register (16-bit word), , Read-Write | 8 (128bit) | 0x0002-0x0011
Mapping

## Slide 16: Lookup table for “energyGeneration Module” mapping to Modbus Object types
energyGeneration Resource name | Type | Readable | Writable
powerGenerationData | xs:float | true | false
roundingEnergy Generation | xs:integer | true | false
significantDigits | xs:integer | true | false
multiplyingFactors | xs:float | true | false
generationSource | xs:string | true | false
Modbus object type | Number of required registers | Address
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0029-0x002A
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x002B-0x002C
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x002D-0x002E
Input Register (16-bit word), Read-Only | 2 (32bit) | 0x002F-0x0030
Input Register (16-bit word), Read-Only | 7 (112bit) | 0x0031-0x0040
Mapping

## Slide 17: Monitoring: Constructing Modbus message(Read)
oneM2M Resource name | Modbus object type | Number of required registers | Address
level | Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0001-0x0002
batteryThreshold | Holding Register (16-bit word), Read-Write | 2 (32bit) | 0x0001-0x0002
. . . |  |  | 
one M2M SDT Device name | Slave ID
deviceSolarPanelA | 01
deviceSolarPanelB | 02
Slave ID | Function Code | Number of registers | Address | CRC (checksum)
01 | 04 | 0002 | 0001 | 200B
Read
Memory | Function Code | Action
Coil | 01 | Read
 | 05 | Write(Single)
 | 15 | Write(Multiple)
Discrete Inputs | 02 | Read
Holding Registers | 03 | Read
 | 06 | Write(Single)
 | 16 | Write(Multiple)
Input Register | 04 | Read

## Slide 18: Monitoring: Constructing Modbus message(Write)
one M2M SDT Device name | Slave ID
deviceSolarPanelA | 01
deviceSolarPanelB | 02
Slave ID | Function Code | Number of registers | Address | Data | CRC (checksum)
01 | 05 | 0002 | 0001 | 40%(0x0028) | 200B
Write
oneM2M Resource name | Modbus object type | Number of required registers | Address
level | Input Register (16-bit word), Read-Only | 2 (32bit) | 0x0001-0x0002
batteryThreshold | Holding Register (16-bit word), Read-Write | 2 (32bit) | 0x0001-0x0002
. . . |  |  | 
Memory | Function Code | Action
Coil | 01 | Read
 | 05 | Write(Single)
 | 15 | Write(Multiple)
Discrete Inputs | 02 | Read
Holding Registers | 03 | Read
 | 06 | Write(Single)
 | 16 | Write(Multiple)
Input Register | 04 | Read

## Slide 19: Monitoring
Use case: In Solar Panel A when battery level decreases below threshold, a user should get a notification

## Slide 20: Monitoring

## Slide 21: Monitoring
IPE continuously monitors Modbus device. Modbus message is constructed as following:
  Find slave ID for deviceSolarPanelA from device lookup table.
    Slave ID = 01
  Find Modbus object type and address from Battery module lookup table. Map Modbus object type (input register) & Action (read) to Modbus function code
    Function code = 04
    Address = 0001
    Number of registers to read = 2

## Slide 22: Monitoring
When battery level below threshold IPE-AE sends a request to hosting CSE by updating [battery] resource and setting lowBattery attribute to 1
CSE updates [battery] resource and publishes a notification

## Slide 23: Updating data in Modbus device
Use case: User wants to change the low battery threshold value in Solar panel A

## Slide 24: Updating data in Modbus device
ADN-AE sends a request to hosting CSE by updating [battery] resource and setting batteryThreshold attribute to a new value
CSE updates [battery] resource and publishes a notification
ADN-AE receives the notification and sends a Modbus message by constructing it as follows:
  From notification message extract device name (deviceSolarPanelA), module name (battery), value
  Find slave ID for deviceSolarPanelA from device lookup table.
    Slave ID = 01
  Find Modbus object type and address for batteryThreshold from Battery module lookup table. Map Modbus object type (holding register) & Action (write) to Modbus function code
    Function code = 10
    Address = 0001

## Slide 25: Updating data in Modbus device
When new value of batteryThreshold is written IPE-AE sends a request to hosting CSE by updating [battery] resource with empty <flexContainer> that indicates successful update
Hosting CSE updates [battery] resource and publishes a notification about successful update

## Slide 26: Status
oneM2M TS-0033 specifies general interworking concept
oneM2M TS-0023 defined models for Home appliances information model & mapping

## Slide 27: Vision of Interworking
Open Standards  “Interworking Glue”

## Slide 28: Thank You!