| CHANGE REQUEST |
| --- |
| Meeting ID:* | SDS#41 |
| Source:* | Feng Zhang, Huawei (zhangfeng49@huawei.com) Yongjing Zhang, Huawei (zhangyongjing@huawei.com) Xiaotao Li, China Mobile (lixiaotao@chinamobile.com) |
| Date:* | 2019-07-01 |
| Reason for Change/s:* | To introduce the solution of semantic query and discovery based on ontology mapping result to meet the requirements ONT-018. |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <WI-0053> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0033 V4.3.0 |
| Clauses * | 8.12.x |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR provides the solution of semantic query and discovery based on ontology mapping result according to requirement ONT-018 in TS-0002. The supporting use cases can be found in TR-0001 clause 12.25.

| Requirement ID | Description | Release |
| --- | --- | --- |
| ONT-018 See REQ-2018-0057R01 | The oneM2M system shall support semantic query and discovery across heterogeneous ontologies including support of automatic ontology mapping and semantic reasoning. | 4 |

### -----------------------Start of change 1-------------------------------------------

## 8.12	Ontology mapping

### 8.12.x	Semantic query / discovery based on the ontology mapping result

##### 8.12.x.1 Introduction

Semantic query and semantic discovery operations can be enhanced by leveraging the ontology mapping result stored in the <ontologyMapping> resource, so that an application which understands only Ontology-A can get the resulting content or resource described in Ontology-B.

There are two approaches to implement this feature: 1) by converting the query statement according to the <ontologyMapping> resource, 2) by converting the target resources according to the <ontologyMapping> resource.

Both approaches require the extension of an optional request parameter - Ontology Mapping Resources, which contains a list of resource identifiers of existing <ontologyMapping> resources that are used as the base of converting the query statement or the target resources into their equivalents.

The following two clauses describes the detailed procedures of the proposed two approaches using the example ontology mapping result in clause 8.12.2.

Note that there is no difference between the semantic query operation and the semantic discovery operation in terms of applying the feature of ontology mapping in addition to the respective original procedures. So the following procedures combine the two operations in to one message flow.

##### 8.12.x.2 Solution 1: Converting the semantic query statement using the ontology mapping result

This procedure is used for performing a semantic query/discovery procedure with enhancement of ontology mapping by covering the query statement into the equivalent one.

Figure 8.12.x.2-1: The semantic query/ discovery procedure with ontology mapping by covering the query statement

The detailed message flow is depicted in Figure 8.12.x.2-1 and explained as follows:

- The hosting CSE (e.g. an oneM2M platform) receives a semantic query/ discovery request from an Originator (e.g. an oneM2M application). The request carries a semanticsFilter request parameter that contains the original query statement described in Ontology-A, as well as an Ontology Mapping Resources request parameter that contains the resource identifiers of one or multiple <ontologyMapping> resources. 
Note that the originator may or may not be the one who created the <ontologyMapping> resources. The use of the <ontologyMapping> resources is subject to the associated access control policy against the originator.

For example, the original query statement may be:

SELECT ?device

WHERE {

?device rdf:type Ontology-A:LightSensor.

}

- The hosting CSE locates the <ontologyMapping> resources according to the resource identifiers in the Ontology Mapping Resources request parameter, and retrieves the mapping results between Ontology-A and Ontology-B from the mappingResult attribute of the <ontologyMapping> resources.

For example, the mappingResult may contain the following triple (mapping relationship):

Ontology-A:LightSensor  owl:equivalentClass Ontology-B:Light_Sensor

- The hosting CSE performs the semantic query/ discovery upon the target resources which reference Ontology-A and Ontology-B, according to the ontology mapping result and the original query statement. This step comprise the following sub-steps:

  - The hosting CSE determines the equivalent query statement described in Ontology-B by converting from the original query statement described in Ontology-A, according to the ontology mapping result between Ontology-A and Ontology-B. This is done by replacing all the ontology class and properties of Ontology-A in the query statement with the corresponding equivalents of Ontology-B.

According to the examples above, the equivalent query statement becomes:

SELECT ?device

WHERE {

?device rdf:type Ontology-B:Light_Sensor.

}

  - The hosting CSE performs the semantic query/ discovery procedure upon the target resources that reference Ontology-A using the original query statement, and collects the first query/ discovery result.

For example, a <container-x> resource may have a <semanticDescriptor> child resource that references Ontology-A (by the ontologyRef attribute) and contains the following triple that matches the original query statement:

dev-x rdf:type Ontology-A:LightSensor.

  - The hosting CSE performs the semantic query/ discovery procedure upon the target resources that reference Ontology-B using the equivalent query statement, and collects the second query/ discovery result.

For example, a <container-y> resource may have a <semanticDescriptor> child resource that references Ontology-B (by the ontologyRef attribute) and contains the following triple that matches the original query statement:

dev-y rdf:type Ontology-B:Light_Sensor.

- The hosting CSE combines the query/ discovery results from both step 3b and step 3c, and return the combined results to the originator.

For example, in the case of semantic query, the results are the IRIs of dev-x and dev-y. In the case of semantic resource discovery, the results are the resource identifiers of <container-x> and <container-y>.

##### 8.12.x.3 Solution 2: Converting the target resources using the ontology mapping result

This procedure is used for performing a semantic query/discovery procedure with enhancement of ontology mapping by covering the target resources into the equivalent ones. The only difference is in step 3 comparing to clause 8.12.x.2.

Figure 8.12.x.3-1: The semantic query/ discovery procedure with ontology mapping by covering the target resources

The detailed message flow is depicted in Figure 8.12.x.3-1 and explained as follows:

- The same as step 1 in clause 8.12.x.2.

- The same as step 2 in clause 8.12.x.2.

- The hosting CSE performs the semantic query/ discovery upon the target resources which reference either Ontology-A or Ontology-B according to the ontology mapping result and the original query statement. This step comprise the following sub-steps:

  - The hosting CSE determines the equivalent semantic description in Ontology-A for the target resources which reference Ontology-B by converting from the original semantic description in Ontology-B, according to the ontology mapping result between Ontology-A and Ontology-B. This is done by replacing all the ontology class and properties of Ontology-B in the related <semanticDescriptor> resources of the target resources into the equivalents of Ontology-A.

For example, a <container-y> resource may have a <semanticDescriptor> child resource that references Ontology-B (by the ontologyRef attribute) and contains the following triple:

dev-y rdf:type Ontology-B:Light_Sensor.

This triple is then converted into the equivalent in Ontology-A as follows:

dev-y rdf:type Ontology-A:LightSensor.

  - The same as step 3b in clause 8.12.x.2.

  - The hosting CSE performs the semantic query/ discovery procedure upon the target resources that reference Ontology-B using the original query statement and the equivalent semantic description, and collects the second query/ discovery result.

Note the converted equivalent semantic description in step 3a should match the original query statement.

- The same as step 4 in clause 8.12.x.2.

### -----------------------End of change 1-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?