## Slide 1: Discussion on CSE Impersonation (TS-0003)
oneM2M SDS#44
Seongyun Kim
KETI

## Slide 2: AE Impersonation Prevention (Registrar CSE)
We have mechanism to prevent AE pretending to other AEs (Manipulate From parameter)
Registrar CSE (entry point of M2M System) checks AE impersonates its ID

## Slide 3: Can’t use this mechanism for CSE Impersonation
CSE pretends to other CSEs / AEs (manipulate from parameter)
Current Deployment Scenario
We already have the scenario where Transit CSE forwards others’ message using credential of Transit CSE
ASN-AE
ID: CAE1
ASN-CSE
ID: ASN-CSE1
MN-CSE
ID: MN-CSE1
IN-CSE
ID: IN-CSE
ADN-AE
ID: CAE2
from: CAE1
to: IN-CSE/res1
from: ASN-CSE1/CAE1
to: IN-CSE/res1
from: CAE2
to: IN-CSE/res2
from: ASN-CSE1/CAE1
to: IN-CSE/res1
from: MN-CSE1/CAE1
to: IN-CSE/res2
Security Association Establishment
Between ASN-CSE1 and MN-CSE1
Security Association Establishment
Between MN-CSE1 and IN-CSE
Security Association Establishment
Between CAE1 and ASN-CSE1
ID specified in From parameter and ID used in security association are different
Security Association Establishment
Between ASN-CSE1 and MN-CSE1

## Slide 4: CSE Impersonation
CSE pretends to other CSEs / AEs (manipulate from parameter)
Currently Hosting or Transit CSE can’t tell whether Originator or Transit CSE manipulates From parameter or not
ASN-AE
ID: CAE1
ASN-CSE
ID: ASN-CSE1
MN-CSE
ID: MN-CSE1
IN-CSE
ID: IN-CSE
ADN-AE
ID: CAE2
from: ASN-CSE1/CAE1
to: IN-CSE/res1
Even though MN-CSE1 manipulates From parameters in a request,
IN-CSE accepts and processes the request and send the response back.
(MN-CSE1 can get more information than his access rights)
Security Association Establishment
Between ASN-CSE1 and MN-CSE1
Security Association Establishment
Between MN-CSE1 and IN-CSE
Security Association Establishment
Between CAE1 and ASN-CSE1
Security Association Establishment
Between ASN-CSE1 and MN-CSE1

## Slide 5: How to prevent AE/CSE Impersonation  ESPrim
“7.2.2 Verification Using End-to-End Security of Primitives (ESPrim)” already covers AE or CSE Impersonation

## Slide 6: What is Missing?
We cannot mandate Hosting CSE to prevent CSE Impersonation since ESPrim is optional feature
Hosting CSE should have the mechanism to require ESPrim requests over more than 0 hop
Transit CSE should have the mechanism to reject non-ESPrim requests when next Transit CSE or Hosting CSE requires ESPrim requests
ASN-AE
ID: CAE1
ASN-CSE
ID: ASN-CSE1
MN-CSE
ID: MN-CSE1
IN-CSE
ID: IN-CSE
ADN-AE
ID: CAE2
Security Association Establishment
Between ASN-CSE1 and MN-CSE1
Security Association Establishment
Between MN-CSE1 and IN-CSE
Security Association Establishment
Between CAE1 and ASN-CSE1
pairwiseESPrimKey Establishment
from: CAE1
to: IN-CSE/res1
from: ASN-CSE1/CAE1
to: IN-CSE/res1
from: CAE2
to: IN-CSE/res2
from: ASN-CSE1/CAE1
to: IN-CSE/res1
from: MN-CSE1/CAE1
to: IN-CSE/res2
Security Association Establishment
Between ASN-CSE1 and MN-CSE1
IN-CSE wants to receive ESPrim requests only
when he communicates entities more than 0 hop,
but there is no way to block it.