| CHANGE REQUEST |
| --- |
| Meeting ID:* | SDS 53.2-1 |
| Source:* | Rana Kamill |
| Date:* | 2022-07-14 |
| Reason for Change/s:* | CR TS-0003 Annex M |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 v2.18 |
| Clauses * | Annex M |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2020 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes some updates to the TS-0003 Release 2 according to the conclusions of ITU-T SG20 and oneM2M joint meeting.

This contribution also proposes some changes for the TS-0003 Release 3.

### ---------------------Start of change 1---------------------------------------------

### 6.2.1	Access Management

#### 6.2.1.1	Identification and Authentication

This component provides authentication services to the Application Layer. Annex B provides a general description of Authentication mechanisms. oneM2M mutual authentication schemes allow oneM2M entities to prove that they know related credentials such as Master Credentials, without having to exchange value of those credentials, and sensitive data such as security identities and security identifiers. To prevent reading and copying of credentials, a secure environment within the Security CSF provides protection against tampering of those credentials and related processed information. For more information see Annex B .

6.2.1.2 Considerations for Long term Key Storage

Long term Provisioned Secure Connection Keys can pose a security risk if not adequately secured, and for this reason long term Provisioned Secure Connection Keys are recommended to be stored in Secure Environments.

Long term Pre-Provisioned Symmetric Enrolee Keys can pose a security risk if not adequately secured, and for this reason it is recommended that Long term Pre-Provisioned Symmetric Enrolee Keys are stored in Secure Environments.

There will be a very wide range of non-3GPP based devices with many different implementations. Standardising these devices is not within the scope of oneM2M or 3GPP. However, security best practice guides are available from:

ETSI-  Cyber Security For Consumer Internet Of Things [i-30]

IoTSF- Secure Design: Best Practice Guide. Release 2. November 2019[i-31]

GSMA- IoT Security Guidelines and Assessment [i-32]

### ---------------------End of change 1---------------------------------------------

### ---------------------Start of change 2---------------------------------------------

Annex O (informative):
Considerations on Long Term Key Storage

Long term Provisioned Secure Connection Keys can pose a security risk if not adequately secured, and for this reason long term Provisioned Secure Connection Keys are recommended to be stored in Secure Environments.

Long term Pre-Provisioned Symmetric Enrolee Keys can pose a security risk if not adequately secured, and for this reason it is recommended that Long term Pre-Provisioned Symmetric Enrolee Keys are stored in Secure Environments.

Since by definition, there will be a very wide range of non-3GPP based devices with many different implementations. As these are not likely to be standardised, this is not in the scope of oneM2M or 3GPP. However, security best practice guides are available from:

ETSI-  Cyber Security For Consumer Internet Of Things [i.31]

IoTSF- Secure Design: Best Practice Guide. Release 2. November 2019[i.32]

GSMA- IoT Security Guidelines and Assessment [i.33 ]

### ---------------------End of change 2---------------------------------------------

### ---------------------Start of change 3---------------------------------------------

Annex M: Void

### ---------------------End of change 3---------------------------------------------

### ---------------------Start of change 4---------------------------------------------

Annex N: Void

### ---------------------End of change 4---------------------------------------------

Annex N: Void

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?