| CHANGE REQUEST |
| --- |
| Meeting ID:* | SDS#56 |
| Source:* | Xiaotao Li, CMCC, lixiaotao@chinamobile.com Shujuan You, CMCC, youshujuan@ chinamobile.com Yawen Niu, CMCC, niuyawen@chinamobile.com |
| Date:* | 2022-09-27 |
| Reason for Change/s:* | To introduce a solution of automatic recognition of identification schemes for heterogeneous IoT identifiers to meet the requirement OSR-111. |
| CR against: Release* | Release 4 |
| CR against: WI* | Active <WI-0069> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0044 V0.6.0 |
| Clauses * | 8.x.x |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | N/A |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR provides a solution of automatic recognition of identification schemes for heterogeneous IoT identifiers according to requirement OSR-111 in TS-0002. The supporting use cases can be found in TR-0001 clause 12.36.

| Requirement ID | Description | Release |
| --- | --- | --- |
| OSR-111 See REQ-2017-0018R01 | The oneM2M system shall be able to support heterogeneous identification services, the recognition of external identification systems and converting an object identifier to a compatible identifier recognized by the oneM2M system. | 5 |

In Internet of Things (IoT), a unique identifier is required for each object to serve as a digital identity. An identifier is represented using a sequence of numbers, characters, or a combination of them, and the detailed description information about the identified object can be indexed and discovered. For example, people can get the price, place of origin and manufacturer information of a commodity by scanning the product barcode, and the serial number on the barcode is the Global Standard 1 (GS1) identifier of this commodity. However, due to political, commercial and other reasons, there are thousands even tens of thousands of types of IoT identifiers co-existing in the IoT ecosystem (e.g. EPC, Handle, OID, etc.). These schemes have different encoding lengths, value ranges and structures, and each scheme has its own customized resolution rules. It requires different resolution systems to resolve these heterogeneous identifiers respectively. So, if we want to obtain the profile information about an object, the identification scheme of this object’s identifier should be known in advance.

Currently, the co-existence of multiple objects tagged by different types of identifiers is becoming the norm. It is unrealistic to require all IoT objects to use the same kind of identifier scheme in IoT applications. Therefore, oneM2M System is required to recognize the identification schemes of IoT identifiers to support the unified resolution of heterogeneous IoT identifiers.

Take commodity source tracing for example. The lifecycle of a commodity is composed of a series of processes including material purchase, manufacturing, storage, transportation, sales, etc. In each process, different manufacturers will choose their conventional identification schemes to identify the commodity. If an application wants to acquire the detailed information about this commodity throughout the chain (of processes), the identification schemes of the identifiers in these processes should be known at first. To satisfy the requirements, the oneM2M System shall be able to recognize the identification schemes of these heterogeneous IoT identifiers from different processes.

### -----------------------Start of change 1-------------------------------------------

### 8.x.x	Automatic recognition of  identification schemes for heterogeneous IoT identifiers

##### 8.x.x.1 Introduction

In Internet of Things (IoT), each object requires a unique identifier to identify itself and index its detailed profile to support mutual recognitions among multiple objects. However, existing IoT identifiers belonging to different identification schemes are heterogeneous from each other, which create a great challenge for the applications that need to resolve the heterogeneous identifiers. To address this challenge, we propose a solution to automatically recognize the heterogeneous identification schemes used by various IoT identifiers, based on a sequence-to-sequence (seq2seq) model consisting of an encoder and a decoder. The encoder uses one Long Short-Term Memory (LSTM) to map the identifier sequence to a vector of fixed dimensionality, and the decoder uses another LSTM to unfold the vector into a target sequence representing the identification scheme of this identifier.  In this way, the unified resolution of heterogeneous identifiers in different forms can be achieved according to the identified result of the identifier recognition model. Based on the seq2seq model, in this clause, a potential solution is specified for the process of automatic recognition of identification schemes for heterogeneous IoT identifiers.

Figure 8.X.X.1-1: Unified resolution of heterogeneous identifiers based on the identifier recognition model

##### 8.x.x.2 	Procedure for automatic recognition of  identification schemes for heterogeneous IoT identifiers

We take an application that a device or a user who wants to recognize the identification scheme of an IoT identifier and configure the identified device in an oneM2M deploymen, to introduce the procedure for automatic recognition of  identification schemes for heterogeneous IoT identifiers. The normal message flow is described as follows:

Figure 8.X.X.2-1: Message flow for automatic recognition of identification schemes for heterogeneous IoT identifiers

Step 1: An application sends a request to the M2M service platform to recognize the identification scheme of an IoT identifier and then configure the device in an oneM2M deployment. The identifier recognition model is deployed on the M2M service platform which manifests as a rule base or a machine learning classification model.

Step 2: After receiving the request, the oneM2M platform recognizes the identification scheme of the identifier based on the heterogeneous identification function.

Step3:   Based on the identifier and its identification scheme, the oneM2M platform captures the device management information from the M2M service provider and populates it with new configuration information.

- This identifier becomes a M2M External Identifier (M2M-Ext-ID);

- Populate node resource and device management resources like firmware object, software object, etc.

Step 4:   The oneM2M platform returns the result to the application. This can be success or configuration complete message.

#### 8.x.x.3	Procedure for initiating a function of  the identifier recognition model training

Solution-1: In this alternative solution, the identifier recognition model is a seq2seq model consisting of an encoder and a decoder. The  illustration of the seq2seq architecture shown in  Figure 8.X.X.3-1, In the seq2seq model, the input is an identifier, and the output is its identification scheme. To satisfy the input and output criteria of the seq2seq model, each identifier and its identification scheme are converted to sequence forms respectively. The encoder uses one Long Short-Term Memory (LSTM) to map the identifier sequence to a vector of fixed dimensionality, and the decoder uses another LSTM to unfold the vector into a target sequence representing the identification scheme of this identifier. The following steps are performed for the identifier recognition model training.

Figure 8.X.X.3-1: An illustration of the seq2seq architecture.

Strategy 1: In this strategy, as shown in Figure 8.X.X.3-2 (a), the identifiers are converted to source sequences through character encoding, and the classes of identification schemes are converted to target sequences through one-hot encoding. The EAN identifier “6945091708456” is transformed into a character sequence of length 13, i.e. {‘6’,‘9’,‘4’,...,‘6’}. We note that each character corresponds to a unique decimal integer in the range of 0 and 127 in the ASCII encoding system. So in the embedding layer of the encoder, we use a 128- dimensional one-hot vector as the embedding of each character, in which the j-th  (j is the ASCII code of this character) element is 1, and other elements are 0. For example, the embedding of ‘6’ is {0,0,…1,0,…,0} in which the 54-th (the ASCII code of ‘6’ is 54) element is set to 1. Let us suppose  the overall number of classes N is 20, and the length of the decoder K is set to 20. The class number of an identification scheme is transformed into a 20-bit 0-1 sequence. Here, the EAN identification scheme is converted to {0,0,1,…,0}, where the 3-th (the class number of EAN identifiers is 3) element is 1. In the embedding layer of the decoder, a 2-dimensional one-hot vector is used to represent each element in the output sequence, in which the vector {1,0} represents the element 0, and the vector {0,1} represents the element 1.

Strategy 2: In Strategy 1, the length of the decoder equals the class number of the sample identifiers and will increase with the growth of N. If N is extremely large (for example, over 1,000), the training time will increase significantly, and the learned model will also decline in stability. In Strategy 2, the encoder part is the same as that of the seq2seq model implemented by Strategy 1, but the class number of an identification scheme is transformed into a fixed-length binary sequence in the decoder to reduce the length of the decoder. In this case, the length of the decoder is

As shown in Figure 8.X.X.3-2 (b), the class number of an identification scheme is represented by a 5-bit sequence, and the EAN identification scheme here is converted to {0,0,0,1,1}. In the decoder embedding layer, we also use a 2-dimensional one-hot vector to represent each element in the output sequence. By this strategy, we can represent 1,000 categories of identifiers with a 10-bit output sequence, while a decoder of length 1,000 is required by Strategy 1 under the same condition.

Figure 8.X.X.3-2: Two strategies for implementing the identifier recognition model

8.x.x.4		Procedure of recognizing the identification scheme of an IoT identifier based on  the identifier recognition model

Figure 8.X.X.4-1:  Procedure of recognizing the identification scheme of an IoT identifier based on  the identifier recognition model

Step 1: The hosting CSE receives a request to recognize the identification scheme of an IoT identifier.

Step 2: The hosting CSE converts the identifier to a character sequence.

Step 3: The hosting CSE inferences the identification scheme sequence to which the identifier belongs based on the identifier identification model.

Step 4: The hosting CSE converts the output sequence to the identification scheme.

Step5:  The hosting CSE returns identification scheme to the originator.

### -----------------------End of change1-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Find the most possible type of the identifier through heterogeneous identification function

Application

M2M service platform

1. Request to recognize the identification scheme of an IoT identifier and configure the identified device

2. Recognize the identification scheme of the identifier through the identifier recognition model

3 Capture the device management information from the M2M service provider based on the identifier and its identification scheme and populate it with new configuration information

4. Return the result