| CHANGE REQUEST |
| --- |
| Meeting ID:* | SDS#54 |
| Source:* | SeungMyeong JEONG, KETI, sm.jeong@keti.re.kr Sungchan Choi, KETI, csc@keti.re.kr |
| Date:* | 2022-09-26 |
| Reason for Change/s:* | To define new resource type and APIs for machine learning dataset support feature |
| CR against: Release* | 5 |
| CR against: WI* | Active: WI-0105 (System enhancements to support AI capabilities) MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0001 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | n/a |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes new resource type(s) for ML dataset support feature for oneM2M platform. This topic has been discussed in the SDS WG with “SDS-2022-0072-discussion_on_AI_ML_dataset_support” at SDS#54 meeting.

In the contribution 0072, there was a suggestion to use one dataset policy resource for training dataset and inference data generation. The original proposal for traning dataset preparation was to retrieve historical data for multiple data sharing resources with virtual resource. In this CR, there is one common resource for training dataset and inference data preparation by the oneM2M platform.

Similar to the <locationPolicy> resource, when <mlDatasetPolicy> resource is created, the dataset is stored in a separate resource by the platform. We may use exising <container> and <contentInstance> resources as generic data sharing resources. However, to store some meta information about dataset, it is suggested to have a new resource types which extends container and contentInstance resource types, which is similar justification as timeSeries and timeSeriesInstance resource types.

In the first version of this contribution, resource type definitions are proposed. When they get more agreeable, other clauses (e.g. parent-child relationship in clause 9, CRUD procedures in clause 10) will be added in the upcoming revisions.

### ********** Start of change 1 **********

### 9.6.x	Resource Type mlDatasetPolicy

The <mlDatasetPolicy> resource represents a policy to create a machine learning dataset with the data from other data sharing resources. This is used to create training datasets with historical data for building machine learning models. When dataset preparation is done, the CSE creates <dataset> and <datasetInstance> resources to store the dataset. Then data scientists fetch, process the dataset and train models. After that, for newly created resources, inference input data is created and stored the by CSE with the policies. Newly created inference input data can be retrieved or notified with subscription to the machine leaerning applications which deploys the trained models.

Table 9.6.x-1: Child resources of <mlDatasetPolicy> resource

| Child Resources of <timeSeries> | Child Resource Type | Multiplicity | Description | <timeSeriesAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |

The <mlDatasetPolicy> resource shall contain the attributes specified in table 9.6.36-2.

Table 9.6.x-2: Attributes of <mlDatasetPolicy> resource

| Attributes of <mlDatasetPolicy> | Multiplicity | RW/ RO/ WO | Description | <mlDatasetPolicyAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announceSyncType | 0..1 | RW | See clause 9.6.1.3. | MA |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. | OA |
| creator | 0..1 | RO | See clause 9.6.1.3. | NA |
| holder | 0..1 | RW | See clause 9.6.1.3. | NA |
| sourceResourceIDs | 1(L) | WO | The resource IDs which builds a dataset When the target resource is a <container> resource, content attribute of the children <contentInstance> resouces get included in the dataset. When the target resource is a <timeSeries> resource, content attribute of the cchildren <timeSeriesInstance> resouces get included in the dataset. When the target resource is a <flexContainer> resource, custom attributes of the children <flexContainerInstance> resouces get included in the dataset. | OA |
| datasetStartTime | 0..1 | WO | The timestamp filter as the start time of source data resources. creationTime or dataGenerationTime depending on the source resource type, gets filtered. If datasetStartTime and datasetEndTime both are not provided, then all data instanes of source resources get included in the dataset. | OA |
| datasetEndTime | 0..1 | WO | The timestamp filter as the end time of source data resources. creationTime or dataGenerationTime depending on the source resource type, gets filtered. If datasetStartTime and datasetEndTime both are not provided, then all data instanes of source resources get included in the dataset. | OA |
| batchWindowStartTime | 0..1 | WO | When more than one data from source resources get batched as one, this timestamp indicates the start time of each recurring windows. | OA |
| batchWindowDuration | 0..1 | WO | This indicates duration for each data batch window. | OA |
| nullValuePolicy | 0..1 | WO | This indicates null(empty) value handling policy (e.g. leave as null, fill with last-known values) for the created dataset. | OA |
| datasetFormat | 1 | WO | The serialization format of the dataset. (e.g. CSV) | OA |
| trainingDatasetID | 0..1 | RO | The ID of the <dataset> resource for training dataset which gets generated with source resources referred by the sourceResourceIDs attribute. | OA |
| numberOfDataForTraining | 0..1 | WO | The number of data fragment of the dataset is stored in a single <datasetInstance> resource. Default is all. | OA |
| numberOfDataForInference | 0..1 | WO | The number of data fragment of the dataset is stored in a single <datasetInstance> resource. Default is 1(one). | OA |
| infefenceInputDataID | 0..1 | RO | The ID of the <dataset> resource for inference input. When the is numberOfDataForInference set, a separate <dataset> resource gets created to store inference input data for newly created source resources. | OA |

### ********** End of change 1 **********

### ********** Start of change 2 **********

### 9.6.x	Resource Type dataset

The <dataset> resource represents a container for a dataset. This is created by a CSE when <mlDatasetPolicy> resource is created. When it is created, the links are stored in trainingDatasetID and  infefenceInputDataID in the <mlDatasetPolicy> resource, and mlDatasetPolicyID attribute in the <dataset> resource.

The <dataset> resource works similar to <container> resource, but has additional attributes to keep dataset related aspects. This supports <latest> and <oldest> resources. The dataset itself is fragmented and stored in each child <datasetInstance> resource.

Table 9.6.y-1: Child resources of <dataset> resource

| Child Resources of <dataset> | Child Resource Type | Multiplicity | Description | <dataset> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <semanticDescriptor> | 0..n | See clause 9.6.30 | <semanticDescriptor>, <semanticDescriptorAnnc> |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscription> |
| la | <latest> | 1 | See clause 9.6.27 | None |
| ol | <oldest> | 1 | See clause 9.6.28 | None |

The <dataset> resource shall contain the attributes specified in table 9.6.y-2.

Table 9.6.y-2: Attributes of <dataset> resource

| Attributes of <dataset> | Multiplicity | RW/ RO/ WO | Description | <datasetAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | RW | See clause 9.6.1.3 | MA |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| labels | 0..1 (L) | RW | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| announceTo | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | RW | See clause 9.6.1.3. | NA |
| announceSyncType | 0..1 | RW | See clause 9.6.1.3. | MA |
| dynamicAuthorizationConsultationIDs | 0..1 (L) | RW | See clause 9.6.1.3. | OA |
| creator | 0..1 | RO | See clause 9.6.1.3. | NA |
| holder | 0..1 | RW | See clause 9.6.1.3. | NA |
| location | 0..1 | RW | See clause 9.6.1.3. | OA |
| mlDatasetPolicyID | 1 | RO | The ID of the <mlDatasetPolicyID> resource which generated this <dataset> resource. | OA |
| listOfFeatures | 1 | RO | The list of dataset feature names. | OA |

### 9.6.z	Resource Type datasetInstance

The <datasetInstance> resource represents a fragment of a dataset. A whole dataset is split into the number of data items which is configured in the corresponding <mlDatasetPolicy> resource of the parent <dataset> resource.

The < timeSeriesInstance> resource shall contain the attributes specified in table 9.6.z-1.

Table 9.6.z-1: Attributes of <datasetInstance> resource

| Attributes of <timeSeriesInstance> | Multiplicity | RW/ RO/ WO | Description | <datasetInstanceAnnc> Attributes |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3. | NA |
| resourceID | 1 | RO | See clause 9.6.1.3. | NA |
| resourceName | 1 | WO | See clause 9.6.1.3. | NA |
| parentID | 1 | RO | See clause 9.6.1.3. | NA |
| labels | 0..1 (L) | WO | See clause 9.6.1.3. | MA |
| creationTime | 1 | RO | See clause 9.6.1.3. | NA |
| expirationTime | 1 | WO | See clause 9.6.1.3. | NA |
| announceTo | 0..1 (L) | WO | See clause 9.6.1.3. | NA |
| announcedAttribute | 0..1 (L) | WO | See clause 9.6.1.3. | NA |
| announceSyncType | 0..1 | RW | See clause 9.6.1.3. | MA |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3. | NA |
| datasetInstanceStartTime | 1 | WO | The oldest timestamp among the data in the dataset attribute. | OA |
| datasetInstanceEndTime | 1 | WO | The latest timestamp among the data in the dataset attribute. | OA |
| numberOfData | 1 | RO | The number of data in the dataset attribute. | OA |
| dataset | 1 | RO | The dataset or dataset fragment generated by the <mlDatasetPolicy> resource, referred by mlDatasetPolicyID of the parent <dataset> resource. | OA |
| datasetFormat | 1 | RO | The serialization format of the dataset. (e.g. CSV) | OA |

### ********** End of change 2 **********

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?