| CHANGE REQUEST |
| --- |
| Meeting ID:* | SDS#56 |
| Source:* | SeungMyeong JEONG, KETI, sm.jeong@keti.re.kr Sungchan Choi, KETI, csc@keti.re.kr |
| Date:* | 2022-09-27 |
| Reason for Change/s:* | To define protocol specifications for <mlDatasetPolicy>, <dataset> and <datasetFragment> resources and procedures. |
| CR against: Release* | 5 |
| CR against: WI* | Active: WI-0105 (System enhancements to support AI capabilities) MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | n/a |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes stage 3 specifications for the following TS-0001 contribution:

- SDS-2022-0143Rxx-TS-0001 mlDatasetPolicy resource

In the first version of this contribution, resource type definitions are proposed. When they get more agreeable, other clauses will be added in the upcoming revisions.

### ********** Start of change 1 **********

### 7.4.X Resource Type <mlDatasetPolicy>

#### 7.4.X.1	Introduction

This resource represents a set of policies to create a dataset which can be used for machine learning applications. When this <mlDatasetPolicy> resource is created, then the CSE creates a corresponding <dataset> resource(s).

The detailed description can be found in clause 9.6.X in oneM2M TS-0001 [6].

Table 7.4.Y.1-1: Data type definition of <mlDatasetPolicy> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| mlDatasetPolicy | CDT-mlDatasetPolicy.xsd |  |

Table 7.4.X.1-2: Universal/Common Attributes of <mlDatasetPolicy> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| creationTime | NP | NP |
| lastModifiedTime | NP | NP |
| labels | O | O |
| accessControlPolicyIDs | O | O |
| expirationTime | O | O |
| dynamicAuthorizationConsultationIDs | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |
| announceSyncType | O | O |
| creator | O | NP |
| holder | O | NP |
| location | O | O |

Table 7.4.X.1-3: Resource Specific Attributes of <mlDatasetPolicy> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| sourceResourceIDs | O | O | list of xs:anyURI | No default |
| datasetStartTime | O | O | m2m:absRelTimestamp | No default |
| datasetEndTime | O | O | m2m:absRelTimestamp | No default |
| timeCorrelationStartTime | O | NP | m2m:absRelTimestamp | No default |
| timeCorrelationDuration | O | NP | xs:duration | No default |
| nullValuePolicy | O | NP | m2m:nullValuePolicy | 1: “Leave as empty” |
| datasetFormat | M | NP | m2m:contentInfo | No default |
| historicalDatasetID | NP | NP | xs:anyURI | No default |
| numberOfRowsForHistoricalDataset | O | NP | xs:positiveInteger | “All” |
| numberOfRowsForLiveDataset | O | NP | xs:positiveInteger | 1 |
| liveDatasetID | NP | NP | xs:anyURI | No default |

Table 7.4.X.1-4: Child resources of <mlDatasetPolicy> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause 7.4.8 |
| <semanticDescriptor> | [variable] | 0..n | Clause 7.4.34 |

#### 7.4.X.2	<mlDatasetPolicy> resource specific procedures for CRUD operations

##### 7.4.X.2.1	Create

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No other changes from the generic procedures in clause 7.2.2.2.

##### 7.4.X.2.2	Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### 7.4.X.2.3	Update

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### 7.4.X.2.4	Delete

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

### ********** End of change 1 **********

### ********** Start of change 2 **********

### 7.4.Y Resource Type <dataset>

#### 7.4.Y.1	Introduction

This resource represents meta data for a dataset, while the dataset is fragmented and stored in children <datasetFragment> resources. A <dataset> resource is created by the CSE when it creates a <mlDatasetPolicy> resource. Therefore, a Create API for AEs are not allowed.

The detailed description can be found in clause 9.6.Y in oneM2M TS-0001 [6].

Table 7.4.Y.1-1: Data type definition of <dataset> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| dataset | CDT-dataset.xsd |  |

Table 7.4.Y.1-2: Universal/Common Attributes of <dataset> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Update |
| @resourceName | NP |
| resourceType | NP |
| resourceID | NP |
| parentID | NP |
| creationTime | NP |
| lastModifiedTime | NP |
| labels | O |
| accessControlPolicyIDs | O |
| expirationTime | O |
| dynamicAuthorizationConsultationIDs | O |
| announceTo | O |
| announcedAttribute | O |
| announceSyncType | O |
| creator | NP |
| holder | O |
| location | O |

Table 7.4.Y.1-3: Resource Specific Attributes of <dataset> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Update |  |  |
| mlDatasetPolicyID | NP | xs:anyURI | No default |
| listOfFeatures | NP | list of xs:token | No default |

Table 7.4.Y.1-4: Child resources of <dataset> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | Clause 7.4.8 |
| <latest> | la | 1 | Clause 7.4.27 |
| <oldest> | ol | 1 | Clause 7.4.28 |
| <semanticDescriptor> | [variable] | 0..n | Clause 7.4.34 |
| <datasetFragment> | [variable] | 0..n | Clause 7.4.Z |

#### 7.4.Y.2	<dataset> resource specific procedures for CRUD operations

##### Editor’s Note: When the CSE creates <dataset> resource after creation of corresponding <mlDatasetPolicy> resource, creator attribute of <dataset> resource is set as the same value as <mlDatasetPolicy> resource’s. So the policy creator can retrieve the dataset and dataset fragments. Also he/she can configure itw own access control policies (e.g. acpi).

##### 7.4.Y.2.1	Create

Originator:

The <datasetFragment> resource shall not be Created via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order:

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

##### 7.4.Y.2.2	Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### 7.4.Y.2.3	Update

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### 7.4.Y.2.4	Delete

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

### 7.4.Z	Resource Type <datasetFragment>

#### 7.4.Z.1	Introduction

The <datasetFragment> resource represents a fragmented dataset.

The detailed description can be found in clause 9.6.Z in oneM2M TS-0001 [6].

Table 7.4.Z.1-1: Data type definition of <datasetFragment> resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| datasetFragment | CDT-datasetFragment.xsd |  |

Table 7.4.Z.1-2: Universal/Common Attributes of <datasetFragment> resource

Attribute Name

@resourceName

resourceType

resourceID

parentID

creationTime

lastModifiedTime

labels

expirationTime

announceTo

announcedAttribute

announceSyncType

Table 7.4.Z.1-3: Resource Specific Attributes of <datasetFragment> resource

| Attribute Name | Data Type | Default Value and Constraints |
| --- | --- | --- |
| datasetFragmentStartTime | m2m:absRelTimestamp | No default |
| datasetFragmentEndTime | m2m:absRelTimestamp | No default |
| numberOfRowsInFragment | xs:positiveInteger | No default |
| datasetFragment | xs:anySimpleType | No default |
| datasetFormat | m2m:contentInfo | No default |

#### 7.4.Z.2	<datasetFragment> resource specific procedures for CRUD operations

##### Editor’s Note: Just like container/contentInstance and timeSeries/timeSeriesInstance, acess control policy of the parent <dataset> resource is used for children <datasetFragment> resources.

##### 7.4.Z.2.1	Create

Originator:

The <datasetFragment> resource shall not be Created via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order:

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

##### 7.4.Z.2.2	Retrieve

Originator:

Same as the generic procedures in clause 7.2.2.1.

Receiver:

Same as the generic procedures in clause 7.2.2.2.

##### 7.4.Z.2.3	Update

Originator:

The <contentInstance> resource shall not be Updated via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order:

- "Create an unsuccessful Response primitive" with the Response Status Code indicating "OPERATION_NOT_ALLOWED" error.

- "Send the Response primitive".

##### 7.4.Z.2.4	Delete

Originator:

Same as the generic procedures in clause 7.2.2.1.

Receiver:

Same as the generic procedures in clause 7.2.2.2.

### ********** End of change 2 **********

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Need to define this enum data type

MIME type should cover CSV, TSV…

Needed?

MIME type should cover CSV, TSV…