## Slide 1
Issues from oneM2M Interop
Andreas Kraft – Deutsche Telekom
Bob Flynn – Exacta GSS
Miguel Angel Reina Ortega - ETSI
1

## Slide 2
Summary
During the oneM2M Interop event #8, several issues have been identified
Issue#1 – Semantics: query parameters
Issue#2 – Semantic query result
Issue#3 – Data content size
Issue#4 – From parameter
Issue#5 – Persistent http connections
For discussion:
  Python Unit tests
  Test specs Release 1
  Test specs coverage

## Slide 3
Issue#1
Semantics: query parameters
Not clearly specified the usage of query parameters for semantic query and semantic discovery
Need of validation of parameters for semantic requests
An issue already raised:
https://git.onem2m.org/issues/issues/-/issues/158

## Slide 4
Issue#2
Semantic query result
Semantic query and query result not fully in sync
  TS-0001 -8.1.2 – Reference to TR-0007 should be replaced by TS-0034
  Can the Number of semanticFilter elements for semantic query be more than 1? What should be the result? Options:
    multiple results to be combined into one string
    changing queryResult to a list of strings
    change semanticFilter from 0..n to 0..1

## Slide 5
Issue#3
Data content size
Data content size (i.e. contentInstance/content) may differ from one implementation to another
It can depend on implementation, CPU architecture:
What’s the size of?
  con = “¡Hola España!” -> 13 bytes/26 bytes/????
  strlen != sizeof

## Slide 6
Issue#4
From parameter
Implementations that use “X-M2M-Origin:” for fresh registration
  Correct use is that it SHALL NOT be present
Although it seems that specs are ok, can/should we add something else to clarify more?
Procedure for AE-ID-Stem assigned by the receiver CSE (when From parameter is not present) seems to be incomplete
  Registration through IN-CSE does not seem to be appropriate

## Slide 7
Issue#5
Persistent http connections
Implementations using non-persistent connections (which is allowed) but created some issues
Non-persistent connections seems to be appropriate for constrained devices. Should TS-0009 include anything about persistent/non-persistent connections?

## Slide 8
For discussion
Python Unit tests:
  They were very appreciated by participants
  How can we promote a more extensive use of those?
    They should not replace or be confused with conformance tests
Test specs Release 1
  Test specs Release 1 running for certification, but many fixes have been implemented for other releases and not for Release 1
  Should we state that it is a deprecated release for people to move forward to other releases (more stable, more interoperable)
Test specs coverage
  Structure of test specs (ATS modules)
  How to use it? Which implementation release are subject for each Test Specs release/module?

## Slide 9
Thank you