## Slide 1: Discussion paper for efficient delivery of public warning messages in oneM2M
Sherzod Elamanov (SyncTechno), TaeHyun Kim (SyncTechno)
SDS 60, June 2023

## Slide 2: Introduction
This discussion paper proposes solutions for enabling efficient delivery of public warning messages in oneM2M.
The issue has been introduced in the SDS-2023-0091 during SDS 59.3.
Warning issuing authority
IN-CSE
CAP*
Warning gateway AE
MN-CSE
ASN-CSE
ASN-CSE
AE
AE
AE
AE
Mca
Mcc
Mca
Mca
Mcc
Mcc
Mca
Mca
* CAP: Common Alerting Protocol
<subscription> enhancements
<localMulticastGroup>, <remoteCSE> enhancements

## Slide 3: Motivation for solutions
Warning messages should have a single “entry point” to the oneM2M system, forwarded to other CSEs using Mcc reference point, and finally distributed to all AEs that are interested in receiving the warning messages.
Warning messages need to be delivered to AEs using «one-to-many» delivery approach (e.g. multicast)
Optionally, AEs may request to receive warning message only if the warning message targets the geographical area where the AE is located.

## Slide 4: Solutions summary
Mca reference point:
  <subscription> notification targeting multiple recipients.
  Repeated sending of notifications to multiple recipients.
  Location-based eventNotificationCriteria of <subscription>
Mcc reference point:
  MQTT multicast type in <localMulticastGroup> (in addition to IP multicast and 3GPP MBMS)

## Slide 5: Mca reference point enhancements

## Slide 6: <subscription> notification targeting multiple recipients (1/3)
Problem statement:
  Currently, the <subscription> notifications target one reciever AE only.
  In Public Warning Service scenario, the <subscription> notifications need to be consumed be multiple AEs and the notifications need to be delivered as quickly as possible.
  To enable multiple recipient AEs for <subscription> notifications, the following needs to resolved:
    What binding protocols can be used?
    What to do with responses from multiple recipients?

## Slide 7: <subscription> notification targeting multiple recipients (2/3)
Proposed enhancements:
  New multipleRecipients attribute for <subscription>. Indicates that each notification URI is consumed by more than one recipient.
  If multipleRecipients is TRUE, restrict the notificationURI to MQTT URIs only.
  If multipleRecipients is TRUE, AEs shall not respond for these notifications.
CSE
AE 3
AE 2
AE 1
MQTT
Server
<CSEBase>
[devicePWSCenter]
notificationURI
PUBLISH /oneM2M/pws
[disseminator]
<subscription>
mqtt://10.154.1.15/oneM2M/pws
SUBSCRIBED TO: /oneM2M/pws
SUBSCRIBED TO: /oneM2M/pws
SUBSCRIBED TO: /oneM2M/pws
multipleRecipients
TRUE

## Slide 8: <subscription> notification targeting multiple recipients (3/3)
Why restrict to MQTT?
  oneM2M currently does not support multicast messages for other protocol bindings
  To add other protocols, a thorough analysis of solutions is needed (e.g. protocol stack, security)

## Slide 9: Repeated sending of notifications to multiple recipients
Problem statement:
  With multipleRecipients is TRUE, recipient AEs do not respond for received notifications => CSE has no knowledge if all AEs received or not
  Some AEs might subscribe for the MQTT topic right after the first notification is sent out, thus they will miss it. This is critical for PWS scenario.
Proposed enhancements:
  If multipleRecipients is TRUE, <subscription> can be configured to send the same notification multiple times.
  The frequency and number of repetitions can be configured in the new repeatedNotifications attribute of <subscription>.

## Slide 10: Location-based eventNotificationCriteria of <subscription> (1/2)
Problem statement:
  Public warning messages are usually sent out to specific region.
  Without this feature, AEs needs to perform device-based geofencing.
  With this feature, AE delegates geo-fencing functionality to CSE (i.e. network-based geofencing)
Proposed enhancements:
  New condition in eventNotificationCriteria: locationFilter. Send a notification if AE’s geographical location is within the notification target area
Sub-attributes of locationFilter | Data type | Description
areaAttibute | xs:NCName | Name of the area attribute in the subscribed-to-resource. This attribute is used to evaluate that AE location is within the area indicated in this attribute. Data type of the referenced area attribute is GeoJSON (Polygon, MultiPolygon)
AEID | m2m:ID | Resource ID of the AE resource to get its location attribute

## Slide 11: Location-based eventNotificationCriteria of <subscription> (2/2)
<CSEBase>
[devicePWSCenter]
eventNotifCrit
[disseminator]
<subscription>
0
1
2
3
1
2
3
<AE>
resourceID
ae1
location
<AE>
resourceID
ae2
location
locationFilter
areaAttribute
AEID
area
eventNotifCrit
<subscription>
locationFilter
areaAttribute
AEID
ae2
ae1
Type: Polygon
Coordinates: [(0,0), (0,2), (2, 0), (2,2)]
area
AE 1
AE 2
area
Latitude
Longitude
When [disseminator] resource is updated, the CSE evaluates weather AE1 and AE2 are within the notification target area.
In this example, notification shall be issued to AE 1 as it is located inside of the notification target area.
Target area
Type: Point
Coordinates: (3,2)
Type: Point
Coordinates: (1,1)

## Slide 12: Comparing MQTT-based mass notification vs location-based notification
 | MQTT-based | Location-based
Recipient | Multiple AEs | Single AE
Geo-fencing | Device-based | Network-based
When to be used | Warning message need to be received as quick as possible Network-based geo-fencing is not possible | MQTT protocol binding is not supported Device-based geo-fencing is not possible
Note, that an AE can have both type of subscriptions at the same time.

## Slide 13: Mcc reference point enhancements

## Slide 14: MQTT multicast type in <localMulticastGroup> (1/2)
Background:
  <localMulticastGroup> is used to fan-out group operations to members of a <group> resource, when these resource are hosted in other CSEs.
  <localMulitcastGroup> can only be created by a Group Hosting CSE.
  Fan-out operations are performed by multicast: IP multicast or MBMS (based on the <remoteCSE> multicastCapability)
Problem statement:
  IP multicast and MBMS are not possible to implement in every network. A simpler way is needed.
    IP multicast requires all nodes (e.g. routers, firewalls) in the network to support multicast protocols.
    MBMS can only be applied to 3GPP networks.

## Slide 15: MQTT multicast type in <localMulticastGroup> (2/2)
Proposed enhancements:
  Add MQTT as the third option for multicast type of <localMulticastGroup>
Resource type changes:
  <remoteCSE>
    New «MQTT» option for multicastCapability
  <localMulticastGroup>
    New mqttURI attribute
    Change multiplicity of multicastAddress attribute from 1 to 0..1
    Note: the multicastAddress attribute can not be reused because of data type mismatch.