| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #39.1 |
| Source:* | ETSI |
| Date:* | 2019-11-03 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | New TPs for registration release 3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.0.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: TDE-2019-0041-TS-0018_New_TPs_for_registration_R2 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

New TPs for registration for release 2 in order to complete AE registration when AE-ID-Stem is/is starting by “S”. As background:

- Initial registration (case A), AE-ID-Stem = “S”, covered by:

  - MN – TP/CSE/REG/CRE/005, TP/CSE/REG/CRE/006, TP/CSE/REG/CRE/007

  - IN – TP/CSE/REG/CRE/0x0 (handling of CREATE AE with From “S”)

- Re-registration (case B), AE-ID-Stem = “S*”, covered by:

  - MN - TP/CSE/REG/CRE/008, TP/CSE/REG/CRE/010

  - IN - TP/CSE/REG/CRE/009,

- Initial registration (case B), AE-ID-Stem = “S*”, covered by:

  - MN - TP/CSE/REG/CRE/003, TP/CSE/REG/CRE/0x2 (handling of response from IN-CSE)

  - IN - TP/CSE/REG/CRE/001_SAE, TP/CSE/REG/CRE/002_SAE, TP/CSE/REG/CRE/0x1 (handling of CREATE AEANNC)

- Deregistration of AE, AE-ID-Stem =”S*”, covered by:

  - MN - TP/CSE/REG/DEL/006 (sending UPDATE AEANNC), TP/CSE/REG/DEL/007 (handling of response from IN-CSE)

  - IN - TP/ CSE/REG/DEL/005

- R01 – A small correction about the link attribute and small typo about formatting.

----------------------- Start of change 1 -----------------------

TP/oneM2M/CSE/REG/CRE/0x0

| TP Id | TP/oneM2M/CSE/REG/CRE/0x0 |
| --- | --- |
| Test objective | Check that the IUT accepts a create request of <AE> resource with attributes multiplicity equals to 1 and asking AE_ID_Stem by indicating AE_ID_Stem starting with character ‘S’. |
| Reference | TS-0001 [1], clause 10.1.1.2.2 case a, TS-0004 [2], clause 7.4.5.2.1 |
| Config Id | CF01 |
| Parent Release | Release 2 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing From set to ‘S’ and Resource Type set to 2(AE) and Content containing AE resource representation } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing AE resource containing ResourceID attribute set to S-AE-ID-STEM } | IUT ( AE |
| NOTE: S-AE-ID-STEM = Value starting with “S” assigned by IN-CSE |

TP/oneM2M/CSE/REG/CRE/0x1

| TP Id | TP/oneM2M/CSE/REG/CRE/0x1 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE registration (preprovisioned S-AE-ID-STEM provided by AE), communication between MN-CSE and IN-CSE |
| Reference | TS-0001 [1], clause 10.1.1.2.2 – case a, step 5-8 |
| Config Id | CF03 |
| Parent Release | Release 2 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from the CSE containing Resource Type set to 10002 (AEAnnc) and From set to SP-RELATIVE-AE-ID and Content containing AEAnnc resource containing link attribute set to SP-RELATIVE-AE-ID and labels attribute indicating ‘Credential-ID:None’ } | IUT( MN-CSE |
|  | then { the IUT creates the AEANNC_RESOURCE_ADDRESS resource and the IUT sends a valid Response to CSE containing Response Status Code set to 2001 (CREATED) and Content containing AEAnnc resource containing link attribute set to SP-RELATIVE-AE-ID* and labels indicating ‘Credential-ID:None’ } | IUT ( MN-CSE |
| NOTE: SP-RELATIVE-AE-ID = {SP-RELATIVE-CSE-ID}/{AE-ID-STEM} SP-RELATIVE-AE-ID* = {SP-RELATIVE-CSE-ID}/{S-AE-ID-STEM} AE-ID-STEM = “S” S-AE-ID-STEM = Valid AE-ID-Stem starting with “S” |

TP/oneM2M/CSE/REG/CRE/0x2

| TP Id | TP/oneM2M/CSE/REG/CRE/0x2 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE re-registration (allowed M2M-SP-assigned AE-ID, S-AE-ID-STEM provided by AE), transfer response to the AE |
| Reference | TS-0001 [1], clause 10.1.1.2.2 – case b, step 8 |
| Config Id | CF02 |
| Parent Release | Release 2 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the MN-CSE and the AE having sent a registration containing From set to S-AE-ID-STEM and the IUT having sent a valid AEAnnc CREATE Request to IN-CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Response from IN-CSE containing Response Status Code set to 2001 (CREATED) and Content containing AEAnnc resource containing link attribute set to SP-RELATIVE-AE-ID and labels attribute indicating ‘Credential-ID:None’ } | IUT ( IN-CSE |
|  | then { the IUT sends a valid Response to the AE containing Response Status Code set to 2001 (CREATED) and Content containing AE resource containing AE-ID attribute set to S-AE-ID-STEM } | IUT ( AE |
| NOTE: SP-RELATIVE-AE-ID = {SP-RELATIVE-CSE-ID}/{S-AE-ID-STEM } S-AE-ID-STEM = Value starting with “S” assigned by IN-CSE |

TP/oneM2M/CSE/REG/DEL/005

| TP Id | TP/oneM2M/CSE/REG/DEL/005 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE de-registration when AE-ID is starting with “S” |
| Reference | TS-0001 [1], clause 10.1.4.2.2 |
| Config Id | CF01 |
| Parent Release | Release 2 |
| PICS Selection | PICS_IN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing From set to “S” and the AE having privileges to perform DELETE operation on the resource AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to AE_RESOURCE_ADDRESS and From set to AE_ID and no Content } | IUT  AE |
|  | then { the IUT deletes the AE_RESOURCE_ADDRESS resource and the IUT sends a valid Response containing Response Status Code set to 2002 (DELETED) } | IUT  AE |

TP/oneM2M/CSE/REG/DEL/006

| TP Id | TP/oneM2M/CSE/REG/DEL/006 |
| --- | --- |
| Test objective | Check that the IUT accepts an AE de-registration when AE-ID is starting with “S” |
| Reference | TS-0001 [1], clause 10.1.1.2.2 |
| Config Id | CF02 |
| Parent Release | Release 2 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing From set to “S” and the AE having privileges to perform DELETE operation on the resource AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DELETE Request from AE containing To set to AE_RESOURCE_ADDRESS and From set to AE_ID and no Content } | IUT  AE |
|  | then { the IUT sends a valid UPDATE Request containing Content containing AEANNC_RESOURCE_ADDRESS resource containing link attribute set to “INACTIVE” } | IUT  IN-CSE |

TP/oneM2M/CSE/REG/DEL/007

| TP Id | TP/oneM2M/CSE/REG/DEL/007 |
| --- | --- |
| Test objective | Check that the IUT accepts the response from IN-CSE for the AE de-registration when AE-ID is starting with “S” |
| Reference | TS-0001 [1], clause 10.1.1.2.2 |
| Config Id | CF02 |
| Parent Release | Release 2 |
| PICS Selection | PICS_MN_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE containing From set to “S” and the AE having privileges to perform DELETE operation on the resource AE and the AE having sent a valid DELETE Request at AE_RESOURCE_ADDRESS resource and the IUT having sent a valid UPDATE Request to IN-CSE containing Content containing AEANNC_RESOURCE_ADDRESS resource containing link attribute set to empty } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Response from IN-CSE containing Response Status Code set to 2004 (UPDATED) } | IUT  IN-CSE |
|  | then { the IUT deletes the AE_RESOURCE_ADDRESS resource and the IUT sends a valid Response containing Response Status Code set to 2002 (DELETED) } | IUT  AE |

## ---------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?