| CHANGE REQUEST |
| --- |
| Meeting:* | TST #39.1 |
| Source:* | ETSI |
| Date:* | 2019-03-19 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | Test strategy and pixits R2 |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0019-V-2.1.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Added test strategy (change 1) and update pixit table (change 2) for Release 2.

----------------------- Start of change 1 -----------------------

## 5.6	Test strategy

This clause introduces the test strategy being used for the TTCN-3 test cases. The chosen strategy permits to have a clear structure of the code that facilitates an easy navigation throw the different test steps.

The use of the TTCN-3 MTC and PTC(s) is as depicted in the following figure:

At the start of the test case execution, the MTC is created. Then, the MTC executes the following steps:

Step 1) initialization of the master PTC

Step 2) initialization of some parameters if required for the permutation test cases

Step 3) running of the appropriate function on the master PTC. The function run on the master PTC implements a given Test Purpose. Such function follows a code structure as indicated herebelow:

  - Local Variables, declaration of local variables

  - Test Control, checking IUT capability parameters required for the proper execution of the test

  - Test Component Configuration, that initializes the given test component and other test components acting as slave PTC(s) as required by a given configuration

  - Test adapter configuration, that configures the test adapter throw the acPort if required

  - Preamble, that implements the necessary test steps as described in the Initial conditions of a Test Purpose. It may also implement additional test steps which are required for the correct execution of the test

  - Test body, that implements the test steps as described in the Expected behaviour of a Test Purpose.

  - Postamble, that implements the necessary test steps to bring the IUT back to the initial state

  - Tear down, that finalizes properly the TTCN-3 ports used by the different test components depending on the configuration

While master PTC follows the test structure described above, slave PTC(s) run only certain prodecures, usually one by one, as mandated by the master PTC.

A procedure usually implements a oneM2M request-response exchange between a given PTC and the IUT, although it can implement any other specific action (sending or reception of a message, several request-response exchanges, etc…).

Step 4) checking of some parameters if required for the permutation test cases

This test strategy may slightly vary for certain cases where specific requirements need to be fulfilled.

## ----------------------- End of change 1 -----------------------

----------------------- Start of change 2 -----------------------

## 7.3	IXIT

The following parameters are used by the oneM2M ATS for the correct execution of the test cases.

Table 7.3-1: oneM2M ATS IXITs

| GROUP | IXIT NAME | DESCRIPTION | DEFAULT VALUE |
| --- | --- | --- | --- |
| IutParameters | PX_IN_CSE | MN-CSE | true |
|  | PX_MN_CSE | IN-CSE | false |
|  | PX_ASN_CSE | ASN-CSE | false |
|  | PX_SUT_ADDRESS | SUT address | "127.0.0.1:8080" |
|  | PX_UT_IMPLEMENTED | Upper Tester implemented | false |
|  | PX_CSE_NAME | IUT CSE Name | "cseName" |
|  | PX_CSE_ID | IUT CSE-ID with SP-relative-CSE-ID format (relative) according to one M2M TS-0001 [1], table 7.2-1 | "/cseId" |
|  | PX_CSE_RESOURCE_ID | IUT CSE resource ID with Unstructured-CSE-relative-Resource-ID (relative) format according to one M2M TS-0001 [1], table 7.2-1 | "cseResourceId" |
|  | PX_SP_ID | IUT M2M-SP-ID with M2M-SP-ID format (absolute) according to one M2M TS-0001 [1], table 7.2-1 Unstructured-CSE-relative -Resource-ID | "//om2m.org" |
|  | PX_SUPER_AE_ID | AE-ID with privileges to CREATE at the IUT CSEBase with AE-ID-Stem format (relative) according to one M2M TS-0001 [1], table 7.2-1 | "admin:admin" |
|  | PX_SUPER_CSE_ID | CSE-ID with privileges to CREATE at the IUT CSEBase with SP-relative-CSE-ID format (relative) according to one M2M TS-0001 [1], table 7.2-1 | "/admin:admin" |
|  | PX_ALLOWED_C_AE_IDS |  | {"C-AllowedAeId"} |
|  | PX_NOT_ALLOWED_C_AE_IDS |  | {"C-NotAllowedAeId"} |
|  | PX_ALLOWED_S_AE_IDS |  | {"S-AllowedAeId"} |
|  | PX_NOT_ALLOWED_S_AE_IDS |  | {"S-NotAllowedAeId"} |
|  | PX_NOT_ALLOWED_APP_ID |  | "NotAllowedAppId" |
|  | PX_ADDRESSING_METHOD | Addressing method | e_hierarchical |
|  | PX_PRIMITIVE_SCOPE | Primitive scope | e_cseRelative |
|  | PX_SERIALIZATION | Serialization | "XML" |
|  | PX_PROTOCOL_BINDING_CSE1 | Protocol binding for CSE1 (mcc) | "HTTP" |
|  | PX_PROTOCOL_BINDING_AE1 | Protocol binding for AE1 (mca) | "HTTP" |
|  | PX_PROTOCOL_BINDING_AE2 | Protocol binding for AE2 (mca) | "HTTP" |
|  | PX_XML_NAMESPACE | XML Namespace | "m2m=""http://www.onem2m.org/xml/protocols""" |
|  | PX_ACOR | AccessControlOriginators | {"all"} |
|  | PX_TCONFIG_IUT | Time to configure IUT after a requested action | 10.0 |
| TesterParameters | PX_AE1_ADDRESS | AE1 component address | "127.0.0.1:3141" |
|  | PX_AE2_ADDRESS | AE2 component address | "127.0.0.1:3142" |
|  | PX_CSE1_ADDRESS | CSE1 component address | "127.0.0.1:4141" |
|  | PX_CSE1_NAME | Test System CSE1 Name | "CSE1_NAME" |
|  | PX_CSE1_ID | Test System CSE1-ID with SP-relative-CSE-ID format (relative) according to oneM2M TS-0001 [1], table 7.2-1 | "/CSE1_ID" |
|  | PX_CSE1_RESOURCE_ID | Test System CSE1 resource ID with Unstructured-CSE-relative-Resource-ID (relative) format according to one M2M TS-0001 [1], table 7.2-1 | "CSE1_RESOURCE_ID" |
|  | PX_CSE1_SRT | CSE1 Supported resource type | {int1, int2, int3, int16} |
|  | PX_SP1_ID | Test System M2M-SP1-ID with M2M-SP-ID format (absolute) according to one M2M TS-0001 [1], table 7.2-1 Unstructured-CSE-relative -Resource-ID | "//onem2m.org" |
|  | PX_AE1_ID_STEM | Test System AE1-ID with AE-ID-Stem format (relative) according to one M2M TS-0001 [1], table 7.2-1 | "" |
|  | PX_AE2_ID_STEM | Test System AE2-ID with AE-ID-Stem format (relative) according to one M2M TS-0001 [1], table 7.2-1 | "" |
|  | PX_APP_ID | Test System APP-ID with App-ID format according to one M2M TS-0001 [1], table 7.2-1 | "NMyAppId" |
| ExecutionParameters | PX_RESOURCES_TO_BE_DELETED | (For debugging purposes) | {"MyAe", "MyAccessControlPolicyResource", "SubscriptionVerificationAcp", "MyAcp", "MyRemoteCSEResource"} |
|  | PX_RUN_POSTAMBLE | (For debugging purposes) | true |

## ----------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?