| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 39.2 |
| Source:* | InSong Lee, KETI, insong@keit.re.kr Seongyoon Kim, KETI, seongyoon.Kim@keti.re.kr |
| Date:* | 2019-04-24 |
| Reason for Change/s:* | Adding re-targeting feature and optional attribute for polingChannel and flexContainer |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0017 v2.0.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

During the TDE #39 meeting, below resources has raised to follow Release 2 specification.

- pollingChannel

- flexContainer

- retargeting

- nonblocking

- group

Change 1: A5.4 Communication Mode Statement changed into Request Handling Statement. It changed to in line with TS-0031. And Re-targeting is added as a new feature.

Change 2: 3GPP features removed, since it will only be included in the Rel-3

New text 1: Adding optional attribute for pollingChannel.

New text 2: Adding optional attribute for flexContainer.

Please refer to the below contents for more details.

### -----------------------Start of change 1-------------------------------------------

## A.5.4	Request Handling Statement

This clause presents request handling features defined in oneM2M TS-0001[1]. Table A.5.4-1 can be used to check whether the IUT support response types listed as below.

Table A.5.4-1: Request Handling Features Supported by CSEs

| Item | Feature | Mnemonic | Reference | Condition | Support |
| --- | --- | --- | --- | --- | --- |
| 1 | Blocking |  | [1] 8.2.1 | C.1 | O Yes O No |
| 2 | Non-Blocking | Synchronous |  | [1] 8.2.2.2 | C.1 | O Yes O No |
|  |  | Asynchronous |  | [1] 8.2.2.3 | C.1 | O Yes O No |
| 3 | Re-targeting |  | [1] 9.3.2.3 | C.1 | O Yes O No |
| C.1: Mandatory IF the IUT is declaimed to be a ASN-CSE OR MN-CSE OR IN-CSE when acting as a Receiver. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of new text 1-------------------------------------------

Table A.5.7-xx: Optional Attributes of <pollingChannel> resource

| Item | Resource Type | Reference | Condition | Support |
| --- | --- | --- | --- | --- |
| 1 | labels | [1] 9.6.22 | C.1 | O Yes O No |
| C.1: The IUT shall be explicitly declared to one or more than one of the above listed resource types per testing session. |

### -----------------------End of new text 1---------------------------------------------

### -----------------------Start of new text 2-------------------------------------------

- Table A.5.7-xx: Optional Attributes of <flexContainer> resource

| Item | Resource Type | Reference | Condition | Support |
| --- | --- | --- | --- | --- |
| 1 | expirationTime | [1] 9.6.35 | C.1 | O Yes O No |
| 2 | accessControlPolicyIDs | [1] 9.6.35 | C.1 | O Yes O No |
| 3 | labels | [1] 9.6.35 | C.1 | O Yes O No |
| 4 | creationTime | [1] 9.6.35 | C.1 | O Yes O No |
| 5 | lastModifiedTime | [1] 9.6.35 | C.1 | O Yes O No |
| 6 | announceTo | [1] 9.6.35 | C.1 | O Yes O No |
| 7 | announcedAttribute | [1] 9.6.35 | C.1 | O Yes O No |
| 8 | dynamicAuthorizationConsultationIDs | [1] 9.6.35 | C.1 | O Yes O No |
| 9 | creator | [1] 9.6.35 | C.1 | O Yes O No |
| 10 | ontologyRef | [1] 9.6.35 | C.1 | O Yes O No |
| C.1: The IUT shall be explicitly declared to one or more than one of the above listed resource types per testing session. |

### -----------------------End of new text 2---------------------------------------------