| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #40.1 |
| Source:* | ETSI |
| Date:* | 2019-06-04 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | TP changes for DAU release 3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.2.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Changes to TPs for DAU (change 1) + CF06 defined (change 2)

----------------------- Start of change 1 -----------------------

| TP Id | TP/oneM2M/CSE/DAU//NOT/001 |
| --- | --- |
| Test objective | Check that the IUT starts the Dynamic Authorization for an incoming request and sends a Notify Request including all mandatory fields. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered an AE and the AE having privileges to perform operations on a resource and the IUT having privileges to send request towards a DAS on DAS_ADDRESS the IUT having received a request from an AE and the targeted resource has a dynamicAuthorizationConsultationID attribute and corresponding <dynamicAuthorizationConsultation> not set to FALSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT, after receiving an request from the AE, is triggered to perform dynamic authorization on that incoming request and to send a valid NOTIFY Request containing To set to DAS_ADDRESS (DAS associated with the resource targeted by the received requestt and From set to IUT address and Notification data containing securityInfo indicating Dynamic Authorization Request } | NA |
|  | then { the IUT sends a valid NOTIFY Request to DAS containing To set to DAS_ADDRESS and From set to CSE_ID and Notification data containing securityInfo containing securityInfoType set to 1 (Dynamic Authorization Request) and originator set to AE_ID and targetedResourceType set to resource targeted by the received request and operation set to type of operation targeted by the received request. } | DAS ( IUT |

| TP Id | TP/oneM2M/CSE/DAU//NOT/002 |
| --- | --- |
| Test objective | Check that the IUT starts the Dynamic Authorization for an incoming request and sends a Notify Request including all mandatory fields and one ore more optional fields. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered an AE and the AE having privileges to perform operations on a resource and the IUT having privileges to send request towards a DAS on DAS_ADDRESS the IUT having received a request from an AE and the targeted resource has a dynamicAuthorizationConsultationID attribute and corresponding <dynamicAuthorizationConsultation> not set to FALSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT, after receiving an request from the AE, is triggered to perform dynamic authorization on that incoming request and to send a valid NOTIFY Request containing To set to DAS_ADDRESS (DAS associated with the resource targeted by the received requestt and From set to IUT address and Notification data containing securityInfo indicating Dynamic Authorization Request } | NA |
|  | then { the IUT sends a valid NOTIFY Request to DAS containing To set to DAS_ADDRESS and From set to CSE_ID and Notification data containing securityInfo containing securityInfoType set to 1 (Dynamic Authorization Request) and originator set to AE_ID and targetedResourceType set to resource targeted by the received request and operation set to type of operation targeted by the received request and optionally containing originatorIP set to AE_IP originatorLocation set to location of originator of the received request originatorRole set to role of originator of the received request requestTimestamp set to time of receipt of request targetedResourceID set to identifier of the targeted resource proposedPrivilegesLifetime set to time duration of requested privileges rolesFromACPs set to list of roles of requested resource tokenIdDs set to list of token identifiers from the received request authorSignIndicator set to value specified by the received request. } | DAS ( IUT |

| TP Id | TP/oneM2M/CSE/DAU//NOT/005 |
| --- | --- |
| Test objective | Check that the IUT correctly processes a Notify response received in response to a Notify request that started Dynamic Authorization. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered an AE and the AE having privileges to perform operations on a resource and the IUT having sent a NOTIFY request to a DAS requesting Dynamic Authorization in reaction to a request received from the AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response containing Notification data containing securityInfo containing securityInfoType set to 2 (Dynamic Authorization Response) } | DAS ( IUT |
|  | then { the IUT accepts the request received from the AE. } | AE ( IUT |

| TP Id | TP/oneM2M/CSE/DAU//NOT/006 |
| --- | --- |
| Test objective | Check that the IUT correctly processes a Notify response including a dynamicACPInfo element received in response to a Notify request that started Dynamic Authorization. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered an AE and the AE having privileges to perform operations on a resource and the IUT having sent a NOTIFY request to a DAS requesting Dynamic Authorization in reaction to a request received from the AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response containing Notification data containing securityInfo containing securityInfoType set to 2 (Dynamic Authorization Response) and dynAuthDasResponse containing dynamicACPInfo } | DAS ( IUT |
|  | then { the IUT creates <accesscontrolPolicy> child resource and configures the privileges, expirationTime and selfPrivileges attributes based on the data received in the dynamicACPInfo, and the IUT accepts the request received from the AE. } | AE ( IUT |

| TP Id | TP/oneM2M/CSE/DAU//NOT/007 |
| --- | --- |
| Test objective | Check that the IUT correctly processes a Notify response including a tokens element received in response to a Notify request that started Dynamic Authorization. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered an AE and the AE having privileges to perform operations on a resource and the IUT having sent a NOTIFY request to a DAS requesting Dynamic Authorization in reaction to a request received from the AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response containing Notification data containing tokens } | DAS ( IUT |
|  | then { the IUT accepts the request received from the AE. } | AE ( IUT |

| TP Id | TP/oneM2M/CSE/DAU//NOT/008 |
| --- | --- |
| Test objective | Check that the IUT correctly processes a Notify response received in response to a Notify request that started Dynamic Authorization. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered an AE and the AE having privileges to perform operations on a resource and the IUT having sent a NOTIFY request to a DAS requesting Dynamic Authorization in reaction to a request received from the AE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response NOT containing Notification data containing securityInfo containing securityInfoType set to 2 (Dynamic Authorization Response) } | DAS ( IUT |
|  | then { the IUT rejects the incoming request from the AE containing Response Status Code set to "ORIGINATOR_HAS_NO_PRIVILEGE". } | AE ( IUT |

## ---------------------- End of change 1 -----------------------

----------------------- Start of change 2 -----------------------

Figure 5.1-6: Test configuration 6 (CF06)

## ---------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?