| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #41.1 |
| Source:* | ETSI STF 559 |
| Date:* | 2019-26-08 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | New TPs from TS-0028 for release 3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.2.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

TPs from TS-0028 imported, reviewed and improved for release 3.

----------------------- Start of change 1 -----------------------

#### 7.2.2.10	Security(SEC)

##### 7.2.2.10.1	Authentication

##### 7.2.2.10.1.1	ESPrim (ESP)

##### 7.2.2.10.1.1.1	NOTIFY Operation

##### TP/oneM2M/CSE/SEC/ESP/NTF/001

| TP Id | TP/oneM2M/CSE/SEC/ESP/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT sends a new ESPrimRandObject when requested |
| Reference | TS-0003 8.4.2 – step B.2C.2, TS-0004 7.5.1.2.11 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with the Originator (AE) } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY request from AE containing To set to TARGET_RECEIVER_ADDRESS and From set to AE1_ID and Content containing securityInfo object containing securityInfoType attribute set to 3 (receiverESPrimRandObject Request)} | IUT  AE1 |
|  | then { the IUT sends a valid NOTIFY Response containing To set to RECEIVER_RECEIVER_ADDRESS and From set to CSE_ID and Content containing securityInfo object containing securityInfoType attribute set to 4 (receiverESPrimRandObject Response) and esprimRandObject set to receiverESPrimRandObject } | IUT  AE1 |

TP/oneM2M/CSE/SEC/ESP/NTF/002

| TP Id | TP/oneM2M/CSE/SEC/ESP/NTF/002 |
| --- | --- |
| Test objective | Check that the IUT responds with a valid ESPrim object when it receives a request |
| Reference | TS-0003 8.4.2 – step C.9, TS-0004 7.6.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a sessionESPrimKey with the Originator (AE) } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from AE containing To set to TARGET_RECEIVER_ADDRESS and From set to AE1_ID and Content containing securityInfo object containing securityInfoType attribute set to 5 (ESPrim Object) and valid esprimObject attribute } | IUT  AE1 |
|  | then { the IUT sends a valid NOTIFY Response containing To set to RECEIVER_RECEIVER_ADDRESS and From set to CSE_ID and Response Status Code set to 2000 (OK) and Content containing securityInfo element containing securityInfoType attribute set to 5 (ESPrim Object) and valid esprimObject attribute } | IUT  AE1 |

TP/oneM2M/CSE/SEC/ESP/NTF/003

| TP Id | TP/oneM2M/CSE/SEC/ESP/NTF/003 |
| --- | --- |
| Test objective | Check that the IUT successfully detects AE impersonation in an End-to-End Security of Primitives |
| Reference | TS-0003 7.2.2 – step 4 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a sessionESPrimKey with AE1_ID } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from AE containing To set to CSE_ID and From set to a value other than AE1_ID and Content containing securityInfo element containing securityInfoType attribute set to 5 (ESPrim Object) and valid esprimObject attribute } | IUT  AE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4116 (ESPRIM_IMPERSONATION_ERROR) } | IUT  AE1 |

7.2.2.10.1.1.2	RETRIEVE Operation

TP/oneM2M/CSE/SEC/ESP/RET/001

| TP Id | TP/oneM2M/CSE/SEC/ESP/RET/001 |
| --- | --- |
| Test objective | Check that the IUT sends a valid request for e2eSecInfo attribute of the Receiver’s <remoteCSE> resource in Target CSE |
| Reference | TS-0003 8.4.2 – step B.2A, TS-0004 7.5.1.2.11 |
| Config Id | CF03 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Receiver CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a RETRIEVE Request for e2eSecInfo attribute of the Receiver’s <remoteCSE> resource at TARGET_REMOTE_ADDRESS} | NA |
|  | then { the IUT sends a valid RETRIEVE Request to Target CSE containing To set to TARGET_REMOTE_ADDRESS and From set to CSE_ID and Content containing attributeList element containing e2eSecInfo } | CSE ( IUT |

TP/oneM2M/CSE/SEC/ESP/RET/002

| TP Id | TP/oneM2M/CSE/SEC/ESP/RET/002 |
| --- | --- |
| Test objective | Check that the IUT sends a notification containing an inner “receiverESPrimRandObject request” to the Receiver if the sharedReceiverESPrimRandObject parameter is not present in the <remoteCSE> resource |
| Reference | TS-0003 8.4.2 – step B.2B |
| Config Id | CF03 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with the Originator and the <remoteCSE> resource at TARGET_REMOTE_ADDRESS contains an e2eSecInfo attribute with no sharedReceiverESPrimRandObject parameter } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_ADDRESS and From set to CSE_ID and Content containing attributeList element containing e2eSecInfo } | NA |
|  | then { the IUT sends a valid NOTIFICATION Request containing To set to TARGET_RECEIVER_ADDRESS and From set to CSE_ID and Content containing securityInfo elementobject containing securityInfoType attribute set to 3 (receiverESPrimRandObject Request)} | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESP/RET/003

| TP Id | TP/oneM2M/CSE/SEC/ESP/RET/003 |
| --- | --- |
| Test objective | Check that the IUT sends a notification containing an inner “receiverESPrimRandObject request” to the Receiver if the sharedReceiverESPrimRandObject in the <remoteCSE> resource is expired |
| Reference | TS-0003 8.4.2 – step B.2B |
| Config Id | CF03 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with the Originator and the <remoteCSE> resource at TARGET_REMOTE_ADDRESS contains an e2eSecInfo attribute with an expired sharedReceiverESPrimRandObject parameter } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_ADDRESS and From set to CSE_ID and Content containing attributeList element containing e2eSecInfo } | NA |
|  | then { the IUT sends a valid NOTIFICATION Request containing To set to TARGET_RECEIVER_ADDRESS and From set to CSE_ID and Content containing securityInfo elementobject containing securityInfoType attribute set to 3 (receiverESPrimRandObject Request) } | IUT  CSE1 |

##### 7.2.2.10.1.2	Roles (ROL)

##### 7.2.2.10.1.2.1	CREATE Operation

##### TP/oneM2M/CSE/SEC/ROL/CRE/001

| TP Id | TP/oneM2M/CSE/SEC/ROL/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT sends a CREATE <role> resource request to the Role Repository when triggered |
| Reference | TS-0003 7.4.2.2 – step 3 |
| Config Id | 3 (CSE) |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid CREATE Request containing To set to ROLE_REPOSITORY_ADDRESS (CSE1) and Resource Type set to 31 (role) and Content containing <role> resource representation } | NA |
|  | then { the IUT sends a valid CREATE Request to CSE containing To set to ROLE_REPOSITORY_ADDRESS and Resource Type set to 31 (role) and Content containing <role> resource representation } | IUT  CSE1 |

##### TP/oneM2M/CSE/SEC/ROL/CRE/002

| TP Id | TP/oneM2M/CSE/SEC/ROL/CRE/002 |
| --- | --- |
| Test objective | Check that the IUT successfully creates the <role> resource requested by the Authorization Authority |
| Reference | TS-0003 7.4.2.2 – step 4 and 5 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from CSE1 (AA) containing From set to CSE1_ID and To set to ROLE_REPOSITORY_ADDRESS and Resource Type set to 31 (role) and Content containing <role> resource representation } | IUT  CSE1 |
|  | then { the IUT creates the <role> resource the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing <role> resource representation } | IUT  CSE1 |

##### TP/oneM2M/CSE/SEC/ROL/CRE/003

| TP Id | TP/oneM2M/CSE/SEC/ROL/CRE/003 |
| --- | --- |
| Test objective | Check that the IUT sends a CREATE <token> resource request to the Token Repository when triggered |
| Reference | TS-0003 7.4.2.3 – step 2 |
| Config Id | CF03 (CSE) |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having assigned a role for the Originator } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid CREATE Request containing To set to TOKEN_REPOSITORY_ADDRESS (CSE1) and Resource Type set to 32 (token) and Content containing <token> resource representation } | NA |
|  | then { the IUT sends a valid CREATE Request to CSE containing To set to TOKEN _REPOSITORY_ADDRESS and Resource Type set to 32 (token) and Content containing <token> resource representation } | IUT  CSE1 |

##### TP/oneM2M/CSE/SEC/ROL/CRE/004

| TP Id | TP/oneM2M/CSE/SEC/ROL/CRE/004 |
| --- | --- |
| Test objective | Check that the IUT successfully creates the <token> resource requested by the Authorization Authority |
| Reference | TS-0003 7.4.2.3 – step 3 and 4 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the Authorization Authority having assigned a role for the Originator } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from CSE1 (AA) containing From set to CSE1_ID and To set to TOKEN_REPOSITORY_ADDRESS and Resource Type set to 32 (token) and Content containing <token> resource representation } | IUT  CSE1 |
|  | then { the IUT creates the <token> resource the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing <token> resource representation } | IUT  CSE1 |

##### 7.2.2.10.1.2.2	RETRIEVE Operation

##### TP/oneM2M/CSE/SEC/ROL/RET/001

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/001 |
| --- | --- |
| Test objective | Check that the IUT returns the <role> resource of the Originator |
| Reference | TS-0003 7.4.2.2 – step 8 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having assigned a role for the Originator at ROLE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE Request containing From set to CSE1_ID and To set to ROLE_RESOURCE_ADDRESS and no Content } | IUT  CSE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing valid <role> resource representation } | IUT  CSE1 |

##### TP/oneM2M/CSE/SEC/ROL/RET/002

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/002 |
| --- | --- |
| Test objective | Check that the IUT returns the <token> resource of the Originator |
| Reference | TS-0003 7.4.2.3 – step 8 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having assigned a role for the Originator and the IUT having created a token associated to the role of the Originator at TOKEN_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE Request containing From set to CSE1_ID and To set to TOKEN_RESOURCE_ADDRESS and no Content } | IUT  CSE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing valid <token> resource representation } | IUT  CSE1 |

##### TP/oneM2M/CSE/SEC/ROL/RET/003

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/003 |
| --- | --- |
| Test objective | Check that the IUT sends a <role> Retrieve request to the Role Repository after receiving a request on a resource protected by role based access control |
| Reference | TS-0003 7.4.3 – step 2 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having assigned a role for the Originator and the IUT having created a token associated to the role of the Originator and the IUT having a <container> resource at RESOURCE_TARGET_ADDRESS protected by role based access control and the IUT having granted the Originator access to the <container> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request containing From set to AE1_ID and To set to RESOURCE_TARGET_ADDRESS and Role ID parameter set to address the <role> resource assigned to the Originator } | IUT  AE1 |
|  | then { the IUT sends a valid RETRIEVE Request to CSE1 containing From set to CSE_ID and To set to Role ID and no Content } | IUT  CSE1 |

##### TP/oneM2M/CSE/SEC/ROL/RET/004

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/004 |
| --- | --- |
| Test objective | Check that the IUT sends a <token> Retrieve request to the Token Repository after receiving a request on a resource protected by role based access control |
| Reference | TS-0003 7.4.3 – step 2 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having assigned a role for the Originator and the IUT having created a token associated to the role of the Originator and the IUT having a <container> resource at RESOURCE_TARGET_ADDRESS protected by role based access control procedure and the IUT having granted the Originator access to the <container> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request containing From set to AE1_ID and To set to RESOURCE_TARGET_ADDRESS and Role ID parameter set to address the <role> resource assigned to the Originator Token ID parameter set to address the <token> resource assigned to the role of the Originator } | IUT  AE1 |
|  | then { the IUT sends a valid RETRIEVE Request to CSE1 containing From set to CSE_ID and To set to Token_ID and no Content } | IUT  CSE1 |

##### TP/oneM2M/CSE/SEC/ROL/RET/005

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/005 |
| --- | --- |
| Test objective | Check that the IUT returns the result of a requeston a resource protected by role based access control, when the appropriate credentials are provided in the request |
| Reference | TS-0003 7.4.3 – step 7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE the IUT having assigned a role for the Originator and the IUT having created a token associated to the role of the Originator and the IUT having a <container> resource at RESOURCE_TARGET_ADDRESS protected by role based access control procedure and the IUT having granted the Originator access to the <container> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request containing From set to AE1_ID and To set to RESOURCE_TARGET_ADDRESS and Role ID parameter set to address the <role> resource assigned to the Originator Token ID parameter set to address the <token> resource assigned to the role of the Originator } | IUT  AE1 |
|  | then { the IUT sends a RETRIEVE Response containing Response Status Code set to 2000 (OK) and Content containing <container> resource } | IUT  AE1 |

##### 7.2.2.10.1.2.3	UPDATE Operation

##### TP/oneM2M/CSE/SEC/ROL/UPD/001

| TP Id | TP/oneM2M/CSE/SEC/ROL/UPD/001 |
| --- | --- |
| Test objective | Check that the IUT updates the tokenLink attribute of the <role> resource after creating its associated <token> resource |
| Reference | TS-0003 7.4.2.3 – step 5 |
| Config Id | CF07 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having assigned a role for the Originator and the IUT having created a token associated to the role of the Originator at TOKEN_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Response from CSE2 (TR) containing Response Status Code set to 2001 (CREATED) and Content containing <token> resource representation } | IUT  CSE2 |
|  | then { the IUT sends a valid UPDATE Request to CSE1 (RR) containing To set to ROLE_REPOSITORY_ADDRESS and Resource Type set to 32 (token) and Content containing <token> resource representation containing tokenLink attribute set to TOKEN_RESOURCE_ADDRESS } | IUT  CSE1 |

##### 7.2.2.10.1.2.4	NOTIFY Operation

##### TP/oneM2M/CSE/SEC/ROL/NTF/001

| TP Id | TP/oneM2M/CSE/SEC/ROL/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT notifies the Originator about a token issuance associated to its role |
| Reference | TS-0003 7.4.2.3 – step 6 |
| Config Id | CF07 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having assigned a role for the Originator and the IUT having created a token associated to the role of the Originator } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Response from CSE2 (TR) containing Response Status Code set to 2001 (CREATED) and Content containing <token> resource representation } | IUT  CSE2 |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 (Originator) containing Content containing notificationEvent attribute containing representation attribute containing <token> resource representation } | IUT  CSE1 |

##### 7.2.2.10.1.4	DAS (DAS)

##### 7.2.2.10.1.4.1	NOTIFY Operation

| TP Id | TP/oneM2M/CSE/SEC/DAS/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT sends a DAS request when it receives a valid request from AE to perform operation on a resource without corresponding permissions |
| Reference | TS-0003 7.3.2.2 – step 1 & 2.3, TS-0001 11.5.2, TS-0004 6.3.5.46 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having registered DAS and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type container under the AE1 resource and the <container> resource has a dynamicAuthorizationConsultationID attribute and corresponding <dynamicAuthorizationConsultation> not set to FALSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1_ID and no Content } | IUT  AE1 |
|  | then { the IUT sends a valid NOTIFY Request to DAScontaining To set to DAS_ADDRESS and From set to AE1_ID and Content containing securityInfo containing securityInfoType set to 1 (Dynamic Authorization Request) and dynAuthDasRequest containing originator set to AE1_ID and targetedResourceType set to 3 (container) and operation set to Retrieve } | IUT  DAS |

| TP Id | TP/oneM2M/CSE/SEC/DAS/NFT/002 |
| --- | --- |
| Test objective | Check that the IUT accepts the response from the DAS processes the authorisation and sends a correct response to the AE1 originator |
| Reference | TS-0003 7.3.2.2 – step 3.2, TS-0001 11.5.2, TS-0004 6.3.5.47 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE1 and the IUT having registered DAS AE2 and the IUT having created a resource TARGET_RESOURCE_ADDRESS of type container under the AE1 resource and the AE having no privileges to perform RETRIEVE operation on the resource TARGET_RESOURCE_ADDRESS and the AE having sent a RETRIEVE request for the TARGET_RESOURCE_ADDRESS resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response from DAS containing ResponseStatusCode set to OK (2000) and Content containing securityInfo containing securityInfoType set to 2 (Dynamic Authorization Response) and dynAuthDasResponse representation } | IUT  DAS AE |
|  | then { the IUT sends a valid Response to AE1 containing ResponseStatusCode set to OK (2000) and Content containing <container> representation } | IUT  AE |

##### 7.2.2.10.1.4	ESCertKE (ESC)

##### 7.2.2.10.1.4.1	NOTIFY Operation

##### TP/oneM2M/CSE/SEC/ESC/NTF/001

| TP Id | TP/oneM2M/CSE/SEC/ESC/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT sends a notify request with ESCertKE message 1 when triggered |
| Reference | TS-0003 8.7.2.2 – step C.1.a, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF03 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered to the CSE and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Terminating End-Point’s Certificate Info & Identity } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid NOTIFY Request containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE_ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | NA |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | IUT  CSE1 |

##### TP/oneM2M/CSE/SEC/ESC/NTF/002

| TP Id | TP/oneM2M/CSE/SEC/ESC/NTF/002 |
| --- | --- |
| Test objective | Check that the IUT sends a notify response with ESCertKE message 2 when it receives a notify request with ESCertKE message 1 |
| Reference | TS-0003 8.7.2.2 – step C.1.b, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered to the CSE and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Initiating End-Point’s Certificate Info & Identity } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE1_ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Response to CSE1 containing To set to INITIATING_ENDPOINT_ADDRESS and From set to CSE_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 2 (TLS Messages: Server Hello, Certificate*, ServerKeyExchange*, CertificateRequest*, ServerHelloDone) } | IUT  CSE1 |

##### TP/oneM2M/CSE/SEC/ESC/NTF/003

| TP Id | TP/oneM2M/CSE/SEC/ESC/NTF/003 |
| --- | --- |
| Test objective | Check that the IUT sends a notify request with ESCertKE message 3 when it receives a notify response with ESCertKE message 2 |
| Reference | TS-0003 8.7.2.2 – step C.1.c, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered to the CSE and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Terminating End-Point’s Certificate Info & Identity the IUT having sent a notify request to the Terminating End-Point with ESCertKE Message 1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response from CSE1 containing To set to INITIATING_ENDPOINT_ADDRESS and From set to CSE1_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 2 (TLS Messages: Server Hello, Certificate*, ServerKeyExchange*, CertificateRequest*, ServerHelloDone) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE_ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 3 (TLS Messages: Certificate*, ClientKeyExchange, CertificateVerify*, [ChangeCipherSpec], Finished) } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESC/NTF/004

| TP Id | TP/oneM2M/CSE/SEC/ESC/NTF/004 |
| --- | --- |
| Test objective | Check that the IUT sends a notify response with ESCertKE message 4 when it receives a notify request with ESCertKE message 3 |
| Reference | TS-0003 8.7.2.2 – step C.1.d, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" the IUT having registered to the CSE and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Initiating End-Point’s Certificate Info & Identity and the IUT having sent a notify request to the Initiating End-Point with ESCertKE Message 2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE1_ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 3 (TLS Messages: Certificate*, ClientKeyExchange, CertificateVerify*, [ChangeCipherSpec], Finished) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Response to CSE containing To set to INITIATING_ENDPOINT_ADDRESS and From set to CSE_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 4 (TLS Messages: [ChangeCipherSpec], Finished) } | IUT  CSE1 |

## ---------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

i.e. applying the selected object security technology using the established parameters

i.e. applying the selected object security technology using the established parameters

?

i.e. applying the selected object security technology using the established parameters

The CSE must be somehow triggered to issue a RETRIEVE request, so maybe a new configuration should be considered (CF08?). This new configuration would be like CF03, but with CSE instead of AE as SUT.

The CSE must be somehow triggered to issue a RETRIEVE request, so maybe a new configuration should be considered (CF08?). This new configuration would be like CF03, but with CSE instead of AE as SUT. A second CSE would also be useful for this one.

Using a <remoteCSE> resource in the receiver (representing itself) as the <remoteCSE> in the middle CSE,, as there is no suitable CF for this TP)

The CSE must be somehow triggered to issue a RETRIEVE request, so maybe a new configuration should be considered (CF08?). This new configuration would be like CF03, but with CSE instead of AE as SUT. A second CSE would also be useful for this one.

Using a <remoteCSE> resource in the receiver (representing itself) as the <remoteCSE> in the middle CSE,, as there is no suitable CF for this TP)

Too generic

Maybe too generic

“The Originator may send role assignment request to the Authorization Authority. The specification about this step is however out of scope of the present document.” (TS-0003, 7.4.2.2-1)

As the role assignment request is out of scope, and the CSE must be somehow triggered to issue a CREATE request, maybe a new configuration should be considered (CF08?). This new configuration would be like CF03, but with CSE instead of AE as SUT.

Not defined (Authorization Authority CSE)

Not defined (Role Repository CSE)

The specification about this step is out of scope

The CSE must be somehow triggered to issue a CREATE request, maybe a new configuration should be considered. This new configuration would be like CF03, but with CSE instead of AE as SUT.

Already tested in TP/oneM2M/CSE/SEC/ROL/RET/001

Quite similar to TP/oneM2M/CSE/DAU//NTF/001. Should unify.

Consider new configuration (CF06?)

Quite similar to TP/oneM2M/CSE/DAU//NTF/005. Should unify.

The CSE must be somehow triggered to issue a NOTIFY request, maybe a new configuration should be considered (CF08?). This new configuration would be like CF03, but with CSE instead of AE as SUT.