| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #42 |
| Source:* | C-DOT |
| Date:* | 2019-07-22 |
| Contact:* | Poornima, C-DOT, poornima@cdot.in Prateek, C-DOT, prateekv@cdot.in Neeta, C-DOT, neeta@cdot.in |
| Reason for Change/s:* | See the introduction |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.2 |
| Clauses/Sub Clauses* | 7.2.1.4, 7.2.2.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR proposes following changes:

Following changes are done for Group AE <subscription> and notification create:

- notificationForwardingURI and groupID attribute test case added for group related subscription

- Updates in aggregatedNotification response case from AE

Following changes are done for Group CSE <subscription> and notification create:

- Missing attribute e.g. childResourceType conditions are added

- missingData conditionTag test case added

- test case added for <subscription> optional attributes

- test cases added for notificationForwardingURI and groupID attribute for group related subscription

- test added for aggregatedNotification from CSE

The notificationForwardingURI is a special case in <subscription> resource and it is associated with fanOutPoint request on a <group>.

| notificationForwardingURI | 0..1(L) | RW | The attribute shall be present only for group related subscriptions. If the subscriber intends the Group Hosting CSE to aggregate the notifications, the attribute shall be set identical to the notificationURI attribute. It shall be used by Group Hosting CSE for forwarding aggregated notifications. See clauses 10.2.7.10 and 10.2.7.11. |
| --- | --- | --- | --- |

----------------------- Start of change 1 -----------------------

#### 7.2.1.4	Subscription and Notification (SUB)

##### 7.2.1.4.1	CREATE Operation

TP/oneM2M/AE/SUB/CRE/002

| TP Id | TP/oneM2M/AE/SUB/CRE/002 |
| --- | --- |
| Test objective | Check that the IUT sends a subscription creation request with optional attribute ATTRIBUTE_NAME when it is triggered |
| Reference | TS-0001 [1], clause 10.1.1.1 and 10.2.11.2, TS-0004 [2], clause 7.2.2.1 and 7.4.9.2.1 |
| Config Id | CF03 |
| Parent Release | Release 1 |
| PICS Selection | PICS_AE. |
| Initial conditions | with { the IUT being registered and the IUT having privileges to perform CREATE operation on resource AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid CREATE Request containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 23 (subscription) and Content containing subscription resource containing notificationURI attribute and valid ATTRIBUTE_NAME attribute } | NA |
|  | then { the IUT sends a valid CREATE Request to CSE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 23 (subscription) and From set to AE_ID and Content containing subscription resource containing notificationURI attribute and valid ATTRIBUTE_NAME attribute } | CSE  IUT |

| TP Id | PICS Selection | Reference | ATTRIBUTE_NAME |
| --- | --- | --- | --- |
| TP/oneM2M/AE/SUB/CRE/002_ACPI | PICS_SUB_ACPI | TS-0001 [1], clause 9.6.8, TS-0004 [Error: Reference source not found], clause 7.4.9.1 | accessControlPolicyIDs |
| TP/oneM2M/AE/SUB/CRE/002_ENC | PICS_SUB_ENC | TS-0001 [1], clause 9.6.8, TS-0004 [Error: Reference source not found], clause 7.4.9.1 | eventNotificationCriteria |
| TP/oneM2M/AE/SUB/CRE/002_EXC | PICS_SUB_EXC | TS-0001 [1], clause 9.6.8, TS-0004 [Error: Reference source not found], clause 7.4.9.1 | expirationCounter |
|  |  | Error: Reference source not found |  |
| TP/oneM2M/AE/SUB/CRE/002_NCT | PICS_SUB_NCT | TS-0001 [1], clause 9.6.8, TS-0004 [Error: Reference source not found], clause 7.4.9.1 | notificationContentType |
| TP/oneM2M/AE/SUB/CRE/002_NEC | PICS_SUB_NEC | TS-0001 [1], clause 9.6.8, TS-0004 [Error: Reference source not found], clause 7.4.9.1 | notificationEventCat |
| TP/oneM2M/AE/SUB/CRE/002_SU | PICS_SUB_SU | TS-0001 [1], clause 9.6.8, TS-0004 [Error: Reference source not found], clause 7.4.9.1 | subscriberURI |

TP/oneM2M/AE/SUB/CRE/003

| TP Id | TP/oneM2M/AE/SUB/CRE/003 |
| --- | --- |
| Test objective | Check that the IUT sends a <group>/fopt subscription creation request with optional attributes notificationForwardingURI and groupID when it is triggered |
| Reference | TS-0001 [1], clause 9.6.8 and clause 10.2.7.10, TS-0004 [2], clause 7.4.14.2.3 |
| Config Id | CF03 |
| Parent Release | Release 1 |
| PICS Selection | PICS_AE. |
| Initial conditions | with { the IUT being registered and and the IUT having a <group> resource as TARGET_RESOURCE_ADDRESS containing members which are subscribable the IUT having privileges to perform CREATE operation on <group> members } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid CREATE Request containing To set to TARGET_RESOURCE_ADDRESS/fopt and Resource Type set to 23 (subscription) and Content containing subscription resource containing groupID, notificationURI attribute and notificationForwardingURI attribute set } | NA |
|  | then { the IUT sends a valid CREATE Request to CSE containing To set to TARGET_RESOURCE_ADDRESS/fopt and Resource Type set to 23 (subscription) and From set to AE_ID and Content containing subscription resource containing groupID, notificationURI attribute and notificationForwardingURI attribute set } | CSE  IUT |

##### 7.2.1.4.2	NOTIFY Operation

TP/oneM2M/AE/SUB/NTF/002

| TP Id | TP/oneM2M/AE/SUB/NTF/002 |
| --- | --- |
| Test objective | Check that the IUT sends a Notify Response to the hosting CSE when receiving a Notify request containing aggregated notifications |
| Reference | TS-0001 [1], clause 6.2.12, TS-0004 [2], clause 7.5.1.2 |
| Config Id | CF03 |
| Parent Release | Release 1 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT having been registered and the IUT having created subscription resource at <group>/fopt with notificationForwardingURI set and the IUT being reachable through a URL ACCESSIBLE_URL } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a NOTIFY Request from hosting CSE containing Content containing aggregatedNotification message representation } | IUT  CSE |
|  | then { the IUT sends a valid Response to the hosting CSE containing Response Status Code set to RESPONSE_STATUS_CODE } | CSE  IUT |

## -------------------------------------- End of change 1 -------------------------------------

## -------------------------------------- Start of change 2 -------------------------------------

#### 7.2.2.4	Subscription and Notification (SUB)

##### 7.2.2.4.1	CREATE Operation

TP/oneM2M/CSE/SUB/CRE/006

| TP Id | TP/oneM2M/CSE/SUB/CRE/006 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a subscription resource with the eventNotificationCriteria attribute which includes a CONDITION_TAG condition provided |
| Reference | TS-0001 [1], clause 9.6.8 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the Originator having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to subscription and To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing supscription resource containing eventNotificationCriteria attribute containing valid CONDITION_TAG condition } | IUT  AE |
|  | then { the IUT creates the subscription resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT  AE |

| TP Id | Reference | CONDITION_TAG |
| --- | --- | --- |
| TP/oneM2M/CSE/SUB/CRE/006_CRB | TS-0001 [Error: Reference source not found], clause 9.6.8 | createdBefore |
| TP/oneM2M/CSE/SUB/CRE/006_CRA | TS-0001 [Error: Reference source not found], clause 9.6.8 | createdAfter |
| TP/oneM2M/CSE/SUB/CRE/006_MS | TS-0001 [Error: Reference source not found], clause 9.6.8 | modifiedSince |
| TP/oneM2M/CSE/SUB/CRE/006_US | TS-0001 [Error: Reference source not found], clause 9.6.8 | unmodifiedSince |
| TP/oneM2M/CSE/SUB/CRE/006_STS | TS-0001 [Error: Reference source not found], clause 9.6.8 | stateTagSmaller |
| TP/oneM2M/CSE/SUB/CRE/006_STB | TS-0001 [Error: Reference source not found], clause 9.6.8 | stateTagBigger |
| TP/oneM2M/CSE/SUB/CRE/006_EXB | TS-0001 [Error: Reference source not found], clause 9.6.8 | expireBefore |
| TP/oneM2M/CSE/SUB/CRE/006_EXA | TS-0001 [Error: Reference source not found], clause 9.6.8 | expireAfter |
| TP/oneM2M/CSE/SUB/CRE/006_SZA | TS-0001 [Error: Reference source not found], clause 9.6.8 | sizeAbove |
| TP/oneM2M/CSE/SUB/CRE/006_SZB | TS-0001 [Error: Reference source not found], clause 9.6.8 | sizeBelow |
| TP/oneM2M/CSE/SUB/CRE/006_ET | TS-0001 [Error: Reference source not found], clause 9.6.8 | eventType |
| TP/oneM2M/CSE/SUB/CRE/006_OM | TS-0001 [Error: Reference source not found], clause 9.6.8 | operationMonitor |
| TP/oneM2M/CSE/SUB/CRE/006_ATR | TS-0001 [Error: Reference source not found], clause 9.6.8 | attribute |
| TP/oneM2M/CSE/SUB/CRE/006_CRT | TS-0001 [Error: Reference source not found], clause 9.6.8 | childResourceType |

TP/oneM2M/CSE/SUB/CRE/007

| TP Id | TP/oneM2M/CSE/SUB/CRE/007 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a subscription resource with the eventNotificationCriteria attribute which includes a missingData condition provided |
| Reference | TS-0001 [1], clause 9.6.8, 9.6.36 |
| Config Id | CF01 |
| Parent Release | Release 2 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a TARGET_RESOURCE_ADDRESS of type <timeSeries> and the Originator having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to subscription and To set to TARGET_RESOURCE_ADDRESS and From set to AE-ID and Content containing supscription resource containing eventNotificationCriteria attribute containing valid missingData condition } | IUT  AE |
|  | then { the IUT creates the subscription resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT  AE |

TP/oneM2M/CSE/SUB/CRE/009

| TP Id | TP/oneM2M/CSE/SUB/CRE/009 |
| --- | --- |
| Test objective | Check that the IUT accepts the creation of a subscription resource with the optional attributes notificationForwardingURI and groupID provided |
| Reference | TS-0001 [1], clause 9.6.8 and clause 10.2.7.10, TS-0004 [2], clause 7.4.14.2.3 |
| Config Id | CF01 |
| Parent Release | Release 1 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a group resource as TARGET_RESOURCE_ADDRESS containing members which are subscribable and the Originator having privileges to perform CREATE operation on <group> members } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing Resource Type set to subscription and To set to TARGET_RESOURCE_ADDRESS/fopt and From set to AE-ID and Content containing supscription resource containing groupID, notificationURI attribute, and notificationForwardingURI attribute set } | IUT  AE |
|  | then { the IUT creates the subscription resource on the <group> members containing groupID, notificationURI attribute and notificationForwardingURI attribute set identical to notificationURI and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT  AE |

-------------------------------------- End of change 2 -------------------------------------

## -------------------------------------- Start of change 3 -------------------------------------

##### 7.2.2.4.4	NOTIFY Operation

TP/oneM2M/CSE/SUB/NTF/009

| TP Id | TP/oneM2M/CSE/SUB/NTF/009 |
| --- | --- |
| Test objective | Check that the IUT sends an aggregatedNotification to the AE according to URI provided in notificationForwardingURI attribute when an event occurs on <group> resource with its members having group related subscriptions. |
| Reference | TS-0001 [1], clause 9.6.8 and clause 10.2.7.11, TS-0004 [2], clause 7.5.1.2.6 |
| Config Id | CF02 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and and the IUT having a <group> resource with members allowing the AE to perform required operation and <subscription> created on these members with notificationForwardingURI attribute set identical to notificationURI. } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a single notifications containing notificationForwardingURI, it forms an aggregatedNotification } | NA |
|  | then { the IUT sends the Notify request containing aggregatedNotification message representation to the AE } | IUT  AE |

## -------------------------------------- End of change 3 -------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?