| CHANGE REQUEST |
| --- |
| Meeting ID:* | TDE 42 |
| Source:* | InSong Lee, KETI, insong@keti.re.kr SungChan Choi, KETI, csc@keti.re.kr |
| Date:* | 2019-09-23 |
| Reason for Change/s:* | Remove the not using attributes Adding description column |
| CR against: Release* | <Release> only ONE Release shall be indicated |
| CR against: WI* | Active WI-0078 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0051 V0.5.1 |
| Clauses * | 5.2.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

If this is  a correction, and the change applies to previous releases, a separate “mirror CR” should be posted at the same time as this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made e.g. a change impacting 5 tables should not only include a proposal to change only 3 tables. Include any changes to references, definitions, and abbreviations in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar.

Use change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the proposed new clause is located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to the content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution is modifying Resource attribute short names table.

Table contents which has not been used in the TR-0051 doucment were deleted. At the same time, for the clear understanding, description column is added.

### -----------------------Start of change 1-------------------------------------------

### 5.2.3	Resource attribute short names

Table 5.2.3-1 shows shot names for the resource attribute. It includes attributes which are used in this document. For more information please refer to the TS-0004 [i.2].

Table 5.2.3-1: Resource attribute short names

| Attribute Name | Description | Occurs in | Short Name |
| --- | --- | --- | --- |
| accessControlPolicyIDs | Containing a list of identifiers of <accessControlPolicy> | All except accessControlPolicy, contentInstance | acpi |
| creationTime | Resource creation date/time | All | ct |
| expirationTime | Date/time which resource will be deleted by the Hosting CSE | All except contentInstance, CSEBase | et |
| labels | Tokens used to store meta-information | All | lbl |
| lastModifiedTime | Last modification date/time | All | lt |
| parentID | ResourceID of the parent resource | All | pi |
| resourceID | Identifier of the resource | All | ri |
| resourceType | Type of the resource | All | ty |
| resourceName | Name of the resource | All | rn |
| privileges | Set of access control rules for resources referencing this accessControlPolicy | accessControlPolicy | pv |
| selfPrivileges | Set of access control rules for the accessControlPlicy itself | accessControlPolicy | pvs |
| App-ID | Application Identifier | AE | api |
| pointOfAccess | Point of Access contains a network address | AE, CSEBase, remoteCSE | poa |
| ontologyRef | A URI of ontology | AE, container, contentInstance, semanticDescriptor. flexContainer, timeSeries | or |
| contentSerialization | List of supported serializations | AE | csz |
| creator | AE-ID or CSE-ID which created the resource | container, contentInstance, eventConfig, group, pollingChannel, statsCollect, statsConfig, subscription, semanticDescriptor, notificationTargetPolicy, flexContainer, timeSeries | cr |
| maxNrOfInstances | Maximum number of direct child resource (contentInstance and timeSeriesInstance) | container, timeSeries | mni |
| maxByteSize | Maximum stored data size in bytes | container, timeSeries | mbs |
| maxInstanceAge | Maximum period of saved data | container, timeSeries | mia |
| currentNrOfInstances | Current number of direct child resource | container, timeSeries | cni |
| currentByteSize | Current stored data size in bytes | container | cbs |
| contentSize | Content size in bytes | contentInstance, timeSeriesInstance | cs |
|  |  |  | c |
| containerDefinition | URI of flexContainer schema | flexContainer | cnd |
| content | Content can be any data such as image, temperature, etc | contentInstance, timeSeriesInstance | con |
| cseType | Type of CSE | CSEBase, remoteCSE | cst |
| CSE-ID | CSE identifier in SP-relative CSE-ID format | CSEBase, remoteCSE, serviceSubscribedNode | csi |
| supportedResourceType | Lists of the resource type which are supported in the CSE | CSEBase | srt |
| memberType | Resource type of the members | group | mt |
| currentNrOfMembers | Current number of members in the group | group | cnm |
| maxNrOfMembers | Mamimum number of members | group | mnm |
| memberIDs | Lists of the members | group | mid |
| memberTypeValidated | Member type validated information | group | mtv |
| consistencyStrategy | Strategy when the memberType validation has been failed | group | csy |
| CSEBase | Address of the CSEBase represented by the remoteCSE | remoteCSE | cb |
| requestReachability | Possiblity of getting request | remoteCSE, AE | rr |
| eventNotificationCriteria | Event type when the notification need to be sent | subscription | enc |
| notificationURI | Lits of the targets that the Hosting CSE need to send notifications | subscription | nu |
| notificationContentType | Content of the notifications | subscription | nct |
| descriptorRepresentation | Serialization type used for the descriptor | semanticDescriptor | dcrp |
| descriptor | Semantic description information | semanticDescriptor | dsp |
| periodicInterval | Expected time term between the two instances of Time Series Data when it is periodic | timeSeries | pei |
| missingDataDetect | Whether the receiver need to detect the missing data when the Time Series Data set to periodic | timeSeries | mdd |
| missingDataMaxNr | Maximum number of missing data | timeSeries | mdn |
| missingDataCurrentNr | Current number of missing data | timeSeries | mdc |
| missingDataDetectTimer | Set time for the considering Time Series Data as lost | timeSeries | mdt |
| dataGenerationTime | Date/time of generation | timeSeriesInstance | dgt |
| supportedReleaseVersions | Supported oneM2M release version | CSEBase, remoteCSE, AE | srv |

### -----------------------End of new text 1---------------------------------------------