| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #42.1 |
| Source:* | ETSI STF 559 |
| Date:* | 2019-10-10 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | New TPs from TS-0028 for release 3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.3.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

TPs from TS-0028 imported, reviewed and improved for release 3 – AE testing

----------------------- Start of change 1 -----------------------

#### 7.2.1.8	Security (SEC)

##### 7.2.2.8.1	Authentication

##### 7.2.2.8.1.1	ESPrim (ESP)

##### 7.2.2.8.1.1.1	NOTIFY Operation

TP/oneM2M/AE/SEC/ESP/NTF/001

| TP Id | TP/oneM2M/AE/SEC/ESP/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT sends an request for receiverESPrimRandObject, if the e2eSecInfo attribute of the Receiver’s <remoteCSE> resource in CSE2 does not include a sharedReceiverESPrimRandObject |
| Reference | TS-0003 8.4.2 – step B.2D, TS-0004 7.5.1.2.11 |
| Config Id | CF07 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Receiver (CSE1) and the IUT having sent a RETRIEVE Request on the e2eSecInfo attribute in resource TARGET_REMOTE_CSE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Response from the CSE2 containing Response Status Code set to 2000 (OK) and Content containing <remoteCSE>resource containing e2eSecInfo attribute containing no sharedReceiverESPrimRandObject parameter } | IUT ( CSE2 |
|  | then { the IUT sends a valid NOTIFY Request to Receiver CSE containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo object containing securityInfoType element set to 3 (receiverESPrimRandObject Request) } | CSE1 ( IUT |

TP/oneM2M/AE/SEC/ESP/NTF/002

| TP Id | TP/oneM2M/AE/SEC/ESP/NTF/002 |
| --- | --- |
| Test objective | Check that the IUT sends a request for receiverESPrimRandObject to the Receiver if the sharedReceiverESPrimRandObject parameter in the Receiver’s <remoteCSE> resource located in CSE2 has expired. |
| Reference | TS-0003 8.4.2 – step B.2D, TS-0004 7.5.1.2.11 |
| Config Id | CF07 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Receiver (CSE1) and the IUT having sent a RETRIEVE Request on the e2eSecInfo on resource TARGET_REMOTE_CSE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Response from CSE2 containing Response Status Code set to 2000 (OK) and Content containing <remoteCSE> resource containing e2eSecInfo attribute containing sharedReceiverESPrimRandObject parameter containing ESPrimRandExpiry field set to an expired date } | IUT ( CSE2 |
|  | then { the IUT sends a valid NOTIFY Request to Receiver CSE containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo object containing securityInfoType element set to 3 (receiverESPrimRandObject Request) } | CSE1 ( IUT |

TP/oneM2M/AE/SEC/ESP/NTF/003

| TP Id | TP/oneM2M/AE/SEC/ESP/NTF/003 |
| --- | --- |
| Test objective | Check that the IUT sends a valid ESPrim object to the Target CSE |
| Reference | TS-0003 8.4.2 – step C.4, TS-0004 7.5.1.2.13, TS-0001 11.4.2 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having received receiverESPrimRandObject and the IUT having established a sessionESPrimKey with the Receiver CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a NOTIFY Request with ESPrimObject to the Receiver } | NA |
|  | then { the IUT sends a valid NOTIFY Request to the Receiver CSE containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo object containing securityInfoType element set to 5 (ESPrim Object) and esprimObject element set to a JSON Web Encryption (JWE) Compact Serialization on inner request primitive } | CSE ( IUT |

##### 7.2.2.8.1.1.2	RETRIEVE Operation

TP/oneM2M/AE/SEC/ESP/RET/001

| TP Id | TP/oneM2M/AE/SEC/ESP/RET/001 |
| --- | --- |
| Test objective | Check that the IUT sends a valid request for e2eSecInfo attribute of the Receiver’s <remoteCSE> resource in Target CSE |
| Reference | TS-0003 8.4.2 – step B.2A, TS-0004 7.5.1.2.11 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Receiver CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a RETRIEVE Request for e2eSecInfo attribute of the Receiver’s <remoteCSE> resource at TARGET_REMOTE_ADDRESS} | NA |
|  | then { the IUT sends a valid RETRIEVE Request to Target CSE containing To set to TARGET_REMOTE_ADDRESS and From set to AE_ID and Content containing attributeList element containing e2eSecInfo | CSE1 ( IUT |

TP/oneM2M/AE/SEC/ESP/RET/002

| TP Id | TP/oneM2M/AE/SEC/ESP/RET/002 |
| --- | --- |
| Test objective | Check that the IUT sends a notification containing an inner “receiverESPrimRandObject request” to the Receiver if the sharedReceiverESPrimRandObject parameter is not present in the <remoteCSE> resource |
| Reference | TS-0003 8.4.2 – step B.2B |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with the Originator and the <remoteCSE> resource at TARGET_REMOTE_ADDRESS contains an e2eSecInfo attribute with no sharedReceiverESPrimRandObject parameter } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_ADDRESS and From set to AE_ID and Content containing attributeList element containing e2eSecInfo } | NA |
|  | then { the IUT sends a valid NOTIFICATION Request containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo elementobject containing securityInfoType attribute set to 3 (receiverESPrimRandObject Request) } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESP/RET/003

| TP Id | TP/oneM2M/AE/SEC/ESP/RET/003 |
| --- | --- |
| Test objective | Check that the IUT sends a notification containing an inner “receiverESPrimRandObject request” to the Receiver if the sharedReceiverESPrimRandObject in the <remoteCSE> resource is expired |
| Reference | TS-0003 8.4.2 – step B.2B |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having established a pairwiseESPrimKey with the Originator and the <remoteCSE> resource at TARGET_REMOTE_ADDRESS contains an e2eSecInfo attribute with an expired sharedReceiverESPrimRandObject parameter } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_ADDRESS and From set to AE_ID and Content containing attributeList element containing e2eSecInfo } | NA |
|  | then { the IUT sends a valid NOTIFICATION Request containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo elementobject containing securityInfoType attribute set to 3 (receiverESPrimRandObject Request) } | IUT  CSE1 |

##### 7.2.2.8.1.2	Roles (ROL)

##### 7.2.2.8.1.2.1	CREATE Operation

##### 7.2.2.8.1.3	ESCertKE (ESC)

##### 7.2.2.8.1.3.1	NOTIFY Operation

TP/oneM2M/AE/SEC/ESC/NTF/001

| TP Id | TP/oneM2M/AE/SEC/ESC/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT sends a notify request with ESCertKE message 1 when triggered |
| Reference | TS-0003 8.7.2.2 – step C.1.a, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered to the CSE and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Terminating End-Point’s Certificate Info & Identity } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid NOTIFY Request containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to AE_ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | NA |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to AE_ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | IUT  CSE1 |

TP/oneM2M/AE/SEC/ESC/NTF/002

| TP Id | TP/oneM2M/AE/SEC/ESC/NTF/002 |
| --- | --- |
| Test objective | Check that the IUT sends a notify response with ESCertKE message 2 when it receives a notify request with ESCertKE message 1 |
| Reference | TS-0003 8.7.2.2 – step C.1.b, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered to the CSE and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Initiating End-Point’s Certificate Info & Identity } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE1_ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Response to CSE containing To set to INITIATING_ENDPOINT_ADDRESS and From set to AE_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 2 (TLS Messages: Server Hello, Certificate*, ServerKeyExchange*, CertificateRequest*, ServerHelloDone) } | IUT  CSE1 |

TP/oneM2M/AE/SEC/ESC/NTF/003

| TP Id | TP/oneM2M/AE/SEC/ESC/NTF/003 |
| --- | --- |
| Test objective | Check that the IUT sends a notify request with ESCertKE message 3 when it receives a notify response with ESCertKE message 2 |
| Reference | TS-0003 8.7.2.2 – step C.1.c, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered to the CSE and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Terminating End-Point’s Certificate Info & Identity the IUT having sent a notify request to the Terminating End-Point with ESCertKE Message 1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response from CSE1 containing To set to INITIATING_ENDPOINT_ADDRESS and From set to CSE1_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 2 (TLS Messages: Server Hello, Certificate*, ServerKeyExchange*, CertificateRequest*, ServerHelloDone) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to AE_ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 3 (TLS Messages: Certificate*, ClientKeyExchange, CertificateVerify*, [ChangeCipherSpec], Finished) } | IUT  CSE1 |

TP/oneM2M/AE/SEC/ESC/NTF/004

| TP Id | TP/oneM2M/AE/SEC/ESC/NTF/004 |
| --- | --- |
| Test objective | Check that the IUT sends a notify response with ESCertKE message 4 when it receives a notify request with ESCertKE message 3 |
| Reference | TS-0003 8.7.2.2 – step C.1.d, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered to the CSE and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Initiating End-Point’s Certificate Info & Identity and the IUT having sent a notify request to the Initiating End-Point with ESCertKE Message 2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE1_ID and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 3 (TLS Messages: Certificate*, ClientKeyExchange, CertificateVerify*, [ChangeCipherSpec], Finished) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Response to CSE containing To set to INITIATING_ENDPOINT_ADDRESS and From set to AE_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo containing securityInfoType set to 6 (ESCertKE Message) and escertkeMessage containing base64 representation of ESCertKE Message 4 (TLS Messages: ChangeCipherSpec], Finished) } | IUT  CSE1 |

## ---------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Using a <remoteCSE> resource in the receiver (representing itself) as the <remoteCSE> in the middle CSE,, as there is no suitable CF for this TP)

Using a <remoteCSE> resource in the receiver (representing itself) as the <remoteCSE> in the middle CSE,, as there is no suitable CF for this TP)

This step is out of scope.