| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #42.1 |
| Source:* | ETSI STF 559 |
| Date:* | 2019-15-10 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | New TPs for semantic release 3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.3.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

New TPs for semantic for release 3 (Change 1).

Minor changes to some semantic TPs (Change 2)

----------------------- Start of change 1 -----------------------

TP/oneM2M/CSE/SEM/CRE/014

| TP Id | TP/oneM2M/CSE/SEM/CRE/014 |
| --- | --- |
| Test objective | Check that the IUT creates successfully the <semanticMashupInstance> resource |
| Reference | TS-0001 [1], clause 9.6.54, TS-0004 [2], clause 7.4.50.2.1, TS-0034 [6], clause 6.4.2 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing <semanticMashupInstance> resource representation containing smjpID attribute set to a reference to the <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS smjpInputParameter set to a value that does conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT creates the semanticMashupInstance resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/015

| TP Id | TP/oneM2M/CSE/SEM/CRE/015 |
| --- | --- |
| Test objective | Check that the IUT creates successfully the <semanticMashupInstance> resource with resultGenType set to WHEN_SMI_IS_CREATED |
| Reference | TS-0001 [1], clause 9.6.54, TS-0004 [2], clause 7.4.50.2.1, TS-0034 [6], clause 6.4.2 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing <semanticMashupInstance> resource representation containing smjpID attribute set to a reference to the <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS smjpInputParameter set to a value that does conform to the RDF/XML syntax and resultGenType is set to WHEN_SMI_IS_CREATED } | IUT ( AE |
|  | then { the IUT creates the semanticMashupInstance resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/016

| TP Id | TP/oneM2M/CSE/SEM/CRE/016 |
| --- | --- |
| Test objective | Check that the IUT creates successfully the <semanticMashupInstance> resource with resultGenType set to PERIODICALLY |
| Reference | TS-0001 [1], clause 9.6.54, TS-0004 [2], clause 7.4.50.2.1, TS-0034 [6], clause 6.4.2 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing <semanticMashupInstance> resource representation containing smjpID attribute set to a reference to the <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS smjpInputParameter set to a value that does conform to the RDF/XML syntax and resultGenType is set to PERIODICALLY with a period of t1 } | IUT ( AE |
|  | then { repeatedly after a period of t1 the IUT creates a new semanticMashupInstance resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

## ---------------------- End of change 1 -----------------------

----------------------- Start of change 2 -----------------------

TP/oneM2M/CSE/SEM/CRE/006

| TP Id | TP/oneM2M/CSE/SEM/CRE/006 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticMashupInstance> resource, indicating a " BAD_REQUEST " error, when the <semanticMashupJobProfile> resource referenced in its smjpID attribute does not exist |
| Reference | TS-0034 [6], clause 6.4.2, and TS-0004 [2], clause 7.4.50.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <CSEBase> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing <semanticMashupInstance> resource representation containing smjpID attribute set to a reference to a non-existent <semanticMashupJobProfile> resource } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupInstance> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/007

| TP Id | TP/oneM2M/CSE/SEM/CRE/007 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticMashupInstance> resource, indicating a " BAD_REQUEST " error, when its smjpInputParameter attribute value does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0034 [6], clause 6.4.2, and TS-0004 [2], clause 7.4.50.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing <semanticMashupInstance> resource representation containing smjpID attribute set to a reference to the <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS smjpInputParameter set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupInstance> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/008

| TP Id | TP/oneM2M/CSE/SEM/CRE/008 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticMashupInstance> resource, indicating a " BAD_REQUEST " error, when its smjpInputParameter attribute value does not meet the input parameter requirement specified by the inputDescriptor attribute of the corresponding <semanticMashupJobProfile> resource |
| Reference | TS-0034 [6], clause 6.4.2, and TS-0004 [2], clause 7.4.50.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform CREATE operation inputDescriptor attribute set to a valid value } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing <semanticMashupInstance> resource representation containing smjpID attribute set to a reference to the <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS smjpInputParameter set to a value of a type not allowed according to the inputDescriptor attribute of the <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupInstance> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/010

| TP Id | TP/oneM2M/CSE/SEM/CRE/010 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticMashupJobProfile> resource, indicating a " BAD_REQUEST " error, when its inputDescriptor attribute value does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0034 [6], clause 6.3.2, and TS-0004 [2], clause 7.4.49.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 40 (semanticMashupJobProfile) and From set to AE-ID and Content containing <semanticMashupJobProfile> resource representation containing inputDescriptor attribute set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupJobProfile> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/011

| TP Id | TP/oneM2M/CSE/SEM/CRE/011 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticMashupJobProfile> resource, indicating a " BAD_REQUEST " error, when its outputDescriptor attribute value does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0034 [6], clause 6.3.2, and TS-0004 [2], clause 7.4.49.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 40 (semanticMashupJobProfile) and From set to AE-ID and Content containing <semanticMashupJobProfile> resource representation containing outputDescriptor attribute set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupJobProfile> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/012

| TP Id | TP/oneM2M/CSE/SEM/CRE/012 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticMashupJobProfile> resource, indicating a " BAD_REQUEST " error, when its functionDescriptor attribute value does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0034 [6], clause 6.3.2, and TS-0004 [2], clause 7.4.49.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation on the resource TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 40 (semanticMashupJobProfile) and From set to AE-ID and Content containing <semanticMashupJobProfile> resource representation containing functionDescriptor attribute set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupJobProfile> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/013

| TP Id | TP/oneM2M/CSE/SEM/CRE/013 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticMashupJobProfile> resource, indicating a " BAD_REQUEST " error, when its memberFilter attribute value does not conform to a valid SPARQL query request |
| Reference | TS-0034 [6], clause 6.3.2, and TS-0004 [2], clause 7.4.49.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a < semanticMashupJobProfile > resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform CREATE operation } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 40 (semanticMashupJobProfile) and From set to AE-ID and Content containing <semanticMashupJobProfile> resource representation containing memberFilter attribute set to a value that does not conform to a valid SPARQL query request } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupJobProfile> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST)} | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/012

| TP Id | TP/oneM2M/CSE/SEM/UPD/012 |
| --- | --- |
| Test objective | Check that the IUT creates a new sematicMashupResult when the parameter smjpInputParameter is updated |
| Reference | TS-0034 [6], clause 6.3.4, and TS-0004 [2], clause 7.4.50.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupInstance> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing smjpInputParameter attribute set to a valid value } | IUT ( AE |
|  | then { the IUT creates a new <sematicMashupResult> resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/013

| TP Id | TP/oneM2M/CSE/SEM/UPD/013 |
| --- | --- |
| Test objective | Check that the IUT changes the mashupMember attribute of sematicMashupInstance when the parameter memberStoreType is updated |
| Reference | TS-0034 [6], clause 6.4.4, and TS-0004 [2], clause 7.4.50.2.3, TS-0001 [1], clause 9.6.54 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupInstance> resource at TARGET_RESOURCE_ADDRESS containing accessControlPolicyIDs attribute set to allow the AE privileges to perform UPDATE operation } |
| Expected behaviour | Test events | Direction |
|  | When { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing memberStoreType attribute set to a new valid value } | IUT ( AE |
|  | then { the IUT updates mashupMember attribute of resource and the IUT sends a valid Response containing Response Status Code set to 2004 (UPDATED) } | IUT ( AE |

## ---------------------- End of change 3 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Spec is not clear

Reference Specs are not clear if response should be sent periodically.