| HANGE REQUEST |
| --- |
| Meeting ID:* | TDE 42.2 |
| Source:* | Bob Flynn (Bob.Flynn@chordant.io) On behalf of STF 559 |
| Date:* | 2019-06-05 |
| Reason for Change/s:* | New TPs for 3GPP triggering |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018 v3.4.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Other TS/TR(s) impacted | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2019 (do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

One of the uses of the triggering request is to have the UE re-establish connectivity with the IN-CSE.  There is an implicit form of this request (requestReachability is FALSE therefore the IN-CSE initiates the request). There is also an explicit form of this request, an AE sends a <triggerRequest> to the IN-CSE, which is then used by the IN-CSE to generate the request.

TS-0018 contains the following 3GPP Interworking test cases

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/001 |
| --- | --- |
| Test objective | Check that the IUT sends an explicit 3GPP Device Trigger Request when it receives a valid <triggerRequest> from an AE. |

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/002 |
| --- | --- |
| Test objective | Check that the IUT sends an implicit 3GPP Device Trigger Request when it receives a valid <notification> from an AE. |

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/003 |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to ERROR_NSE_NOT_FOUND when the SCEF does not respond to the Device Trigger Request prior to the timeout period. |

TP/oneM2M/CSE/3GPP/TRIG/001 is based on procedure defined in TS-0026 clause 7.5.1 step 1

TP/oneM2M/CSE/3GPP/TRIG/002 is based on procedure defined in TS-0026 clause 7.5.1 step 1

TP/oneM2M/CSE/3GPP/TRIG/003 is based on procedure defined in TS-0026 clause 7.5.1 step 3

Since the IUT is an IN-CSE, these test purposes should cover the oneM2M primitives to/from the CSE as well as the 3GPP SCEF messages sent as a result of appropriate stimuli.

The following TPs cover more procedures in clause 7.5.1.

Pre-conditions

The UE that hosts the ASN/MN-CSE or ADN-AE is available to receive the Device Trigger Request using one of the connectivity establishment methods described in clause 6.

Step 1 (Optional): Request targeted to ASN/MN-CSE or ADN-AE

An AE may initiate a device trigger to an ASN/MN-CSE or ADN-AE explicitly by creating or updating a <triggerRequest> resource as specified in clause 9.6.49 of oneM2M TS-0001[1]. Alternatively, an AE may initiate a device trigger to an ASN/MN-CSE or ADN-AE implicitly by issuing a request to an IN-CSE that requires device triggering. For example, if an IN-CSE receives a request to perform a CRUD operation targeting an ASN/MN-CSE or ADN-AE hosted on a 3GPP UE that is not reachable by the IN-CSE, the IN-CSE may generate a trigger request.

Step-2: Determine if Device Triggering is required

The IN-CSE determines whether to send a device trigger to the targeted ASN/MN-CSE or ADN-AE.  Further details are provided in clause 8.3.3.2.1 of oneM2M TS-0001 [1].

If device trigger was initiated by an AE, initiating AE determines device trigger.

Step 3a: Request for Device Triggering

The IN-CSE or AE sends the Device Triggering request that contains information as specified in 3GPP TS 29.122 [4]. Such information includes:

- An HTTP POST method shall be used

- URI shall be set to {apiRoot}/3gpp-device-triggering/v1/{scsAsId}/transactions.  The {apiRoot} and {scsAsId} segments are configured based on Service Provider and MNO policies.

- The request payload shall include a DeviceTriggering data structure as specified in 3GPP TS 29.122 [4] with the following attributes:

  - supportedFeatures shall be set to a string value of “0” indicating that trigger notifications over Websockets or trigger notification test events are not supported.

  - validityPeriod shall be set to either the triggerValidityTime attribute of the <triggerRequest> resource if the trigger request is initiated by an AE.

  - triggerPayload shall be configured as described in clause 8.3.3.2.1 of oneM2M TS 0001 [1] and clause 9.2.1 of oneM2M TS-0004 [3]. An empty payload indicates that the targeted ASN/MN-CSE or ADN-AE shall re-establish connectivity with the IN-CSE.

  - externalId shall be set to the M2M-Ext-ID of the targeted UE hosting an ASN/MN-CSE or ADN-AE.

  - applicationPortID shall be set to Trigger-Recipient-ID attribute of the <triggerRequest> resource, if specified.

  - notificationDestination shall be configured with a URI that the SCEF can target Device Trigger notifications towards.  The value of this URI shall be based on internal IN-CSE policies or IN-CSE identifier.

  - priority may be set to either PRIORITY or NO_PRIORITY per internal IN-CSE policies and/or agreements between the Service Provider and MNO or  the triggerPriority attribute of the <triggerRequest> resource.

  - msisdn, requestTestNotification and websockNotifConfig are not supported by the present document and shall not be included.

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/00x |
| --- | --- |
| Test objective | Check that the IUT sends a properly formatted trigger request to the SCEF. |
| Reference | TS-0026 [5], clause 7.5.1, step 3a |

General Exceptions:

- The SCEF is not reachable when IN-CSE tries to send DeviceTriggering message. In this case the IN-CSE shall update the triggerStatus attribute of the <triggerRequest> to ERROR_NSE_NOT_FOUND after a prior timeout period (IN-CSE local policy)

Step 3b (Optional): Response to Device Triggering request

The SCEF may send a Device Triggering response to the IN-CSE to acknowledge the successful reception of the Device Trigger request before the request is delivered to the targeted UE as specified in 3GPP TS 29.122 [4].  Otherwise an HTTP error status code as defined in clause 8.3 may be returned. The response includes the following information.

A response code of 201 CREATED

The URI of the device triggering resource created by the SCEF. The URI is returned in the HTTP Location header with a format of {apiRoot}/3gpp-device-triggering/v1/{scsAsId}/transactions {transactionId}. The {apiRoot} and {scsAsId} segments are configured based on Service Provider and MNO policies.  The {transactionId} segment is configured by the SCEF.

The response payload will include a DeviceTriggering data structure as specified in 3GPP TS 29.122 [4] that includes the attributes present in the request along with the following additional attributes:

  - self is configured with a URI to the resource created by the SCEF for the request

  - deliveryResult configured with one of the following status for confirmation:

    - TRIGGERED: that the request for device triggering has been received and is accepted by the SCEF but has not yet been delivered. In this case the IN-CSE shall update the triggerStatus attribute of the <triggerRequest> to TRIGGER_TRIGGERED

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/00x |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to TRIGGER_TRIGGERED when the SCEF responds to the Device Trigger Request with the deliveryResult set to TRIGGERED. |
| Reference | TS-0026 [5], clause 7.5.1, step 3b |

General Exceptions:

If the SCEF responds with one of the error response codes defined in clause 8.3,  the IN-CSE shall update the triggerStatus attribute of the <triggerRequest> to TRIGGER_FAILED.

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/00x |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to TRIGGER_FAILED when the SCEF responds to the Device Trigger Request with the deliveryResult set to an error status code. |
| Reference | TS-0026 [5], clause 7.5.1, step 3b and step 5 |

Step 4: Device Trigger Delivery procedure

The device trigger message shall be delivered to the UE hosting the ASN/MN-CSE or ADN-AE.

Step 5: Response to DeviceTriggering

The SCEF may send a Device Trigger response to the IN-CSE to acknowledge the successful delivery of the Device Trigger request to the targeted UE as specified in 3GPP TS 29.122 [4].  Otherwise an HTTP error status code defined in clause 8.3 may be returned.  The response includes the following parameters:

A response code of 201 CREATED

The URI of the device triggering resource created by the SCEF. The URI is returned in the HTTP Location header with a format of {apiRoot}/3gpp-device-triggering/v1/{scsAsId}/transactions {transactionId}. The {apiRoot} and {scsAsId} segments are configured based on Service Provider and MNO policies.  The {transactionId} segment is configured by the SCEF.

The response payload will include a DeviceTriggering data structure as specified in 3GPP TS 29.122 [4] that includes the attributes present in the request along with the following additional attributes:

  - self parameter configured with a URI to the resource created by the SCEF for the Device Trigger request.

  - deliveryResult is included in the HTTP response to indicate one of the following status for delivery of the device trigger:

    - SUCCESS: that the device triggering delivery is successfully completed. In this case the IN-CSE shall update the triggerStatus attribute of the <triggerRequest> to TRIGGER_DELIVERED.

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/00x |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to TRIGGER_DELIVERED on receiving Device Trigger Notification with “SUCCESS” in “result” attribute. |
| Reference | TS-0026 [5], clause 7.5.1, step 5 |

    - UNKNOWN: that indicates any unspecified errors.

    - FAILURE: that this trigger encountered an error during delivery or processing and is deemed permanently undeliverable. In this case the IN-CSE shall update the triggerStatus attribute of the <triggerRequest> to TRIGGER_FAILED

    - EXPIRED: that the validity period expired when processing the device triggering request. In this case the IN-CSE shall update the triggerStatus attribute of the <triggerRequest> to TRIGGER_EXPIRED.

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/009 |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to TRIGGER_DELIVERED on receiving Device Trigger Notification with “SUCCESS” in “result” attribute. |
| Reference | TS-0026 [5], clause 7.5.1, step 5 |

    - TERMINATE: that the delivery of the device triggering request is terminated by the IN-CSE. In this case the IN-CSE shall update the triggerStatus attribute of the <triggerRequest> to TRIGGER_TERMINATED.

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/009 |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to TRIGGER_DELIVERED on receiving Device Trigger Notification with “SUCCESS” in “result” attribute. |
| Reference | TS-0026 [5], clause 7.5.1, step 5 |

General Exceptions:

If the SCEF responds with one of the error response codes defined in clause 8.3, and the device trigger was initiated by an AE via a <triggerRequest> resource, the IN-CSE shall update the triggerStatus attribute of the <triggerRequest> to TRIGGER_FAILED.

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/00x |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to TRIGGER_FAILED on receiving Device Trigger Response message with error status(UNKNOWN, FAILURE, UNCONFIRMED) in "deliveryResult" attribute. |
| Reference | TS-0026 [5], clause 7.5.1, step 5 |

Step 6: Device Triggering Delivery Report Notification request

The SCEF sends a Device Triggering Delivery Report Notification message to the {notification_uri} of the IN-CSE with the results of the trigger delivery outcome. This message is defined in 3GPP TS 29.122 [4] and shall include the following:

- An HTTP POST method is used

- URI is set to {notification_uri}.  The {notification_uri} is configured by the IN-CSE in the Device Triggering Request.

- transaction is configured with a link to the related device triggering transaction resource to which this notification is related to.

- The request payload will include a deliveryResult data structure as specified in 3GPP TS 29.122 [4].  The IN-CSE shall process the deliveryResult and update the the triggerStatus attribute of the <triggerRequest> as defined in Step 5.

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/00x |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to TRIGGER_FAILED on receiving DeviceTriggeringDeliveryReportNotification Report message with error status(UNKNOWN, FAILURE, UNCONFIRMED) in deliveryResult attribute. |
| Reference | TS-0026 [5], clause 7.5.1, step 6 |

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/00x |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to TRIGGER_TRIGGERED when the SCEF responds to the DeviceTriggeringDeliveryReportNotification Report message with the deliveryResult set to TRIGGERED. |
| Reference | TS-0026 [5], clause 7.5.1, step 6 |

Step 7: Device Triggering Delivery Report Notification response

After receiving a Device Triggering Delivery Report Notification request, the IN-CSE or AE returns a HTTP response having a response code of 204 NO CONTENT and no payload.

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/00x |
| --- | --- |
| Test objective | Check that the IUT returns a HTTP response when it receives a valid DeviceTriggeringDeliveryReportNotification Report message |
| Reference | TS-0026 [5], clause 7.5.1, step 7 |

Steps 8  (optional) and 9: IN-CSE Updates <triggerRequest> and Response to 1a or 1b

If the device trigger was initiated by an AE via a <triggerRequest> resource, then the IN-CSE shall update triggerStatus attribute of <triggerRequest> resource.

Step 10: ASN/MN-CSE or ADN-AE performs trigger actions

If the trigger has no payload, the ASN/MN-CSE or ADN-AE shall re-establish connectivity with the IN-CSE. Otherwise, based on the type of trigger request received, the ASN/MN-CSE or ADN-AE performs the corresponding trigger actions such as establish connectivity with the IN-CSE, enrol with the MEF, register to the IN-CSE, update its PoA, or execute a CRUD request on a specified resource.

Further details are described in clause 8.3.3.2.1 of oneM2M TS-0001 [1] and clause 9.2.1 of oneM2M TS-0004 [3]

### -----------------------Start of new text 1-------------------------------------------

TP/oneM2M/CSE/3GPP/001

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/001 |
| --- | --- |
| Test objective | Check that the IUT sends an explicit 3GPP Device Trigger Request when it receives a valid <triggerRequest> from an AE. |
| Reference | TS-0026 [5], clause 7.5.1, step 3a |
| Parent Release | Release 3 |
| Config Id | CFG05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE1 and the AE1 being hosted on a 3GPP UE and the IUT allowing to register an AE2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE2 containing To set to AE2_RESOURCE_ADDRESS and From set to AE2_ID and Resource Type set to 38 (triggerRequest) and Content containing triggerRequest resource containing triggerPurpose set to TRIGGER_PURPOSE } | IUT ( AE1 |
|  | then { the IUT sends a Request to the SCEF containing 3GPP Device Trigger Request message containing a valid 3GPP Device Trigger Request containing triggerPayload attribute } | IUT ( SCEF |

| TP Id | TRIGGER_PURPOSE |
| --- | --- |
| TP/oneM2M/CSE/3GPP/TRIG/001_CON | establishConnection |
| TP/oneM2M/CSE/3GPP/TRIG/001_REQ | registrationRequest |
| TP/oneM2M/CSE/3GPP/TRIG/001_EXE | executeCRUD |
| TP/oneM2M/CSE/3GPP/TRIG/001_ENR | enrolmentRequest |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of new text 2-------------------------------------------

TP/oneM2M/CSE/3GPP/004

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/004 |
| --- | --- |
| Test objective | Check that the IUT sets the triggerStatus attribute of the <triggerRequest> to the proper value when the SCEF responds to the Device Trigger Request. |
| Reference | TS-0026 [5], clause 7.5.1, step 3b |
| Parent Release | Release 3 |
| Config Id | CFG05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE1 and the AE1 being hosted on a 3GPP UE and the IUT allowing to register an AE2 and AE2 having created a TRIGGER_REQUEST and the IUT having sent a POST 3GPP Device Trigger Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Device Triggering response from SCEF containing deliveryResult set to SCEF_RESULT } | IUT ( SCEF |
|  | then { the IUT sets triggerStatus attribute of TRIGGER_REQUEST to TRIGGER_RESULT } | IUT ( SCEF |

| TP Id | SCEF_RESULT | TRIGGER_RESULT |
| --- | --- | --- |
| TP/oneM2M/CSE/3GPP/TRIG/004_1 | SUCCESS | TRIGGER-DELIVERED |
| TP/oneM2M/CSE/3GPP/TRIG/004_2 | UNKNOWN | TRIGGER-FAILED |
| TP/oneM2M/CSE/3GPP/TRIG/004_3 | FAILURE | TRIGGER-FAILED |
| TP/oneM2M/CSE/3GPP/TRIG/004_4 | TRIGGERED | TRIGGER-TRIGGERED |
| TP/oneM2M/CSE/3GPP/TRIG/004_5 | EXPIRED | TRIGGER-EXPIRED |
| TP/oneM2M/CSE/3GPP/TRIG/004_6 | UNCONFIRMED | TRIGGER-UNCONFIRMED |
| TP/oneM2M/CSE/3GPP/TRIG/004_7 | REPLACED | TRIGGER-FAILED |
| TP/oneM2M/CSE/3GPP/TRIG/004_8 | TERMINATE | TRIGGER-TERMINATED |

TP/oneM2M/CSE/3GPP/005

| TP Id | TP/oneM2M/CSE/3GPP/TRIG/005 |
| --- | --- |
| Test objective | Check that the IUT returns a HTTP response when it receives a valid DeviceTriggeringDeliveryReportNotification Report message |
| Reference | TS-0026 [5], clause 7.5.1, step 6 and 7 |
| Parent Release | Release 3 |
| Config Id | CFG05 |
| PICS Selection | PICS_CSE, PICS_3GPP |
| Initial conditions | with { the IUT being in the "initial state" and the IUT allowing to register an AE1 and the AE1 being hosted on a 3GPP UE and the IUT allowing to register an AE2 and AE2 having created a TRIGGER_REQUEST and the IUT having sent a POST 3GPP Device Trigger Request } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid DeviceTriggeringDeliveryReportNotification request from SCEF containing deliveryResult set to SCEF_RESULT } | IUT ( SCEF |
|  | then { the IUT sets triggerStatus attribute of TRIGGER_REQUEST to TRIGGER_RESULT and the IUT sends a valid HTTP response containing Response Code set to 204 (NO_CONTENT) } | IUT ( SCEF |

| TP Id | SCEF_RESULT | TRIGGER_RESULT |
| --- | --- | --- |
| TP/oneM2M/CSE/3GPP/TRIG/005_1 | SUCCESS | TRIGGER-DELIVERED |
| TP/oneM2M/CSE/3GPP/TRIG/005_2 | UNKNOWN | TRIGGER-FAILED |
| TP/oneM2M/CSE/3GPP/TRIG/005_3 | FAILURE | TRIGGER-FAILED |
| TP/oneM2M/CSE/3GPP/TRIG/005_4 | TRIGGERED | TRIGGER-TRIGGERED |
| TP/oneM2M/CSE/3GPP/TRIG/005_5 | EXPIRED | TRIGGER-EXPIRED |
| TP/oneM2M/CSE/3GPP/TRIG/005_6 | UNCONFIRMED | TRIGGER-UNCONFIRMED |
| TP/oneM2M/CSE/3GPP/TRIG/005_7 | REPLACED | TRIGGER-FAILED |
| TP/oneM2M/CSE/3GPP/TRIG/005_8 | TERMINATE | TRIGGER-TERMINATED |

### -----------------------End of change 2-------------------------------------------

# Comments

TP/oneM2M/CSE/3GPP/TRIG/001 - existing

TP/oneM2M/CSE/3GPP/TRIG/002 - existing

This should have a permutation for each type of trigger request. Each permutation should verify the triggerPayload content from the CSE.

This is a permutation of TRIG/001. Added permutation table below.

TP/oneM2M/CSE/3GPP/TRIG/003

Verify in TS 29.122. update text in ts-0026

Need to specify the triggerStatus value for this

  - triggerPayload shall be configured as described in clause 8.3.3.2.1 of oneM2M TS 0001 [1] and clause 9.2.1 of oneM2M TS-0004 [3]. An empty payload indicates that the targeted ASN/MN-CSE or ADN-AE shall re-establish connectivity with the IN-CSE.

Should “TRIG” be in this path?

Should “TRIG” be in this path?