| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #42.2 |
| Source:* | Yann Garcia (yann.garcia@fscom.fr) On behalf of STF559 |
| Date:* | 2019-11-15 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | Changes for ontology interworking TPs release 3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.4.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Changes for ontology interworking TPs release 3 (change 1)

Addtion of TS-0030 as normative reference (change 2)

Addition of new config 07 (change 3)

----------------------- Start of change 1 -----------------------

TP/oneM2M/AE/OBI/REG/001

| TP Id | TP/oneM2M/AE/OBI/REG/001 |
| --- | --- |
| Test objective | Check that the IUT sends an AE initial registration request when it is started |
| Reference | TS-0001 [1], clause 10.1.1.2.2 - case C, and clause 9.6.19, TS-0030 [8], clause 6.2.1.2 |
| Config Id | CF07 |
| Parent Release | Release 3 |
| PICS Selection | PICS_AE_IPE |
| Initial conditions | with { the IUT never being registered and the IUT being in the "initial state" and the IUT having got a valid APP-ID } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid CREATE Request containing To set to CSE_RESOURCE_ADDRESS and Resource Type set to 2 (AE) and Content containing AE resource representation } | NA |
|  | then { the IUT sends a valid CREATE Request to CSE containing Resource Type set to 2 (AE) and To set to CSE_RESOURCE_ADDRESS and From set to empty and Content containing AE-IPE resource representation } | CSE ( IUT |

TP/oneM2M/AE/OBI/INI/001

| TP Id | TP/oneM2M/AE/OBI/INI/001 |
| --- | --- |
| Test objective | Check that the IUT starts the Initialization sequence of an Ontology based Interworking IPE and retrieves the formal description of the ontology |
| Reference | TS-0001 [1], clause 10.1.1.1 and 10.2.4.16, TS-0004 [2], clause 7.2.2.1 and 7.4.37, TS-0030 [8], clause 6.2.1.2 item 1. |
| Config Id | CF07 |
| Parent Release | Release 3 |
| PICS Selection | PICS_AE_IPE, PICS_RESTFULL_API, PICS_TS_ONTOLOGY_SERVER |
| Initial conditions | with { the IUT being registered and the IUT being in the "initial state" and the IUT having privileges to perform RETRIEVE operation on formal description of the ontology at AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a request to get the formal description of the Ontology } | NA |
|  | then { the IUT sends a valid HTTP GET Request to Ontology server containing anURI indicating the address where to get the Ontology } | OS ( IUT |

TP/oneM2M/AE/OBI/DIS/001

| TP Id | TP/oneM2M/AE/OBI/DIS/001 |
| --- | --- |
| Test objective | Check that the IUT has performed DISCOVERY of non-oneM2M devices during initialization sequence |
| Reference | TS-0001 [1], clause 10.1.1.1 and 10.2.4.16, TS-0004 [2], clause 7.2.2.1 and 7.4.37, TS-0030 [8], clause 6.2.1.2 item 5. |
| Config Id | CF07 |
| Parent Release | Release 3 |
| PICS Selection | PICS_AE_IPE, PICS_AE_IPE_DISCOVERY |
| Initial conditions | with { the IUT being registered and the IUT being in the "initial state" and the IUT having retrieved and parsed the formal description of the ontology and the IUT having performed DISCOVERY of non-oneM2M devices and the IUT having discovered a non-oneM2M device with a valid address value indicating NON_ONEM2M_AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from CSE containing To set to NON_ONEM2M_AE_RESOURCE_ADDRESS and From set to CSE_ID } | CSE ( IUT |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing non-oneM2M devices resource representation } | CSE ( IUT |

TP/oneM2M/AE/OBI/DIS/002

| TP Id | TP/oneM2M/AE/OBI/DIS/002 |
| --- | --- |
| Test objective | Check that the IUT continues to discover the devices in the non-oneM2M area |
| Reference | TS-0001 [1], clause 10.1.1.1 and 10.2.4.16, TS-0004 [2], clause 7.2.2.1 and 7.3.3.14, TS-0030 [8], clause 6.2.2.1. |
| Config Id | CF07 |
| Parent Release | Release 3 |
| PICS Selection | PICS_AE_IPE, PICS_AE_IPE_DISCOVERY |
| Initial conditions | with { the IUT being registered and the IUT being in the "initial state" and the IUT having retrieved and parsed the formal description of the ontology and the IUT having performed DISCOVERY of non-oneM2M devices and the IUT having discovered a new non-oneM2M device with a valid address value indicating NON_ONEM2M_NEW_AE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from CSE containing To set to NON_ONEM2M_NEW_AE_RESOURCE_ADDRESS and From set to CSE_ID } | CSE ( IUT |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing non-oneM2M devices resource representation } | CSE ( IUT |

TP/oneM2M/AE/OBI/DIS/003

| TP Id | TP/oneM2M/AE/OBI/DIS/003 |
| --- | --- |
| Test objective | Check that the IUT continues to discover the devices in the non-oneM2M area |
| Reference | TS-0001 [1], clause 10.1.1.1 and 10.2.4.16, TS-0004 [2], clause 7.2.2.1 and 7.3.3.14, TS-0030 [8], clause 6.2.2.1. |
| Config Id | CF07 |
| Parent Release | Release 3 |
| PICS Selection | PICS_AE_IPE, PICS_AE_IPE_DISCOVERY |
| Initial conditions | with { the IUT being registered and the IUT being in the "initial state" and the IUT having retrieved and parsed the formal description of the ontology and the IUT having performed DISCOVERY of non-oneM2M devices and An existing non-oneM2M (NON_ONEM2M_NEW_AE_RESOURCE_ADDRESS) device was switched off } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from CSE containing To set to NON_ONEM2M_NEW_AE_RESOURCE_ADDRESS and From set to CSE_ID } | CSE ( IUT |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4004 (NOT_FOUND) } | CSE ( IUT |

TP/oneM2M/AE/OBI/DIS/004

| TP Id | TP/oneM2M/AE/OBI/DIS/004 |
| --- | --- |
| Test objective | Check that the IUT accepts “on demand” discovery |
| Reference | TS-0001 [1], clause 10.1.1.1 and 10.2.4.16, TS-0004 [2], clause 7.2.2.1 and 7.3.3.14, TS-0030 [8], clause 6.2.2.1. |
| Config Id | CF07 |
| Parent Release | Release 3 |
| PICS Selection | PICS_AE_IPE, PICS_AE_IPE_DISCOVERY |
| Initial conditions | with { the IUT being registered and the IUT being in the "initial state" and the IUT having retrieved and parsed the formal description of the ontology and the IUT having performed DISCOVERY of non-oneM2M devices } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to IPE_RESOURCE_ADDRESS and Resource Type set to 28 (flexContainer) and From set to CSE_ID and Filter Criteria containing filterUsage set to 1 (IPE On-demand Discovery) } | CSE ( IUT |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing URIList representation } | CSE ( IUT |

TP/oneM2M/AE/OBI/RET/001

| TP Id | TP/oneM2M/AE/OBI/RET/001 |
| --- | --- |
| Test objective | Check that the IUT accepts a retrieval request resource and responds 2000 (OK) status. |
| Reference | TS-0001 [1], clause 10.2.3.2 and clause 9.6.3, TS-0004 [2], clause 7.4.3.2.2, TS-0030 [8], clause 6.2.2.2.1. |
| Config Id | CF07 |
| Parent Release | Release 3 |
| PICS Selection | PICS_AE_IPE |
| Initial conditions | with { the IUT being registered and the IUT being in the "initial state" and the IUT having retrieved and parsed the formal description of the ontology and the IUT having performed DISCOVERY of non-oneM2M devices } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from CSE containing To set to AE_IPE_ID and From set to CSE_RESOURCE_ADDRESS and no Content } | IUT ( CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Resource Type set to 28 (flexContainer) and Content containing Non-oneM2M AE resource representation as a specialization of <flexContainer> } | IUT ( CSE |

TP/oneM2M/AE/OBI/RET/002

| TP Id | TP/oneM2M/AE/OBI/RET/002 |
| --- | --- |
| Test objective | Check that the IUT accepts a retrieval request resource with the optional ATTRIBUTE. |
| Reference | TS-0001 [1], clause 10.2.3.2and clause 9.6.3, TS-0004 [2], clause 7.4.3.2.2, TS-0030 [8], clause 6.2.2.2.1. |
| Config Id | CF07 |
| Parent Release | Release 3 |
| PICS Selection | PICS_AE_IPE |
| Initial conditions | with { the IUT being registered and the IUT being in the "initial state" and the IUT having retrieved and parsed the formal description of the ontology and the IUT having performed DISCOVERY of non-oneM2M devices } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to CSEBASE_RESOURCE_ADDRESS and From set to AE_ID and no Content } | IUT ( CSE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Resource Type set to 28 (flexContainer) and Content containing Non-oneM2M resource as a specialization of <flexContainer> containing valid ATTRIBUTE attribute } | IUT ( CSE |

## ---------------------- End of change 1 -----------------------

----------------------- Start of change 2 -----------------------

[8]	oneM2M TS-0030: “Ontology based Interworking”.

## ---------------------- End of change 2 -----------------------

----------------------- Start of change 3 -----------------------

Figure 5.1-7: Test configuration 7 (CF07)

## ---------------------- End of change 3 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Ontoogy Server, can be simulated by the TS or can be an external resource