| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #43 |
| Source:* | STF559 |
| Date:* | 2019-11-15 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | Changes for security TPs release 3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.5.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Changes for security TPs release 3 (change 1)

----------------------- Start of change 1 -----------------------

## ---------------------- End of change 1 -----------------------

TP/oneM2M/AE/SEC/ESP/NTF/001

| TP Id | TP/oneM2M/AE/SEC/ESP/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT sends a request for receiverESPrimRandObject, if the e2eSecInfo attribute of the Receiver’s <remoteCSE> resource in CSE2 does not include a sharedReceiverESPrimRandObject. |
| Reference | TS-0003 8.4.2 – step B.2D, TS-0004 7.5.1.2.11 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Receiver (CSE1) and the IUT having sent a RETRIEVE Request on the e2eSecInfo attribute in resource TARGET_REMOTE_CSE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Response from CSE2 containing Response Status Code set to 2000 (OK) and Content containing <remoteCSE>resource containing e2eSecInfo attribute containing no sharedReceiverESPrimRandObject parameter } | IUT ( CSE2 |
|  | then { the IUT sends a valid NOTIFY Request to Receiver CSE (CSE1) containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo elementcontaining securityInfoType element set to 3 (receiverESPrimRandObject Request) } | CSE1 ( IUT |

TP/oneM2M/AE/SEC/ESP/NTF/002

| TP Id | TP/oneM2M/AE/SEC/ESP/NTF/002 |
| --- | --- |
| Test objective | Check that the IUT sends a request for receiverESPrimRandObject to the Receiver if the sharedReceiverESPrimRandObject parameter in the Receiver’s <remoteCSE> resource located in CSE2 has expired. |
| Reference | TS-0003 8.4.2 – step B.2D, TS-0004 7.5.1.2.11 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Receiver CSE (CSE1) and the IUT having sent a RETRIEVE Request on the e2eSecInfo on resource TARGET_REMOTE_CSE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Response from CSE2 containing Response Status Code set to 2000 (OK) and Content containing <remoteCSE> resource containing e2eSecInfo attribute containing sharedReceiverESPrimRandObject parameter containing ESPrimRandExpiry field set to an expired date } | IUT ( CSE2 |
|  | then { the IUT sends a valid NOTIFY Request to Receiver CSE containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo elementcontaining securityInfoType element set to 3 (receiverESPrimRandObject Request) } | CSE1 ( IUT |

TP/oneM2M/AE/SEC/ESP/NTF/003

| TP Id | TP/oneM2M/AE/SEC/ESP/NTF/003 |
| --- | --- |
| Test objective | Check that the IUT sends a valid ESPrim object to the Receiver CSE |
| Reference | TS-0003 8.4.2 – step C.4, TS-0004 7.5.1.2.13, TS-0001 11.4.2 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having received receiverESPrimRandObject and the IUT having established a sessionESPrimKey with the Receiver CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid NOTIFY Request containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo element containing securityInfoType element set to 5 (ESPrim Object) and esprimObject element } | NA |
|  | then { the IUT sends a valid NOTIFY Request to the Receiver CSE containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo elementcontaining securityInfoType element set to 5 (ESPrim Object) and esprimObject element set to a JSON Web Encryption (JWE) Compact Serialization on inner request primitive } | CSE ( IUT |

###### 7.2.1.8.1.1.2	RETRIEVE Operation

TP/oneM2M/AE/SEC/ESP/RET/001

| TP Id | TP/oneM2M/AE/SEC/ESP/RET/001 |
| --- | --- |
| Test objective | Check that the IUT sends a valid request for e2eSecInfo attribute of the Receiver’s <remoteCSE> resource in the CSE Registered with Receiver CSE |
| Reference | TS-0003 8.4.2 – step B.2A, TS-0004 7.5.1.2.11 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Receiver CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to AE_ID and Content containing attributeList element containing e2eSecInfo attribute } | NA |
|  | then { the IUT sends a valid RETRIEVE Request to CSE1 containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to AE_ID and Content containing remoteCSE resource containing e2eSecInfo attribute | CSE1 ( IUT |

TP/oneM2M/AE/SEC/ESP/RET/002

| TP Id | TP/oneM2M/AE/SEC/ESP/RET/002 |
| --- | --- |
| Test objective | Check that the IUT sends a notification containing an inner “receiverESPrimRandObject request” to the Receiver if the sharedReceiverESPrimRandObject parameter is not present in the <remoteCSE> resource in the CSE Registered with Receiver CSE |
| Reference | TS-0003 8.4.2 – step B.2D, TS-0004 7.5.1.2.11 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Originator and the <remoteCSE> resource at TARGET_REMOTE_CSE_ADDRESS containing e2eSecInfo attribute with no sharedReceiverESPrimRandObject parameter } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to AE_ID and Content containing attributeList element containing e2eSecInfo attribute } | NA |
|  | then { the IUT sends a valid NOTIFICATION Request containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo element containing securityInfoType elementset to 3 (receiverESPrimRandObject Request) } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESP/RET/003

| TP Id | TP/oneM2M/AE/SEC/ESP/RET/003 |
| --- | --- |
| Test objective | Check that the IUT sends a notification containing an inner “receiverESPrimRandObject request” to the Receiver if the sharedReceiverESPrimRandObject in the <remoteCSE> resource is expired |
| Reference | TS-0003 8.4.2 – step B.2D, TS-0004 7.5.1.2.11 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Originator and the <remoteCSE> resource at TARGET_REMOTE_CSE_ADDRESS containing e2eSecInfo attribute with an expired sharedReceiverESPrimRandObject parameter } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to AE_ID and Content containing attributeList element containing e2eSecInfo attribute } | NA |
|  | then { the IUT sends a valid NOTIFICATION Request containing To set to TARGET_RECEIVER_ADDRESS and From set to AE_ID and Content containing securityInfo element containing securityInfoType elementset to 3 (receiverESPrimRandObject Request) } | IUT  CSE1 |

TP/oneM2M/AE/SEC/ESC/NTF/001

| TP Id | TP/oneM2M/AE/SEC/ESC/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT sends a notify request with ESCertKE message 1 when triggered |
| Reference | TS-0003 8.7.2.2 – step C.1.a, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Terminating End-Point’s Certificate Info & Identity } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid NOTIFY Request containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to AE_ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | NA |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to AE_ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | IUT  CSE1 |

TP/oneM2M/AE/SEC/ESC/NTF/002

| TP Id | TP/oneM2M/AE/SEC/ESC/NTF/002 |
| --- | --- |
| Test objective | Check that the IUT sends a notify response with ESCertKE message 2 when it receives a notify request with ESCertKE message 1 |
| Reference | TS-0003 8.7.2.2 – step C.1.b, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Initiating End-Point’s Certificate Info & Identity } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE1_ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Response to CSE containing To set to INITIATING_ENDPOINT_ADDRESS and From set to AE_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 2 (TLS Messages: Server Hello, Certificate*, ServerKeyExchange*, CertificateRequest*, ServerHelloDone) } | IUT  CSE1 |

TP/oneM2M/AE/SEC/ESC/NTF/003

| TP Id | TP/oneM2M/AE/SEC/ESC/NTF/003 |
| --- | --- |
| Test objective | Check that the IUT sends a notify request with ESCertKE message 3 when it receives a notify response with ESCertKE message 2 |
| Reference | TS-0003 8.7.2.2 – step C.1.c, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF03 |
| PICS Selection | PICS_AE, |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Terminating End-Point’s Certificate Info & Identity and the IUT having sent a notify request to the Terminating End-Point with ESCertKE Message 1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response from CSE1 containing To set to INITIATING_ENDPOINT_ADDRESS and From set to CSE1_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 2 (TLS Messages: Server Hello, Certificate*, ServerKeyExchange*, CertificateRequest*, ServerHelloDone) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to AE_ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 3 (TLS Messages: Certificate*, ClientKeyExchange, CertificateVerify*, [ChangeCipherSpec], Finished) } | IUT  CSE1 |

TP/oneM2M/AE/SEC/ESC/NTF/004

| TP Id | TP/oneM2M/AE/SEC/ESC/NTF/004 |
| --- | --- |
| Test objective | Check that the IUT sends a notify response with ESCertKE message 4 when it receives a notify request with ESCertKE message 3 |
| Reference | TS-0003 8.7.2.2 – step C.1.d, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF03 |
| PICS Selection | PICS_AE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Initiating End-Point’s Certificate Info & Identity and the IUT having sent a notify request to the Initiating End-Point with ESCertKE Message 2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE1_ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 3 (TLS Messages: Certificate*, ClientKeyExchange, CertificateVerify*, [ChangeCipherSpec], Finished) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Response to CSE1 containing To set to INITIATING_ENDPOINT_ADDRESS and From set to AE_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 4 (TLS Messages: ChangeCipherSpec], Finished) } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESP/NTF/001

| TP Id | TP/oneM2M/CSE/SEC/ESP/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT sends a new ESPrimRandObject when requested |
| Reference | TS-0003 8.4.2 – step B.2C.2, TS-0004 7.5.1.2.11 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Originator (AE1) } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY request from AE1 containing To set to TARGET_RECEIVER_ADDRESS and From set to AE1_ID and Content containing securityInfo elementcontaining securityInfoType elementset to 3 (receiverESPrimRandObject Request) } | IUT  AE1 |
|  | then { the IUT sends a valid NOTIFY Response containing To set to TARGET_ORIGINATOR_ADDRESS and From set to CSE_ID and Content containing securityInfo elementcontaining securityInfoType elementset to 4 (receiverESPrimRandObject Response) and esprimRandObject element containing receiverESPrimRandObject } | IUT  AE1 |

TP/oneM2M/CSE/SEC/ESP/NTF/002

| TP Id | TP/oneM2M/CSE/SEC/ESP/NTF/002 |
| --- | --- |
| Test objective | Check that the IUT responds with a valid ESPrim object when it receives a request |
| Reference | TS-0003 8.4.2 – step C.9, TS-0004 7.6.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT having established a sessionESPrimKey with the Originator (AE1) } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from AE1 containing To set to TARGET_RECEIVER_ADDRESS and From set to AE1_ID and Content containing securityInfo elementcontaining securityInfoType elementset to 5 (ESPrim Object) and valid esprimObject element } | IUT  AE1 |
|  | then { the IUT sends a valid NOTIFY Response containing To set to RECEIVER_RECEIVER_ADDRESS and From set to CSE_ID and Response Status Code set to 2000 (OK) and Content containing securityInfo element containing securityInfoType elementset to 5 (ESPrim Object) and valid esprimObject element } | IUT  AE1 |

TP/oneM2M/CSE/SEC/ESP/NTF/003

| TP Id | TP/oneM2M/CSE/SEC/ESP/NTF/003 |
| --- | --- |
| Test objective | Check that the IUT successfully detects AE impersonation in an End-to-End Security of Primitives |
| Reference | TS-0003 7.2.2 – step 4, TS-0004 7.6.2 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT having established a sessionESPrimKey with with the Originator (AE1) } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from AE1 containing To set to CSE_ID and From set to a value other than AE1_ID and Content containing securityInfo element containing securityInfoType elementset to 5 (ESPrim Object) and valid esprimObject element } | IUT  AE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4116 (ESPRIM_IMPERSONATION_ERROR) } | IUT  AE1 |

TP/oneM2M/CSE/SEC/ESP/RET/001

| TP Id | TP/oneM2M/CSE/SEC/ESP/RET/001 |
| --- | --- |
| Test objective | Check that the IUT sends a valid request for e2eSecInfo attribute of the Receiver’s <remoteCSE> resource in the CSE Registered with Receiver CSE |
| Reference | TS-0003 8.4.2 – step B.2A, TS-0004 7.5.1.2.11 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and and the IUT having established a pairwiseESPrimKey with the Receiver CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to AE_ID and Content containing attributeList element containing e2eSecInfo attribute } | NA |
|  | then { the IUT sends a valid RETRIEVE Request to Target CSE containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to CSE_ID and Content containing remoteCSE resource containing e2eSecInfo attribute } | CSE ( IUT |

TP/oneM2M/CSE/SEC/ESP/RET/002

| TP Id | TP/oneM2M/CSE/SEC/ESP/RET/002 |
| --- | --- |
| Test objective | Check that the IUT sends a notification containing an inner “receiverESPrimRandObject request” to the Receiver if the sharedReceiverESPrimRandObject parameter is not present in the <remoteCSE> resource in the CSE Registered with Receiver CSE |
| Reference | TS-0003 8.4.2 – step B.2D, TS-0004 7.5.1.2.11 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Originator and the <remoteCSE> resource at TARGET_REMOTE_CSE_ADDRESS containing e2eSecInfo attribute with no sharedReceiverESPrimRandObject parameter } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to CSE_ID and Content containing attributeList element containing e2eSecInfo attribute } | NA |
|  | then { the IUT sends a valid NOTIFICATION Request containing To set to TARGET_RECEIVER_ADDRESS and From set to CSE_ID and Content containing securityInfo element containing securityInfoType elementset to 3 (receiverESPrimRandObject Request) } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESP/RET/003

| TP Id | TP/oneM2M/CSE/SEC/ESP/RET/003 |
| --- | --- |
| Test objective | Check that the IUT sends a notification containing an inner “receiverESPrimRandObject request” to the Receiver if the sharedReceiverESPrimRandObject in the <remoteCSE> resource is expired |
| Reference | TS-0003 8.4.2 – step B.2B, TS-0004 7.5.1.2.11 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT having established a pairwiseESPrimKey with the Originator and the <remoteCSE> resource at TARGET_REMOTE_CSE_ADDRESS containing e2eSecInfo attribute with an expired sharedReceiverESPrimRandObject parameter } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid RETRIEVE Request containing To set to TARGET_REMOTE_CSE_ADDRESS and From set to CSE_ID and Content containing attributeList element containing e2eSecInfo attribute } | NA |
|  | then { the IUT sends a valid NOTIFICATION Request containing To set to TARGET_RECEIVER_ADDRESS and From set to CSE_ID and Content containing securityInfo element containing securityInfoType elementset to 3 (receiverESPrimRandObject Request) } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/CRE/001

| TP Id | TP/oneM2M/CSE/SEC/ROL/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT sends a CREATE <role> resource request to the Role Repository (CSE1) when triggered |
| Reference | TS-0003 7.4.2.2 – step 3 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT acting as an Authorization Authority } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid CREATE Request containing To set to ROLE_REPOSITORY_ADDRESS (CSE1) and Resource Type set to 31 (role) and Content containing <role> resource representation } | NA |
|  | then { the IUT sends a valid CREATE Request to CSE1 containing To set to ROLE_REPOSITORY_ADDRESS and Resource Type set to 31 (role) and Content containing <role> resource representation } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/CRE/002

| TP Id | TP/oneM2M/CSE/SEC/ROL/CRE/002 |
| --- | --- |
| Test objective | Check that the IUT successfully creates the <role> resource requested by the Authorization Authority |
| Reference | TS-0003 7.4.2.2 – step 4 and 5 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and and the IUT being switched on and and the IUT acting as a Role Repository } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from CSE1 (AA) containing From set to CSE1_ID and To set to ROLE_REPOSITORY_ADDRESS and Resource Type set to 31 (role) and Content containing <role> resource representation } | IUT  CSE1 |
|  | then { the IUT creates the <role> resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing <role> resource representation } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/CRE/003

| TP Id | TP/oneM2M/CSE/SEC/ROL/CRE/003 |
| --- | --- |
| Test objective | Check that the IUT sends a CREATE <token> resource request to the Token Repository when triggered |
| Reference | TS-0003 7.4.2.3 – step 2 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT acting as an Authorization Authority " and the IUT having assigned a role for the Originator } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid CREATE Request containing To set to TOKEN_REPOSITORY_ADDRESS (CSE1) and Resource Type set to 32 (token) and Content containing <token> resource representation } | NA |
|  | then { the IUT sends a valid CREATE Request to CSE containing To set to TOKEN _REPOSITORY_ADDRESS and Resource Type set to 32 (token) and Content containing <token> resource representation } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/CRE/004

| TP Id | TP/oneM2M/CSE/SEC/ROL/CRE/004 |
| --- | --- |
| Test objective | Check that the IUT successfully creates the <token> resource requested by the Authorization Authority |
| Reference | TS-0003 7.4.2.3 – step 3 and 4 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT acting as a Token Repository and the Authorization Authority having assigned a role for the Originator } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from CSE1 (AA) containing From set to CSE1_ID and To set to TOKEN_REPOSITORY_ADDRESS and Resource Type set to 32 (token) and Content containing <token> resource representation } | IUT  CSE1 |
|  | then { the IUT creates the <token> resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) and Content containing <token> resource representation } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/RET/001

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/001 |
| --- | --- |
| Test objective | Check that the IUT returns the <role> resource of the Originator |
| Reference | TS-0003 7.4.2.2 – step 8 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT acting as a Role Repository and the Authorization Authority having assigned a role for the Originator at ROLE_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE Request containing From set to CSE1_ID and To set to ROLE_RESOURCE_ADDRESS and no Content } | IUT  CSE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing valid <role> resource representation } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/RET/002

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/002 |
| --- | --- |
| Test objective | Check that the IUT returns the <token> resource of the Originator |
| Reference | TS-0003 7.4.2.3 – step 8 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT acting as a Token Repository and the Authorization Authority having assigned a role for the Originator and and the IUT having a token associated to the role of the Originator at TOKEN_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a RETRIEVE Request containing From set to CSE1_ID and To set to TOKEN_RESOURCE_ADDRESS and no Content } | IUT  CSE1 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Content containing valid <token> resource representation } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/RET/003

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/003 |
| --- | --- |
| Test objective | Check that the IUT sends a <role> Retrieve request to the Role Repository after receiving a request on a resource protected by role based access control |
| Reference | TS-0003 7.4.3 – step 2 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the Authorization Authority having assigned a role for the Originator and the Authorization Authority having created a token associated to the role of the Originator and the IUT having a <container> resource at RESOURCE_TARGET_ADDRESS protected by role based access control and the IUT having granted the Originator access to the <container> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request containing From set to AE1_ID and To set to RESOURCE_TARGET_ADDRESS and Role ID parameter set to address the <role> resource assigned to the Originator } | IUT  AE1 |
|  | then { the IUT sends a valid RETRIEVE Request to CSE1 containing From set to CSE_ID and To set to Role ID and no Content } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/RET/004

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/004 |
| --- | --- |
| Test objective | Check that the IUT sends a <token> Retrieve request to the Token Repository after receiving a request on a resource protected by role based access control |
| Reference | TS-0003 7.4.3 – step 2 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the Authorization Authority having assigned a role for the Originator and the Authorization Authority having created a token associated to the role of the Originator and the IUT having a <container> resource at RESOURCE_TARGET_ADDRESS protected by role based access control procedure and the IUT having granted the Originator access to the <container> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request containing From set to AE1_ID and To set to RESOURCE_TARGET_ADDRESS and Role ID parameter set to address the <role> resource assigned to the Originator Token ID parameter set to address the <token> resource assigned to the role of the Originator } | IUT  AE1 |
|  | then { the IUT sends a valid RETRIEVE Request to CSE1 containing From set to CSE_ID and To set to Token_ID and no Content } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/RET/005

| TP Id | TP/oneM2M/CSE/SEC/ROL/RET/005 |
| --- | --- |
| Test objective | Check that the IUT returns the result of a request on a resource protected by role based access control, when the appropriate credentials are provided in the request |
| Reference | TS-0003 7.4.3 – step 7 |
| Config Id | CF01 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the Authorization Authority having assigned a role for the Originator and the Authorization Authority having created a token associated to the role of the Originator and the IUT having a <container> resource at RESOURCE_TARGET_ADDRESS protected by role based access control procedure and the IUT having granted the Originator access to the <container> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request containing From set to AE1_ID and To set to RESOURCE_TARGET_ADDRESS and Role ID parameter set to address the <role> resource assigned to the Originator Token ID parameter set to address the <token> resource assigned to the role of the Originator } | IUT  AE1 |
|  | then { the IUT sends a RETRIEVE Response containing Response Status Code set to 2000 (OK) and Content containing <container> resource } | IUT  AE1 |

TP/oneM2M/CSE/SEC/ROL/UPD/001

| TP Id | TP/oneM2M/CSE/SEC/ROL/UPD/001 |
| --- | --- |
| Test objective | Check that the IUT updates the tokenLink attribute of the <role> resource after creating its associated <token> resource |
| Reference | TS-0003 7.4.2.3 – step 5 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched on and the IUT acting as an Authorization Authority and the IUT having assigned a role for the Originator and the IUT having created a token associated to the role of the Originator at TOKEN_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Response from CSE2 (TR) containing Response Status Code set to 2001 (CREATED) and Content containing <token> resource representation } | IUT  CSE2 |
|  | then { the IUT sends a valid UPDATE Request to CSE1 (RR) containing To set to ROLE_REPOSITORY_ADDRESS and Resource Type set to 32 (token) and Content containing <token> resource representation containing tokenLink attribute set to TOKEN_RESOURCE_ADDRESS } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ROL/NTF/001

| TP Id | TP/oneM2M/CSE/SEC/ROL/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT notifies the Originator about a token issuance associated to its role |
| Reference | TS-0003 7.4.2.3 – step 6 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being switched onthe IUT being in the "initial state" and the IUT acting as an Authorization Authority and the IUT having assigned a role for the Originator and the IUT having created a token associated to the role of the Originator } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Response from CSE2 (TR) containing Response Status Code set to 2001 (CREATED) and Content containing <token> resource representation } | IUT  CSE2 |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 (Originator) containing Content containing notificationEvent attribute containing representation attribute containing <token> resource representation } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESC/NTF/001

| TP Id | TP/oneM2M/CSE/SEC/ESC/NTF/001 |
| --- | --- |
| Test objective | Check that the IUT sends a notify request with ESCertKE message 1 when triggered |
| Reference | TS-0003 8.7.2.2 – step C.1.a, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Terminating End-Point’s Certificate Info & Identity } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT is triggered to send a valid NOTIFY Request containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE_ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | NA |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE1 ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESC/NTF/002

| TP Id | TP/oneM2M/CSE/SEC/ESC/NTF/002 |
| --- | --- |
| Test objective | Check that the IUT sends a notify response with ESCertKE message 2 when it receives a notify request with ESCertKE message 1 |
| Reference | TS-0003 8.7.2.2 – step C.1.b, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Initiating End-Point’s Certificate Info & Identity } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE1_ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 1 (TLS Message: Client Hello) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Response to CSE1 containing To set to INITIATING_ENDPOINT_ADDRESS and From set to CSE_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 2 (TLS Messages: Server Hello, Certificate*, ServerKeyExchange*, CertificateRequest*, ServerHelloDone) } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESC/NTF/003

| TP Id | TP/oneM2M/CSE/SEC/ESC/NTF/003 |
| --- | --- |
| Test objective | Check that the IUT sends a notify request with ESCertKE message 3 when it receives a notify response with ESCertKE message 2 |
| Reference | TS-0003 8.7.2.2 – step C.1.c, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having been provisioned with the corresponding private key and certificate and and the IUT having configured Terminating End-Point’s Certificate Info & Identity and the IUT having sent a notify request to the Terminating End-Point with ESCertKE Message 1 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response from CSE1 containing To set to INITIATING_ENDPOINT_ADDRESS and From set to CSE1_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 2 (TLS Messages: Server Hello, Certificate*, ServerKeyExchange*, CertificateRequest*, ServerHelloDone) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Request to CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE_ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 3 (TLS Messages: Certificate*, ClientKeyExchange, CertificateVerify*, [ChangeCipherSpec], Finished) } | IUT  CSE1 |

TP/oneM2M/CSE/SEC/ESC/NTF/004

| TP Id | TP/oneM2M/CSE/SEC/ESC/NTF/004 |
| --- | --- |
| Test objective | Check that the IUT sends a notify response with ESCertKE message 4 when it receives a notify request with ESCertKE message 3 |
| Reference | TS-0003 8.7.2.2 – step C.1.d, TS-0001 11.4.3, TS-0004 6.3.5.48 |
| Config Id | CF04 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT is being registered and the IUT being switched on and the IUT having been provisioned with the corresponding private key and certificate and the IUT having configured Initiating End-Point’s Certificate Info & Identity and the IUT having sent a notify request to the Initiating End-Point with ESCertKE Message 2 } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Request from CSE1 containing To set to TERMINATING_ENDPOINT_ADDRESS and From set to CSE1_ID and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 3 (TLS Messages: Certificate*, ClientKeyExchange, CertificateVerify*, [ChangeCipherSpec], Finished) } | IUT  CSE1 |
|  | then { the IUT sends a valid NOTIFY Response to CSE containing To set to INITIATING_ENDPOINT_ADDRESS and From set to CSE_ID and ResponseStatusCode set to OK (2000) and Content containing securityInfo element containing securityInfoType element set to 6 (ESCertKE Message) and escertkeMessage element containing base64 representation of ESCertKE Message 4 (TLS Messages: [ChangeCipherSpec], Finished) } | IUT  CSE1 |

TP/oneM2M/CSE/DAU/NOT/001

| TP Id | TP/oneM2M/CSE/DAU/NOT/001 |
| --- | --- |
| Test objective | Check that the IUT starts the Dynamic Authorization for an incoming request and sends a Notify Request to DAS including all mandatory fields. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered AE1 and the IUT having registered the DAS and the IUT having a <container> resource at TARGET_RESOURCE_ADDRESS and the <container> resource having a dynamicAuthorizationConsultationID attribute and corresponding <dynamicAuthorizationConsultation> not set to FALSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1_ID and no Content } | IUT ( AE1 |
|  | then { the IUT sends a valid NOTIFY Request to DAS containing To set to DAS_ADDRESS and From set to CSE_ID and Notification data containing securityInfo containing securityInfoType set to 1 (Dynamic Authorization Request) and dasRequest containing originator set to AE_ID and targetedResourceType set to 3 (container) and operation set to 2 (Retrieve) } | DAS ( IUT |

Editor’s Note: Config Id will be newly proposed to cover this test purpose.

TP/oneM2M/CSE/DAU/NOT/002

| TP Id | TP/oneM2M/CSE/DAU/NOT/002 |
| --- | --- |
| Test objective | Check that the IUT starts the Dynamic Authorization for an incoming request and sends a Notify Request including all mandatory fields and one ore more optional fields. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered AE1 and the IUT having registered the DAS and the IUT having a <container> resource at TARGET_RESOURCE_ADDRESS and the <container> resource has a dynamicAuthorizationConsultationID attribute and corresponding <dynamicAuthorizationConsultation> not set to FALSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1_ID and no Content } | IUT ( AE1 |
|  | then { the IUT sends a valid NOTIFY Request to DAS containing To set to DAS_ADDRESS and From set to CSE_ID and Notification data containing securityInfo containing securityInfoType set to 1 (Dynamic Authorization Request) and dasRequest containing originator set to AE_ID and targetedResourceType set to 3 (container) and operation set to 2 (Retrieve) and optionally containining originatorIP set to AE_IP originatorLocation set to location of originator of the received request originatorRole set to role of originator of the received request requestTimestamp set to time of receipt of request targetedResourceID set to identifier of the targeted resource proposedPrivilegesLifetime set to time duration of requested privileges rolesFromACPs set to list of roles of requested resource tokenIdDs set to list of token identifiers from the received request authorSignIndicator set to value specified by the received request } | DAS ( IUT |

TP/oneM2M/CSE/DAU/NOT/003

| TP Id | TP/oneM2M/CSE/DAU/NOT/003 |
| --- | --- |
| Test objective | Check that the IUT does not start the Dynamic Authorization for an incoming request and rejects that incoming request if the dynamicAuthorizationConsultationID attribute and corresponding <dynamicAuthorizationConsultation> resource can not be found. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered AE1 and the IUT having registered the DAS and the IUT having a <container> resource at TARGET_RESOURCE_ADDRESS and the <container> resource does not have a dynamicAuthorizationConsultationID attribute nor corresponding <dynamicAuthorizationConsultation> } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1_ID and no Content } | IUT ( AE1 |
|  | then { the IUT rejects the incoming request from the AE1 containing Response Status Code set to "ORIGINATOR_HAS_NO_PRIVILEGE" } | AE1 ( IUT |

TP/oneM2M/CSE/DAU/NOT/004

| TP Id | TP/oneM2M/CSE/DAU/NOT/004 |
| --- | --- |
| Test objective | Check that the IUT does not start the Dynamic Authorization for an incoming request and rejects that incoming request if the dynamicAuthorizationEnabled of a <dynamicAuthorizationConsultation> is set to FALSE. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered AE1 and the IUT having registered the DAS and the IUT having a <container> resource at TARGET_RESOURCE_ADDRESS and the <container> resource has <dynamicAuthorizationConsultation> with dynamicAuthorizationEnabled set to FALSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE request from AE1 containing To set to TARGET_RESOURCE_ADDRESS and From set to AE1_ID and no Content } | IUT ( AE1 |
|  | then { the IUT rejects the incoming request from the AE1 containing Response Status Code set to "ORIGINATOR_HAS_NO_PRIVILEGE" } | AE1 ( IUT |

TP/oneM2M/CSE/DAU/NOT/005

| TP Id | TP/oneM2M/CSE/DAU/NOT/005 |
| --- | --- |
| Test objective | Check that the IUT correctly processes a Notify response received in response to a Notify request that started Dynamic Authorization. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered AE1 and the IUT having registered the DAS and the IUT having a <container> resource at TARGET_RESOURCE_ADDRESS and the AE1 having sent a Retrieve request for the resource at TARGET_RESOURCE_ADDRESS and the AE1 having no privileges to perform RETRIEVE operation on the resource and the IUT having sent a NOTIFY Request to DAS to start Dynamic Authorization } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response containing Notification data containing securityInfo containing securityInfoType set to 2 (Dynamic Authorization Response) } | DAS ( IUT |
|  | then { the IUT sends a valid Response to AE1 containing ResponseStatusCode set to OK (2000) and Content containing <container> representation } | AE1 ( IUT |

TP/oneM2M/CSE/DAU/NOT/006

| TP Id | TP/oneM2M/CSE/DAU/NOT/006 |
| --- | --- |
| Test objective | Check that the IUT correctly processes a Notify response including a dynamicACPInfo element received in response to a Notify request that started Dynamic Authorization. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered AE1 and the IUT having registered the DAS and the IUT having a <container> resource at TARGET_RESOURCE_ADDRESS and the AE1 having sent a Retrieve request for the resource at TARGET_RESOURCE_ADDRESS and the AE1 having no privileges to perform RETRIEVE operation on the resource and the IUT having sent a NOTIFY Request to DAS to start Dynamic Authorization } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response containing Notification data containing securityInfo containing securityInfoType set to 2 (Dynamic Authorization Response) and dynAuthDasResponse containing dynamicACPInfo } | DAS ( IUT |
|  | then { the IUT creates <accesscontrolPolicy> child resource and configures the privileges, expirationTime and selfPrivileges attributes based on the data received in the dynamicACPInfo, and the IUT sends a valid Response to AE1 containing ResponseStatusCode set to OK (2000) and Content containing <container> representation } | AE1 ( IUT |

TP/oneM2M/CSE/DAU/NOT/007

| TP Id | TP/oneM2M/CSE/DAU/NOT/007 |
| --- | --- |
| Test objective | Check that the IUT correctly processes a Notify response including a tokens element received in response to a Notify request that started Dynamic Authorization. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered AE1 and the IUT having registered the DAS and the IUT having a <container> resource at TARGET_RESOURCE_ADDRESS and the AE1 having sent a Retrieve request for the resource at TARGET_RESOURCE_ADDRESS and the AE1 having no privileges to perform RETRIEVE operation on the resource and the IUT having sent a NOTIFY Request to DAS to start Dynamic Authorization } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response containing Notification data containing tokens element } | DAS ( IUT |
|  | then { the IUT sends a valid Response to AE1 containing ResponseStatusCode set to OK (2000) and Content containing <container> representation } | AE1 ( IUT |

TP/oneM2M/CSE/DAU/NOT/008

| TP Id | TP/oneM2M/CSE/DAU/NOT/008 |
| --- | --- |
| Test objective | Check that the IUT correctly processes a Notify response received in response to a Notify request that started Dynamic Authorization. |
| Reference | TS-0001 [1], clause 10.1.6 and 10.2.10.6, TS-0004 [2], clause 7.2.2.1 and 7.5.1.2.10 |
| Config Id | CF06 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being registered and the IUT being a hosting CSE and the IUT having registered AE1 and the IUT having registered the DAS and the IUT having a <container> resource at TARGET_RESOURCE_ADDRESS and the AE1 having sent a Retrieve request for the resource at TARGET_RESOURCE_ADDRESS and the AE1 having no privileges to perform RETRIEVE operation on the resource and the IUT having sent a NOTIFY Request to DAS to start Dynamic Authorization } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid NOTIFY Response NOT containing Notification data containing securityInfo containing securityInfoType set to 2 (Dynamic Authorization Response) } | DAS ( IUT |
|  | then { the IUT rejects the incoming request from the AE1containing Response Status Code set to "ORIGINATOR_HAS_NO_PRIVILEGE" } | AE1 ( IUT |

----------------------- Start of change 2 -----------------------

## ---------------------- End of change 2 -----------------------

----------------------- Start of change 3 -----------------------

## ---------------------- End of change 3 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

i.e. applying the selected object security technology using the established parameters

Not defined (Role Repository CSE)

The CSE must be somehow triggered to issue a CREATE request, maybe a new configuration should be considered. This new configuration would be like CF03, but with CSE instead of AE as SUT.