| CHANGE REQUEST |
| --- |
| Meeting:* | TDE #43 |
| Source:* | STF559 |
| Date:* | 2019-11-30 |
| Contact:* | Miguel Angel Reina Ortega, ETSI, MiguelAngel.ReinaOrtega@etsi.org |
| Reason for Change/s:* | Changes for semantic TPs release 3 |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0018-V-3.5.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Changes for semantic TPs release 3 (change 1)

----------------------- Start of change 1 -----------------------

TP/oneM2M/CSE/SEM/CRE/001

| TP Id | TP/oneM2M/CSE/SEM/CRE/001 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticDescriptor> resource which descriptor attribute does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0034 [6], clause 6.1.2, and TS-0004 [2], clause 7.4.34.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a parent resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing descriptor attribute set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not create the <semanticDescriptor> resource and the IUT sends a valid Response containing failure information with additional error information } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/002

| TP Id | TP/oneM2M/CSE/SEM/CRE/002 |
| --- | --- |
| Test objective | Check that the IUT generates a Response Status Code indicating a “ONTOLOGY_NOT_AVAILABLE” error when referenced ontology cannot be retrieved during a semantic validation process |
| Reference | TS-0004 [2], clause 7.4.34.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a local policy that allows semantic validation procedures } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and ontologyRef attribute set to a non-resolvable URI } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4118 (ONTOLOGY_NOT_AVAILABLE) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/003

| TP Id | TP/oneM2M/CSE/SEM/CRE/003 |
| --- | --- |
| Test objective | Check that the IUT generates a Response Status Code indicating a “LINKED_SEMANTICS_NOT_AVAILABLE” error when local linked <semanticDescriptor> resources cannot be retrieved during a semantic validation process |
| Reference | TS-0004 [2], clause 7.4.34.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a local policy that allows semantic validation procedures } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and relatedSemantics attribute set to a non-resolvable URI } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 4119 (LINKED_SEMANTICS_NOT_AVAILABLE) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/004

| TP Id | TP/oneM2M/CSE/SEM/CRE/004 |
| --- | --- |
| Test objective | Check that the IUT retrieves the referenced ontology from the ontology hosting CSE when performing a semantic validation as a result of a creation of a stand-alone <semanticDescriptor> resource |
| Reference | TS-0034 [6], clauses 6.1.2 and 7.10.3, and TS-0004 [2], clause 7.4.34.2.1 |
| Parent Release | Release 3 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a local policy that allows semantic validation procedures and the ontology hosting CSE having an <ontology> resource at REFERENCED_ONTOLOGY_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and descriptor attribute and ontologyRef attribute set to REFERENCED_ONTOLOGY_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a valid RETRIEVE Request containing To set to REFERENCED_ONTOLOGY_ADDRESS and Content containing <ontology> resource representation } | IUT ( CSE |

TP/oneM2M/CSE/SEM/CRE/005

| TP Id | TP/oneM2M/CSE/SEM/CRE/005 |
| --- | --- |
| Test objective | Check that the IUT sends a valid response when performing a semantic validation as a result of a creation of a stand-alone <semanticDescriptor> resource |
| Reference | TS-0034 [6], clauses 6.1.2 and 7.10.3, and TS-0004 [2], clause 7.4.34.2.1 |
| Parent Release | Release 3 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a local policy that allows semantic validation procedures and the ontology hosting CSE having an <ontology> resource at REFERENCED_ONTOLOGY_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and descriptor attribute and ontologyRef attribute set to REFERENCED_ONTOLOGY_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code indicating success of validation Content containing <semanticDescriptor> resource representation } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/006

| TP Id | TP/oneM2M/CSE/SEM/CRE/006 |
| --- | --- |
| Test objective | Check that the IUT rejects the creation request of a <semanticMashupInstance> resource, indicating a "BAD_REQUEST" error, when the <semanticMashupJobProfile> resource referenced in its smjpID attribute does not exist |
| Reference | TS-0034 [6], clause 6.4.2, and TS-0004 [2], clause 7.4.50.2.1 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing <semanticMashupInstance> resource representation containing smjpID attribute set to a reference to a non-existent <semanticMashupJobProfile> resource } | IUT ( AE |
|  | then { the IUT does not create the <semanticMashupInstance> resource and the IUT sends a valid Response containing Response Status Code set to 4000 (BAD_REQUEST) } | IUT ( AE |

TP/oneM2M/CSE/SEM/CRE/016

| TP Id | TP/oneM2M/CSE/SEM/CRE/016 |
| --- | --- |
| Test objective | Check that the IUT creates successfully the <semanticMashupInstance> resource with resultGenType set to PERIODICALLY |
| Reference | TS-0001 [1], clause 9.6.54, TS-0004 [2], clause 7.4.50.2.1, TS-0034 [6], clause 6.4.2 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform CREATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid CREATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 41 (semanticMashupInstance) and From set to AE-ID and Content containing <semanticMashupInstance> resource representation containing smjpID attribute set to a reference to the <semanticMashupJobProfile> resource at TARGET_RESOURCE_ADDRESS smjpInputParameter set to a value that does conform to the RDF/XML syntax and resultGenType is set to PERIODICALLY with a period of t1 } | IUT ( AE |
|  | then { the IUT creates a new semanticMashupInstance resource and the IUT sends a valid Response containing Response Status Code set to 2001 (CREATED) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/001

| TP Id | TP/oneM2M/CSE/SEM/UPD/001 |
| --- | --- |
| Test objective | Check that the IUT rejects the update request of a <semanticDescriptor> resource indicating a "NOT_ACCEPTABLE" error when the request contains both semanticOpExec and descriptor attributes |
| Reference | TS-0004 [2], clause 7.4.34.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS And the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing descriptor attribute set to a valid value semanticOpExec attribute set to a valid value } | IUT ( AE |
|  | then { the IUT does not update the <semanticDescriptor> resource and the IUT sends a valid Response containing Response Status Code set to 5207 (NOT_ACCEPTABLE) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/002

| TP Id | TP/oneM2M/CSE/SEM/UPD/002 |
| --- | --- |
| Test objective | Check that the IUT rejects the update request of a <semanticDescriptor> resource indicating a "NOT_ACCEPTABLE" error when the request contains a semanticOpExec attribute which does not contain a valid SPARQL query request |
| Reference | TS-0004 [2], clause 7.4.34.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing no descriptor attribute and semanticOpExec attribute set to a non-valid SPARQL query request } | IUT ( AE |
|  | then { the IUT does not update the <semanticDescriptor> resource and the IUT sends a valid Response containing Response Status Code set to 5207 (NOT_ACCEPTABLE) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/003

| TP Id | TP/oneM2M/CSE/SEM/UPD/003 |
| --- | --- |
| Test objective | Check that the IUT rejects the update request of a <semanticDescriptor> resource when the request contains a descriptor attribute which does not conform to the RDF/XML syntax as defined in RDF 1.1 XML Syntax |
| Reference | TS-0004 [2], clause 7.4.34.2.3 |
| Config Id | CF01 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing no semanticOpExec attribute and descriptor attribute set to a value that does not conform to the RDF/XML syntax } | IUT ( AE |
|  | then { the IUT does not update the <semanticDescriptor> resource and the IUT sends a valid Response containing Response Status Code set to 5207 (NOT_ACCEPTABLE) } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/004

| TP Id | TP/oneM2M/CSE/SEM/UPD/004 |
| --- | --- |
| Test objective | Check that the IUT retrieves the referenced ontology from the ontology hosting CSE when performing a semantic validation as a result of an update of a stand-alone <semanticDescriptor> resource |
| Reference | TS-0034 [6], clauses 6.1.4 and 7.10.3, and TS-0004 [2], clause 7.4.34.2.3 |
| Parent Release | Release 3 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a local policy that allows semantic validation procedures and the ontology hosting CSE having an <ontology> resource at REFERENCED_ONTOLOGY_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and descriptor attribute and ontologyRef attribute set to REFERENCED_ONTOLOGY_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a valid RETRIEVE Request containing To set to REFERENCED_ONTOLOGY_ADDRESS and Content containing <ontology> resource representation } | IUT ( CSE |

TP/oneM2M/CSE/SEM/UPD/005

| TP Id | TP/oneM2M/CSE/SEM/UPD/005 |
| --- | --- |
| Test objective | Check that the IUT sends a valid response when performing a semantic validation as a result of an update of a stand-alone <semanticDescriptor> resource |
| Reference | TS-0034 [6], clauses 6.1.4 and 7.10.3, and TS-0004 [2], clause 7.4.34.2.3 |
| Parent Release | Release 3 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> resource at TARGET_RESOURCE_ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a local policy that allows semantic validation procedures and the ontology hosting CSE having an <ontology> resource at REFERENCED_ONTOLOGY_ADDRESS } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to TARGET_RESOURCE_ADDRESS and Resource Type set to 24 (semanticDescriptor) and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and descriptor attribute and ontologyRef attribute set to REFERENCED_ONTOLOGY_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2002 (UPDATED) and Content containing <semanticDescriptor> resource } | IUT ( AE |

TP/oneM2M/CSE/SEM/UPD/006

| TP Id | TP/oneM2M/CSE/SEM/UPD/006 |
| --- | --- |
| Test objective | Check that the IUT retrieves the linked <semanticDescriptor> resource from the hosting CSE when performing a semantic validation as a result of an update of the <semanticValidation> virtual resource |
| Reference | TS-0034 [6], clauses 6.9.4 and 7.10.3, and TS-0004 [2], clause 7.4.48.2.3 |
| Parent Release | Release 3 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <ontologyRepositoy> resource at TARGET_RESOUCE ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a <ontology> resource at REFERENCED_ONTOLOGY_ADDRESS and the IUT having a local policy that allows semantic validation procedures and the hosting CSE having a <semanticDescriptor> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to the TARGET_RESOURCE_ADDRESS/smv and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and descriptor attribute and ontologyRef attribute set to REFERENCED_ONTOLOGY_ADDRESS and relatedSemantics attribute set to LINKED_SEMANTIC_DESCRIPTOR_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a valid RETRIEVE Request containing To set to LINKED_SEMANTIC_DESCRIPTOR_ADDRESS and Content containing <semanticDescriptor> resource representation } | IUT ( CSE |

TP/oneM2M/CSE/SEM/UPD/007

| TP Id | TP/oneM2M/CSE/SEM/UPD/007 |
| --- | --- |
| Test objective | Check that the IUT sends a valid response when performing a semantic validation a semantic validation as a result of an update of the <semanticValidation> virtual resource |
| Reference | TS-0034 [6], clauses 6.9.4 and 7.10.3, and TS-0004 [2], clause 7.4.48.2.3 |
| Parent Release | Release 3 |
| Config Id | CF02 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <ontologyRepositoy> resource at TARGET_RESOUCE ADDRESS and the AE having privileges to perform UPDATE operation at TARGET_RESOURCE_ADDRESS and the IUT having a <ontology> resource at REFERENCED_ONTOLOGY_ADDRESS and the IUT having a local policy that allows semantic validation procedures and the hosting CSE having a <semanticDescriptor> resource } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid UPDATE Request from AE containing To set to the TARGET_RESOURCE_ADDRESS/smv and From set to AE-ID and Content containing <semanticDescriptor> resource representation containing validationEnable attribute set to “True” and descriptor attribute and ontologyRef attribute set to REFERENCED_ONTOLOGY_ADDRESS and relatedSemantics attribute set to LINKED_SEMANTIC_DESCRIPTOR_ADDRESS } | IUT ( AE |
|  | then { the IUT sends a valid response containing Response Status Code indicating success of validation Content containing <semanticDescriptor> resource representation } | IUT ( CSE |

TP/oneM2M/CSE/SEM/RET/006

| TP Id | TP/oneM2M/CSE/SEM/RET/006 |
| --- | --- |
| Test objective | Check that the IUT accepts a valid semantic discovery request for group members hosted at other CSE and sends a discovery request to the remote CSE |
| Reference | TS-0034 [6], clauses 6.2.2 and 7.4 |
| Config Id | CF02 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having <semanticDescriptor> having linked semantic resource at remote CSE and no restrictions from ACPs } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS containing <semanticFanOutPoint> and not containing <Semantic Query Indicator> parameter } | IUT ( AE |
|  | then { the IUT sends a valid RETRIEVE Request containing To set to address of linked semantic resource at remote CSE } | IUT ( CSE2 |

TP/oneM2M/CSE/SEM/RET/007

| TP Id | TP/oneM2M/CSE/SEM/RET/007 |
| --- | --- |
| Test objective | Check that the IUT accepts a valid semantic discovery response for group members hosted at other CSE and sends a discovery response to the originating AE |
| Reference | TS-0001 [1], clauses 8.1.2, 9.6.14a, 10.2.7.12 and 10.2.14, and TS-0034 [6], clauses 6.2.2 and 7.4 |
| Config Id | CF02 |
| Parent Release | Release 3 |
| PICS Selection | PICS_CSE |
| Initial conditions | with { the IUT being in the "initial state" and the IUT having registered the AE and the IUT having a <semanticDescriptor> resource having linked semantic resource at remote CSE and no restrictions from ACPs and the IUT having received a valid RETRIEVE Request from AE containing To set to TARGET_RESOURCE_ADDRESS containing <semanticFanOutPoint> and Filter Criteria containing semanticsFilter condition set to a valid SPARQL query request not containing <Semantic Query Indicator> parameter and the IUT having sent a valid RETRIEVE Request containing To set to address of linked semantic resource at remote CSE } |
| Expected behaviour | Test events | Direction |
|  | when { the IUT receives a valid Response from CSE2 containing Response Status Code set to 2000 (OK) and containing Semantic resource from remote CSE } | IUT ( CSE2 |
|  | then { the IUT sends a valid Response containing Response Status Code set to 2000 (OK) and Semantic resource discovery result containing URI (of child resource with target semanticDescriptor) } | IUT ( AE |

## ---------------------- End of change 1 -----------------------

----------------------- Start of change 2 -----------------------

## ---------------------- End of change 2 -----------------------

----------------------- Start of change 3 -----------------------

## ---------------------- End of change 3 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

Spec is not clear

Reference Specs are not clear if response should be sent periodically.